## Slide 1: Target station and optimization studies for ESS Super Beam
E. Baussan, M. Dracos, N. Vassilopoulos IPHC/CNRS

## Slide 2: layout
Target station description
Target
Horn
Studies on physics potential (sys. errors 5 % signal, 10% background, mass hierarchy assumed not known )
Proton beam energy
Horn’s current
Target and decay tunnel length
also
Particle yield
Perfect focusing vs horn’s focusing vs no focusing
Energy deposition, radiation (neutrons), muons (near detector location)
Thanks to
Chris Densham and his team for the target studies et
Enrique Fernandez for the globes calculations and his input on results

## Slide 3: ESS Super beam layout (adopted from SPL Super Beam - EUROnu)
Switching yard to four proton beams or accumulator rings
Iron (2.2 m) and concrete (3.7 m) shielding
Decay tunnel
He vessel (25 m)
PSU
Beam dump
Concrete surrounding shielding) (8 m)
Concrete surrounding shielding (8 m)
4-targets/horns
Vessel (He)

## Slide 4: Super beam Four-horn/target station

## Slide 5
He vessels

## Slide 6: Target: packed bed
Large surface area for heat transfer
Coolant able to access areas with
highest energy deposition
Potential heat removal rates at the hundreds of kW level
Pressurised cooling gas required at high power levels
Minimal stresses
Tests of such a target are planned using the
HiRadMat high intensity proton irradiation facility at CERN
Full study in EUROnu.org, arXiv:1212.0732 (SPL super beam)
Beam window, Be is a candidate
Pressure stresses can be dealt by having a hemispherical window design
Separation from target station coolant
Titanium alloy cannister containing packed bed of titanium or beryllium spheres
Cannister perforated with elliptical holes graded in size along length

## Slide 7: Stresses for the Packed bed target
EUROnu example, 24mm diameter cannister packed with 3mm Ti6Al4V spheres
Quasi thermal and Inertial dynamic stress components
ideally spill time > oscillation period

## Slide 8: Horn evolution
evolution of the horn shape after many studies:
triangle shape (van der Meer) with target inside the horn : in general best configuration for low energy beam
triangle with target integrated to the inner conductor : very good physics results but high energy deposition and stresses on the conductors
forward-closed shape with target integrated to the inner conductor : best physics results, best rejection of wrong sign mesons but high energy deposition and stresses
forward-closed shape with no-integrated target:
best compromise between physics and reliability
4-horn/target system to accommodate the MW power scale
details in WP2 notes @ http://www.euronu.org/

## Slide 9: Horn studies
horn structure
  Al 6061 T6 alloy good trade off between mechanical strength, resistance to corrosion, electrical conductivity and cost
  horn thickness as small as possible: best physics, limit energy deposition from secondary particles but thick enough to sustain dynamic stress
horn stress and deformation
  static mechanical model, thermal dilatation
  magnetic pressure pulse, dynamic displacement
  Horn lifetime at least 1 year from fatigue analysis (30 – 60 MPa max stress depending on HTCs)
  60 water jets for cooling
Full study in EUROnu,
arXiv:1212.0732

## Slide 10
displacements and stress plots just
before and on the peak
  stress on the corner and convex region
  stress on the upstream inner due to pulse
  uniform temperature minimizes stress, max = 30 MPa
peak magnetic field each T=80ms (4-horns operation)
Stress due to thermal dilatation and magnetic pressure for 350 kA @ 12.5 Hz
  Smax = 30 MPa
modal analysis, eigenfrequencies
f = {63.3, 63.7, 88.3, 138.1, 138.2, 144.2} Hz
TAl-uniform= 60 0C
umax = 2.4 mm
  Smax = 60 MPa
TAl-max= 60 0C,
umax = 1.12 mm
inner
outer
t= 79.6 ms
t= 80 ms
t= 80 ms

## Slide 11: Are the adopted SPL Super Beam parameters fit well the ESS case ?
Parameter | SPL | ESS
Power (MW) | 4 | 5
Ep+ (GeV) | 4.5 | 2, 2.5
Baseline (km) | 130 | 365, 540
Target | Packed-bed | Packed-bed
Target length (cm) | 78 | 53-78
Target radii (cm) | 1.5 | 1.5
Horn | Forward closed | Forward closed
Horn current (kA) | 350 @ 12.5 Hz | 350 @ 14 Hz
# of horns/targets | 4 | 4
Tunnel length (m) | 25 | 15-25
Tunnel radii (m) | 2 | 2
Exposure (years) | 2 ν + 8 anti-ν | 2 ν + 8 anti-ν

## Slide 12: Reminder: collection of possible detector locations in Sweden
Many mines (active or not) are available
What is the optimal position for CPV?
MH might be discovered at 5σ with including atmospheric ν
P(νμ− νe)
L/E (km/GeV)
Dm2sun=7.6x10-5 eV2
Dm2atm=2.4x10-3 eV2
q23=44.4°
q12=34.4°
q13=9.3°
dCP=0
E~290 MeV

## Slide 13: are our candidate baselines good enough?
Yes

## Slide 14
Very good baselines for the following mines :
Zinkgruvan at 365 km
Garpenberg at 540 km
Site studies under way

## Slide 15: Horn Current ?
lower p.o.t. per year for this study
– not to compare with main results
The larger the better (B~I/r)
350 kA baseline
PSU study: Arxiv:1304.7111
Very good fit to 365 and 540 km baselines
3σ
5σ
450 kA
350 kA
300 kA
365 km
540 km

## Slide 16
νe contamination increases with respect to DT length, radii
Lower than 1 %
@ L = 25 m, 50 % of π+ s decay
νe contamination, for detected neutrinos
current situation

## Slide 17
anti-νμ contamination decreases with respect to DT length
anti-νμ contamination for detected neutrinos
current situation

## Slide 18: is the increased νe contamination more significant than the increased flux ?
try the following tunnel parameters:
Length (m) | Radius (m) | % of decayed π+
25 (baseline) | 2 (low-limit for 4-horns) | 50
50 | 2 | 72
100 | 2 | 92

## Slide 19
No significant increase in physics performance by using lengthier decay tunnel
tunnel length

## Slide 20: Systematics, time vs physics
Baseline
time x 2
time x 0.5

## Slide 21
Can we use a smaller target and decay tunnel ?
not-defocused wrong signπs

## Slide 22
Can we use a smaller target and decay tunnel ?
for neutrino beam
detected

## Slide 23: Particle production at target
ESS Ti packed-bed |  |  | 
particles/p+ | π+ | π- | n
r1.25 | 0.27 | 0.17 | 4.4
r1.50, L78 (baseline) | 0.29 | 0.17 | 4.8
r1.50, L63 | 0.28 | 0.17 | 4.5
r1.50, L53 | 0.26 | 0.16 | 4.3
r2.00 | 0.30 | 0.18 | 5.3
SPL | 0.67 | 0.52 | 6.6
For a year there are 2.8 more protons in ESS than SPL
Particles per p+ for baseline ESS target parameters and also for different radii, lengths
SPL is shown for comparison (fluka 2013)

## Slide 24
the target size and decay tunnel length could be reduced at no-cost
Less irradiation
Smaller civil-engineering cost
target length

## Slide 25: Perfect focusing studies is the horn focusing well ?
Examine the quality of focusing
Compare neutrino fluxes or events of perfect focus and no focus with the specified optics
Application depends on the focusing optics and particle production for low, medium and high energy beams
Method: focus parallel (PT=0, PZ=P) in respect to the beam axis all charged particles at the exit of target with a given acceptance limit
Comparison between ESS and CNGS beams

## Slide 26: pf vs nf vs focus
perfect focusing
present focusing
no focusing
ESS, no reflector
CNGS, 1 horn + 1 reflector
pf with 22 mrad
acceptance
with 1500 mrad acceptance

## Slide 27: focusing-defocusing effect of the optics π+, π- at the entrance of decay tunnel
CNGS
ESS
CNGS: Stronger focusing effect due to higher beam energy, lower θs
and acceptance @ production
ESS: good focusing effect, large θs and wider acceptance range @ production
100 (mrad)

## Slide 28: ESS with adopted parameters offers the best physics after LENF
LENF, Low Energy Neutrino factory (2000 m, 100 kt MIND, 4 MW)
SPL Super Beam, CERN to Frejus (120 km, 500 kt WC, 4 MW)
ESS Super Beam (540 km, 365 km 500 kt WC, 5 MW)
LBNO, CERN to Pyhasalmi (SPS, 2300km, 20 kt, 100 kt LAr, 0.8 MW )
T2HK Japan Super Beam Project(300 km, 560 kt WC, 1.6 MW)
LBNE USA long Baseline (1300 km, 10 kt, 33 kt LAr, 0.8 MW, 2.3 MW)
Unknown
Mass Hierarchy
Normal
Mass Hierarchy discovered

## Slide 29: simulation layout for radiation fluka, flair gui/analysis iron-shields, concrete, molasse, He
decay tube
beam dump
horn/target gallery
superbeam

## Slide 30: horn/target gallery
geometry for horn/target gallery – including holes:
5 cm longitudinal holes
transversal 3 cm see-through holes –
to see the effect

## Slide 31: ESS/SPL power distribution iron, concrete, molasse, He
P tot = 4.2 / 3.4 MW
beam dump
graphite = 950/778 kW
iron = 195/229 kW
surr. concrete= 4/4 kW
decay tunnel
iron vessel = 424/390 kW
upstream iron = 670/610 kW
surr. concrete = 467/485 kW
horns/target gallery
iron = 613/437 kW
horn = 50/ 32 kW
target = 168/ 85 kW
kW/cm3

## Slide 32: ESS neutron flux iron, concrete, molasse, He
neutron/cm2/p+
SPL shielding achieves 10 μSv/h above target and horn, for ESS might be sufficient
On-going studies

## Slide 33: ESS muon flux iron, concrete, molasse, He
μ+/cm2/p+
Preliminary, needs more stats
Near detector could be placed few 10ths
of meters after the bump dump gallery

## Slide 34: summary
ESS has the best physics performance after LENF with adopted SPL’s secondary beam parameters
Additional irradiation due to higher power and less proton energy for ESS looks manageable
Studies on going
Thanks

## Slide 35: Energy Deposition from secondary particles @1.3 MW @SPL
Ptg = 105kW
Ph = 62kW
9.5kW
2.4kW
1.7kW
1.3kW
36kW, t=30mm
2.5kW
target Ti=65%dTi , RTi=1.5cm
8.6kW, t=35mm
radial profile of power density kW/cm3
max

## Slide 36: horn lifetime
lower than 60 MPa expected
highly conservative
1.25 108 pulses = 200 days = 1 year

## Slide 37
Cumulative pion production at target

## Slide 39: Reminder: ESS neutrino super beam
Based on ESS arXiv:1212.5058, EUROnu WP2 for SPL super beam, WP5 for MEMPHYS studies, Phys. Rev. ST Accel. Beams 16, 061001 (2013)
ESS Linac, (2.5 (2) GeV, 5 MW, modified for 50 Hz super beam)
Target
~ 290 MeV νμ beam to far MEMPHYS
water Cherenkov detector
decay tunnel
Accumulator
ring
Magnetic
horn capture
(collector)
Proton driver
hadrons
νμ
p
~400 – 500 km
Beam switchyard or
Four accumulators
four horns/targets
station
PSU
decay tunnel
beam dump

## Slide 41: SPL: Activation in molasse
study set up:
packed Ti target, 65%dTi
4MW beam, 4horns, 200days of irradiation
minimum activation leads to minimum water contamination
22 Na and tritium could represent a hazard by contaminating the ground water
CERN annual activity constraints in molasse (0.3mSv/year for the public through water) |  | Super Beam
22 Na | 4.2 x 1011 Bq | ~108 Bq
tritium | 3.1 x 1015 Bq | ~108 Bq
molasse @ CERN
concrete
Activity distribution
preliminary
Activation lower than CERN’s limits

## Slide 42
Radiation Studies for horn/target gallery
prompt dose rates vs. concrete depth above shielding
power distributions @ 4 MW
iron collimator for power supply area
10 μSv