## Slide 1: Mu2e Extinction Systems
Peter Kasper
NuFACT 2013

## Slide 2: Mu2E
Mu2E goal is to measure the ratio of rates m- + N  e- + N / m- + N  νμ + N- with single event sensitivity of <10-16
Will use a proton beam to create muons that are transported and captured on an Al target
m
105 MeV e-
Signal is the delayed production of a 105 MeV mono-energetic electron

## Slide 3: Extinction
Most backgrounds are prompt
So use a pulsed beam and look for the signal candidates between pulses
To maintain sensitivity out-of-time protons must be suppressed at the 10-10 level
Extinction is the out-of-time to in-time ratio
10-10 Extinction

## Slide 4: Overview: Proton Delivery
Booster
Main Injector/Recycler
Delivery Ring (formerly pBar Debuncher)
Mu2e
One Booster batch (4x1012 protons) is injected into the Recycler.
It is divided into 4 bunches.
These are extracted one at a time to the Delivery Ring
  Period = 1.7 msec
As a bunch circulates, it is resonantly extracted to produce the desired beam structure.
  ~3x107 protons/bunch

## Slide 5: Extinction Systems
In ring
  Beam delivery technique automatically gives good extinction < 10-5 going into the Delivery Ring
  Studying possible degradation during the spill
In beam line
  System of dipoles and collimators
  Additional factor of 10-7 should be possible
Monitoring
  Need to show that 10-10 has been achieved

## Slide 6: Delivery Ring
Start with < 10-5 level of extinction going into the Delivery Ring, so the issue is how will it grow during the spill.
Effects considered
  RF noise
  Intrabeam scattering
  Beam loading
  Beam-gas interaction
  Scattering off of extraction septum
Should be possible to maintain an extinction level of 10-5

## Slide 7: Extinction Beam Line
Delivery Ring
Extinction Beam Line
Mu2e Experiment
The proton delivery beam line will contain a system of resonant dipoles (“AC dipoles”) and collimators to eliminate out of time beam

## Slide 8: Generic Extinction Analysis
Beam fully extinguished when deflection equals twice full admittance (A) amplitude
At collimator:
Angle to extinguish beam
Assume resonant dipole deflects out-of-time beam into a collimation system
Assume that the beam line admittance is equal to the collimation channel’s admittance
Assume beam occupies entire admittance
At dipole:

## Slide 9: Magnet Considerations
Bend strength to extinguish:
Stored Energy:
Large bx, long weak magnets
- Assume bx=250m, L=6m
- Factor of 4 better than bx=50m, L=2m

## Slide 10: AC Dipole Wave Form
Of the options considered:
½ harmonic – (2/17) * 17/2 harmonic seems most promising
Bunch length
Transmission window

## Slide 11: Beam Line Structure
Upstream of extinction dipole
  Collimation to define a 50 p-mm-mr beam line admittance
AC dipole region
  Bend plane: b=250m
  Non-bend plane: waist
Extinction collimation
  Minimize transmission of scraping particles
Post-extinction
  High dispersion region for momentum collimation.

## Slide 12: Extinction Beam Line Optics
Momentum collimation
AC Dipole section
Collimation section
Momentum collimation and targeting optics

## Slide 13: Proton flux vs time of flight
Time (ns)
Extinction Region
Collimator Material:
Extinction < 5x10-8 over range of interest for optimized collimators
This is multiplied by the Delivery Ring factor to produce a total extinction of < 5x10-12
The extinction beam line was simulated using STRUCT and MARS

## Slide 14: Monitor Objectives
Demonstrate 10-10 extinction
  Assume ≈ 3 x 107 protons/bunch
  Not possible to measure 10-10 with a single bunch
     Integrate over many bunches
  Integration time should be < ≈ 1 hour
Only protons hitting the target can cause backgrounds
  Monitoring beam itself will lead to a potentially large over estimate of the background to the experiment
   Monitor target interaction products

## Slide 15: Requirements: Signal Rate
Determined from beam intensity
  ~3 x 107 protons/bunch
  Bunch rate: 0.6 MHz @ 33% duty factor
   ~2 x 1016 in-time protons/hr
  10-10 extinction  ~2 x 106 out-of-time protons/hr
A signal detection rate of ~10-6 events per proton-on-target will result in ~2 out-of-time events per hour if the extinction is 10-10

## Slide 16: Requirements: Background
Out-of-time background << a few events/hr
Background sources
  Cosmic rays
  Late hits from in-time interactions
  Induced radioactivity
  Electronic noise
  Off-target beam interactions
    Potentially the most dangerous source
    Cannot be measured with beam-off running
    Not easily distinguished from real signal

## Slide 17: Filter + Detector Strategy
Filter
  Selects a sample of suitable secondaries and delivers them to the detector
  Sets the per proton detector signal rate
  Shields the detector from unwanted interaction products
Detector
  Measure “in-time” and “out-of-time” signal rates with equal or known relative efficiency
  Must have LOW “out-of-time” backgrounds compared to signal rate

## Slide 18: Layout
Target
(too small to see)
Production solenoid
Protection collimator
Proton beam line
20 m
Proton absorber and extinction monitor filter
Muon transport solenoid
Extinction monitor is located above and behind primary beam dump

## Slide 19: Filter Design
Locates detector outside target hall
  Easy access for detector maintenance
  Lots of room for shielding
  Low radiation levels for detector + electronics
Entry collimator
  Located in concrete above the primary beam dump
  Access forward produced high momentum secondaries
Filter magnet
  Permanent dipole oriented to transmit ~4.5 GeV/c secondaries
Exit collimator
  Admits signal particles through a 2m thick shield wall

## Slide 20: Filter Layout
Primary beam absorber
Exit collimator
Filter magnet
Entry collimator
Detector room

## Slide 21: Detector Components
Pixel spectrometer
  Reconstruct and count tracks in 25 ns time bins
  Provides the extinction measurement
6 fast scintillator counters
  Provide a trigger for the pixels
  Also measure the time structure of the beam
Hadron calorimeter / muon range stack
  Measures the muon content of the signal
  Expected to be low
  A higher out-of-time muon fraction would indicate an upstream source

## Slide 22: Detector Layout
Pixel detectors
8 planes
Dipole magnet
Trigger counters
Calorimeter

## Slide 23: Expected Signal Rate
0.83x10-6 /p.o.t. tracks pass through all 8 pixel planes
Momentum range 3.5 to 5.5 GeV/c
Parallel to within 0.02 radians
85% protons and 13% pions

## Slide 24: Pixels
Signal/noise = 15,000 / 121 electrons
Radiation hard to 300 Mrad (expect <1 Mrad/yr)
Tracking efficiency >97%
Signal non-linearity <1%
4 upstream planes with 4 x 3.5 cm active area
  Each plane comprised of 4 Atlas style FE-14 sensor chips with 26,880 pixels per chip
  Pixel size is 250 x 50 μm
4 downstream planes with 4 x 5.1 cm active area
  6 chips per plane
Magnet
  Permanent dipole 0.14 T.m.
  Main purpose is to prevent electrons from stopped muon decays from forming tracks

## Slide 25: Background Simulations
Cosmic rays < 0.01 tracks/hr
Fake out-of-time track rate << 7x10-4 /hr
Calculated using hits from any of
  Late hits from in-time interactions
    Spatially correlated
  Radioactive decays (3x10-4 hits/25ns clock tick)
  Electronic noise (6x10-5 hits/25ns clock tick)
  Cosmic rays (< 6x10-8 hits/25ns clock tick)

## Slide 26: Off-target Backgrounnd
Interactions where the beam enters the production solenoid generate signals in the extinction monitor
Rate depends on beam structure
Assume out-of-time beam is flat over defining aperture at end of extinction beam line
Simulated beam transport through final focus optics
  Only about 0.2% hit the target
Without the protection the off-target extinction signal would be twice the on-target rate
With the protection it is <5% of the on-target rate

## Slide 27: Summary
Looks feasible
Extinction at the 10-12 level seems to be achievable
Monitoring at the 10-10 level on a 1 hour time scale should also work