## Slide 1
2026 MicroTCA/ATCA Workshop for Large Scientific Facility Control Sep.14-Sep.17 2026, HEPS Campus, Huairou, Beijing, China
Design and Application of a MicroTCA.4-Based Embedded Event Receiver for CSNS-II
Sinong Cheng*, Peng Zhu, Yuliang Zhang

## Slide 2: CSNS Timing System
The timing system using an Event system, that the event generator (EVG) and event receivers (EVR) as the main structures of a multi-level star structure.
Standard VME architecture @ MRF

## Slide 3: Requirements of CSNS-II Timing System
CSNS & CSNS II
80MeV
324MHz Spoke
Cavities
648MHz elliptical
Cavities
154MeV
303MeV
To rise the beam power
1st harmonic cavity
2nd harmonic cavity
LINAC LLRF  add
3 additional 2nd harmonic (MA) cavities
1.6GeV
RCS LLRF  upgrade
Notes: CSNS II工程已通过国家审批，今年正式开工建设。直线加速器采用低温超导加速技术将负氢粒子从80MeV提升至300MeV，快同步循环加速器增加多个磁合金腔，进一步提高束流通过率和降低束流损失，由此看出，高频系统的LLRF是CSNS II加速器稳定运行的关键之一，为此，定时系统的顶层方案设计应符合主流架构基础上优先考虑LLRF需求。

## Slide 4: Limitations of Existing Event Receivers
Existing CSNS timing hardware (VME-based)
EVG / EVR / Fanout to devices
Existing EVRs rely on an external CPU / VME controller for register access and control
-> redundant per-station hardware, higher integration & maintenance cost
-> core devices (VME controller) obsolete, supply hard to sustain
Goal: a self-reliant, single-board embedded EVR on an indigenous MicroTCA.4 platform

## Slide 5: General Design of the Embedded EVR
Xilinx Zynq-7000 SoC (PS: dual-core ARM Cortex-A9 + PL: Kintex-7-class fabric); no dedicated CPU / MCH controller required for the timing function itself
Embedded EVR AMC block diagram (Zynq SoC)
One MicroTCA.4 chassis shared by Timing AMC and device AMCs (M-LVDS & PCIe backplane)

## Slide 6: Embedded EVR Hardware
Embedded EVR AMC board (Zynq-7045)
Front-panel FMC board: 4 out / 2 in (LEMO), DS1023 delay chips
• Core: Xilinx Zynq XC7Z045 SoC (dual ARM Cortex-A9 + programmable logic)
• Optical event input: pluggable QSFP module, 1.62 Gbps line rate; GTX transceiver up to 9.72 Gbps
• Dual 10 GbE ports for network management and data transfer
• FMC (FPGA Mezzanine Card) interface for pulse I/O expansion, and gives 4 out / 2 in
• AMC / MMC compliant with MicroTCA.4 hot-swap and management

## Slide 7: I/O Expansion via the Rear Transition Module (RTM)
Optical RTM: 8 TX + 1 RX (fiber)
Electrical RTM: 12 out + 1 in (RX fiber)
• Same AMC, rear backplane connector accepts either RTM variant to scale I/O without redesigning the core board:
• Optical RTM -> 8 optical outputs + 1 optical input
• Electrical RTM -> 12 electrical outputs + 1 electrical input
• Lets one embedded EVR platform serve both fiber-based and coax-based downstream devices

## Slide 8: Event Decoding and Trigger Generation Logic
On-chip logic analyzer capture of the decoded event-code stream
• GTX CDR + byte/word alignment + 8B/10B decode -> recovered event clock & event code
• Event FIFO buffers decoded codes; Mapping RAM converts event code -> channel; Programmable Pulse block generates delay/width-configurable outputs
• FPS Map: dynamic mapping between Distributed Bus (DBus) and pulse channels
• “Reset-relock” phase strategy: repeatedly reset the CDR until the recovered clock locks to the target phase relative to the EVG event clock -> deterministic multi-node sync

## Slide 9: Three-Layer EPICS Software Architecture
Embedded Linux (PetaLinux) on the Zynq PS; UIO maps AXI-Lite registers into user space
Hardware Abstraction Layer
register_read/write, dma_transfer_start - hides UIO/DMA details
Record Adapter Layer
binds EPICS records (ai/ao/waveform) to the HAL API
Application Interface Layer
waveform loading, parameter validation, data read-back
-> a fully standardized, on-board IOC (EPICS Channel Access) in a single MicroTCA.4 slot

## Slide 10: Jitter Test Against the RF Reference
A 324 MHz RF source is split to (1) an oscilloscope reference channel and (2) the VME event-generation chain; the embedded EVR recovers the event clock / trigger pulse from the same optical event stream, so the measured jitter excludes any commercial-EVR intermediate stage.

## Slide 11: Synchronization Jitter vs. RF Reference
(a) Event clock vs. RF reference - RMS = 13.7 ps
(b) Trigger pulse edge vs. RF reference - RMS = 14.1 ps
RMS synchronization jitter of both the output event clock and pulse signals, relative to the RF reference, is less than 15 ps

## Slide 12: Comparison with Commercial Timing Systems
Key metric | MRF timing system | SINAP timing system | Embedded EVR
System architecture | Separate (needs external controller) | Separate (needs external controller) | Highly integrated, single board (SoC runs standalone)
Control method | Remote bus access (PCIe / VME) | Remote bus access (PCIe / VME) | On-board IOC (Linux + EPICS)
Output jitter (RMS) | ~ 10 ps | ~ 8 ps | ~ 14 ps
Serial line rate | 2.5 Gbps | 2.5 Gbps | Up to 9.72 Gbps
Comparable (or better) synchronization precision, without a dedicated CPU controller or remote-bus dependency, at a higher serial line rate.

## Slide 13: CSNS-II RCS LLRF Timing Substation
Timing AMC
Middle: Timing AMC; Bottom: RCS ring-RF (LLRF) MicroTCA.4 chassis (12 AMC slots)
• Deployed during the 2025 summer maintenance of CSNS-II: the Timing AMC chassis is co-located, in the same equipment rack, with the RCS ring-RF (LLRF) 12-slot MicroTCA.4 chassis
• Timing-to-LLRF signal interconnect (m-LVDS interface): pk-pk jitter only 270 ps
• Field-measured output after fiber transmission to the device terminal:
• RMS jitter 118 ps, pk-pk jitter 970 ps (req. 1 ns RMS / 5 ns pk-pk)
• delay resolution: coarse 1 ns + fine 10 ps, two-stage tuning
• Continuous online operation for over six months with no functional or performance degradation

## Slide 14: Summary
• Designed and implemented a highly integrated embedded EVR on an indigenous MicroTCA.4 platform: Xilinx Zynq SoC decodes high-speed optical event frames and generates high-precision triggers without any external controller
• Built a tightly integrated embedded-Linux + EPICS software stack (hardware abstraction / record adapter / application interface layers) implementing a standardized on-board IOC
• Measured RMS synchronization jitter of the output event clock and pulse signals, relative to the RF reference, of less than 15 ps - on par with, or better than, existing commercial MRF / SINAP timing systems
• Deployed in the CSNS-II RCS LLRF timing substation with over six months of continuous, fault-free online operation, fully meeting CSNS-II's timing and synchronization requirements

## Slide 15: Thanks for your attention!