## Slide 1: Experiment of Parity-Violation Measurement on GTAF-II
Luo Qiuyue
Sep. 23, 2026
Notes: Opening: self-introduction; topic: NOPTREX parity-asymmetry measurement on CSNS Back-n GTAF; outline of principle / setup / target sections.

## Slide 2: Contents
1. Experimental principle
2. Experimental setup
3. Data processing
4. Follow-up plan
Notes: Outline of the four sections; highlights: logic chain of the principle, four setup components, comparison of three target nuclides.

## Slide 3: NOPTREX(Neutron Optics Parity and Time Reversal Asymmetry Experiment)
New source of CP violation
  Sakharov conditions: the baryon asymmetry of the universe (BAU) requires C/CP violation.
  The CP violation from the CKM matrix of the SM is ~10 orders of magnitude smaller than required by observation.
T violation and P violation
  CPT theorem: CP violation ⇔ T violation.
  Towards T violation: the same matrix element amplifies the P-odd T-odd cross section:
S-p wave mixing model in neutron nuclear reactions
  S wave () and p wave ( have opposite parity; when the total angular momentum is the same, weak-interaction mixing occurs.
  The observable of s-p mixing is the longitudinal asymmetry
  P-odd effects are amplified by 1.
  Longitudinal asymmetries of have been observed in 75 resonances of 18 nuclides.
Basic principle of NOPTREX
  Amplification platform: s-p mixing of low-energy neutron compound-nucleus resonances
  Method: polarized neutrons (+ polarized target) measure the longitudinal asymmetry at the p-wave resonance;
Fig. 1 Neutron helicity under parity transformation
[1] V. V. Flambaum, O. P. Sushkov, Nucl. Phys. A 435, 352 (1985). [2] G. E. Mitchell, J. D. Bowman, S. I. Penttilä, E. I. Sharapov, Phys. Rep. 354, 157 (2001). [3] D. C. Schaper, Ph.D. Dissertation, University of Kentucky (2022).
4] X. Qin et al., Sci. China-Phys. Mech. Astron. 69, 282011 (2026).
Fig. 2 Feynman diagram of s-p weak mixing in the (n,γ) channel
Notes: Line 1: why a new CP-violation source is needed (Sakharov / SM shortfall / CPT→TRIV).
Line 2: how NOPTREX searches (s-p mixing amplification; polarized neutrons measure P-odd, observable A_L; same matrix element amplifies T-odd).
Bottom line: the PV measurement is the calibration step towards CP/T violation.

## Slide 4: Setup system of parity-violation measurement on GTAF-II
Overall beamline layout
  The main detector sits at white-beam station ES#2, flight path ~77 m
  The polarizer and flipper are placed between ES#1 and ES#2 to reduce scattered-neutron background;
Fig. 3 Layout of the Back-n GTAF polarized-neutron measurement system
[1] D. C. Schaper, Ph.D. Dissertation, University of Kentucky (2022).
[2] X. Qin et al., Sci. China-Phys. Mech. Astron. 69, 282011 (2026).
Fig. 4 Polarizer and spin flipper
Fig. 5 One of the guide-field solenoids
Fig. 6 GTAF-II detector array
Polarizer
Flipper
Guide-field solenoid(~7m)
GTAF-II
ES#1
Beam dump
Notes: Use Fig. 5 for the layout: Back-n ~77 m, 25 Hz; collimator→polarizer→flipper→guide→GTAF→dump.
Long flight path → TOF resolution resolves the 0.75 eV resonance.
Design: polarizer/flipper upstream to cut background, non-magnetic materials, 8-step sequence suppresses systematic errors.

## Slide 5: In-situ SEOP polarized 3He neutron polarizer
In-situ 3He neutron polarizer
  Alkali-metal polarization: circularly polarized laser polarizes alkali atoms via SEOP (spin-exchange optical pumping)
  3He polarization: spin exchange in alkali-3He collisions
  Neutron polarization: n+3He→3H+p+0.764 MeV; neutrons with spin anti-parallel to the 3He nuclear spin have a higher reaction cross section;
  Neutron polarization:
  where is the neutron polarization; the 3He number density; the neutron absorption cross section; the polarizer cell length; the 3He polarization.
Performance
  Compact system: 55×56×48 cm³, mass <50 kg, ,
Polarizer (in-situ 3He)
Spin flipper
Guide-field solenoids
Fig. 7 Polarizer-flipper-guide-field transport system
[1] X. Qin et al., Sci. China-Phys. Mech. Astron. 69, 282011 (2026).
[2] J. Tang et al., Chin. Phys. Lett. 42, 022901 (2025).
Fig. 8 Polarizer
Notes: Three arrows in Fig. 7: polarizer (in-situ 3He) / flipper / guide field.
Polarization principle: spin-dependent absorption of n+3He; P_n=tanh(nσlP_He).
SEOP chain and in-situ advantages; P_He=70.33% → P_n=30.31% at 0.75 eV; compact-system specs.

## Slide 6: Adiabatic spin flipper
Purpose
  Flip the spin at high frequency to cancel systematic errors from stray transverse fields and detector temperature drift;
  the 3He system cannot reverse at high frequency.
Structure and performance
  Length 1.75 m; longitudinal gradient coils (16 A) + transverse rotating coils (10 A) + three compensation coil sets; zero-crossing deviation <2 mm.
  Flipping efficiencies ~90% (on) and ~70% (off) at 0.34 Å
  Flipper states tagged with the T0 time base, synchronization error <1 ms; 8-step flip sequence (+,0,0,-,0,-,+,0), flip period 10 pulses (0.4 s).
Fig. 9 Coil field direction in flipper OFF/ON states
Fig. 10 Spin flipper
[1] G. E. Mitchell, J. D. Bowman, S. I. Penttilä, E. I. Sharapov, Phys. Rep. 354, 157 (2001).
[2] D. C. Schaper, Ph.D. Dissertation, University of Kentucky (2022).
[3] X. Qin et al., Sci. China-Phys. Mech. Astron. 69, 282011 (2026).
Notes: Purpose: high-frequency flipping suppresses false asymmetry from temperature drift; 3He cannot reverse fast.
Adiabatic criterion κ: κ≫1 ON, κ≪1 OFF (Fig. 9).
Structure/efficiency ON~90% OFF~70% calibrated per wavelength; t0 sync <1 ms, 0.4 s switching (Fig. 10).

## Slide 7: Detection system -- GTAF-II
Structure
  A gamma total-absorption detector array of 40 equal-solid-angle BaF2 crystals (12 pentagonal + 28 hexagonal frusta), covering nearly 4π solid angle (95.2%);
  Inner radius 10 cm, crystal thickness 15 cm; single crystal Ø14 cm×15 cm.
Performance
  Energy resolution ~15% @1274 keV;
  Detection efficiency >85%.
Capture experiment
  Thin sample, free of potential-scattering background; with ideal resolution the γ yield ∝ capture cross section:
  In the GTAF experiment the flipper ON/OFF efficiencies differ, so a correction is applied to the neutron polarization:
  where is the raw longitudinal asymmetry; the (n, γ) counts for the two neutron spin states; the parity-violating longitudinal asymmetry; , the neutron polarization; , the efficiencies of spin-flipping and transmission
Fig. 11 GTAF-II detector array
[1] X. Qin et al., Sci. China-Phys. Mech. Astron. 69, 282011 (2026).
Fig. 12 GTAF detection efficiency vs energy
Notes: Structure: 40 BaF2 crystals, 95.2% solid angle (Fig. 11).
Performance: 10% @1274 keV, 677 ps → TOF (Fig. 12).
Cuts: PSD + M>3 + ΣE>3 MeV; the 1/v law shows the background is negligible.

## Slide 8: Experimental setup
In this experiment, the digitalized waveform electronics and the XIA system acquire data independently.
Table 1 Target parameters and digitalized waveform electronics beam time
 | natLa |  | natPd |  | Empty |  | C | 
Abundance | ¹³⁹La 99.91% |  | ¹⁰⁵Pd 22.33%; ¹⁰⁸Pd 24.64% |  | — |  | — | 
Specification | φ45 mm×1 mm×3 |  | φ45 mm×1 mm×2 |  | — |  | φ45 mm×1 mm×2 | 
Purity | La/RE ≥ 99.9% |  | 99.95% |  | — |  | 99.99% | 
Beam condition | no absorber | Cd-Ag-Co | no absorber | Cd-Ag-Co | no absorber | Cd-Ag-Co | no absorber | Cd-Ag-Co
Beam time (h) | 47.39 | 2.05 | 66.72 | 2.02 | 2.73 | 0.56 | 2.62 | 1.22

## Slide 9: Data processing
Hot electrons or other noise
gamma
alpha particles
a)
b)
Fig. 13 Flow of event reconstruction
Fig. 14 qlong vs. PSD
Fig. 15 (logx)
Fig. 16 Multiplicity distribution at the p-wave resonance peak
Fig. 17 Summed energy for different multiplicities at the p-wave resonance peak
Fig. 18 (logx-logy)

## Slide 10: Physics analysis
 | P-wave(0.744eV) | S-wave(71.07eV)
= |  | 
 | P-wave(0.744eV) | S-wave(71.07eV)
Background composition: plateau background, sample-independent beam background, scattered-neutron background
Fig. 19 Flow of background treatment and physics-analysis
Fig. 20 (logx-logy)
Fig. 21 Comparison of the peaks at 0.744 eV (a) or 71.07 eV (b) when the flipper is on (-) and off (+)
(a)
(b)
Table 2 Comparison of measured longitudinal asymmetries
p-wave@0.744eV
(139La)
s-wave@3.02eV
(138La)
s-wave@71.07eV
(139La)

## Slide 11: Follow-up plan
Tune the PSD;
Finalize the event-selection criteria;
Adopt the eight-step calculation to reduce statistical errors from temperature drift;

## Slide 12: Thanks for you attention!
Notes: This page: abundance, specification and purity of the four targets (natLa, natPd, Empty, natC), and the shared-electronics beam time under the two beam conditions (no absorber / Cd-Ag-Co).