## Slide 1: Cherenkov Detector Group Meeting Report
Institute of High Energy Physics
Wang Jian
2026.09.11

## Slide 2: Cherenkov detector
2026/09/11
The ePIC dual-radiator RICH
The new MIP timing detector in the CMS upgrade experiment
3. The ALICE 3 bRICH detector
Cooling scheme for the SiPM on the detector

## Slide 3: Cherenkov detector
2026/09/11
PhotoDetector Unit (PDU)
Readout Box
cables and services (not shown)
The ePIC dual-radiator RICH
Method：cooling（water-cooled Peltier）
Cooling medium：Water （15℃）
Scheme：SiPM array backside → ceramic PCB substrate → copper heat-spreading frame (cold manifold ring) → cold side of side-mounted Peltier module; the hot side of the Peltier is bonded to a water-cooled plate, and the pumped heat is directly removed by the water.
Performance：SiPM cooling for low-temperature operation (−30 °C )
High-temperature annealing temperature: 150°C

## Slide 4: Cherenkov detector
2026/09/011
The ePIC dual-radiator RICH
Method：Cold plate cooling
Cooling medium：Silicone oil
Scheme：SiPM array backside → ceramic PCB substrate → cold plate → red piping → temperature controller. Performance：SiPM cooling for low-temperature operation (−30 °C or lower)
The temperature controller has a working range of −55 °C to 250 °C
its maximum cooling capacity (1.5 kW) achieved at −40 °C.
Alternative cooling scheme

## Slide 5: Cherenkov detector
2026/09/11

## Slide 6: Cherenkov detector
2026/09/11
Transverse section of a BTL detector module attached to the cooling plate
CMS MTD BTL= Compact Muon Solenoid MIP Timing Detector Barrel Timing Layer
Pictures of SiPM array (front side) and of a BTL detector module, before insertion inside a copper housing, consisting of: 2 LYSO:Ce crystal arrays, 4 SiPM arrays including flex cable for signal routing to the front-end board, 4 thermo-electric coolers (TECs) and one RTD temperature sensor on each array.
Method：TECs + Cold Plate
Cooling medium：CO₂ (−30°C)
Scheme：LYSO → SiPM → Thermal interface pad → Peltier → Copper housing → CO₂ cooling tubes.
Performance：SiPM cooling for low-temperature operation (−45 °C)
High-temperature annealing temperature：60°C

## Slide 7: Cherenkov detector
2026/09/11
The ALICE 3 bRICH detector
Localized Cooling for SiPM Sensors
Active Cooling：A new housing board design integrates a ceramic PCB with fluid coolant circulation, in order to achieve sensor temperatures of −60°C to −80°C
Compact and High-Performance Design：
• SiPMs directly soldered onto metalized pads on the ceramic surface
• Hollow PCB structure enables coolant flow
• Optimized signal routing through PCB vias minimizes analog signal length, preserving integrity and timing performance
3D-printed AlN ceramic prototypes

## Slide 8: Cherenkov detector
2026/09/11
Chart: 
heating+cooling
cooling
room temperature
sensor test
Temperature /℃
cold plate
graphite plate
Time /s
Chart: 
Time /s
温度/℃
heating
heating+cooling
cold plate
room temperature
graphite plate
graphite plate
cold plate
heating pad and pt100
water cold plate
heating pad and pt100
PI heating pad 0.5 W, distance from the cold plate ~95 mm, temperature ~15°C
Comparative test:
Graphite: thickness 1 mm, width 50 mm, thermal conductivity 200 W
Cold plate: 0.37 mm, width 70 mm,
Conclusion: The cold plate responds more easily to the cooling water temperature, with larger fluctuations The cooling effect of the cold plate is better than that of the graphite plate

## Slide 9: Cherenkov detector
This is a TEC product that can be bought on Taobao. Its temperature range is -35°C to 230°C.
Next step plan: Buy the peltier cooler and learn about it, for future applications. Expected to arrive next week.
Peltier cooler
PID temperature controller
Thermoelectric cooler (TEC)
2026/09/11

## Slide 10: Thanks!