## Slide 1: Progress of HERD Simulation
Ming XU (徐明), IHEP
2013.12.02
HERD 2nd Workshop, IHEP, Beijing

## Slide 2: The HERD Mission
A space mission devoted to CR physics, DM search and gamma ray astronomy
Scientific goals of the mission:
  DM search
    rays from 30GeV to TeV region, searching for spectrum anomalies that might result from DM annihilation
  CR nucleon
    CR chemical components spectrum measurement from z = 1 to 26 for energies form hundreds of GeV To PeV with large geometry factor, study the origin, propagation and acceleration of CR
  CR electron
    Spectrum measurement from 100GeV–10TeV with high energy resolution, show the possible cutoff and different components of different origins

## Slide 3: Mission Requirement
smoking gun from DM annihilation
  energy resolution
  PID
CR nuclei detection requirement
  geometry factor
  detector thickness
electron detection
  energy resolution
  PID

## Slide 4: Smoking Gun from DM Annihilation Requirement
10-5
10-4
10-7
10-6
/ p
10-6
γ/p
2.0%
5.0%
1.0%
1.5%
σE
/ p
10-2
10-1
10-4
10-3
ϒ / e
10-3
/ e
40°
90°
60°
FOV > 60°
FOV
exposure time | 1 year
area | 1m2
energy resolution | 1.5%
FOV | 90°
/ e | 10-4
/ p | 10-7
exposure time | 1 year
area | 1m2
energy resolution | 1.5%
FOV | 90°
 | 10-4
 | 10-7
Configuration of standard detector:

## Slide 5: CR Nuclei Requirement: Geometry Factor
  heavy-dominated model
  proton-dominated model
  model B
the integrated flux curve in 2 years
P (Atomic mass: ~ 1)
He(A: ~ 4)
L (A: ~ 8) 3≤Z≤5
M (A: ~ 14) 6≤Z≤9
H ( A: ~ 25) 10≤Z≤19
VH (A: ~ 35) 20≤Z
Fe (A: ~ 56)
parallel line means observe 10 events with different geometry factor
suppose GF=1m2sr, and detection efficiency=100%，the table shows the number of observed events beyond PeV in 2 years
HD

## Slide 6: CR Nuclei Requirement: Detector Thickness
define 50% events of the distribution as the minimum length we need in a certain energy range
shower maximum distribution of different nuclei(proton, helium, carbon and iron)@30TeV

## Slide 7: Electron Requirement

## Slide 8: Mission Requirement: Summary
  Large geometry factor (some m2sr)
Good nucleon energy measurement (2 nucl.inter.length)
Good electron and gamma energy resolution(~1%)
Good e/p separation power (<)

## Slide 9: Baseline Design

## Slide 10: Simulation Setup: Only CALO
GEANT4
  version 4.9.2
  electron (50GeV-1TeV)
  gamma (50GeV-1TeV)
  proton (100GeV-5TeV)
  QGSP model
FLUKA
  version 2011.2
  proton (TeV to PeV)
  heavy nuclei (He, C, Fe, 100GeV to PeV)
  DPMJET3 model
Fine segmented (no gap)
Weighs nothing (no mechanical support)
simple readout chain, no saturation
  energy deposition with Poisson sampling (energy to N p.e.)
 | type | size | X0,λ | unit | read out
CALO | 9261 LYSO cubes 1.85 tons | 63 cm × 63 cm × 63 cm | 55 X0 3 λ | 3 cm × 3 cm × 3 cm | wls fiber + ICCD

## Slide 11: Electron Hit Map
cell > 0.1 MIP
200GeV
1TeV

## Slide 12: Proton Hit Map
200GeV
50TeV

## Slide 13: Electron () Energy Detection
EM resolution is parameterized as:
: stochastic term
  Fluctuations is signal generation process
: noise term
  Due to readout electronics
: constant term
  Non-uniform response
  Channel to channel inter-calibration
  Energy leakage
  Energy lost in dead material

## Slide 14: Proton Interactions in CALO
energy escape
EM shower

## Slide 15: Proton Energy Reconstruction(100TeV)
with shower max cut
Reconstructed with liner function

## Slide 16: Effective Geometry Factor
effective geometry factor means the counting efficiency:
Toy MC method: using the counting ration between flat panel and CALO to estimate the CALO GF
of a flat panel is easy to know:
:
  earth + atmosphere block
  minimum path length

## Slide 17: Effective Geometry Factor

## Slide 18: The CALO Structure
CR nuclei detection capability is related to energy resolution and GF. Under the weight constraint (totally 2t):
good resolution，need “thick” CALO，but GF decrease
bigger GF，need “flat” CALO，but worse resolution
smear (folding) and unfolding method to get the reconstructed spectrum affected by these two factors, and the residual of reconstructed spectrum and input spectrum tells which factor dominate in CR nucleon measurement.
structure cm×cm×cm | nucl.inter.length | GF (m2sr) @100TeV | resolution
63×63×63 | 3 | 2.6 | 20%
77×77×42 | 2 | 3 | 30%
thick
flat

## Slide 19: Goodness of Unfolding Test
energy resolution is more important
in CR nuclei spectrum measurement

## Slide 20: Flux of Each Components
to identify rays and electrons, excellent capability of proton rejection power is necessary

## Slide 21: PID: MVA Method
Define 8 parameters for a shower in CALO
.
Var 1
Var 2
Var 3
Var 4
Var 5
Var 6
Var 7
Var 8
Signals: electrons
Background: protons

## Slide 22: e/p Separation (TMVA)
6.0×10-6

## Slide 23: Expected Performance of HERD CALO
γ/e energy range (CALO) | tens of GeV-10TeV
nucleon energy range (CALO) | up to PeV
γ/e energy resolution (CALO) | <1%@200GeV
proton energy resolution (CALO) | 20%
e/p separation power (CALO) | <10-5
electron eff. geometrical factor (CALO) | 3.8 m2sr@200 GeV
proton eff. geometrical factor (CALO) | 2.6 m2sr@100 TeV

## Slide 24: Expected HERD Proton and He Spectrum
Horandel model as HERD input
Only statistical error
Notes: 新添加了AMS02的质子和氦核测量数据，AMS02公布的能谱最后一个点都在1TeV附近
对AMS的结果，选取了从几十GeV开始到其公布的上限，每个谱选了均匀挑选了15个数据点，放在图中一并比较

## Slide 25: Expected HERD of Abundant Heavy Nuclei

## Slide 26: About DM: The Ray Line Spectrum

## Slide 27: Dynamic Range and Readout Sensor Requirement
Dynamic range estimation
  cell MIP response (LYSO, 3cm cube) ~ 30MeV
  cell MAX Energy deposit response(PeV shower) ~ 20TeV
  dynamic range = 20TeV / (1/3 MIP) =
  Dual fiber readout for one cell (high/low gain) is a possible solution
Readout sensor (ICCD frame requirement)
Trigger Threshold (GeV) | Counting Rate (Hz) | Detection Efficiency (200 frame) | Detection Efficiency (500 frame) | Detection Efficiency (1000 frame)
20 | 300 | 42% | 63% | 78%
30 | 100 | 70% | 85% | 92%
50 | 50 | 83% | 92% | 96%
see Zhi-Gang WANG’s talk for details

## Slide 28: Summary
  Large effective geometry factor
    > 3m2sr for electron
    > 2m2sr for proton
Good nucleon energy measurement (proton, 20%)
Good electron and gamma energy measurement (~1%)
Good e/p separation power (<10-5)
These factors are quite advanced and essential for CR spectrum measurement and the searching of DM.
Thank You!

## Slide 29: Backup

## Slide 30: The LYSO Crystal
Crystal | CsI(Na) | BGO | PWO | LYSO
Density (g/cm3) | 4.51 | 7.13 | 8.3 | 7.4
1 X0 (cm) | 1.86 | 1.12 | 0.89 | 1.14
1 λ (cm) | 39.3 | 22.8 | 20.7 | 20.9
Decay time (ns) | 690 | 300 | 30 | 40
Light yield (%) | 88 | 21 | 0.3 | 85
Element | Mass Fraction(%)
Lu | 71.44
Y | 4.03
Si | 6.37
O | 18.14
Ce | 0.02
Cerium-doped Lutetium Yttrium Orthosilicate
Simulation Configuration

## Slide 31: Earth Atmosphere Cover Effect
atmosphere（km） | blocked（°） | remained（°）
0 | 70 | 20
100 | 73 | 17
200 | 76 | 14
300 | 80 | 10
orbit @400km(H=400km) R(earth) = 6370km |  | 
R
R+H
R+h

## Slide 32: Effective GF under Different Condition

## Slide 33: Proton Energy Resol vs Detector Thickness
63*63*63cm
3 nucl.inter.length,
20% resolution
77*77*42cm
2 nucl.inter.length,
30% resolution
90*90*31cm
1.5 nucl.inter.length,
50% resolution
CALO weight: 1850 kg
GF@
100 TeV
2.6
GF 3.0
GF 2.0

## Slide 34: Unfolding Workflow
training measured
response matrix
training truth
measured data
RooUnfold
unfolded distribution
and errors
sample from power law function(500GeV-5PeV)
Nsample depends on obs_time and GF
training truth with gaussion smearing
power law gauss
Integral the convoluted function with GF, resolution, obs_time and energy
goodness of unfolding test

## Slide 35: proton, 53TeV, 1cm cell, 100cm3, hit map