## Slide 1
CERN Future Circular Colliders Study
Frank Zimmermann
International Workshop on Future High Energy Circular Colliders
IHEP Beijing,
16 December 2013
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
Many thanks to Roy Aleksan, Michael Benedikt (FCC Design Study Coordinator), Alain Blondel (FCC Kick-Off LOC Chair), Frederick Bordry (new CERN DAT), Luca Bottura, Francesco Cerutti, John Ellis, Hector Garcia, Cedric Garion,, Bernhard Holzer, Patrick Janot, Erk Jensen, Eberhard Keil, Roberto Kersevan, Max Klein, Mike Koratzinos, Luisella Lari, Eugene Levichev, Nicolas Mounet, Robert Rimmer, Daniel Schulte, Valery Telnov, Rogelio Tomas, Jörg Wenninger

## Slide 2
with emphasis on proton-proton and electron-positron high-energy frontier machines. These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures, in collaboration with national institutes, laboratories and universities worldwide.
high-field magnets: VHE-LHC/FHC
“to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update”:
d) CERN should undertake design studies for accelerator projects in a global context,
European Strategy Update (ESU) on Particle Physics
Design studies and R&D at the energy frontier
high-gradient acceleration:
CLIC and TLEP/FLC

## Slide 3
15 T  100 TeV in 100 km
20 T  100 TeV in 80 km
80-100 km tunnel infrastructure in Geneva area
design driven by pp-collider requirements
with possibility of e+-e- (TLEP) and p-e (VLHeC)
CERN-hosted study performed in international collaboration
FCC Study (Future Circular Colliders)
CDR and cost review for the next ESU (2018)

## Slide 4
To prepare international collaborations, study scope and topics will be discussed in kick-off meeting at U. Geneva 12-15 February 2014
CERN would like to promote global collaboration of future circular collider studies
Kick-Off Meeting for FCC Study
Earlier topical workshops on HE-LHC (2010), LEP3/TLEP (6 meetings in 2012-13) and VHE-LHC (2013) in the frame of EuCARD
Kick-off meeting covers accelerator, detectors, physics case, technology, infrastructure & tunnel construction
Total no. of participants limited to 500 (early registration suggested)
http://indico.cern.ch/e/fcc-kickoff

## Slide 5
Infrastructure
tunnels, surface buildings, transport (access roads), civil engineering, cooling ventilation, electricity, cryogenics, communication & IT, fabrication and installation processes, maintenance, environmental impact and monitoring, safety
Hadron collider
Optics and beam dynamics
Functional specifications
Performance specs
Critical technical systems
Related R+D programs
HE-LHC comparison
Operation concept
Detector concept
Physics requirements
Hadron injectors
Beam optics and dynamics
Functional specs
Performance specs
Critical technical systems
Operation concept
e+ e- collider
Optics and beam dynamics Functional specifications
Performance specs
Critical technical systems
Related R+D programs
Injector (Booster)
Operation concept
Detector concept
Physics requirements
e- p option: Physics, Integration, additional requirements
Future Circular Colliders - Conceptual Design Study
for next European Strategy Update (2018)
FCC Study Scope and Structure

## Slide 6
Infrastructure, cost estimates
P. Lebrun
VL Hadron collider
D. Schulte
Hadron injectors
B. Goddard
e- p option
Integration aspects O. Brüning
Future Circular Colliders - Conceptual Design Study
Study coordination, host state relations, global cost estimate
M. Benedikt, F. Zimmermann
e+ e- collider
J. Wenninger
High Field Magnets
L. Bottura
Supercon-ducting RF
E. Jensen
Cryogenics
L. Tavian
Specific Technologies
(MP, Coll, Vac, BI, BT, PO)
JM. Jimenez
Physics and experiments
Hadron physic Experiments, infrastructure
A. Ball, F. Gianotti,
M. Mangano
e+ e- exper., physics
A. Blondel J.Ellis, P.Janot
e- p physics +
M. Klein
Operation aspects,
energy efficiency, OP & mainten., safety, environment.
P. Collier
Planning (Implementation roadmap, financial planning, reporting)
F. Sonnemann
Team preparing FCC Kick-Off & Study

## Slide 7
Main Parameters for FHC (VHE-LHC)
Energy 100 TeV c.m.
Dipole field 15 T (baseline) [20 T option]
Circumference ~ 100 km
#IPs 2+2
Beam-beam tune shift 0.01 (total for 2 IPs)
Bunch spacing 25 ns [5 ns option]
Bunch population (25 ns) 1011–2x1011 (beam current 0.5-1 A)
Normalized rms emittance 2.2 mm
Luminosity 5x1034 cm-2s-1
b* 1.1 m [2 m conservative option]
Synchroton radiation arc 26 W/m/ap. [arc fill factor 78%]
Stored beam energy 8.3 GJ/beam
Longit. emit damping time 0.5 h
Straight section length 1400-2000 m (8 or 12)
Option: Polarized proton beams (with Siberian snakes)
preliminary

## Slide 8
Some FHC Challenges
High-field SC magnet system
Vacuum system & synchrotron radiation heat load
  warm photon absorbers in dipole interconnects? antechamber, higher-T beam screen? Vacuum stability, impedance, e- cloud, bunch spacing
Synchrotron radiation damping
  controlled blow up? shorter bunch spacing? crab waist collisions??
Luminosity limits
  Radiation damage, pile up, bunch spacing, detector technology
Machine protection
  Energy in beam & magnets, dump, collimation; quench protection
Optics
  Maximizing fill factor, IR design & length (&#) of straight section

## Slide 9
E. Todesco, L. Rossi, P. McIntyre
20-T dipole
15-T dipole
beam
pipe
beam
pipe
15 T dipoles + 100 km circumference
→ 100 TeV pp
Cost-Optimized Magnets for FHC

## Slide 10
Evolution of Nb-Ti & Nb3Sn SC Cable
L. Bottura (CERN), J. Parrell (OST)
US-CDP

## Slide 11
16 T
Flat racetracks no bore
Record fields
Practical magnets
Data by courtesy of L. Rossi (CERN) and S. Caspi (LBNL)
High-Field Dipoles

## Slide 12
Demonstrate the required performance (11.25 T at 11850 A)
Achieve accelerator field quality
Study in depth mechanics and manufacturing
Address specific issues such as quench protection
NOTE: virtual reality models
FNAL MBHSP02 ready for test
CERN 54/61 practice coil
Next 2 years !
L. Bottura (CERN), D. Mitchell, F. Nobrega (FNAL), M. Karppinen (CERN)
FNAL short model
CERN coil
11-T accelerator dipoles for HL-LHC

## Slide 13
Encouraging results !
  Bmax= 11.7 T (78% of expected SSL at 1.9 K)
  Improving field quality (reduced sub-element diameter, cored cable)
Future work:
  Ramp-rate quench dependence
  Holding current quenches
  Geometric harmonics
MBHSP01
MBHSP02
11850 A
4.2 K
1.9 K
L. Bottura (CERN), G. Chlachidze, J. Di Marco, images E. Barzi (FNAL)
HL-LHC 11-T performance so far

## Slide 14
SR heat load 3 MW total;
26 W/m/aperture
one option: dedicated
warm photon stops
in magnet interconnects
as developed by FNAL for VLHC
with or w/o anterchamber
FHC – extracting SR heat
M. Geynisman et al., “Report on the First VLHC Photon Stop Cryogenic Design Experiment,” Advances in cryogenic engineering, Anchorage, AIP Conf.Proc. 710 (2004) 379-388 ;
Also P. Bauer et al., "Report on the First Cryogenic Photon Stop Experiment," FNAL TD-03-021, May 2003

## Slide 15
FHC beam power & collimation
Energy stored: 8 GJ per beam (LHC: 0.4 GJ)
  beam dumping system design, interlock system
Collimation
  higher energy density: more robust materials? collimators are first hit by beam in case of failure; LHC collimators made from fibre-reinforced carbon (CFC); for FHC more robust composite materials?
  cleaning efficiency degrading with beam energy collimators minimize beam loss in the cold regions; nuclear processes inside collimator jaw vary with energy (cross section of single-diffractive scattering increases)
  smaller beam sizes and collimator gaps
    Full collimator gaps of 1 mm or less, requiring higher precision in collimator control, setup and reproducibility.
  magnets in cleaning insertion
    warm magnets at the technological limit; shielded superconducting magnets?

## Slide 16
Main Parameters for FLC (TLEP)
Energy c.m. 91 (Z), 160 (W) , 240 (H), 350 () GeV
(energy upgrade 500-ZHH/ttH)
Circumference ~ 100 km
Total SR power ≤ 100 MW
#IPs 4
Beam-beam tune shift / IP scaled from LEP
Beam current 7 mA (TLEP-t) to 1400 mA (TLEP-Z)
Horiz. geom. emittance 2-30 nm
Vert. geom. Emittance 2-60 pm
Luminosity / IP 6x1035 cm-2s-1 at 91 GeV c.m.
5x1034 cm-2s-1 at 240 GeV c.m.
1x1034 cm-2s-1 at 350 GeV c.m.
Top-up injection to cope with short lifetime from rad. Bhabha scattering & beamstrahlung
Polarization at Z pole and WW threshold
by* 1 mm ~ sz
preliminary

## Slide 17
Lifetime limitation by beamstrahlung from 120 GeV requires robust ring optics with small b*y (~ 1 mm) & large momentum acceptance (≥ 2%).
  Nano-beam / crab waist schemes are considered as options
Reaching small vertical emittance in large machine
Optimization of the machine layout compatible with high currents and larger number of bunches at Z
  Number of rings and size of the RF system
Polarization & precise energy calibration at Z pole, with nat. polarization time ~150 h, & at WW (~5 h)
RF w >50% wall-plug to beam power efficiency
Optics changes with energy; lepton injector chain
Some Challenges for FLC (TLEP)

## Slide 18
mitigations:
(1) large momentum acceptance h
(2) flat beams [i.e. small ey & large bx*]
(3) fast top up
synchrotron radiation in the strong field of opposing beam
makes some e± emit significant part of their energy
h: momentum acceptance
sx: horizontal beam size at IP
with
→minimize ke=ey/ex, by~bx(ey/ex) & respect by≥sz
V. Telnov, PRL 110 (2013) 114801
Note: Many theoretical beamstrahlung studies in 1980’s. Example R. Blankenbecler, S.D. Drell , “A Quantum Treatment of Beamstrahlung,” Phys.Rev. D36 (1987) 277
lifetime limit: beamstrahlung (BS)
& then be lost→ limited beam lifetime
note recent new formula from BINP!

## Slide 19
lifetime values (summer 2013 baseline)
parameters | TLEP Z | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 91 | 160 | 240 | 350 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
# bunches/beam | 7500 | 3200 | 167 | 160 | 20
#e±/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 29.2, 0.06 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 121, 0.25 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 2 | 2 | 6 | 12 | 
/IP[1034cm−2s−1] | 59 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (r.Bhabha) | 99 | 38 | 24 | 21 | 26
tbeam[min] (BS,h=2%) | >1025 | >106 | 9 | 3.5 | 0.5
parameters | TLEP Z | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 91 | 160 | 240 | 350 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
# bunches/beam | 7500 | 3200 | 167 | 160 | 20
#e±/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 29.2, 0.06 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 121, 0.25 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 2 | 2 | 6 | 12 | 
 | 59 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (r.Bhabha) | 99 | 38 | 24 | 21 | 26
tbeam[min] (BS,h=2%) | >1025 | >106 | 9 | 3.5 | 0.5
multiple beamstrahlung
increases bunch length
single beamstrahlung
limits beam
lifeitme
based on Telnov formula

## Slide 20
A. Blondel
short lifetime → booster ring
for top up injection
into collider

## Slide 21
IR Design
off-momentum
dynamic
aperture
d=1%
H. Garcia Moralez, R. Tomas
(reduced from 4 m)

## Slide 22
developing FLC/TLEP parameters …

## Slide 23
b*x/y (mm) | 500 / 1 | 500 / 1 | 500 / 1 | 500 / 1
Nb [1011] | 1.0 | 4.0 | 4.7 | 4.0
sz [mm] | 5.9 | 9.1 | 8.2 | 6.6
ex,y(nm, pm) | 0.14, 1 | 0.44, 2 | 1, 2 | 2.1, 4.3
xx,y/IP | .032/.175 | .031, .187 | .029, .160 | .024, .077
L/IP(1032cm-2s-1) | 22970 | 3980 | 933 | 129
Nb [1011] | 1.5 | 1.0 | 3.0 | 0.88
sz [mm] | 1.7 | 1.6 | 1.65 | 0.84
ex,y(nm, pm) | 30, 90 | 4.1, 22 | 8.8, 19 | 2.3, 2.3
xx,y/IP | .029/.024 | .068, .051 | .065, .054 | .055, .036
L/IP(1032cm-2s-1) | 2100 | 1150 | 350 | 175
Parameter | TLEP-Z | TLEP-W | TLEP-H | TLEP-t | LEP2
E (GeV) | 45 | 80 | 120 | 175 | 104
I (mA) | 1400 | 150 | 30 | 7 | 4
Nb [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 5.8
sz [mm] | 2.93 | 1.98 | 2.11 | 0.77 | 16..1
b*x/y (mm) | 500 / 1 | 200 / 1 | 500 / 1 | 1000 / 1 | 1500 / 50
ex,y(nm, pm) | 30, 60 | 3.3, 17 | 7.5, 15 | 2, 2 | 40,~250
xx,y/IP | .068 | .086 | .094 | .057 | .066 (y)
L/IP(1032cm-2s-1) | 5800 | 1600 | 500 | 132 | 1.2
baseline
(analytical)
S. White,
TLEP6 WS
A.Bogomyagkov, E.Levichev,
D.Shatilov,
TLEP6 WS
baseline
(simulated
+ opt.)
nano-beam
option
higher luminosity + much
better beamstrahlung lifetime (>100 min)

## Slide 24
TMCI instability, 3 cm y half aperture, 5.5 m dipole
N. Mounet, S. White, TLEP6

## Slide 25
TLEP RF - relevant parameters
Main RF parameters
Synchrotron radiation power: 50 MW per beam
Energy loss per turn: 7.5 GeV (at 175 GeV, t)
Beam current up to 1.4 A (at 45 GeV, Z)
Up to 7500 bunches of up to 4 x 1011 e per ring.
CW operation w. top-up operation, injectors & booster pulsed
First look on basic frequency choice & RF system dimension
Frequency range (200-800) MHz with 400 MHz starting point
  Disadvantage lower frequency: mechanical stability, He amount for cooling, size …
  Disadvantage higher frequency: denser HOM spectrum (multi-cell), BBU limit, larger impedance, smaller coupler dimensions
Example scaling from LHC (per beam):
  LHC 400 MHz  2 MV and ~250 kW per cavity, (total 8 cavities)
  Lepton collider ~500 cavities 20 MV / 100 kW RF  10 GV / 50 MW
Erk Jensen

## Slide 26
Low cost, highly efficient RF source
  IOT’s, magnetrons, diacrodes, solid state ampliifers?
Higher Q0
  High temp furnace treatments
  Nb3Sn
  MgB2 or something new?
Improved HOM damping (on-cell dampers?)
  First tried on ANL crab cavity, plan to try on JLAB MEIC
  Higher packing factor
Reduced cryomodule costs
  Cheaper materials, reduced labor
R&D issues for FLC SC RF system
Robert
Rimmer,
JLAB

## Slide 27
High efficiency, high power RF sources?
  200 MHz: Tetrodes, Diacrodes; probably least expensive/MW; efficiency > 70%
  400 MHz, 800 MHz:
      Klystrons: ; R&D for larger has started
      IOTs: today limited to ; R&D on MB IOT ( pulsed) has started with ESS!
Thales 1MW diacrode
LEP 1.3 MW CW klystron
CPI MB-IOT prototype, 1MW, 700MHz
RF power sources – frequency scaling
Erk Jensen

## Slide 28
potential of Nb3Sn for SRF cavities
Data from P. Dhakal
R&D
progressing
at JLAB
& Cornell
Robert Rimmer, JLAB

## Slide 29
Synchrotron Radiation for FLC (TLEP)
SR power per unit length 8 W/cm/beam
compare SLAC PEP-II & SPEAR3: 100 W/cm
critical photon energy Ec=(3/2)ħcg3/r
0.35 MeV for TLEP-H (240 GeV c.m.)
1.08 MeV for TLEP-t (350 GeV c.m.)
compare LEP-2: 0.82 MeV (1.58 MeV design)

## Slide 30
TLEP SR compared with ESRF
R. Kersevan, C. Garion, TLEP6

## Slide 31
first look at vacuum system
R. Kersevan, C. Garion, TLEP6
lumped pumps
NEG coating

## Slide 32: 10.5 m long dipole for 1 beam line
Beam pipe without shielding (no lead) but with cooling water channel
TLEP 80 km
FLUKA model for radiation study
L. Lari, TLEP6

## Slide 33
10.5m Dipole
10.5m Dipole
1.5m Quadrupole implemented just as the analytical magnetic field
0.3 m
0.3 m
5* 24 cm long Absorbers
0.3 m
Centered
S
S
0.3 m
0.3 m
25 mm
Cu-OFS (0.085% Ag)
(20:10)
QD
Lead
FLUKA model for radiation study
L. Lari, TLEP6

## Slide 34
Power in H20 for all absorbers: 14.7 W (shield) & 4.5 W (no shield)
Power in H20 for all magnets: 6.7 W (shield) & 87 W (no shield)
Dipole
Dipole
S
S
Abs
Abs
Abs
Abs
Abs
Q
39 W
42 W
6 W
0.9 W
0.9 W
0.9 W
0.9 W
0.9 W
1.7 W
4.9 W
0.1 W
7 W
7.2 W
0.16 W
0.2 W
0.05 W
Heating of the in-pipe shield: need to move the H2O channel further in ?
L. Lari, F. Cerutti, A. Ferrai, TLEP6
heating of cooling water

## Slide 35
peak dose on the coils
L. Lari, F. Cerutti, A. Ferrai, TLEP6
ozone production to be looked at

## Slide 36
polarization
r = 9000 m, C = 80 km
U Wienands, April 2013
TLEP
optimized scenario
LEP
observations
+ model predictions
loss of polarization due to growing energy spread
 100 keV beam energy calibration by resonant depolarization (using pilot bunches) around Z peak and W pair threshold:
mZ ~0.1 MeV, Z ~0.1 MeV, mW ~ 0.5 MeV
A. Blondel
R. Assmann
lower energy spread, high polarization up to W threshold
LEP
TLEP
polarization scaling (energy spread!):
LEP at 61 GeV → TLEP at 81 GeV

## Slide 37
Beam energy e± 60, 120, (250) GeV
Beam energy p 50 TeV
Spot size set by p (6x3 mm rms)
e- current from FLC (SR power ≤ 50 MW)
#IPs 1
Luminosity 2x1035 cm-2s-1 at 60 GeV
1034 cm-2s-1 at 120 GeV
~1033 cm-2s-1 at 250 GeV
Main Parameters for FLHC (VLHeC)

## Slide 38
PSB
PS (0.6 km)
SPS (6.9 km)
LHC (26.7 km)
TLEP (80-100 km,
e+e-, up to
~350 GeV c.m.)
VHE-LHC/FHC
(pp, up to
100 TeV c.m.)
& e± (120 GeV) – p (7, 16 & 50 TeV) collisions ([(V)HE-]TLHeC)
≥50 years of e+e-, pp, ep/A physics at highest energies
possible long-term strategy

## Slide 39
1980
1990
2000
2010
2020
2030
LHC
Constr.
Physics
Proto.
Design,
R&D
HL-LHC
Constr.
Physics
Design,
R&D
VHE-LHC
Constr.
Design,
R&D
2040
TLEP
Constr.
Physics
Design,
R&D
Physics
Design,
R&D
a tentative time line
FCC

## Slide 40
today
Project
Kick-off meeting: 11th Nov. 2013 (Daresbury)
CDR and Cost Review 2018
FCC official study milestones
ESU
Kick-off meeting
12th-14th February 2014
CDR and Cost Review 2018
Study
FCC

## Slide 41
CERN is undertaking an international study for the design of future circular colliders (FCC) in the 100 km range
CDR and cost review for next ESU (2018)
Main emphasis on hadron collider (FHC) with 100 TeV cm at the energy frontier, determining the infrastructure
Study will also consider an e+e- collider (TLEP/FLC) as potential intermediate step, and look at an e-p option.
FCC kick-off meeting 12-15 February 2014 in Geneva University
  - Establish international collaborations
  Define WPs and set-up study groups
  International Advisory Committee (IAC)
Collaboration with CepC/SppC/IHEP design study much welcome & important to make progress!
FCC Summary

## Slide 42
thank you for your attention!

## Slide 43: TLEP/FLC past events & references
A. Blondel, F. Zimmermann, “A High Luminosity e+e- Collider in the LHC Tunnel to study the Higgs Boson,” arXiv:1112.2518v1, 24.12.’11
K. Oide, “SuperTRISTAN - A possibility of ring collider for Higgs factory,”
KEK Seminar, 13 February 2012
1st EuCARD LEP3 workshop, CERN, 18 June 2012
A. Blondel et al, “LEP3: A High Luminosity e+e- Collider to study the Higgs Boson,” arXiv:1208.0504, submitted to ESPG Krakow
P. Azzi et al, “Prospective Studies for LEP3 with the CMS Detector,”
arXiv:1208.1662 (2012), submitted to ESPG Krakow
2nd EuCARD LEP3 workshop, CERN, 23 October 2012
P. Janot, “A circular e+e- collider to study H(125),” PH Seminar, CERN, 30 October 2012
ICFA Higgs Factory Workshop: Linear vs Circular, FNAL, 14-16 Nov. ’12
A. Blondel, F. Zimmermann, “Future possibilities for precise studies of the X(125) Higgs candidate,” CERN Colloquium, 22 Nov. 2012
3rd TLEP3 Day, CERN, 10 January 2013
4th TLEP mini-workshop, CERN, 4-5 April 2013
5th TLEP mini-workshop, 25-26 July 2013, Fermilab
6th TLEP workshop (TLEP6), CERN, 16-18 Oct. 2013
http://tlep.web.cern.ch
http://cern.ch/accnet
http://cern.ch/xbeam

## Slide 44: VHE-LHC/FHC past events & references
R. Assmann, R. Bailey, O. Brüning, O. Dominguez, G. de Rijk, J.M. Jimenez, S. Myers, L. Rossi, L. Tavian, E. Todesco, F. Zimmermann, “First Thoughts on a Higher- Energy LHC,” CERN-ATS-2010-177
E. Todesco, F. Zimmermann (eds), “EuCARD-AccNet-EuroLumi Workshop: The High-Energy Large Hadron Collider,” Proc. EuCARD-AccNet workshop HE-LHC’10 , Malta, 14-16 October 2010, arXiv:1111.7188 ; CERN Yellow Report CERN-2011-003
HiLumi LHC WP6 HE-LHC
Joint Snowmass-EuCARD/AccNet-HiLumi meeting `Frontier Capabilities for Hadron Colliders 2013,‘ CERN, 21-11 February 2013
https://cern.ch/accnet
http://hilumilhc.web.cern.ch/HiLumiLHC/activities/HE-LHC/WP16/

## Slide 45
Additional slides

## Slide 46
parameters | TLEP Z | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 91 | 160 | 240 | 350 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
# bunches/beam | 7500 | 3200 | 167 | 160 | 20
#e−/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 29.2, 0.06 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 121, 0.25 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 2 | 2 | 6 | 12 | 
ξx,,y/IP | 0.068 | 0.086 | 0.094 | 0.057 | 
/IP[1034cm−2s−1] | 59 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (rad.Bhabha) | 99 | 38 | 24 | 21 | 26
tbeam[min] (BS, h=2%) | >1025 | >106 | 9 | 3.5 | 0.5
parameters | TLEP Z | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 91 | 160 | 240 | 350 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
# bunches/beam | 7500 | 3200 | 167 | 160 | 20
#e−/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 29.2, 0.06 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 121, 0.25 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 2 | 2 | 6 | 12 | 
ξx,,y/IP | 0.068 | 0.086 | 0.094 | 0.057 | 
 | 59 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (rad.Bhabha) | 99 | 38 | 24 | 21 | 26
tbeam[min] (BS, h=2%) | >1025 | >106 | 9 | 3.5 | 0.5

## Slide 47
parameters | LEP2 | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 209 | 160 | 240 | 350 | 
beam current [mA] | 4 | 154 | 29.8 | 6.7 | 
# bunches/beam | 4 | 3200 | 167 | 160 | 20
#e−/bunch [1011] | 5.8 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 48, 0.25 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 1500, 50 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 270, 3.5 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 16.1 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 3.41 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 3.64 | 2 | 6 | 12 | 
ξx,,y/IP | 0.066 (y) | 0.086 | 0.094 | 0.057 | 
/IP[1034cm−2s−1] | 0.0125 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (rad.Bhabha) | 363 | 38 | 24 | 21 | 26
tbeam[min] (BS, h=2%) | >1035 | >106 | 9 | 3.5 | 0.5
parameters | LEP2 | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 209 | 160 | 240 | 350 | 
beam current [mA] | 4 | 154 | 29.8 | 6.7 | 
# bunches/beam | 4 | 3200 | 167 | 160 | 20
#e−/bunch [1011] | 5.8 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 48, 0.25 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 1500, 50 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 270, 3.5 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 16.1 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 3.41 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 3.64 | 2 | 6 | 12 | 
ξx,,y/IP | 0.066 (y) | 0.086 | 0.094 | 0.057 | 
 | 0.0125 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (rad.Bhabha) | 363 | 38 | 24 | 21 | 26
tbeam[min] (BS, h=2%) | >1035 | >106 | 9 | 3.5 | 0.5
com-parison
with LEP2

## Slide 48
parameters | TLEP W | TLEP H | TLEP t |  | ZHH&ttH
Ec.m. [GeV] | 160 | 240 | 350 |  | 500
beam current [mA] | 154 | 29.8 | 6.7 |  | 1.6
# bunches/beam | 3200 | 167 | 160 | 20 | 10
#e±//bunch [1011] | 1.0 | 3.7 | 0.88 | 7.0 | 3.3
ex, ey [nm] | 3.3,0.017 | 7.5, 0.015 | 2, .002 |  | 4., 0.004
β∗x,y [mm] | 200, 1 | 500, 1 | 1000, 1 |  | 1000, 1
σ∗x,y[μm] | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13 | 63, 0.063
σtotz,rms [mm] (w BS) | 1.98 | 2.11 | 0.77 | 1.95 | 1.81
ESRloss/turn [GeV] | 0.3 | 1.7 | 7.5 |  | 31.4
VRF,tot [GV] | 2 | 6 | 12 |  | 35
ξx,,y/IP | 0.086 | 0.094 | 0.057 |  | 0.075
/IP[1034cm−2s−1] | 16 | 5 | 1.3 | 1.0 | 0.5
#IPs | 4 | 4 | 4 |  | 4
tbeam[min] (rad.B) | 38 | 24 | 21 | 26 | 13
tbeam[min] (BS,h=2%) | >106 | 9 | 3.5 | 0.5 | ~1(h=3%)
parameters | TLEP W | TLEP H | TLEP t |  | ZHH&ttH
Ec.m. [GeV] | 160 | 240 | 350 |  | 500
beam current [mA] | 154 | 29.8 | 6.7 |  | 1.6
# bunches/beam | 3200 | 167 | 160 | 20 | 10
#e±//bunch [1011] | 1.0 | 3.7 | 0.88 | 7.0 | 3.3
ex, ey [nm] | 3.3,0.017 | 7.5, 0.015 | 2, .002 |  | 4., 0.004
β∗x,y [mm] | 200, 1 | 500, 1 | 1000, 1 |  | 1000, 1
σ∗x,y[μm] | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13 | 63, 0.063
σtotz,rms [mm] (w BS) | 1.98 | 2.11 | 0.77 | 1.95 | 1.81
ESRloss/turn [GeV] | 0.3 | 1.7 | 7.5 |  | 31.4
VRF,tot [GV] | 2 | 6 | 12 |  | 35
ξx,,y/IP | 0.086 | 0.094 | 0.057 |  | 0.075
 | 16 | 5 | 1.3 | 1.0 | 0.5
#IPs | 4 | 4 | 4 |  | 4
tbeam[min] (rad.B) | 38 | 24 | 21 | 26 | 13
tbeam[min] (BS,h=2%) | >106 | 9 | 3.5 | 0.5 | ~1(h=3%)
TLEP
energy
upgrade?

## Slide 49: Top-up scheme
20 GeV
10 s
energy of accelerator ring
120 GeV
injection into collider
injection into
accelerator
beam current in collider (15 min. beam lifetime)
100%
99%
almost constant current
acceleration time = 1.6 s
(assuming SPS ramp rate)

## Slide 50
collider parameters | e± scenarios |  |  |  | protons
species | e± | e± | e± |  | p
beam energy [GeV] | 60 | 120 | 250 |  | 50000
bunch spacing [ms] | 0.125 | 2 | 33 |  | 0.125 to 33
bunch intensity [1011] | 3.8 | 3.7 | 3.3 |  | 3.0
beam current [mA] | 477 | 29.8 | 1.6 |  | 384 (max)
rms bunch length [cm] | 0.25 | 0.21 | 0.18 |  | 2
rms emittance [nm] | 6.0, 3.0 | 7.5, 3.75 | 4, 2 |  | 0.06, 0.03
bx,y*[mm] | 5.0, 2.5 | 4.0, 2.0 | 9.3, 4.5 |  | 500, 250
sx,y* [mm] | 5.5, 2.7 |  |  |  | 
b-b parameter x | 0.13 | 0.050 |  | 0.056 | 0.017
hourglass reduction | 0.42 | 0.36 |  | 0.68 | 
CM energy [TeV] | 3.5 | 4.9 |  | 7.1 | 
luminosity[1034cm-2s-1] | 21 | 1.2 |  | 0.07 | 
parameters for FHLC

## Slide 51: … and in formulae
SR radiation
power limit
beam-beam limit
constrained by beamstrahlung
to be reduced as much as possible!
FLC (TLEP) luminosity formulae

## Slide 52
lifetime limit: rad. Bhabha scattering
LEP2: tbeam,LEP2~ 6 h (~30% suppression: s~0.21 barn)
TLEP with L~5x1034 cm−2s−1 at 4 IPs:
tbeam,TLEP~21 minutes, unavoidable
beam lifetime
at beam-beam limit:
s for rad. Bhabha:
→
H. Burkhardt, R. Kleiss,
EPAC1994

## Slide 53
S. Henderson
TLEP-Z
TLEP-W
TLEP-H
TLEP-t
luminosity of e+e- colliders

## Slide 54: optics – TLEP arc cell
r=3100 m, Lcell=79 m
r=9100 m (C=80 km), Lcell=50 m
Y. Cai,
B. Holzer,
H. Burkhardt
ex=48 nm at 104.5 GeV → ex=1.5 nm at 175 GeV
from LEP to TLEP
beta functions
dispersion
: at lower beam energy increase cell length (“q”) x2 or x6!