## Slide 1: Advances in RF Deflector and Pulse Compression System
Juwen Wang 王聚文
SLAC National Accelerator Laboratory
加速器物理学术交流会
August 15, 2014
Lanzhou, China

## Slide 2
Basics on RF Deflector and Its Application
Various Pulse Compression Systems
3. Design of a Super-Compact SLED
for LCLS Deflector System
Outline

## Slide 3
Basics on RF Deflector
and Its Application
Principles
Application at LCLS, SLAC

## Slide 4
The RF deflectors are special types of microwave structures in which the charged particles interact with transversely deflecting modes for a variety of purposes.
In 1960’s, SLAC built several RF deflectors called LOLA named by the designers: Gregory Loew, Rudy Larsen and Otto Altenmueller.
For fifty years since then, the RF deflectors have been extensively studied and widely used in the accelerator field for the high energy physics research and beam diagnostics of FEL and many other projects.
TM Longitudinally Accelerating Mode HEM Transversely Deflecting Mode
RF Deflector versus Accelerator
Snapshot of RF Electrical Field

## Slide 5
RF Deflector Applications
Three Types and 7 Examples
- Separator for High Energy Physics Experiments
- Time-resolved electron bunch diagnostics for the LCLS
- Measurement of bunch time jitter at LCLS
- Bunch longitudinal profile diagnostics at DESY
- Ultra short e- and x-ray beams temporal diagnostics for LCLS
  - Drive/witness bunch longitudinal profile diagnostics for PWFA at FACET
- Increase slice energy spread σE as well as measure of slice parameters for Upgrade ECHO-7

## Slide 6
What the RF Deflectors Look Like?
A LOLA-IV
Ready for Sending to DESY
A Short 13-Cell S-Band LOLA Structure Under Measurement for LCLS Injector
Final Assembly
of a 1m X-Band Deflector for LCLS
Two Short X-Band Deflectors for ECHO-7

## Slide 7
Principle of TW RF Deflector
Panofsky-Wenzel Theorem
As a measure of the deflecting efficiency, the transverse shunt impedance r┴ is defined as:
where z and r are longitudinal and transverse axes respectively, Ez is the electrical field amplitude for the dipole mode with angular frequency ω, and P is the RF power as function of z.
Using the simulation codes for electromagnetic field in RF structures, the transverse shunt impedance can be calculated from:

## Slide 8
2.44 m
.
In order to characterize the extremely short bunch of the LCLS project, we need to extend the time-resolved electron bunch diagnostics to the scale of 10-20 fs. The peak deflecting voltage necessary to produce a temporal bunch resolution Δt is:
where E is the electron energy and the transverse momentum of the electron at time Δ t (with respect to the zero-crossing phase of the RF) is py = eV┴/c, n is the kick amplitude in the unit of nominal rms beam size, λ is the RF wavelength, εN is the normalized rms vertical emittance, c is the speed of light, and βd is the vertical beta function at the deflector. This is for an RF deflector, which is π/2 in betatron phase advance from a downstream screen.
Application Example
Maximum Kick of 33 MV for LCLS Bunch Length Measurement

## Slide 9
Microwave Tuning and Measurement
with a Dielectric Bead Attached String

## Slide 10
5 10 15 20 25 30 35
Relative scaling
Relative Electrical Field Amplitude
1E-10
35 40 45 50 55 60 65
Relative scaling
65 70 75 80 85 90 95
Relative scaling
RF Electric Field Amplitude along the Central Axis of the Deflector.

## Slide 11
System Layout for Deflector Usage at LCLS
XTCAV streaks horizontally;
Dipole bends vertically.
High resolution, ~ few fs;
Applicable to all FEL wavelength;
Single shot;
Noninvasive to operation;
Both e-beam and x-ray profiles.
Frequency | 11.424 GHz
Maximum kick | 45 MeV/c
length | 2 x 1 m
Measured time resolution | 
HXR (10keV) | ~ 4 fs rms
SXR (1keV) | ~ 1 fs rms

## Slide 12
Layout of Deflector RF System
after the LCLS Undulators
Beam Direction
RF Direction

## Slide 13
Two Deflector Section
Installed on Strongback

## Slide 14
Beam Direction
RF Direction
Directions of Electron Beam and RF Wave

## Slide 15
Deflector Measurement for Soft X-Ray
Soft X-Ray
1keV, 150pc
Soft X-Ray
1keV, 20pc
Ding, Yuantao

## Slide 16
Deflector Measurement for Hard X-Ray
Ding, Yuantao

## Slide 17
2. Various Pulse Compression Systems
SLED
SLED-II
Others
New Development

## Slide 18
Strong Demand for the Pulse Compression System
In June 1974, forty years ago, a clever invention named “SLED” by Perry B. Wilson, David Z. Farkas and Harry A. Hoag for “SLAC Energy Development” was announced at the laboratory. The goal of the invention was to come up with an affordable scheme that would eventually double the energy of the electrons and positrons accelerated by the SLAC three-kilometer linac. The increase of the peak RF power is in exchange for the RF pulse length reduction by a passive technique called “pulse compression”.
The first 1.7 microsecond part of the 2.5 microsecond klystron pulse was stored in two low-loss cylindrical tuned cavities installed downstream of the klystron. For the remaining 0.8 microsecond, the phase of the klystron was reversed by 180 electrical degrees, and the sum of the power now being discharged by the cavities plus the direct klystron power resulted in a net power gain.
RF amplifier
RF energy storage element

## Slide 19
Forty-Year Anniversary
of S-Band SLED System in SLAC
Two SLED Cavities,
3db
Coupler

## Slide 20
SLED System Application Worldwide
Forty Years Anniversary of the Invention, Several Hundreds of S-Band SLED Systems Operated
KEK, ATF&KEKB, Japan 1992.
Pohang, Korea, 1994
BINP, Novosibirsk, Russia, 2000
CERN 1985 at CTF3, CERN

## Slide 21
Four-port device: two cross-over transmission lines over a length of one-quarter wavelength, corresponding with the center frequency of operation. When power is introduced at the IN port, half the power (3dB) flows to the 0° port and the other half is coupled (in the opposite direction) to the 90° port.
Feed for regular 2 x 2 regular accelerator sections
Reflections from mismatches sent back to the output ports will flow directly to the ISO port and cancel at the input.
Feed for two cylindrical TM115 SLED cavities through a 3db coupler
3 dB, 90° degree hybrids are also know as quadrature hybrids because a signal applied to any input, will result in two equal amplitude signals that are quadrant (90° apart)..
Key Microwave Components –
3db 90° Hybrid Coupler and SLED Cavities

## Slide 22
SLED-II - Type of Resonate Delay Lines

## Slide 23
Evolution of SLED-II System at SLAC
2 Klystrons each with
75 MW for 2.4 µsecs
Dual-Mode
SLED-II
“Single-Feed”
Test Section
600 MW for 400 nsec
Completed at the end of calendar 2002 to demonstrate dual-mode capability and test DLDS components in 2003.
Cross-Potent
(Cold Test Model)
S.Tantawi

## Slide 24
5.7 GHz BOC RF pulse compressor for PCI (2012)
BOC’s unloaded Quality factor
Goal: ≥ 190000
Measured: 204000
Beta: 9.4
Barrel
Open
Cavity RF pulse compressor
Igor Saratchev

## Slide 25
SLED with beating modes in cavity (BMC)
2009 (GYCOM, Russia).
H10->H01 mode converter
Mode mixing taper
Beating wave cavity
3-db hybrid
Q0 ~ 2x105
Measured Q0 ~ 1.6x105 (expected ~ 2x105 )
Tuning plungers heating up problem.
Backlashes problem with plungers movement.
First BMC is now successfully operated at XBOX #1.

## Slide 26
X-Band SLED Pulse Compressor at 2013
Cavity operating mode H0,1,32
Integrated cooling
Compact mode launcher
Double-height -3dB hybrid, made at CEA/CERN
Manual resonant frequency de-tuners
Common vacuum circuit
Fixed tuners
Compact (inexpensive) RF design
Relaxed fabrication tolerances
Fixed frequency tuners (frequency control by temperature)
Detuning option.
Igor Saratchev

## Slide 27
3. Design of a Super-Compact SLED
for LCLS Deflector System
Motivation
Basic Design
Technical Challenges
R&D Program

## Slide 28
Motivation
Maximum Kick for one 1m Section: 5.46 (Pin is Peak RF Power)
Limited by an Old Klystron of 35 MW Peak, little more than 40 MV Kick obtained.
In Order to Reach Higher Resolution,
The SLED System is under Design to Double the Kick to more than 80MV.
The work started last November, S. Tantawi, Chen Xu and G. Bowden actively paticipated.

## Slide 29
SLED RF System
1.394μs3
0.106μs3
0.106μs3
1.394μs3
1.5μs3
DEFLECTOR

## Slide 30
SLED RF System Waveforms
Direct wave Ek
Emitted wave Ee
Net load wave EL
Normalized energy
Gain V

## Slide 31
Calculation of Loaded Waveform from SLED
SLED Cavity Parameters
Qo =105
β=Pe/Pc=Q0/Qe
Optimization Needed
Tc=2QL/ω=2Q0/ω(1+β)

## Slide 32
Dipole Mode Field Distribution along Deflector Axis at the End of SLED Pulse
Deflector Parameters
Structure Length L=1.0 m
Transverse r┴= 41.9 MΩ/m
(Constant Impedance)
1.0
Group Velocity Vg/c=- 3.165 %
Filling Time Tf=106 ns
Attenuation Factor τ=0.62 Neper
Beam Direction
RF Feeding Direction
If the pulse is flat
without SLED E=e-τz/L

## Slide 33
Kick Factor as a Function of
Beam Injection Time for β=9

## Slide 34
Kick Factor as a Function
of SLED Cavity Coupling Coefficient
Optimized
β = 8 – 9
for a gain larger than factor of 2.2

## Slide 35
  Unified 3db Coupler/Mode Convertor/Polarizer
  Single High Q Sphere Cavity Studies
  HE11 Mode Cavity Studies
New Super Compact SLED System

## Slide 36
36
    TE20-> TE11
    Two Rectangular Waveguide Modes Couple
    to two Polarized Circular Waveguide Modes
    TE10-> TE11

## Slide 37
  Movie to animate
  the Unified 3db Coupler/Mode Convertor/Polarizer
Superposition of Two Linear Polarized TE11 Modes with 90° quadrature
TE10 Mode input from WR90 Waveguide
Mixed TE10 and TE20 Modes
TE10 Mode output to Deflectors via WR90 Waveguide
Notice:
Circular port is a matching port without reflection in this simulation

## Slide 38
  Geometry of the New SLED System
Sphere Cavity for Energy Storage
Integrated
3db Coupler/Mode Convertor/Polarizer

## Slide 39
Some TE Modes in a Sphere at 11424 MHz
Magnetic field lines

## Slide 40
Some TM Modes in a Sphere at 11424 MHz
Electric field lines

## Slide 41
Wave potential of TE Modes
Where Ĵn is sphere Bessel Function and Pnm is associated Legendre Polynomials
For TE mode, the Eφ = Hθ = 0 at surface r=a.
It means Ĵn (unp)=0. The following table shows the lower order modes.
TE Modes in Sphere Cavity - I
Sphere Radius can be calculated using wave propagation constant k and value of unp (cm)
1st interesting property:
Sphere Radius a is independent with mode index m, there are numerous degeneracies because Ĵn (unp) is independent with m.

## Slide 42
TE Modes in Sphere Cavity - II
Examples:
For TE014 mode a=5.8749 cm Q = 0.963x105 SLED Gain 2.248 (β= 8-9)
Quality Factor for TE Modes
2nd interesting properties:
Q0 is only depend with sphere radius, and independent with the mode type.
δ is the skin depth (for Copper 0.61μm)
For perfect sphere cavity, these three modes have the same mode patterns except that they are rotated 90° in space from each other.
In reality, they can be slightly distinguished in frequencies due to the perturbation from the different coupling in the coupler port. The TE014 mode is higher and could not be excited by the feeding orientation.
Practically, let’s choose TEm14 modes. There are three possible modes:

## Slide 43
Examples for TE Mode Studies
Where the Legendre Function Pm n has m≤n
If we select TE0np mode, the degeneracy possibility is only 0 and 1

## Slide 44
Other Modes Studies
for TE034 R=7.06865 cm Sphere

## Slide 45
Coupling Simulation to the Sphere Cavity
Nearest mode is TE014 mode which is much undercoupled
One of the two TE114 mode

## Slide 46
Two Polarized SW TE114 modes
With perfect coupler TE114 modes are 10 MHz lower than TE014, they are well separated.

## Slide 47
Put iris 2x5.8=11.6 mm aperture Sweep 50/2500 =0.02 MHz / point
S11 = 0.915 db or 0.803
β=9.15 -- it is almost the optimized design goal for SLED system QL=9556
Δf=1.2 MHz
Q0=97000
Coupling Simulation to the Sphere Cavity

## Slide 48
Movie to animate the SLED System
TE10 Mode input from WR90 Waveguide
TE10 Mode output to Deflectors via WR90 Waveguide

## Slide 49
Studies on Tuning and Detuning
Both tuning and detuning by using plunger inside a circular waveguide
Push-pull deformation
Circular ridge for fine machining
Temperature control for tuning

## Slide 50
Field Patterns with Different Tuners

## Slide 51
Add Iris in Tuner Waveguide Limits the Field
and β Change, but no Much Tuning Range

## Slide 52: Extreme of Tuning Ridge Sizes

## Slide 53: to avoid several possible complications: field and β change, plunger heating, multipacting.
Conservative Fixed Tuner
18mm x 1.5 mm
indentation (-1.8 MHz)

## Slide 54
Detuner Studies(1.5 mm Detuning Rod)

## Slide 55: Sketch of a Coming X-Band SLED Assembly

## Slide 56
Tolerances
  The Coupler/Mode convertor is a broad band microwave component
  The Sphere cavity is a high Q0 , but low QL cavity. If we add proper push-pull tuning studs, the tuning should not be problem.
Manufacturability
  Several kinds of X-Band mode convertors have been successfully designed, built and operated.
  There are many sphere parts were applied like X-Band and S-Band Race-track cavities and L-Band regular cavities
  With TE modes, the sphere cavity does not have cooling problem due to very loss, but temperature stabilization is needed.
Technical Challenges
This is a brand new device, certainly there will be some new design and manufacture problems, but there are no predictable difficulties, which could not be resolve easily.

## Slide 57
Precision simulation served for mechanical design
Further studies for more broad applications
  The scheme can be easily used for S-Band, L-Band …
  It opens a door for flat top SLED pulse for multi-bunch train operation with degenerating higher order mode
Mechanical design for fabrication under way
Fabrication will be in September or earlier
Microwave measurement confirmation
LLRF control design and testing
Final assembly and microwave check
Commissioning
R&D Program

## Slide 58
Wish You All
Great Success in your Career!