## Slide 1: PEPX-type BAPS Lattice Design and Beam Dynamics Optimization
Speaker：Ji Daheng
Jiao Yi, Xu Gang
Institute of High Energy Physics, Beijing, CHINA
2014/08

## Slide 2: PEPX-type lattice, 6 GeV, ~1.3 km, ~90 pm
参数 | 幅度 | 单位
Beam energy E0 | 6 (5) | GeV
Beam current I0 | 200 | mA
Bunch number nB | 2000 | 
Circumference | 1294.2 | m
Horizontal damping partition number Jx /Jy/Jz | 2.05/1./0.95 | 
Natural emittance | 88 (61) | pm
Working point (x/y/z) | 93.14/49.40/0.0058 | 
Natural chromaticity (x/y) | -112/-107 | 
Number of 7BA achromats | 44 | 
Number of high-beta 10-m injection sections | 2 | 
Beta functions in high-beta injection section (x/y) | 90/30 | m
Number of low-beta 5-m ID sections | 42 | 
Beta functions in low-beta straight section (x/y) | 10/3 | m
Damping times (x/y/z) | 11.2/23.0/24.3 | ms
Energy loss per turn, U0 | 2.25 | MeV
Energy spread sd | 0.001 | 
Momentum compaction | 5.9×10-5 | 
RF voltage, Vrf | 10 | MV
RF frequency, frf | 500.36 | MHz
Harmonic number | 2160 | 
Natural bunch length sz | 2.2 | mm

## Slide 3: Linear lattice design
40 standard 7BAs + 4 non-standard 7BAs (for injection)
Similar to PEP-X design (Cai, et al., PRST-AB 2012, 054002), each standard 7BA, phase advance is about (4p + p/4, 2p + p/4), thus every 8 such 7BAs form a quasi-3th order achromat (to cancel the nonlinearities as much as possible).
For each non-standard 7BA, high-beta, 10-m long straight section is designed for injection, the phase advance is matched to (4p, 2p) to restore the symmetry of the beam optics.

## Slide 4: Standard 7BA
Standard 7BA, 29.04 m, 5-m long ID drift
Nine families of chromatic sextupoles
Two families of harmonic sextupoles
Three families of octupoles
Unit cell, compact design, horizontal defocusing gradient combined in dipole, total length 3 m.
Magnet aperture (radius 12.5 mm), vacuum chamber inner radius 11 mm.
Reserve room for correctors (between SD and QF).
QF gradient: < 80 T/m, QD gradient in dipole: < 20 T/m, sext. gradient: < 11400 T/m2, oct. gradient: < 106 T/m3
SD
SD
QF
QF
SF
SF
DIPOLE

## Slide 5: Non-standard 7BAs
Two non-standard 7BAs, 10-m long drift for injection, phase advance are (8p, 4p).
There is not any sextupole or octupole in these non-standard 7BAs.
High beta functions result in relatively large dynamic aperture, promising both off-axis and on-axis injection.
However, the phase advance will deviates from 2np for off-momentum particles, leading to difficulty in optimizing the momentum acceptance.

## Slide 6: Nonlinear optimization
Strong nonlinearities caused by the chromatic sextupoles make it hard to obtain a large dynamic aperture and a large momentum acceptance at the same time.
The deviation of the phase advance of the injection section from 2np adds the difficulty of the optimization.
Three modes (only different in sextupole and octupole strengths) are explored, and are used to inject and store the beam, respectively.
  Mode 1, horizontal dynamic aperture (DA) >+/- 11 mm, momentum acceptance (MA) ~1%
  Mode 2, horizontal dynamic aperture (DA) ~+/- 10 mm, momentum acceptance (MA) ~1.8%
  Mode 3, horizontal dynamic aperture (DA) ~+/- 5 mm, momentum acceptance (MA) ~3%

## Slide 7: Mode 1 for injecting & Mode 3 for storing beam
Mode 1
Injection
Beam current
Mode 2
Mode 3
Ramping sext. & oct. magnets
For user experiments
……
Mode 3
Time
This procedure will take several seconds
Three modes are different only in sextupole and octupole strengths

## Slide 8: Mode 1, Dynamic aperture, Frequency map
Mode 1 is designed specifically for injection
Large horizontal dynamic aperture (larger than the physical aperture, +/- 11 mm), and robust beam dynamics (clear of low order resonances as horizontal amplitude increases).
Dynamic aperture (DA)
Frequency map (FM)

## Slide 9: Mode 1, resonance analysis
nx = 93
nx + 2ny = 192
2ny - 2nx = 6
7nx = 652
4nx + 4ny = 570
For x amplitude within 10 mm and small y amplitude (e.g., < 2 mm), two high order resonances take effects, but disturb the motion only in a very weak degree.

## Slide 10: Mode 1, frequency map for the injection area
with |x| < 10 mm & |y| < 2 mm
nx + 2ny = 192
4nx + 4ny = 570
7nx = 652

## Slide 11: Mode 1, detune curves
AT tracking results agree reasonably well with the analytical predictions, especially in horizontal plane!
Detune terms are well controlled!
Tune shift with x amplitude
Tune shift with y amplitude

## Slide 12: Mode 1, chromatic curve
Due to extremely strong sextupole and octupole strengths, it is very difficult to obtain reasonably small detune terms and well control the high order chromatic terms at the same time. For mode 1, the available maximum momentum acceptance (MA) is ~ 1%.
Black solid: dp/p = 0,
red dashed: 1%, red dotted: -1%
Also due to the inj. section phase advance deviates from 2np as dp/p  0

## Slide 13: Mode 2, moderate DA & MA
Mode 2
Horizontal dynamic aperture (~ +/-10 mm),
Coupling resonance nx – ny = 44 take effects (occurs at x ~ 6 mm),
Momentum acceptance is ~ 1.8%.

## Slide 14: Mode 2, resonance analysis
nx = 93
nx - ny = 44
3nx + 2ny = 378
4nx + 4ny = 570

## Slide 15: Mode 2, detune & chromatic curves
Detune curves: simulation results agree well with the analytical prediction;
Chromatic curves: although the analytical results predict MA > 2%, but actually at dp/p = -2%, nx & ny tend to integer.

## Slide 16: Mode 3, large MA but relatively small DA
Mode 3 is used to store the beam after injection
Large enough dynamic aperture (stable area of x ~ +/-5 mm & y ~ +/-2 mm) to store the beam and large momentum acceptance (>3%), promising long enough Touschek lifetime.
The coupling resonance nx – ny = 44 and the integer resonance nx = 93 dominate the beam dynamics in x and y planes, respectively. Due to large detune terms, the motion reaches these two resonances at relatively small amplitudes.

## Slide 17: Mode 3, resonance analysis
The area of |x| < 4 mm (about 40sx) and |y| < 2 mm (about 40sy) is enough to store the beam, where only a 8th order resonance 4nx + 4ny = 570 slightly distorts the motion.
nx = 93
nx - ny = 44
4nx + 4ny = 570

## Slide 18: Mode 3, detune terms
Tune shift with x amplitude
Tune shift with y amplitude
The detune terms are larger than those of mode 1 and mode 2.

## Slide 19: Mode 3, chromatic curves
Black solid: dp/p = 0,
red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 20: Mode 1 for injecting & Mode 3 for storing beam
Mode 1
Injection
Beam current
Mode 2
Mode 3
Ramping sext. & oct. magnets
For user experiments
……
Mode 3
Time
This procedure will take several seconds
Three modes are different only in sextupole and octupole strengths

## Slide 21: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 01/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%
Mode 1

## Slide 22: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 02/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 23: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 03/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 24: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 04/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 25: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 05/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 26: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 06/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 27: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 07/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 28: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 08/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 29: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 09/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 30: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 10/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 31: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 11/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%
Mode 2

## Slide 32: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 12/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 33: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 13/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 34: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 14/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 35: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 15/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 36: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 16/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 37: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 17/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 38: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 18/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 39: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 19/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 40: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 20/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%

## Slide 41: From Mode 1 to 2, then to 3
* Assume the sext. & oct. strengths are varied averagely from one mode to another, totally 21 steps. No. 21/21.
Black solid: 0, red dashed: 1%, red dotted: -1%,
blue dashed: 2%, blue dotted: -2%,
green dashed: 3%, green dotted: -3%
Mode 3

## Slide 42: Conclusion
Linear lattice of 1.3 km BAPS ring, with natural emittance of ~90 pm @ 6 GeV has been designed.
Due to strong chromatic sextupole strengths and specifically designed injection section, the nonlinear optimization is difficult, and it is barely to well control the detune, chromaticity, and resonance driving terms at the same time.
A solution is to inject the beam at one mode with large dynamic aperture, and store the beam at another mode with large momentum acceptance.
Simulation shows that during the transportation from the injection mode to the storage mode, the beam dynamics keeps stable.

## Slide 43: Thanks for your attention!

## Slide 44
Backup slides

## Slide 45: DA & FM with only two families of sext. & oct.
nx = 93
nx - ny = 44
4nx + 4ny = 570

## Slide 46: Detune & chromatic results
Black solid: dp/p = 0,
red dashed: 1%, red dotted: -1%