## Slide 1
IWAA 2014 - Beijing
Alignment of LIPAC
the Linear IFMIF Prototype Accelerator: requirements and current status F. Scantamburlo et al.
(IFMIF/EVEDA Project Team)

## Slide 2
World energy scenario
In 2 years,
the growth of energy consumption in China was greater than total consumption in Germany
Medium term Problems
Greenhouse effect
Resources are finite
FUSION ENERGY WILL BECOME A SOLUTION
80% of world energy generated
from fossil fuels

## Slide 3
The first wall
of the reactor vessel shall
absorb neutrons energy
and
breed tritium
ITER first wall will present
<2 dpa at the end of its operational life
In a Fusion power plant
~150 dpa within 5 years are expected
Transmutation energies threshold
of Fe >3 MeV yield α-particles
He induced embrittlement
Neutrons in first wall
Section of Vacuum Vessel
of a Tokamak

## Slide 4
14 MeV beyond transmutation thresholds
The accumulation of gas in the materials lattice is intimately related with the neutron energy
56Fe(n,α)53Cr
(incident n threshold at 2.9 MeV)
and
56Fe(n, p)56Mn
(incident n threshold at 0.9 MeV)
Noble gases are not dissolved in metals
Swelling and embrittlement of materials takes place

## Slide 5
Existing neutron sources
do not provide the needed answers
Fission reactors n average energy ~2 MeV
Spallation sources present a wide spectrum
with tails in the order of hundreds of MeV
Generation of light isotopes in the order of ppm
No efficient
p+ or α-particle generation
Fission and spallation sources no fusion n relevant
Watt
Distribution
(fission n spectrum)

## Slide 6
Understanding the degradation of physical properties
of the materials critically exposed to 14.1 MeV n flux
is a key parameter for all machines after ITER to allow
accomplishment of the design
and
facility licensing
Do we need Fusion relevant n source?
Material scientists need experimental data
given the number of variables playing a primary role
in materials degradation
neutrons flux
neutrons spectrum
neutrons fluence
material temperature,
thermo-mechanical history and microstructure
mechanical loading
lattice kinetics…
ITER expects ~2 dpa
at the end of its operational life
A fusion power plant ~30 dpa/year
In ITER ~3 dpa at its end of life
In a Fusion Power plant ~30 dpa/year

## Slide 7
Broader Approach Agreement
IFMIF/EVEDA
A fruitful Japanese- European
International collaboration
(Broader Approach Agreement)
with 7 countries involved
with the respective main research labs in Europe
and main universities in Japan

## Slide 8
IFMIF
International Fusion Materials Irradiation Facility
EVEDA
Engineering Validation & Engineering Design Activities
Article 1.1 of Annex A of the BA Agreement
mandates IFMIF/EVEDA
…to produce an integrated engineering design of IFMIF and the data necessary for future decisions on the construction, operation, exploitation and decommissioning of IFMIF, and to validate continuous and stable operation of each IFMIF subsystem
Signed in February 2007
Entered into force on June 2007
IFMIF/EVEDA

## Slide 9
Deuterons at 40 MeV
collide on a liquid Li screen
flowing at 15 m/s
IFMIF concept
A flux of 1018 n·m-2s-1
is stripped
with a broad peak
at 14 MeV
Availability of facility >80%
International Fusion Materials Irradiation Facility

## Slide 10
The Design of IFMIF is broken down in 5 facilities
Accelerator Facility
Lithium Target Facility
Test Facility
Post-irradiation and Examination Facility
Conventional Facilities
Objective of Validation activities
Engineering Validation Activities (EVA) Phase

## Slide 11
Accelerator facility of IFMIF
10
10 m
the highest intensity
the highest beam power
the highest space charge
the longest RFQ
2 x 5 MW beams
Individual availability of >90%
2 accelerators, 2 x 125 mA, 2 x 5MW
D+ source
CW 140 mA
100 keV
SRF Linac
HWR 175 MHz
40 MeV
Beam shape
200 x 50 mm2
RFQ
175 MHz
5 MeV

## Slide 12
  Features of IFMIF vs LIPAc
  d+ accelerator
  125 mA CW
  5 MW vs 1.125 MW
  Space charge issues
  Low energy/high power
  So are LIPAc as IFMIF
  within present accelerator technology
NGHIEM, P.H.P. et al., The IFMIF-EVEDA Challenges in Beam Dynamics and their Treatment, Nucl. Inst. Meth. 654 (2011) 63–71
Linear IFMIF Prototype Accelerator - LIPAc
WEI, J. et al., The very high intensity future, IPAC 2014, Dresde, www.jacow.org

## Slide 13
Space charge issues are severe at low
They cancel in relativistic regions
LEDA reached 100 mA CW in 1999
at 6.7 MeV protons at the exit of the RFQ
Many lessons learnt have been implemented in LIPAc
LIPAC&IFMIF target 125 mA
at 5 MeV deuterons at the exit of the RFQ
Spoke resonators have been
demonstrated in 2000s to perform for light hadrons at low β
Deuterons present high inelastic cross sections
commissioning would be difficult if done with deuterons
but protons at half energy and half intensity behave
as deuterons at nominal conditions
Features of LIPAc
SCANTAMBURLO, F. et al., LIPAc, the 125 mA/9 MeV CW deuteron IFMIF’s prototype accelerator: what lessons have we learnt from LEDA?, IPAC2014

## Slide 14
Injector + LEBT
CEA Saclay
RFQ
INFN
JAEA Tokai
MEBT
CIEMAT Madrid
SRF Linac
CEA Saclay
CIEMAT Madrid
HEBT
CIEMAT Madrid
BD
CIEMAT Madrid
Diagnostics
CEA Saclay
CIEMAT Madrid
RF Power
CIEMAT Madrid
CEA Saclay
SCK Mol
36 m
★
★
Rokkasho
Oarai
Installed and commissioned in Rokkasho
Accelerator facility validation

## Slide 15
LEDA reached 100 mA @ 6.7 MeV at the exit of the RFQ
with protons in CW in 1999:
beam losses mainly due to beam halo
Beam dynamics calculation on IFMIF accelerator
indicates feasibility of nominal performance
125 mA @ 5 MeV at the exit of the RFQ + SC accelerating stages
The alignment/learning the position of some components
in ± 0.1 mm respect the beam axis is indispensable to:
ramp up correctly the current,
contain beam losses to 1 W/m to allow hands-on maintenances
P. Nghiem et al., “A catalogue of losses for a high power, high intensity accelerator”, Laser and Particle Beams (2014), 32, 461–469.
N. Chauvin et al., Start-To-End beam dynamics simulations for the prototype accelerator of the IFMIF/EVEDA Project, IPAC 2011
Why accurate alignment in LIPAc is important?

## Slide 16
C.K. Allen et al., Beam Halo Measurements in high current Proton Beams, Phys. Rev. Lett. 89, 214802
Beam halo is known to be a major cause
of beam loss and activation
in high current hadron Linacs
LEDA reached 100 mA at 6.7 MeV with protons
and demonstrated that beam halo is due to resonances between individual particles and beam core oscillations
through optical mismatches in transition regions
Installation & commissioning key aspects
Precise alignment
Halo-matching approach
P. Nghiem et al., The IFMIF-EVEDA Challenges in Beam Dynamics and their Treatment, Nucl. Inst. Meth. 654 (2011) 63–71
J. Wei, The very high intensity future, IPAC 2014
Beam halo physics

## Slide 17
35 m
Accuracy assembly requirements
to meet beam halo requirements
are on the limit
of instrumentation performances
± 0.1 mm
Linear IFMIF Prototype Accelerator
LIPAc
LIPAc Alignment requirements

## Slide 18
Instrumentation and software
LEICA AT401 Laser Tracker:
  One of the most accurate tracker in the market (MPE angle accuracy ±(16mm+5mm/m), MPE distance accuracy: ±10 mm, level accuracy: ± 1 arcsec);
  Portability
Spatial Analyzer Ultimate metrology software:
  Experience of F4E ITER Metrology team
  Capability of estimate the uncertainty of measurements through USMN algorithm
  Capability of simulations of measurements to optimize measurement process;
  Verification of instrument performance in the real environment

## Slide 19
Metrology objective
According to ISO and NIST, GUM,
the measurements must be accompanied
with their uncertainty
To asses device position tolerance range +/- 0.1 mm in the assembly hall
ITER metrology handbook:
Target measuring uncertainty
< 0.02 mm in the assembly hall

## Slide 20
Former original existing Network
According to Spatial Analyzer Simulation made by F4E
the uncertainty of locating the tracker would be
0.13 mm
which was not compatible
with the tolerance range to be assessed
+/- 0.1 mm

## Slide 21: New network design - simulations
Placement of 120 new fiducials surveyed 5 times by 5 station will limit
measurement uncertainties <0.02 mm with the laser tracker Leica AT401 suitably located
in the accelerator hall during all future alignment tasks

## Slide 22
Laser Tracker stations
Target
uncertainty
Uncertainty field evaluation
along the beam line
after USMN 1000 samples @ 2 σ
New network design - simulations

## Slide 23: Upgrade of the alignment network - survey
Leica AT 401
69 Wall supports ad hoc machined
50 Floor nests
1 datum Pillar with
Micro-adjustable screws

## Slide 24
Real vs simulated measurements Uncertainty plot

## Slide 25: Beam Line Coordinate Frame (BLF)
The BLF is intrinsically defined by the coordinate of the
130 network fiducials
Horizontality has been improved using the AT401 levelling capabilities

## Slide 26
Global Coordinate Frame (GCF)
Since the beam line frame is not materialized
we retained worth to materialize a coordinate frame
in the accelerator vault to make quick checks
of the impact on the alignment of exceptional events (i.e. an earthquake)
The origin is placed on a particular floor fiducial.
The position of a reference on a pillar has been adjusted
to obtain an axis parallel to the beam line

## Slide 27: Effect of thermal expansion of the building
Rokkasho enjoys hard winters and hot summers
we established a simple procedure to study and eventually compensate
the effect of thermal expansion of the building:
Weekly measurement by LT the distance between two particular points on the floor
almost aligned with the beam line
Weekly measurement of the air temperature in the vault and external temperature
Weekly measurement thermometer the temperature of the floor on 30 points evenly spread
Monitoring will continue on a period including at least one winter and one summer

## Slide 28
The injector and the LEBT have been successfully assembled and aligned with TH system in May 2014
Differentely from the other components which will be fiducialized in Europe before delivery in Rokkasho
the Injector and the LEBT were fiducialized
by AT401 after TH alignment.
Injector alignment

## Slide 29
With good success!
Max uncertainty 0.04 mm
Injector alignment

## Slide 30: Redefinition of the network
An update of the network has been performed in August 2014
movements of the building
not related to the thermal expansion
did not allow anymore locating the instrument within the target uncertainty
RMS< 0.025 mm
A deviation of 0.05 mm in transversal (X axis) and vertical (Y axis)
of the beam line has been registered

## Slide 31
SA software with USMN has been a key factor for the definition of the network in the accelerator hall
Simulation tool demonstrated to be very effective to plan, organize and optimize measurement campaigns
Thermal expansion study is ongoing
Efficient alignment actions have been in place and we are ready for the alignment of the components coming in the coming months
Conclusions

## Slide 32
L. Semeraro, A. Lo Bue, L. Poncet, F4E
T. Morishita, H. Sakaki, H. Shidara, JAEA
THANK YOU!!!

## Slide 33
Thank you for your attention