## Slide 1
Performance of the Iris diaphragm laser alignment system of the SPring-8
C. Zhang
JASRI / SPring-8
IWAA2014, October 13-17, 2014, IHEP, Beijing

## Slide 2
Contents
& laser-iris alignment system
& Where to use this system
& System’s components and adjustment
& Stability and resolution tests
& Accuracy estimation
& Measurement verification

## Slide 3: Iris and Airy pattern
Plane wave
Iris
2a
R
Airy pattern
From Wikipedia
z >> a2 /

R = 0.61z /a

## Slide 4: SPring-8 storage ring magnets
Chasman-Green lattice of 48 cells :
Bending : 2 , Multipole : 17 on three girders
Alignment accuracy achieved:
Between girders : 50 mm (s)
On girder : 20 mm (s)

## Slide 5: Iris diaphragm laser alignment system of the SPring-8
fiber-coupled diode laser
CCD camera with CameraLink I/F
10 m
Close
(iris)
open
open
Iris diaphragms with remote control
open

## Slide 6: Iris diaphragm laser alignment system of the SPring-8
laser head
CCD camera
targets
and
controller
controller

## Slide 7: Alignment of the magnets on common girder
target
controller
laser

## Slide 8: Laser and CCD camera
Expander
Diode laser
S.M.fiber
Collimator
Laser and CCD camera
3.5mW fiber-coupled diode laser, beam size: 4.7mm
CCD size: 15x15mm2, pixel size: 7.4mm, total of 4Mpixel

## Slide 9: Commercial Iris diaphragm and center reproducibility
Commercial iris diaphragm reproducibility
Large than ±2mm (s), getting worse when used at larger caliber
20mm
Blades
Base plate
Actuating
ring

## Slide 10: SPring8 Iris diaphragm and center reproducibility
100-times measurement for the center positions of four targets
Reproducibility is well under ±1mm (s).

## Slide 11: Iris diaphragm target

## Slide 12: Iris diaphragm target

## Slide 13: Target center displacement
Adjustment of target centers in Z direction with a displacement sensor, and XY with laser –iris system.
Diameters of irises are set to 1, 1.6, 1.6, 2.0 (mm) respectively.
Displacement of Dz is 5mm, and Dx, Dy: 2mm.
Dz, f
Dx, Dy

## Slide 14: Laser beam profiles
Laser size measured in tunnel of cell30.
Varied from 4.4 to 6 mm. Distance covers 50m
Distance from laser (m)
2m 45m

## Slide 15: Laser beam pointing stability
8 hours stability, measured in tunnel, with air conditioner, cooling water stopped.
Drifts of both directions are small, Fluctuations are under ±2 mm (s) in 8 meters.

## Slide 16: Laser beam fluctuations for the irises
Fluctuations of the laser beams for the four targets
Under ±2 mm (s), proportional to the distance from iris to camera

## Slide 17: Camera resolution
The camera was set on a precise stage, and was moved in 1mm step. distance to laser ~2 m.
Quantity of camera indication is 1mm in a probability of 90%.
Set camera Instead of target

## Slide 18
Estimation of measurement accuracy
2
0.7
2
1.5
Displacement of center
Center reproducibility
Laser fluctuation at ref. pt
Laser fluctuation
at measurement pt
Measurement accuracy is estimated ±7 mm (2s)
@in tunnel, air conditioner, cooling water stopped.

## Slide 19: Measurement verification on B-girder
Relative positions of 4 magnets were measured 10 times, setting targets again every time.
Measurement reproducibility was within ±7mm w.r.t the average.

## Slide 20: About laser beam size
6.2mm Beam size is tested a little large to a f12mm pathway because it is seen diffraction patterns
The beam is reduced to 4.7mm afterward
6.2mm
4.7mm

## Slide 21: Conclusion
An iris diaphragm laser alignment system is developed. The system is composed of a diode laser head, CCD camera and four iris diaphragm targets. Performance of this system was examined and it is verified that the system has a measurement accuracy of ±7mm (2s) in 8 meters range. This reaches the aim of our intention at first, 10mm (2s) in 10 meters.