## Slide 1: Laser beam trajectory measurement with a CCD camera
Georg Gassner

## Slide 2: Motivation
  Determine angle of a reflective surface by measuring the trajectory of an incoming laser beam and its reflection of the surface.
Reflective Surface
d
d
Incoming beam
Reflected beam

## Slide 3: Laser trajectory measurement
Principle
  Determine points on the laser trajectory at two different locations

## Slide 4: Hardware - Laser
Laser (Hamar L-705 Bore Laser Alignment System)
  <1mW Cw
  670nm
  Beam Stability:
  10µrad/hr/degC

## Slide 5: Hardware
Point Grey - FL2-20S4M-C
  1624x1224 pixel
  4.4µm pixel size
  Natural Density
  Filter (OD=2)
Newport Stages
  12.7mm travel
  XZ

## Slide 6: Measurement System
Camera
Computer
Screen
Laser
Retro reflectors
Screen shot

## Slide 7: Fiducialization
Relative position of fiducials on CMM.
Offset determination by setting the camera up on a laser line and measuring at different orientations to the laser line.
Mapping with laser tracker.

## Slide 8: Solve Least Squares Problem
Numeric Approach
  Calculate Orientation of Camera relative to CMM data with a six par transformation for every setup.
  Iteratively change offsets (Dx, Dy, Dz) apply transformation parameters and fit new line to the data.
  Calculate distance of the individual camera positions to the estimated line and find minimum of .
  Standard deviation single shot: 30µm

## Slide 9: Application: HXRSS (1)
Align a crystal at a nominal orientation without touching it.

## Slide 10: Application – HXRSS (2)
Bench Top alignment in the lab by mapping the camera at 3 different locations for the incoming beam and 3 different locations for the outgoing beam

## Slide 11: Application: Mirror tool for e-gun diagnostic
Benchtop alignment of two mirrors with laser and CCD camera

## Slide 12: Aligning the laser to simulate beam
Laser
Precision Lift
Translation stage
Two rotation stages

## Slide 13: Laser Fiducialization
Map Camera at 3 different locations
Map cross structure fiducials
Fit line through calculated camera positions
Laser Tracker
Camera Positions
Fiducials

## Slide 14: Application: Thin crystal spectrometer (1)
In-situ replacement of bent crystal (5x15mm).
Alignment of Laser to be in-line with x-ray beam

## Slide 15: Pinhole
To reduce the beam diameter we used a 0.8mm pinhole:
Pro: simple
Con: bigger beam
divergence
compared with lens
system

## Slide 16: Application: Thin crystal spectrometer (2)
Align the laser in place of the x-ray beam
Manually manipulate the crystal until centered on the camera.

## Slide 17: Variable Energy Spectrometer (1)
Chamber sub-assy.
Detector sub-assy.
Detector Arm sub-assy.
Crystal sub-assy.

## Slide 18: Variable Energy Spectrometer (2)
Establish local coordinate system
Setup laser to emulate beam
Calculate z and y position by intersecting in and outgoing line

## Slide 19: E-gun setup
Place the Spiricon camera at the desired cathode location relative to the mirror chamber.
Replace camera
with gun

## Slide 20: Summary
Most components of the system are available at labs.
Laser beam trajectory measurements with a camera can achieve about 50µm point accuracy when used in combination with a Leica AT401.