## Slide 1
Alignment of Superconducting Undulators at the APS
Jaromir M. Penicka
for the APS SCU team
IWAA2014 Beijing, October 13-17, 2014

## Slide 2: Outline
Introduction
SCU design overview
SCU0 Assembly and fiducialization
Cooling displacement compensation
Alignment in the APS storage ring
Final beam-based alignment and monitoring
Summary

## Slide 3: Advanced Photon Source (APS)

## Slide 4
Core Team
Management: E. Gluskin*(ASD-MD)
Simulation: R. Dejus (ASD-MD)
S. Kim (ASD-MD)
R.L. Kustom (ASD-RF)
Y. Shiroyanagi (ASD-MD)
Design: D. Pasholk (AED-DD)
D. Skiadopoulos (AES-DD)
E. Trakhtenberg (AES-MED)
Cryogenics: J. Fuerst (ASD-RF)
Q. Hasse (ASD-MD)
J. Kaluzny (ASD-RF)
Measurements: M. Abliz (ASD-MD)
C. Doose (ASD-MD)
M. Kasa (ASD-MD)
I. Vasserman (ASD-MD)
Controls: B. Deriy (ASD-PS)
M. Smith (AES-CTL)
Tech. support: S. Bettenhausen (ASD-MD)
K. Boerste (ASD-MD)
J. Gagliano (ASD-MOM)
M. Merritt (ASD-MD)
J. Terhaar (ASD-MD)
Budker Institute Collaboration
(Cryomodule and Measurement System Design)
N. Mezentsev
V. Syrovatin
V. Tsukanov
V. Lev
FNAL Collaboration
(Resin Impregnation)
A. Makarov
UW-Madison Collaboration
(Cooling System)
J. Pfotenhauer
D. Potratz
D. Schick
Y. Ivanyushenkov (ASD)
Technical Lead and Commissioning Co-Lead
Technical Support
R. Bechtold (AES-MOM) D. Capatina (AES-MED)
J. Collins (AES-MED) P. Den Hartog* (AES-MED)
R. Farnsworth* (AES-CTL) G. Goeppner* (AES-MOM)
J. Hoyt (AES-MOM) W. Jansma (AES-SA)
J. Penicka* (AES-SA) J. Wang* (ASD-PS) S. Wesling (AES -SA)
SCU0 team
*Group Leader † Former group leader
K. Harkay (ASD-AOP) Commissioning Co-Lead
Commissioning Team
L. Boon (ASD-AOP)
M. Borland (ASD-ADD)
G. Decker† (ASD-DIA)
J. Dooling (ASD-AOP)
L. Emery† (ASD-AOP)
R. Flood (ASD-AOP)
M. Jaski (ASD-MD)
J. Lang (ASD-ESH/QA)
J. Lang (XSD-ADD)
F. Lenkszus (AES-CTL)
D. Robinson (XSD-MM)
V. Sajaev* (ASD-AOP)
K. Schroeder (ASD-AOP)
N. Sereno* (ASD-DIA)
H. Shang (ASD-AOP)
R. Soliday (ASD-AOP)
X. Sun (ASD-DIA)
A. Xiao (ASD-AOP)
A. Zholents (ASD-DD)
Former management: E. Moog† (ASD-MD)
Associate Project Manager: M. White (APS-U)

## Slide 5: SCU cryostat

## Slide 6: SCU0 cryostat structure

## Slide 7: SCU0 and SCU1 parameters
Parameter | SCU0 | SCU1
Electron beam energy | 7.0 GeV | 7.0 GeV
Photon energy at 1st harmonic | 20-25 keV | 12-25 keV
Undulator period | 16 mm | 18 mm
Magnetic gap | 9.5 mm | 9.5 mm
Magnetic length | 0.33 m | 1.14 m
Cryostat length | 2.06 m | 2.06 m

## Slide 8: Alignment Tolerances*
Alignment Tolerance | X [mm] | Y [mm]
Magnetic structure | ±0.150 | ±0.150
SCU0 vacuum chamber relative to the magnetic structure | N/A | ±0.150
SCU0 vacuum chamber relative to the U33 ID chamber | ±0.150 | ±0.150
* K. Harkay et al., “APS-U Superconducting Undulator Physics Requirements Document,” Technical Report APS_1425203, APS, 2011.

## Slide 9: The Challenge of Alignment?
How to align an object suspended by Kevlar
That changes temperature by 300 degrees K
And is encapsulated like this?

## Slide 10: Cold Mass

## Slide 11: 20 K Radiation Shield

## Slide 12: 60 K Radiation Shield

## Slide 13: Vacuum Vessel

## Slide 14: Cold Mass Assembly
Conventional optical tooling methods
Tolerance ±75 microns in X,Y achievable
Support frame – magnet structure – vacuum chamber

## Slide 15: Cold Mass Fiducialization
Optical Tooling
Articulating CMM (FARO)

## Slide 16: Cold Mass - Vacuum Vessel Assembly

## Slide 17: Kevlar band suspension system
Upstream end
Downstream end
The alignment of the cold mass within the vacuum vessel assembly was accomplished by adjusting the Kevlar suspension bands .
The coordinates of the vacuum vessel and cold mass fiducials were monitored with the laser tracker and N3 optical level.

## Slide 18: Cooling Displacement Test

## Slide 19: Cooling Displacement Test
The seven pairs of spherical targets were placed in the beam chamber at predefined locations .
The pairs of sphere targets were "spring-loaded" with stiff wire to engage the cylindrical profile of the chamber in the horizontal plane.
By observing the top and bottom edges of the spheres by N3 optical level the vertical position of the beam chamber was measured during the cool-down and warm-up cycle.
Spherical target inside the prototype of the SCU0 vacuum chamber photographed through the alignment scope of the optical level.

## Slide 20: Location of Spherical Targets
Positions 1, 3, 5, and 7 are at the beam chamber support locations.
Courtesy M. Kasa

## Slide 21: Cool-down and Warm-up Cycle
Courtesy M. Kasa

## Slide 22: Cool-down and Warm-up Cycle
Courtesy M. Kasa

## Slide 23: Cool-down and Warm-up Cycle
Courtesy M. Kasa

## Slide 24: Cool-down and Warm-up Cycle
Courtesy M. Kasa

## Slide 25: Aluminum Links Compensation
Upstream end
Downstream end
To eliminate displacement of the beam chamber/magnets assembly during the cooling process the Kevlar strings were modified with the aluminum links.
The length of the aluminum links was calculated to compensate for the thermal elongation of Kevlar and thermal contraction of stainless steel part as well as mechanical elongation of the Kevlar caused by pressure difference.

## Slide 26: SCU magnetic measurement
Cold (20K) Al beam chamber
Warm (~300K) Ti guiding tube
Warm (~300K) carbon fiber tube holding Hall probe or 4 mm wide Integral coil or fiber optic alignment target
X
Y
Vacuum
Air
Mitigation of the thermal shift verified during the next cool-down warm-up cycle.
Beam chamber monitoring was incorporated into the magnetic measurement procedure.
Courtesy C. Doose

## Slide 27: Alignment in the APS storage ring
The SCU0 was installed in SR sector 6, downstream of a half-length ID chamber with 7.5 mm vertical aperture.
An optical level and precision transit-square were utilized to position the SCU0 at its ideal location.
A laser tracker oriented to the storage ring control network was used to provide a redundant quality assurance check.
Beam-based alignment was foreseen as a necessary final step to confirm and fine tune the position of the SCU0 after cool-down.

## Slide 28: Beam-based Chamber Alignment
Chamber alignment critical to protect SCU0 from excessive beam-induced heat loads.
Novel beam-based alignment using thermal sensors mounted on the SCU0 beam chamber was developed at APS.*
Electron beam steering vertically and thermal sensor minima determine the vertical center of the SCU0 chamber with respect to the user beam orbit with 0.100 mm accuracy.
Vertical center of chamber with respect to the user beam orbit. Sensors 2-6, January 2013 data.
* K. Harkay et al.

## Slide 29: Chamber alignment stability
Courtesy K. Harkay

## Slide 30: Realignment of SCU0
Courtesy K. Harkay

## Slide 31: User experiments with SCU0
Cover image for August 2013 issue of Nature Materials features image taken with SCU0.
A. Goldman et al., Nature Mat. 12, 714 (2013)
Diffraction pattern of 10-fold axis in new GdCd magnetic quasicrystal
UO2 3.12
UO2 1.15
UO2 3.39
UO2 0.92
UO2 0.33
ThO2
ThO2
ThO2
rods
8 x 25 mm
Th Image
U Image
Uranium and Thorium fluorescence maps of mock fuel pellets encased in Zirconium.
G.J. Havrilla et al. to be published
Fluorescence mapping from nuclear fuel pellets

## Slide 32: SCU1 improvements for alignment
Added beam chamber viewports.
Permanent fiducial cups in place of bushings.
Improved Kevlar bands (no braiding, no knots).

## Slide 33: Summary
The first prototype superconducting undulator was successfully installed and aligned in the APS storage ring and has reliably delivered 80 – 100 keV photons to APS users for the last 19 months.
A new spherical bead target technique was implemented for quantifying thermal shift of the SCU0 beam chamber.
A unique suspension system combining Kevlar string with aluminum links was designed to eliminate any displacement of the chamber during the cooling of the SCU0.
A novel beam-based measurement method using thermal sensors mounted on the SCU0 beam chamber was developed for fine alignment and stability monitoring.
Significant knowledge was gained from the SCU0 installation, and many improvements are being implemented in the assembly and alignment of the next superconducting undulator, SCU1.

## Slide 34
Thank you for your attention
感謝您的關注