## Slide 1: Shielding of the Electronics in the Tunnel
L.S. Esposito, M. Brugger, F. Cerutti, A. Ferrari, R. Losito

## Slide 2: What are we talking about?
memory bit flit in collimator controls

## Slide 3: What are we talking about?
Electronics
Ventilation Units
CV,crane,
fire
Gy per 4.5 1019 p.o.t.
CNGS 2007 physics run, 8 1017 p.o.t. delivered ( 2% of a nominal CNGS year )
Single event upsets in ventilation electronics caused ventilation control failure and interruption of communication
Predicted dose levels
in agreement with measurements

## Slide 4: Outline
Introduction to Radiation to Electronics (R2E)
  Radiation environment and sources
  Radiation effects
  Radiation levels
Case study for FCC-ee
Conclusions

## Slide 5: Ingredients for R2E studies
PHYSICS MODELS
RADIATION ENVIRONMENT
ELECTRONIC COMPONENTS
RADIATION EFFECTS ANALYSIS TESTS MITIGATION

## Slide 6: High-Energy Particle Interactions

## Slide 7: Radiation Areas and Sources
Source of Radiation
Direct Losses
  collimators and collimator like objects injection, extraction, dump
  levels scale with beam intensity
Collisions
  around experimental areas
  scale with luminosity
Beam-Residual-Gas
  all areas along the ring
  scales with both intensity and residual gas density

## Slide 8: Radiation source for lepton machine
  Synchrotron Radiation
  along bending dipole
  scales with beam intensity and energy
An outline plan for a future tunnel in Geneva that could house a 80–100 km particle collider. (Courtesy: CERN)

## Slide 9: Electronics: Radiation Effects
TID. Total Ionizing Dose
DD. Displacement damage
SEE. Single event effect
EFFECTS
SEE
DD
TID
Single Events
Cumulative
Effects with time Critical for injection lines From performance worsening… to damage
Stochastic
Immediate effects
Bit flip, rupture…

## Slide 10: Radiation Physics/Effects/Monitoring
Dose
Displacement
Single Events
EM cascade
h, e,.. > 100 KeV
h > 20 MeV
Radfet
PIN Diodes
SEU counter
nuclear cascade
radiation damage in semiconductors
Radiation Monitor
Radiation Field
Effect in the Device
Measurement

## Slide 11: CERN Radiation Levels
LHC + Experiments
Avionic
Sea Level
ISS
R2E Single-Event
Effects
R2E Cumulative Damage
Material Damage
COTS Systems
Hardened Electronics
Electronics
Damage
Custom Boards with COTS
Space & Deep Space
CNGS
Failure

## Slide 12: Mitigation Options
SHIELDING
RELOCATION
CIVIL ENGINEERING
RAD-TOL DESIGN

## Slide 13: R2E Project Building Blocks
Calculations
Radiation Tests
Production & Implementation
Radiation Monitoring
Developments
Test Facilities

## Slide 14: Selected energy deposition studies for LHC
The agreement is within 30%!!!
FLUKA model for LHC right P1
 | Hadron > 20 MeV [cm-2] | 
 | RM08S | RM09S
FLUKA | 6.1×108 | 3.0×107
DATA | 4.56×108 (25 upsets) | 4.32×107 (25 upsets)
Courtesy of N.V. Shetty, EN-STI-EET, CERN
Normalized at total integrated luminosity in 2012 operation

## Slide 15: FCC arc cell model in FLUKA
10.5 m dipole
Iron + plastic
1.5 m
Q
Copper (2mm tube)
water cooling
25 mm
24 cm absorber
Lead
To be considered as a case study of a possible FCC cell
Ref: L.Lari et al., IPAC2014, THPRI011

## Slide 16: Synchrotron radiation: generalities

## Slide 17: Synchrotron radiation: FCC-ee case
E= 8.5 GeV/turn (dE/ds=1.375 keV/cm in the dipoles)
P = 8.5 x I[mA] MW = 8.5 x 10mA = 85 MW in the whole accelerator
(dP/ds= 1.375 x I[mA] W/cm in the dipoles)
95.75% of the photon amount
<E>=395 keV
99.99964% of the total power
E>100 eV

## Slide 18: Radiation field in the FCC tunnel
Neutrons from photo-nuclear interactions

## Slide 19: SEE
SEEs to be considered (depending on the location), but nothing which is not unsolvable

## Slide 20: NIEL
Dominated by e.m. component
Not to be considered as limiting factor

## Slide 21: TID
Above 100 kGy, electronics damage must be considered
  optical fibers might degrade
  cables can get problems
  some organic materials are to be avoided
Notes: § PMMA (Plexiglas) < 50 kGy
§ Butyle based Caoutchoucs < 30 kGy
§ Perfluoro-ethylène-propylène (FEP) < 30 kGy
§ Acetal Resins (POM) (Delrin) < 10 kGy
§ PTFE (Teflon) < 1 kGy

## Slide 22: Radiation levels in FCC-e+e-
LHC + Experiments
FCC-e+e-
FCC-e+e-
FCC-e+e-
22
COTS Systems
Hardened Electronics
Electronics
Damage
Custom Boards with COTS

## Slide 23: Conclusions
R2E represents a crucial issue to be taken into account as design criterion of any high energy and intensity machine
The R2E project at CERN allowed to create a diffuse knowledge and expertise covering all the aspects of radiation hardening
A case study for HF-e+e- was presented
TID effect has to be mitigated through a carefully shielding design

## Slide 24
Backup

## Slide 25: Relevant FLUKA capabilities
Sophisticated low energy photon transport including polarization effects for Compton, photoelectric and coherent scattering, and full account for bound electron effects: already available in FLUKA since several years
New: dedicated “generic” source for SR radiation accounting for:
  Spectrum sampling
  Polarization as a function of emitted photon energy
  Angular distribution
  Arbitrary orientation emitting particle vs magnetic field
  Photon emission along arcs/helical paths

## Slide 26: Energy deposition on FCC elements
normalized to 10 mA beam current
25 mm
24 cm absorber
Lead

## Slide 27
Reliability & Radiation
Notes: FIT = Failure In Time

## Slide 28
Required Reliability
© R. Baumann
LHC: few thousand electronic units exposed
Aim: less than one radiation induced failure per operational week
Reliability in FIT: -> aiming for few FITs/SYSTEM!
Per Chip? (better don’t do it)

## Slide 29
R2E Qualification Steps
10-Oct-14
Radiation tests are part of any new development
Rad constraints to be considered from day-0
REQUIREMENTS
Electrical/system
Radiation environment and effects
Timeline
Complexity
DESIGN
Specifications
Selection
Design
Time
TEST
System
Component
Qualification
PROCUREMENT
Test boards
Prototype
Production

## Slide 30: RadMon System in the LHC
Online (through WorldFIP) and Standalone version
Deported unit (for TID/1MeV)
3 types of sensors:
  RadFets (NMRC) for TID
  PIN diodes (Siemens) for 1MeV n eq.
  SRAMs for high-E hadron fluence (SEEs)
System of ~400 online radiation monitors
Several detailed calibration campaigns
  thermal neutron response and intermediate energy (few MeV) neutrons
  additional RadFet calibration (& batch) tests
  Additional 1MeV verifications

## Slide 31: Test Facilities
EFFECTS
SEE
DD
TID
PSI
CEA
Co60 source
Standard facilities
  PSI. Proton beam (>15 tests per year, see 2013 list)
  CEA, Fraunhofer. Displacement damage (few tests per year)
  Fraunhofer. Co-60. Total Ionizing dose (blanket contract:>10/y)
In-house
  (CNRAD, H4IRRAD)
  CHARM (soon operational)
    A unique test facility for CERN and external institutes/groups/customers
  Co-60 (under construction)
Coordination and Operation
    >20 equipment groups affected