## Slide 1: Superconducting RF Cavity and Power Source for CEPC
SUN Yi (孙毅), ZHAI Jiyuan (翟纪元), ZHOU Zusheng
(周祖圣) , ZHENG Hongjuan (郑洪娟) , GAO Jie (高杰)
IHEP
The 4th International Workshop on Future High Energy Circular Colliders
September 12-13, 2014, Shanghai

## Slide 2: Outline
CEPC SRF system overview
Design criteria with New Technology
Cavity design
  RF power source
Technical challenges (HOM, coupler, industrialization)
Summary

## Slide 3: CEPC SRF System Layout and Parameters

## Slide 4: CEPC SRF System Layout
8 RF sections
In each ~ 150m section
Main ring: - 12 x 8m cryomodules - 650 MHz 5-cell SRF cavity - 4 cavities / cryomodule
Booster: - 4 x 12m cryomodules - 1.3 GHz 9-cell SRF cavity - 8 cavities / cryomodule
Superconducting RF Cavity
~ 20 x CW gradient
less disruption to beam
100s times more efficient
LLRF benefits
compared to normal conducting

## Slide 5: SRF Cryomodule

## Slide 6
RF power coupler (with ceramic windows)
2 K superfluid liquid helium
Frequency tuner (fast and slow)

## Slide 7: Superconducting Cavity and HOM Damper
High purity Niobium
more expensive than Silver
HOM damping, R/Q: HOM impact to the beam
Q ~ HOM power extracted or damping time

## Slide 8: IHEP Cryomodules for Euro-XFEL (60 12-meter-long modules)

## Slide 9: IHEP 1.3GHz 9-cell Cavity Module
Final assembly and liquid nitrogen 80K cooling down experiment

## Slide 10: Cleanroom Assembly

## Slide 11: Coupler, 2K pipe, Tuner, HOM coupler

## Slide 12: Cold Mass Assembly & Cavity Alignment

## Slide 13: Vacuum Vessel Assembly and Alignment

## Slide 14: Warm Coupler and Interfaces

## Slide 15: CEPC SRF System Parameters
Parameters | CEPC-Collider | CEPC-Booster | LEP2
Cavity Type | 650 MHz 5-cell Nb N-doped | 1.3 GHz 9-cell Nb N-doped | 352 MHz 4-cell Nb/Cu sputtered
Cavity number | 384 | 256 | 288
Vcav / VRF | 18 MV / 6.87 GeV | 20 MV / 5.04 GeV | 12 MV / 3.46 GeV
Eacc (MV/m) | 15.5 | 20 peak | 6 ~ 7.5
Q0 | 2(3)E10 @ 2K | 2E10 @ 2K | 3.2E+9 @ 4.2K
Cryo AC power (MW) | 20 | 2.5 (15% DF) | 6.1
Cryomodule number | 96 (4 cav) | 32 (8 cav) | 72 (4 cav)
RF input power / cav (kW) | 260 | 20 peak | 125
RF source number | 384 (300 kW kly) | 256 (25 kW SSA) | 36 (1.2 MW/8 cav)
RF AC power (MW) | 200 (260 installed) | 2.4 (15% DF) | 85
HOM damper power (W) | 26 k (ferrite+hook) | 5 (hook) (15% DF) | 300 (hook)

## Slide 16: What’s NEW in CEPC SRF?
Breakthrough N-doping High Q Technology
  major discovery at FNAL in 2013, immediately used in LCLS-II
  save billions for CEPC, and SRF linacs (ADS, XFEL, ERL, ILC)
Most advanced Cavity Production and Preparation technique
  ILC-standard electro-polishing and high pressure rinsing process
  semiconductor-grade clean room assembly of 8~12 m cavity string
  world largest SRF infrastructures and talent pool for future accelerators
Most powerful, but remarkably power efficient accelerator
  create new technologies to power the beam & extract huge parasitic loss
  increase RF+Cryo AC to beam power efficiency > 50 %

## Slide 17: What’s NEW in CEPC SRF?
Big jump from LEP2/BEPCII to CEPC
  10 ~ 30 x Q0
  2 ~ 3 x Eacc
  3 ~ 8 x Cryogenic efficiency
Develop new Thin Film material as alternative for dramatically high Q (1011) and high gradient (100 MV/m)
  completely change the landscape and application of SRF
  huge decrease in cryo plant cost and power consumption
  open up the route to green linear collider of > 3 TeV
  SRF science at IHEP

## Slide 18: Design Criteria and Parameter Choice with New Technology

## Slide 19: CEPC SRF System Design Criteria
qb = 60 nC
PSR 100 MW
Vrf 6.87 GeV
U0 = 3 GeV
T
frf
Q0
η↑, τBS ↑, σz↓
ρ = 6.1 km
Pcoupler < 300 kW
Ncavity
↓
Eacc
Ncell
R/Q
Impedance T.H.
↑
HOM Power
↓
Vc
￥
Lc
Riris
Ep Bp
↓
￥
↑
↓
HOM QL
QL
G
HOM R/Q, k
↓
H
H
H
H
Rs
Thin Film
Nmodule
Ncav/module
￥
H
￥
H
HOM Damping
WG
Hook
Ferrite
Bulk Nb
Nb3Sn/Nb
Nb/Cu
N-dope
↓
Dynamic Cryo Load
↑
↑
H
Cavity Shape
Large iris
Low loss
PS Efficiency
↑
Cavity Material
I = 33.3 mA
Nb = 50
Mode Propagate
￥
C
H
RF AC < 200 MW ?
Cryo AC < 20 MW ?
↓
2 K
4.2 K
↓
↓
f0 = 5.6 kHz
￥
￥
Vc
↓
H: handling or LLRF control

## Slide 20: RF Frequency Choice
Energy acceptance (lower frequency)
Bunch Length (higher frequency)
HOM impedance and power (lower frequency, beam aperture)
Cavity size and cost (higher frequency)
Booster current 1/20 of collider (higher frequency)
Collider RF frequency harmonic of the booster
Use mature tech and synergy with other projects (ILC, XFEL, ADS…)
Thus
CEPC collider RF frequency = 650 MHz
CEPC booster RF frequency = 1.3 GHz
But, booster has lower energy and radiation damping =>
Analyze beam instability caused by the 1.3 GHz cavity (WANG Na’s talk)

## Slide 21: Cavity Number and Gradient Choice
Within the reasonable gradient, main ring cavity number is limited by the input coupler power handling capability.
If coupler power ~ 156 kW (BEPCII level)
  640 cavities, 10.7 MV (5-cell 9.3 MV/m, if 4-cell 11.6 MV/m)
  4 cav / mod, 160 cryomodules, 20 mod / RF section
If coupler power ~ 260 kW (KEKB 380 kW, LHC 300 kW)
  baseline
  384 cavities, 18 MV (5-cell 15.5 MV/m, if 4-cell 19.5 MV/m)
  4 cav / mod, 96 cryomodules, 12 mod / RF section
  KEKB and LHC coupler number ~ 10

## Slide 22: Coupler Power Handling Capability Impact on Main Ring Cost and Risk
Coupler Power (kW) | Eacc (MV/m) | Cavity # | Module Cost (Billion CNY)
156 | 9.3 | 640 | 2.6
260 | 15.5 | 386 | 1.5
330 | 19.7 | 302 | 1.2
4M CNY / cavity (including coupler, tuner , LLRF, cryomodule, etc)
Balance and optimize: coupler high power yield and operation risk, module and power distribution cost reduction, cavity operation margin risk, cryogenic installation and operation cost (due to Q-drop, field emission, gradient change), ring impedance …

## Slide 23: 650 MHz Cavity Q0 Choice
Q0 | Installed 4K equiv. (kW) | Cryo installed power (MW) | Cryo-system Cost (Billion CNY)
3.0E+10 | 76 | 16 | 1.6
2.0E+10 | 95 | 20 | 2.0
1.0E+10 | 155 | 34 | 3.4
5.0E+09 | 273 | 60 | 6.0
Eacc = 15.5 MV/m, 384 cavities, 21M CNY / kW 4K equiv. cryo-system
Note: ILC 500GeV machine installed cryo AC power 45 MW

## Slide 24: Theoretical limit of Cavity Gradient and Q
 | 9.2 | 18.3 | 39 | 16.2 | 17.5 | 15
 | 2 | 20 | 0.3-5 | 70 | 35 | 
 | 40 | 85 | 140 | 200 | 151 | 140
 | 200 | 540 | 430 | 230 |  | 430
 | 170 | 50 | 30 | 20 | 30 | 30
 | 0.4 | 30 | 3.5 | 15 |  | 3.5
 | 9.2 | 18.3 | 39 | 16.2 | 17.5 | 15
 | 2 | 20 | 0.3-5 | 70 | 35 | 
 | 40 | 85 | 140 | 200 | 151 | 140
 | 200 | 540 | 430 | 230 |  | 430
 | 170 | 50 | 30 | 20 | 30 | 30
 | 0.4 | 30 | 3.5 | 15 |  | 3.5
↑
↓
↓
↑
Possible Superconducting Material for RF Cavity (s-wave only)

## Slide 25
LEP-II sputtered 352 MHz 4.2K
KEKB bulk 500 MHz 4.2K
CEPC sputtered 650 MHz 4.2K
Q = 8E8 at 10 MV/m, too low!
600 cavities
CEPC bulk 650 MHz 4.2K
Q = 5E8 at 15 MV/m
If very clean, Q=1E9 at 15 MV/m
extrapolated
CEPC bulk 650 MHz 2K
Q = 2E10 at 15 MV/m
even Q=1E10 still gain a lot
~ 4 times cryo-plant cost and power
~ 1.6 times cavity cost
~ + billions of CNY
~ 5 times cryo-plant cost and power
~ + billions of CNY
Baseline for Main Ring
η (4.2K/2K) = 3.6
384 cavities
How to guarantee 2E10 or even higher at 2K?
Can we increase thin film Q at 4.2K?
Beyond normal recipe and Nb

## Slide 26: FNAL 650 MHz Cavity
CEPC
Bp/Eacc=3.75
CEPC cavity with large iris Bp/Eacc = 4.2
Melnychuk, IPAC2014

## Slide 27: IHEP 1.3 GHz and 650 MHz Cavity
ADS 650 MHz β=0.82 5-cell cavity
Vertical test soon
1.3 GHz 9-cell cavity vertical test (VT) in 2013. In module horizontal test (HT), the cavity performance will have degradation.
 | ILC TC-1 | CEPC
VT Eacc | 20 MV/m | 22 MV/m
VT Q0 | 1.4E10 | 3E10
HT Eacc | 18 MV/m | 20 MV/m
HT Q0 | 1E10 | 2E10

## Slide 28: Cavity Q performance with “ILC standard” surface processing recipe
IHEP 1.3GHz 9-cell Cavity test at 2013
theoretical limit

## Slide 29: Nb N-Doping and Flux Expulsion
Two major discoveries at Fermilab
Nitrogen doping to lower the BCS surface resistance
  Lower than the previously perceived “theoretical limit”
  Example at 16 MV/m: Q > 3x1010 by doping vs Q ~ 1.5x1010 with the standard ILC/XFEL cavity processing
  Also lowers residual
Effective magnetic flux expulsion by fast/high thermal gradient cooldown around Tc, drastically affects the Meissner effect and achieve record low residual resistances
  Example: Q = 2.7x1011 in 27 mG ambient field (only 2 W is needed to excite 15 MV/m e-field for CEPC 5-cell cavity)
  Relax very tight magnetic shield for high Q operation, otherwise high Q is not usable in real accelerator

## Slide 30
2x higher Q leads to a factor of 2 decrease in required refrigeration => 1 cryoplant less => 50-100M$ in capital costs + 10s of M$ in operational costs

## Slide 31
LEP-II sputtered 352 MHz 4.2K
KEKB bulk 500 MHz 4.2K
CEPC sputtered 650 MHz 4.2K
Q = 8E8 at 10 MV/m, too low!
600 cavities
CEPC bulk 650 MHz 4.2K
Q = 5E8 at 15 MV/m
If very clean, Q=1E9 at 15 MV/m
extrapolated
CEPC bulk 650 MHz 2K
Q = 2E10 at 15 MV/m
even Q=1E10 still gain a lot
~ 4 times cryo-plant cost and power
~ 1.6 times cavity cost
~ + billions of CNY
~ 5 times cryo-plant cost and power
~ + billions of CNY
Baseline for Main Ring Cavity
η (4.2K/2K) = 3.6
384 cavities
How to guarantee 2E10 or even higher at 2K?
Can we increase thin film Q at 4.2K?
Beyond normal recipe and Nb

## Slide 35: Nb3Sn Impact on CEPC 650 MHz cavity
Coupler 156kW, 600 cavities, 10MV/m, 4.2K, Q=4E10 (RBCS~f 2 )
  Cryogenic power 1/10 of the baseline, save ~ 1.6B CNY
  But 200 more cavities ~ add 0.8B, so net save 0.8B
  If further R&D to 15 MV/m, 4.2K, 4E10, save 1.6B
In ideal case, Nb3Sn 25MV/m, 4.2K, 4E10, coupler 420kW, 140 less cavities save 0.6B + cryo save 1.6B = 2.4B
Seems not big amount for CEPC, but for a 7GeV CW XFEL or ERL, save 1/3~1/2 capital cost and 2/3 power consumption
Problem with Nb3Sn at high field is its low thermal conductivity compared to Nb (1/1000). Overheating. R&D needed.

## Slide 36: CEPC SRF Cavity Design

## Slide 37: 650 MHz 5-cell Cavity
 | internal | Left end half cell | Right end half cell
Riris(mm) | 77.96 | 84.46 | 84.46
Alpha(deg) | 2.24 | 16.727 | 16.39
A(mm) | 94.4 | 92.1 | 91
B(mm) | 94.4 | 92.1 | 91
a(mm) | 20.03 | 13.76 | 13.71
b(mm) | 22.09 | 21.14 | 20.29
L(mm) | 115 | 114 | 113
D(mm) | 206.6 | 206.6 | 206.6
flatness | 2.17% |  | 
coupling | 3.04% |  | 
Ep/Eacc | 2.43 |  | 
Hp/Eacc [mT/(MV/m)] | 4.23 |  | 
Need further shape optimization, especially for the HOM properties

## Slide 38: 650 MHz 5-cell Cavity Parameters
Parameter | Symbol | Unit | Value
RF frequency | fRF | MHz | 650
RF voltage | VRF | GV | 6.87
Cavity gradient | Eacc | MV/m | 15.6
Effective length (five cells) | Leff | m | 1.147
Cavity voltage | Vc | MV | 18
Number of cavities |  |  | 384
Cavities in one cryomodule |  |  | 4
Cryomodule length |  | m | 8
Number of cryomodules |  |  | 96
R/Q | R/Q | Ω | 514
Geometry factor | G | Ω | 268
Iris diameter |  | mm | 156
Quality factor | Q0 |  | 2~3×1010
External Q of input coupler | Qext |  | 2.4×106
RF power per cavity | Pin | kW | 260
Cavity longitudinal loss factor※ | k∥ | V/pC | 1.87
Cavity transverse loss factor※ | k⊥ | V/pC m | 10
※ σz = 2.66 mm
3~4×1010 for Vertical Test
18 MV/m for vertical test

## Slide 39: 650 MHz Cavity Impedance Budget
Chart: Longitudinal Impedance Threshold
 | 50.6 | 25.3 | 16.8667 | 12.65 | 10.12 | 8.4333 | 7.2286 | 6.325 | 5.6222 | 5.06 | 4.6 | 4.2167 | 3.8923 | 3.6143 | 3.3733 | 3.1625 | 2.9765 | 2.8111 | 2.6632 | 2.53 | 2.4095 | 2.3 | 2.2 | 2.1083 | 2.024 | 1.9462 | 1.8741 | 1.8071 | 1.7448 | 1.6867 | 1.6323 | 1.5813 | 1.5333 | 1.4882 | 1.4457 | 1.4056 | 1.3676 | 1.3316 | 1.2974 | 1.265

## Slide 40: 650 MHz 5-cell Cavity HOMs
Monopole Mode | f (GHz) | R/Q (Ω) * | QL Limit
TM011 | 1.173 | 84.8 | 2.54E+5
TM020 | 1.427 | 54.15 | 3.28E+5
Dipole Mode | f (GHz) | R/Q (Ω/m)** | QL Limit
TE111 | 0.824 | 832.23 | 1.13E+4
TM110 | 0.930 | 681.15 | 1.39E+4
TE122 | 1.232 | 544.5 | 1.73E+4
TM112 | 1.440 | 101.53 | 9.3E+4
* k∥mode = 2πf ·(R/Q) / 4 [V/pC]
** k⊥mode = 2πf ·(R/Q) / 4 [V/(pC·m)]

## Slide 41: 1.3 GHz 9-cell Cavity Parameters
Parameter | Symbol | Unit | Value
RF frequency | fRF | GHz | 1.3
RF voltage | VRF | GV | 5.04
Cavity gradient | Eacc | MV/m | 20
Effective length (nine cells) | Leff | m | 1.038
Cavity voltage | Vc | MV | 20
Number of cavities |  |  | 256
Cavities in one cryomodule |  |  | 8
Cryomodule length |  | m | 12
Number of cryomodules |  |  | 32
R/Q | R/Q | Ω | 1036
Geometry factor | G | Ω | 270
Iris diameter |  | mm | 70
Quality factor | Q0 |  | 2×1010
External Q of input coupler | Qext |  | 1×107
RF power per cavity | Pin | kW | 20
Lorentz force detuning factor | kL | Hz/(MV/m)2 | 1
Cavity longitudinal loss factor※ | k∥ | V/pC | 5.8
Cavity transverse loss factor※ | k⊥ | V/pC m | 25
※ σz = 3.89 mm
Over-coupled for larger BW

## Slide 42: 1.3 GHz 9-cell Cavity HOMs
Monopole Mode | f (GHz) | R/Q (Ω) * | QL measured
TM011 | 2.450 | 156 | 58600
TM012 | 3.845 | 44 | 240000
Dipole Mode | f (GHz) | R/Q (Ω/m)** | Q
TE111 | 1.739 | 4283 | 3400
TM110 | 1.874 | 2293 | 50200
TM111 | 2.577 | 4336 | 50000
TE121 | 3.087 | 196 | 43700
* k∥mode = 2πf ·(R/Q) / 4 [V/pC]
** k⊥mode = 2πf ·(R/Q) / 4 [V/(pC·m)]

## Slide 43: 1.3 GHz Cavity Impedance Budget
Chart: Longitudinal Impedance Threshold
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20
 | 832 | 416 | 277.3333 | 208 | 166.4 | 138.6667 | 118.8571 | 104 | 92.4444 | 83.2 | 75.6364 | 69.3333 | 64 | 59.4286 | 55.4667 | 52 | 48.9412 | 46.2222 | 43.7895 | 41.6 | 39.619 | 37.8182 | 36.1739 | 34.6667 | 33.28 | 32 | 30.8148 | 29.7143 | 28.6897 | 27.7333 | 26.8387 | 26 | 25.2121 | 24.4706 | 23.7714 | 23.1111 | 22.4865 | 21.8947 | 21.3333 | 20.8
R per cavity is 267 Ω
Transverse impedance threshold
Cavity Impedances close to the budget upper limit,
more serious at low energy. But HOM frequency spread will relax it.

## Slide 44: RF Power Source

## Slide 45: Booster RF Power Source
256 1.3GHz 9-cell cavities, 20 MV/m, 20 kW
Solid State Amplifier (SSA)
1.3 GHz 25 kW, one per cavity
mature technology, 80 CNY/W
SSA 2M + LLRF 0.4M + distribution 0.4M
Booster PS unit cost: 2.8M CNY
Booster PS total cost: 0.72B CNY
Installed RF AC Power 6.4 MW
Average RF AC Power ~ 1 MW (15% DF)
ELBE 2×10 kW SSA combined @IPAC2014

## Slide 46: Main Ring RF Power Source
384 650MHz 5-cell cavities, 15.5 MV/m, 260 kW
300 kW CW Klystron
R&D on 300kW SSA (based on ADS 650MHz 150kW SSA)
 | Klystron | SSA
Total efficiency | 50% | 40%
Beam power (MW) | 100 | 100
AC power (MW) | 200 | 250
AC power required (MW) 30% redundant, refer to BNL | 260 | 325
  Note: total AC power of 250 GeV center-of-mass ILC : 100 MW
  and Beijing city peak power load: 20000 MW (1 kW per person)

## Slide 47: Power Source Choice and R&D
Main ring klystron PS unit cost: 300kW Klystron 3M CNY + PSM 2.5M+ LLRF0.4M + power distribution 2.5M = 8.4M CNY
Main ring klystron power source total: 3.36B CNY
Main ring SSA PS unit cost: 300kW SSA 12M CNY(40 CNY/W) + LLRF0.4M + power distribution 0.5M = 12.9M CNY
Main ring SSA power source total: 5.16B CNY
Klystron as baseline for CEPC main ring
Increase power efficiency!
R&D to reduce the klystron & SSA unit cost

## Slide 48: SRF Technical Challenges

## Slide 49: HOM Power of the Collider
 | CEPC Collider | LEP2 |  |  | 
Loss factor (HOM) V/pC | 3.29 | 0.66 |  | below cut-off | above cut-off
 |  |  |  | 0.22 | 0.44
HOM power per cavity | 6.51 kW | Operation 66nC 2*4 bunches | 300W | 100 W | 200 W
 |  | Design 100nC 2*36 bunches | 6.6kW | 2.2 kW (LHC 1 kW) | 4.4 kW
1 ~ 2 kW extracted by the HOM coupler technically possible (LEP and LHC) |  |  |  | KEKB | 16 kW
 |  |  |  | SuperKEKB | 40 kW
Add the broad band loss, 4 cavity module will generate ~ 40 kW HOM power
A small fraction of power extracted by HOM coupler, most HOM power propagates in the cavities and finally go outside of the module.

## Slide 50: HOM Damping Scheme (hook and ferrite)
CESR
KEKB
Ferrite Outside
LEP-2 & SOLEIL, BNL
Hook => + Ferrite
For the propagating HOM power, how much is absorbed by the couplers, waveguides and outside absorbers and how much within the cryos at 2K? )
Waveguide?
Hot topic in HF2014

## Slide 51: BEPCII Spare Module and HOM Damper
Ferrite: 6 kW HOM power absorption
7.7 MV/m

## Slide 52: Input Coupler Power Clean Assembly
For high Q cavity without field emission, two windows for clean assembly (cold+warm or warm+warm) , or one warm window assembly in cleanroom.
Cold window cooling is challenging.
Or two couplers per cavity?

## Slide 53: IHEP Power Couplers for SC Cavity
500 MHz
BEPCII spare
420 kW CW TW
1.3 GHz
ILC
1 MW pulse TW
162.5 MHz
China ADS HWR
20 kW CW TW
325 MHz
China ADS Spoke
10 kW CW TW

## Slide 54: SRF Infrastructures & Industrialization
FNAL SRF Lab
Zanon facility for XFEL cavity production

## Slide 55: SRF Facilities in JLab TEDF
Chemistry, cavity treatments, and support areas
Cavity and cryomodule cryo/RF testing
R&D
Cleanroom
Cryomodule assembly
Fabrication
JLAB SRF LAB
Advanced Conceptual Design 4/1/09
New

## Slide 56
STF building
COI: Center-of-Innovation Building at KEK
COI building
COI building construction area
2012 supplementary-budget: model facility for ILC assembly & Testing

## Slide 57
COI: Center-of-Innovation Building
Cantilever
Vertical-EP
As a model facility for ILC assembly & Testing
Clean-room
He Cryogenics
EP(vertical-EP)
Cavity Testing(4-cavities-test)
Cryomodule Assembly(cantilever)
Cryomodule Testing

## Slide 58: Cavity Automatic Tuning, Processing and Testing

## Slide 59: Cavity Surface High Resolution Inspection and Precise Local Repairing

## Slide 60: Cryomodule Assembly and Testing

## Slide 61
Only with the two large scale, well-equipped and well-run SRF labs at Fermilab/Argonne and Jlab can US LCLS-II project realize in 6 years.
  The same for Europe to build XFEL, and KEK in Japan to host ILC.
  CEPC SRF scale: 3 x cavities (larger size, coupler & HOM power), 8 x cryo plants, 60 x RF power than LCLS-II.
These new SRF labs or technology will never exist if without previous 30-year large SRF projects, and especially 8-year ILC GDE endeavor.
Collaborate with industry from very beginning to ensure technology transfer, quality control and mass production in tight schedule.
Key Findings

## Slide 62: Summary
CEPC SRF system: unique challenge and opportunity for China & world SRF accelerator community.
New breakthrough technologies: cavity processing & material for very high quality factors; push frontiers of SRF.
Very high power handling capabilities of HOM Damper & Input Coupler: hard limits to machine design and performance.
RF power source: major part of CEPC capital cost and power. We need a green machine.
Synergy with R&D and industrialization: CADS & PIP-II (650 MHz, high power RF source and coupler, high Q), Euro-XFEL, LCLS-II, ERLs & ILC (1.3 GHz, high Q, HOM), FCC etc.

## Slide 63
Run for your life, Nature, Vol 487, 19 July 2012
“Running is essential to the molecular memory of who we are.”
“The best weapon was endurance.”

## Slide 64: Back up

## Slide 66
Right SRF Material Should Provide:
(1) Low surface resistance, including low residual resistance at T → 0;
(2) An s-wave Cooper pairing state with a full superconducting gap on the entire Fermi surface;
(3) A high lower critical magnetic field Hc1 at which the weakly dissipative Meissner state is destroyed due to penetration of vortices;
(4) A high superheating magnetic field which definesthe theoretical limit of the SRF breakdown;
(5) High thermal conductivity to transfer the rf dissipated power through the cavity wall;
(6) Grain boundaries transparent to high rf screening currents in polycrystalline cavities;
(7) Comparatively simple chemical composition, so that the material is not contaminated by nonsuperconducting second phases, and the superconducting properties are not degraded by local chemical nonstoichiometry;
(8) Good mechanical properties and malleability to minimize crack formation during cavity manufacturing (forging, deep drawing, etc.)

## Slide 67: Theoretical Q Limit of Nb and Nb/Cu
 | f / MHz | T / K | RBCS / Ω | Rm (10 mG) / Ω | Rs / Ω | Q at zero field
LEP sputtered | 352 | 4.2 | < 39 | > 1.8 | 40.8 | 7 E9
KEKB/BEPCII bulk | 500 | 4.2 | 78.8 | 2.1 | 80.9 | 3.2 E9
CEPC bulk or sputtered | 650 | 4.2 | 133.1 | 2.4 | 135.5 | 2 E9
 |  | 2 | 2.7 | 2.4 | 6.1 | 4.4 E10
CEPC bulk | 1300 | 2 | 10.9 | 3.4 | 14.3 | 1.9 E10
Due to medium field Q-slope and field emission, Q will drop, especially the Nb/Cu sputtered cavity.

## Slide 74
Lab | Project/ Coupler | Window | Freq [MHz] | Aver Power test/oper [kW] | Peak Power test/oper [kW] | Qty | Years of oper.
KEK | Tristan | Disk | 500 | 200/70 | CW | 16 | 10
KEK /IHEP | KEKB /BEPCII | Disk | 508 500 | 800/400 420/150 | CW | 10 2+2 | 10 7+0
DESY | HERA | Cylindrical | 500 | 80 | CW | 16 | 17
CERN | LEP II | Cylin | 352 | 565/100 | CW | 288 | 7
CERN | LHC (var.) | Cylin | 400 | 350 | CW | 16 | 6
CERN | APS | Cylin | 352 | 80 | CW | 20 | 18
CERN | ESRF | Cylin | 352 | 100 | CW | 16 | 19
KEK | ADS | Disk | 972 | 165 | 2000/350 | 4 | 0
ORNL | SNS | Disk | 805 | 45 | 1000/350 | 81 | 9
IPN | ESS spoke | Disk | 352 | spec 15 | spec 335 | ..28 | design
CEA | ESS ellip | Disk | 704 | spec 54 | spec 1100 | ..180 | design
CERN | SPL | Disk and Cyli | 704 | 40 spec 100 | 1000 | .. 246 | 0
One Window Couplers

## Slide 75
Lab | Project / Coupler | Window | Freq [MHz] | Average Power test/oper [kW] | Peak Power [kW] | Qty | Years of oper.
CEA | IFMIF | Disk | 175 | spec 200/153 | CW | 8+ | 0
LPSC | SPIRAL2 QWR | Disk | 88 | 20/12 | CW | 2..12+14 | 0
ANL | FRIB QWR (var.) | Disk | 80.5 | 4 | CW | ..112 | 0
MSU | FRIB HWR (var.) | Disk | 322 | 8/spec. 14 | CW | ..222 | 0
IHEP | CADS HWR | Disk | 162.5 | 20 / 15 | CW | 4+8 | 0
IHEP | CADS Spoke | Disk | 325 | 10 / 10 | CW | 6+3..103 | 0
IHEP | CADS | Disk | 650 | spec 120 | CW | ..113 | design
FNAL | PX | Disk | 325 | spec 30 | CW | 3..52 | 0
FNAL | PX | Disk | 650 | spec 120 | CW | ..>100 | design
BNL | ERL SRF Gun | Disk | 704 | 125/spec500 | CW | 2 | 0
KEK | cERL inj. | Disk | 1300 | 40/5 spec 180 | CW | 6 | 1
HZB | BERLinPro inj. gun | Disk | 1300 | spec 130 | CW | 2 | design
One Window Couplers

## Slide 76: Two Windows Couplers
Lab | Project Coupler | Window | Freq. [MHz] | Average Power test/oper [kW] | Peak power [kW] | Qty | Years of oper.
LANL | APT (var.) | Disk + Disk | 700 | 1000/510 | CW | 2 | 0
DESY | TTFIII/XFEL | Cyl + Cyl | 1300 | 4.5 | 1100 | 32..+ 800 | 15
LAL | TTF V (fix) | Cyl + Cyl | 1300 | 4.0 | 2000 | 2 | 0
KEK/IHEP | STF1 (fix) | Disk + Disk | 1300 | 3 | 1200 | 4/2 | 1
KEK | STF2 | Disk + Disk | 1300 | 3 | 1200/450 | 2+16 | 1+0
KEK | Capacitive Coupled (fix) | Demountable Disk | 1300 | 5 | 2000 | 2 | 0
Cornell | ERL-inj. | Cyl + Cyl | 1300 | 61/40 | CW | 12 | > 1
HZB | TTFIII CW | Cyl + Cyl | 1300 | 8/spec.10 | CW | 1 | 0
Cornell | ERL-ML(fix) | Cyl + Cyl | 1300 | 5 | CW | 4 | 0
KEK | cERL-ML | Disk + Disk | 1300 | 43/15(4.5) | CW | 2 | 1
SLAC | LCLS-II | Cyl + Cyl | 1300 | sepc 6 | CW | .. | design

## Slide 78: CW Klystrons in the Market
Frequency (MHz) | Power (kW) |  | 
 | CPI | THALES | TOSHIBA
400 |  | 180/250/300/800 | 
476 | 1200 |  | 
499 | 800 |  | 
500 | 70/100/800 | 180/250/300/800 | 165
500.08 |  |  | 180
508.6 |  |  | 1200
700 | 1000 |  | 
704 | 1000 |  | 
805 |  | 180/250/300/800 | 

## Slide 79: 法国SOLEIL光源 4*190KW 全固态机SSA 单机3千多模块组成、每模块350W no HV, no Vacuum
Beam operation since 2005
运行九年, 年均替换约50模块
ESRF七台150kW替换了klystron

## Slide 80: One PS feeds one cavity or 4 cavities
Cavity trip may result in the machine interlocked and beam loss.
One SSA feeds one cavity, beam can sustain in a cavity trip.

## Slide 81: LEP-II 1.2 MV Feeds 8 cavities (352MHz)
HV
vacuum
Lifetime
1E+4hrs
1.2MW
4MW
125kW/cav
650MHz
1.2MW
Kly. tube
research?
Price?
20RMB/w?