## Slide 1
Progress of CEPC CALO/MUON system
Boxiang Yu
On behalf of CEPC Calor Group
2014 CEPC workshop of Shanghai Jiao Tong University (SJTU)
2014-09-12

## Slide 2
Outline
CEPC Calor system Introduction;
The progress of Pre-CDR;
The progress of ScECAL, THGEM-DHCAL and MUON
（ The talk of SiW ECAL and RPC-DHCAL will be given by Imad，Vincent and Lei ）

## Slide 3
We need a PFA Calor system.

## Slide 4
Introduction and general layout to calorimeters
ECAL for Particle Flow Approach (Two options)
  Scintillator Tungsten Sandwich - Zhigang Wang(IHEP)
  Silicon Tungsten Sandwich – Vincent. Balagura, J.-C Brient, V. Boudry (IN2P3)
HCAL for Particle Flow Approach (Three options)
  SDHCAL (RPCs) – Imad LAKTINEH (IPNL) , Ran Han (NCEPU)
  DHCAL (RPCs) – Lei Xia (ANL/SJTU)
  DHCAL (ThGEM) – Boxiang Yu (IHEP)
Muon system – Yuguang Xie (IHEP), Qinming Zhang (XJTU)
Calorimeter Calibration and Alignment (included in sub-detector option)
Front-End Readout System (included in sub-detector option)
Power and Cooling System (included in sub-detector option)
Cost Estimation (included in sub-detector option)
Progress of CEPC-Calor pre-CDR 2nd draft is ready for circulating
(current 29 pages for CALOR, 8 pages for Muon)

## Slide 5
A scintillator-tungsten sandwich sampling calorimeter (ScECAL) is proposed to build a fine-segmented calorimeter in a stable, robust and cost effective way.
A super-layer is made of a tungsten plate (3 mm thick), scintillator strips (2 mm thick), and a readout/service layer (2 mm thick). The thickness of a super-layer is 7 mm.
Structure of the ScECAL
PS and SiPM
The progress of ScECAL（By Zhigang）
Layer structure
From ILD TDR
2mmx5mmx5cm

## Slide 6
Energy resolution Vs thickness
A SiPM has a saturation phenomenon due to its finite number of pixels. According to the ILD estimation considering of e+e-  e+e- events at , 15000-18000 pixel SiPM is needed. What about CEPC ScEcal? 10000 pixel?
Linearity of SiPM
25 layers is an optimized option for CEPC energy, it is a balance between performance and cost.
Simulation result
σ/E of e- energy

## Slide 7
BNU SiPM: 1mm*1mm Hamamatsu MPPC: 1mm*1mm
Pixel size: 10um*10um Pixel size: 100um*100um
10000 pixel 100 pixel
BNU SiPM Vs Hamamatsu MPPC
BNU is Beijing Normal University
BNU SiPM
MPPC

## Slide 8
ADC
Temperature: 25 0C,
Humidity: 30%,
Voltage:
BNU SiPM: 27.5V
Hamamatsu MPPC: 71.5V
Gain: 7.8×104
~2×105(BNU report)
Gain: 2.2×106
Pulse height spectrum distribution
MPPC

## Slide 9
From CALICE
The progress of THGEM-DHCAL

## Slide 10
RD51 research WELL-THGEM DHCAL;
The beam studies showed a single-THGEM structure operating at a low gain (~1×103) can run at 96% efficiency with low discharge probability (10-6 or lower).
The particular configuration tested, which can still be optimized, had a total thickness of 5.5 mm within the requirement of the ILC-DHCAL.
Discharge Probability
KPiX readout electronics
THGEM DHCAL research of RD51

## Slide 11
three structure can be selected;
  Double THGEM;
  Single-THGEM;
  WELL-THGEM;
WELL-THGEM is the-best selection.
  thinner, high gain, lower discharge
Structure of THGEM-DHCAL
40cm×40cm THGEM
Structure of GEM-DHCAL
Including electronics

## Slide 12
Gain with voltage
Maximum gain of double THGEM reach to 2×105(using Neon);
Long time stability;
High energy resolution;
IHEP&UCAS THGEM detector performance study
1 month Gain Stability

## Slide 13
16cmX16cm THGEM detector
Cosmic ray test，measure the detection efficiency of 16cmX16cm THGEM detector;
Detection efficiency reach to 94.2% with 4mm drift gap detector.
Double THGEM cosmic ray test
THGEM detector experiment

## Slide 14
WELL-THGEM detector Research (UCAS, GXU)
A WELL-THGEM detector was constructed;
Some performance was measured;

## Slide 15
WELL-THGEM
Proton
Pion
Beam test of THGEM and WELL-THGEM
Using π, p beam，WELL-THGEM and single THGEM was test;
Beam-test result show detection efficiency of π is >95%， detection efficiency of proton is >96% ，WELL-THGEM is better。
500 MeV/c

## Slide 16
THGEM-DHCAL fast simulation
1x1cm2-50 Layers-100GeV π+
QGSP_BERT physics list was used;
Layer numbers for simulation: 30, 40, 50
1m*1m*40 Layers
Fast simulation result of THGEM-DHCAL

## Slide 17
Absorber: 2cm stainless steel
Drift gap: 3mm
Ecell = 1, 5 and 10MIPs (the thresholds typically placed at 0.5, 2 and 8 MIPs)
σ/E of Pi+ energy
One layer absorber: 20mm stainless steel
Need: 40layers, 4.7λI
Absorber:
2cm ss
1cm Pb+1cm ss
σ/E of Pi+ energy
Very preliminary result

## Slide 18
Functions:
the muon identifier, to separate the muons from hadrons(pions);
the solenoid flux return yoke;
Physics requirement( need discussion):
Production peak of e+eZh @√s = 250GeV
Main channel of muon production
The progress of MUON system (By Yuguang)
We have fine-segmented ECAL and HCAL. So we may Identify the muon from the analysis of ECAL and HCAL data。
Do we need a muon system？

## Slide 19
Technologies( not decided )
1. RPC
( glass RPC,
bakelite RPC)
2. Scintillator strip
The cross section of BESIII RPC module
Scintillator strip option
IHEP had produced and applied more than 4500m2 bakelite RPCs for BESIII and Dayabay.

## Slide 20
Simulations( stand-alone)
Plastic Scintillator 3cm×8layers
Steel 8/8/12/12/16/16/20/20/24cm, Sum=136cm(~8λ)
gap 0.5cm
absorbers before mu detector
  9cm tungsten for ECAL
  80cm steel for HCAL
Our results
Refs
Configuration I for simulating the finding efficiency
Not magnetic fields
Equivalent absorber is simple
Momentum should be > 4GeV

## Slide 21
Configuration II for simulating the mu/pi identification
Absorber: W(tungsten)。
Layers: 14
Each layer: 1λ
The simulation results validate that 8 λ absorber thickness and 8 detection layers are reasonable. The muon finding efficiency by 8 layers is >95% for mu >6GeV, and the pi misidentification rate is <1% if absorber thickness > 6 λ.

## Slide 22
Baseline design(preliminary)
The layout of the muon system.
The segmentation options of the muon system

## Slide 23
CEPC pre-CDR (29pages for CALO, 8 pages for Muon)
  DHCAL (ThGEM) – available (4 Institutions, 5 people)
  SDHCAL (RPC) – available (2 Institutions, 4 people)
  DHCAL (RPC) – available (3 Institutions, 5 people)
  ECAL(SciW) – available (1 Institution, 2 people)
  ECAL (SiW) – available (1 Institution, 3 people)
  Muon system – available (2 Institutions, 2 people)
CEPC-Calo simulations (standalone)
  DHCAL simulation, ECAL simulation
Using simulation studies to determine ECAL/HCAL geometry, sensors and absorbers, number of layers etc. key parameters and integrate in CEPC baseline detector design
Circulating and improving the draft of pre-CDR
Summary and Future Plan

## Slide 24
Thanks！

## Slide 25
Backup

## Slide 26
Tungsten: 123$/kg(quote from manufacture).
SiPM: 1$/pc (Based on extrapolation).
ASIC: 0.25$/ch
PCB: 2600$/m2.
  According to the structure of the SciEcal, the cost of it is list as below:
Tungsten + carbon parts: 15300 k$
Module realization: 1400 k$
Scintillators: 850 k$
SiPM: 8500 k$
Readout ASIC: 2000 k$
Readout Board: 20000 k$
Readout System: 5160 k$
Cables, connectors: 830 k$
Power supplies: 3400 k$
Cooling: 3150 k$
Total: 370 M RMB
Cost estimation of SciEcal ( 2mmx5mmx5cm)

## Slide 27
Item | Cost(k US Dollar) | Comment
Stainless steel | 5,200 | 1100 tons absorber
Module mechanics | 2,000 | Estimation from ILD
THGEM cassettes | 9,000 | 1800/m2，WELL-THGEM
ASIC | 16,500 | 0.3USD/ch，55M ch
Readout Board | 10,800 | Estimation from ILD
Readout system | 3,200 | Estimation from ILD
Power supply | 300 | Estimation from ILD
Gas System | 900 | Estimation from ILD
Cooling System | 1,000 | Estimation from ILD
Assemble | 3,500 | Estimation from ILD
total | 52,400 | 325 M RMB
Cost estimation of THGEM-DHCAL ( 1x1 cm2)

## Slide 28
The progress of Pre-CDR
ECAL (one option)
  ECAL based on Scintillator-Tungsten (by Zhigang Wang)
HCAL (three options):
  GRPC-SDHCAL by Ran Han
  GRPC-DHCAL by Lei Xia
  THGEM-DHCAL by Boxiang Yu
Muon (two options):
  Scintillators Strips or RPC Muon by Yuguang Xie
Reconstruction of RPC-SDHCAL
From Ran
Prototype of DHCAL
Structure of THGEM-DHCAL
MUON-RPC(Yuguang)
BNU SiPM: 1mm*1mm