## Slide 1: Commissioning experience of J-PARC RCS
Hiroyuki Harada
J-PARC beam commissioning group
ICFA mini-Workshop on Beam Commissioning for High Intensity Accelerators

## Slide 2
JFY 2009
JFY 2008
JFY 2006 / 2007
Neutrino Beam Line to Kamioka (NU)
Materials & Life Science Facility (MLF)
3 GeV Rapid Cycling Synchrotron (RCS)
Hadron Experimental Hall (HD)
400 MeV H- Linac
30 GeV Main Ring Synchrotron (MR)
J-PARC
(JAEA & KEK)
1 MW
0.75 MW

## Slide 3: Contents of this talk
Introduction and operational history of J-PARC 3GeV RCS
Simulation model for beam commissioning
Ring optics tuning and lattice imperfection measurement
Injection tuning, painting injection study and foil scattering
Extraction kicker field ringing compensation
High intensity beam study
Summary

## Slide 4
Design parameters of the J-PARC RCS
Circumference | 348.333 m
Superperiodicity | 3
Harmonic number | 2
Number of bunches | 2
Injection | Charge-exchange, Multi-turn
Injection energy | 181 MeV
Injection period | 0.5 ms (307 turns)
Extraction energy | 3 GeV
Repetition rate | 25 Hz
Particles per pulse | 5e13
Output beam power | 600 kW
Transition gamma | 9.14 GeV
Number of dipoles | 24
quadrupoles | 60 (7 families)
sextupoles | 18 (3 families)
steerings | 52
RF cavities | 12
Ring Collimator | <4 kW (< 3%)
The RCS have just got all the design hardware parameters
to try the 1-MW design beam operation.
Recently the hardware improvement of the injector linac
has been completed.
⇒ 400 MeV in 2013
⇒ 8.3e13 in 2014
⇒ 1 MW
400 MeV H-
3GeV
proton
MLF : Material and Life Science
Experimental Facility
MR : 50-GeV Main Ring Synchrotron
Pulse dipole magnet
to switch the beam destination

## Slide 5
Chart: 
Startup of the user program
in December 2008
Einj=181 MeV
Imax=30 mA
Injection peak
current upgrade
Einj=181 MeV
Imax=30 mA
Injection energy
upgrade
Einj=400 MeV
Imax=30 mA
Einj=400 MeV
Imax=50 mA
539-kW
beam test
573-kW-eq
beam test
1-MW-eq
beam test
Output power to MLF (kW)
500 kW
for users
Operational history of the RCS
Startup of the RCS beam commissioning in October 2007
The beam power ramp-up of RCS has steadily proceeded following;
- Progression in beam tuning, beam dynamics numerical simulation, hardware improvements
High intensity beam tests of up to 573 kW for both injection energies of 181 MeV and 400 MeV
1-MW beam tests from October 2014
Successful achievement of 1-MW eq. intensity output on January 2015
Present output beam power for the routine user program : 500 kW
Recovery works
from damages caused by
the “3/11-earthquake”
4 kW
120 kW
220 kW
300 kW

## Slide 6: RCS injection process and acceleration cycle
0 20 40 Time (ms)
Acceleration
Fast Extraction
0.28
0.93
1.13
B (T)
Injection
1st bunch
2nd bunch
Dp/p0
f
h=2
* Multi-turn H- stripping injection (0.5ms~307turns).
* Acceleration in rapid cycling (25Hz).
* Fast extraction.
600ns
Fast extraction
by kicker
~200ns
. . . . . .
B field
Intermediate
Pulses
Time (ms)
0.5ms (307turns)
Multi-turn H-
stripping injection
456ns
814ns
. . . . . .
Magnetic field of Bending

## Slide 7: RCS Injection System
PB1,2
PB3,4
QFL
QDL
SB1
SB2
SB3
SB4
x
ISEP1,2
1st foil
s
MWPM3
MWPM4
MWPM5
To beam dump
2nd foil
3rd foil
H-
H-
H0
Circulating
beam
H+
H-
H0
H+
- depress beam density
- decrease foil scattering
Beginning of painting
End of painting
<Injection scheme>
  Chopped beam
  H－charge exchange
  307 multi-turns (400MeV)
“Painting injection”

## Slide 8: Horizontal Painting Injection Process
PB1,2
PB3,4
QFL
QDL
SB1
SB2
SB3
SB4
x
ISEP1,2
1st foil
s
MWPM3
MWPM4
MWPM5
H-
H0
H+
2nd foil
3rd foil
SB
PB
Injection Beam
124.1
93
-4.4
0
To beam dump
H-
current
time
Injection period(500μsec)
x[mm]
x’[mrad]
Circulating beam
Circulating beam
foil

## Slide 9: Horizontal Painting Injection Process
PB1,2
PB3,4
QFL
QDL
SB1
SB2
SB3
SB4
x
ISEP1,2
1st foil
s
MWPM3
MWPM4
MWPM5
H-
H0
H+
To beam dump
2nd foil
3rd foil
Injection Beam
124.1
93
-4.4
0
H-
SB
PB
current
time
Injection period(500μsec)
Ring orbit
x[mm]
x’[mrad]
Circulating beam
Circulating beam
foil

## Slide 10: Horizontal Painting Injection Process
PB1,2
PB3,4
QFL
QDL
SB1
SB2
SB3
SB4
x
ISEP1,2
1st foil
s
MWPM3
MWPM4
MWPM5
H-
H0
H+
To beam dump
2nd foil
3rd foil
x[mm]
x’[mrad]
Painting Area
Injection Beam
124.1
93
-4.4
0
H-
Circulating beam
Circulating beam
SB
PB
current
time
Injection period(500μsec)
Ring orbit
foil

## Slide 11: Vertical Painting Injection process
y
1st foil
s
MWPM3
MWPM4
MWPM5
H-
VPB1
VPB2
H+
y
y‘
foil

## Slide 12
Longitudinal injection painting
Momentum offset injection
Dp/p=0, -0.1 and -0.2%
RF voltage pattern
Uniform bunch distribution is formed through
emittance dilution by the large synchrotron motion excited by momentum offset.
The second harmonic rf fills the role in shaping flatter and wider rf bucket potential, leading to better longitudinal motion to make a flatter bunch distribution.
Fundamental rf
Second harmonic rf
V2/V1=80%
Time (ms)
RF voltage (kV)
V1
V2
F. Tamura et al, PRST-AB 12, 041001 (2009).
M. Yamamoto et al, NIM., Sect. A 621, 15 (2010).
7/23

## Slide 13
V2/V1=0
Vrf=V1sinf-V2sin{2(f-fs)+f2}
(A) f2=-100 deg
(B) f2=-50 deg
(C) f2=0
The second harmonic phase sweep method enables further bunch distribution control through a dynamical change of the rf bucket potential during injection.
Additional control in longitudinal painting ; phase sweep of V2 during injection
f2=-100⇒0 deg
V2/V1=80%
f (Degrees)
RF potential well (Arb.)
8/23
Longitudinal injection painting

## Slide 14
to MLF
to MR
RCS
RCS
to MLF / MR
RCS
to MLF
to MR
RCS
8 kicker magnets
3 DC septum magnets
Beam transport line
RCS fast extraction system

## Slide 15: Contents of this talk
Introduction and operational history of J-PARC 3GeV RCS
Simulation model for beam commissioning
Ring optics tuning and lattice imperfection measurement
Injection tuning, painting injection study and foil scattering
Extraction kicker field ringing compensation
High intensity beam study
Summary

## Slide 16
Simulation Codes:
  SAD (Powerful code in designs, simulations, commissioning developed by KEK)
  Simpsons (PIC particle tracking code developed by Dr. Shinji Machida[STFC/RAL])
Imperfections included:
  Time independent imperfections
  - Measured main and multipole field components for all the main magnets:
  BM (K0~6), QM (K1, 5, 9), and SM (K2, 8) obtained from field measurements
  - Alignment errors (Δx, Δy, Δs, Δq) after the earthquake
  Time dependent imperfections
  - Edge focus of the injection bump magnets:
  K1 estimated from measured optical functions
  - Static leakage fields from the extraction beam line:
  K0,1 and SK0,1 estimated from measured COD and optical functions
  - BM-QM field tracking errors
  estimated from measured tune excursion over acceleration
  - 1-kHz BM ripple
  estimated from measured orbit variation
  - 100-kHz ripple induced by injection bump magnets
  estimated from turn-by-turn BPM data
  Foil scattering:
  Coulomb & nuclear scattering angle distribution calculated with GEANT
Simulation codes and imperfections

## Slide 17: Contents of this talk
Introduction and operational history of J-PARC 3GeV RCS
Simulation model for beam commissioning
Ring optics tuning and lattice imperfection measurement
Injection tuning, painting injection study and foil scattering
Extraction kicker field ringing compensation
High intensity beam study
Summary

## Slide 18: Tune Measurement ~Tune meter system and beam condition
Tune BPM
Transverse RF as exciter
Tune meter system
Transverse RF for beta oscillation excitation
Tune BPM for beta oscillation detection
Dp/p
f
Dp/p
f
Chopped width of injection beam :
489nsec ⇒ 150nsec
Typical RF capture
RF capture for tune measurement
Beam condition
Momentum spread control by shorter chopped width of injection beam (489 ⇒ 150nsec) for reduction of oscillation damping by chromatic tune spread
Dp/p:±0.60%
Dp/p:±0.15%

## Slide 19: Tune Measurement ~FFT spectrum in DC mode (beam storage mode)
FFT spectrum @ 2ms in the DC mode (DT=160μsec)
Revolution frequency of h=5
Sideband of betatron tune
Zoom of FFT spectrum @ 2ms in the DC mode (DT=160μsec)
Revolution frequency of h=5
Sideband of betatron tune
Revolution frequency of h=5
Sideband of betatron tune
Zoom of FFT spectrum @ 2ms in the DC mode (DT=1600μsec)
Pickup of betatron oscillation and FFT analysis
Identification of both revolution and betatron sideband peaks
Calculation of betatron tune
Dn depends on Df = 1/DT
DT : 160msec, Dn = ±0.013
DT : 1600msec, Dn = ±0.0013

## Slide 20: Tune Measurement ~FFT spectrum in AC mode
Time(frame)
160μsec
FFT spectrum in the AC mode (T=160μsec)
1
2
3
4
5
6
Tune is measured frame by frame
0msec
Injection
20msec
Extraction
TuneX
time[msec]
6.37
6.46

## Slide 21: Tune Measurement ~FFT spectrum in AC mode
Time
160μsec
FFT spectrum in the AC mode (T=160μsec)
1
1600μsec
FFT spectrum in the AC mode (T=1600μsec)
Accuracy of measured tune must be increased to understand tune tracking during acceleration
Revolution frequency shifts to higher one quickly in synchrotron such as RCS
FFT spectrum with the same method as DC mode has wider peaks

## Slide 22: Tune Measurement ~New analytical technic in AC mode
Time(frame)
160μsec
Tune is NOT measured frame by frame.
Tunes are measured with sliding 1 frame (step = 8msec)
0ms
2.5ms
TuneX
160ms
Moving average
0ms
20ms
TuneX
Moving average tune

## Slide 23: Tune Measurement ~Comparison between general and new analysis
general
new
Tunes during acceleration were measured with high accuracy by using new analysis.
We can clearly discuss tune excursion caused by B-Q tracking.

## Slide 24
Tune control during acceleration
Time (ms)
Tune
Horizontal
Vertical
Measured tune
Calculated tune
Measured tune
Calculated tune
The measured tune patterns were well reproduced in our simulation.
Tune during acceleration was well controlled by changing QMs top current.
Failure of peak search

## Slide 25
s(m)
Measured
Designed
Reproduced
The measured optics was reasonably well-reproduced in our accelerator model.
Optics Correction
Injection + Arc
Extraction + Arc
RF + Arc
βx, βy(m)
ηx(m)
Beta functions : Estimated from a response of the closed orbit for a dipole kick (STM) :
Dispersion functions : Measured by looking at a rf-frequency dependence of the closed orbit
Betatron tunes : Measured by Fourier transform analysis of detected transverse beam oscillation
Set tune : (6.640, 6.250)
Measured tune : (6.672, 6.240)
@ Day-1

## Slide 26
The ring optics were well corrected to the design value with no iteration by our accelerator model.
Optics Correction
- Based accelerator model
Injection + Arc
Extraction + Arc
RF + Arc
ηx(m)
βx, βy(m)
“Fudge factor”: the difference of the set and reproduced quadrupole strength of 7 families in our accelerator model
s(m)
Measured
Designed

## Slide 27
Optics control
Beta function
Dispersion function
bx, by (m)
hx (m)
s (m)
s (m)
Design curves
Measurements
Design curves
Measurements
We can control ring optics easily.
It was possible to do many beam tunings based-on our accelerator model.

## Slide 28
Beam-based measurements
of lattice imperfections in the RCS - I -
βx , βy (m)
s (m)
Edge focus
estimated; K1~-0.003335m-1
~58 mrad
Edge focus of the injection-bump magnets
(0.5 ms flattop + 0.5 ms fall time)
Result of beta modulation measurements
calculation (injection bump ; ON)
● measurement (injection bump ; ON)
Horizontal beta function
Vertical beta function
calculation (injection bump ; OFF)
Beta modulation caused by the edge focus;
- makes a distortion of the lattice super-periodicity
- drives random lattice resonances.
Injection or bit bump

## Slide 29
Beam-based measurements
of lattice imperfections in the RCS - II -
Extraction beam line DC magnets
Leakage fields from the extraction beam line DC magnets;
- evaluation of dipole and normal quadrupole components
Normal quadrupole component estimated
from the optics measurements; 0.0048 m-1
RCS ring
Leakage field includes;
・ Dipole component;
- makes COD
(correctable by steering magnets)
・ Normal quadrupole component;
- makes a distortion of the lattice
super-periodicity
- drives random lattice resonances
・ Skew quadrupole component;
- causes linear coupling
s (m)
Dipole component
estimated;
-1.14 mrad (hor.)
-0.12 mrad (ver.)
COD caused by the leakage fields
Δx (m)
Δy (m)
□ - calculation
● - measurement
□ - calculation
● - measurement
±1.5 mm
±10 mm

## Slide 30
Δx (mm)
Δy (mm)
s (m)
Δx (mm)
Δy (mm)
Kick
Kick
ν±
frev
FT spectrum of BPM signal
(Hz)
Orbit leak (Δy) to the vertical plane
by a horizontal single kick
Systematic measurement of
two normal mode betatron tunes (ν±)
near a linear coupling resonance
Skew quadrupole component estimated;
-0.00112 m-1
Beam-based measurements
of lattice imperfections in the RCS - II -
Leakage fields from the extraction beam line DC magnets;
- evaluation of skew quadrupole component
□ - calculation
● - measurement

## Slide 31: Contents of this talk
Introduction and operational history of J-PARC 3GeV RCS
Simulation model for beam commissioning
Ring optics tuning and lattice imperfection measurement
Injection tuning, painting injection study and foil scattering
Extraction kicker field ringing compensation
High intensity beam study
Summary

## Slide 32: Identification of phase space coordinates at injection point
x0 : Initial position, x0’ : Initial angle,
νx : betatron tune , ｎ : Turn number
αx, bx : Twiss parameter
Fourier transform
Injection beam
Injection bump
Closed orbit
Injection error correction
Painting injection process

## Slide 33: Measurement of response matrix
Detected signals at left-side and right-side electrode
A11
A12
A21
A22

## Slide 34: Injection error and betatron oscillation
Mountain view of Ionization profile monitors in the ring (Injection to first 10 turns)
20 μsec
Injection
20 μsec
Injection
Horizontal plane
Vertical plane

## Slide 35: Horizontal and vertical painting injection process
Horizontal phase space
100π
PB
500ms
time
Single pulse injection
100π
Vertical phase space
VPB
500ms
time

## Slide 36: Recent measurement method of painting injection process
PB
500ms
time
Multi-turn injection just before PB decay
Take BPM data
s[m]
x[mm]
T=0ms
T=250ms
T=500ms
Measured DX (PBON – OFF)
Calculated orbit
(x,x’)
(y,y’)
x‘ (mrad)
y‘ (mrad)
x (mm)
y (mm)

## Slide 37: Switching transverse painting area pulse-by-pulse between MLF and MR
100p
150p for MLF
Foil
edge
Inj. beam
Inj. beam
Inj. beam
50p
150p
Foil
edge
Foil
edge
100p for MR
50p for MR
50p
100p
150p
Inj. start
Inj. end
500msec
Calculation
The RCS are required different beam emittance from the MLF and MR.
So, RCS is operating with switching transverse painting are pulse-by-pulse between MLF and MR.
Horizontal Paint bump patterns

## Slide 38: Beam loss issue by foil scattering
1st Foil
QDL
QFL
To H0 dump
BPM
H0-Septum1
H0-Septum2
Ring Collimator
Circulating beam
Injection beam
Circulating beam
H0 branch
QDL
H0
branch
BPM
QFM
1st foil
Beam loss
Ring Col.
Observed dose rates at surface
120kW Operation : 2 ~ 3 mSv/h
220kW Operation : 4 ~ 6 mSv/h
Notes: 38

## Slide 39
Hot spots
Foil
QDL
PBH3-4
QFM
20- 30mrad
<20 mrad
qscattering;
Shield
Install absorber to catch a foil scattered particles into hot spots (A)
Build a shield of (A) including the new absorbers
Measures for the beam loss by the foil scattering
Absorbers
Simulation
BPM

## Slide 40
・Beam Power : 220kW-eq. & 300kW-eq.
・Catcher Positions
Outside ： 66.0mm, Inside ： -55.0mm
w/o Catcher
220kW-eq.
w/ Catcher
220kW-eq.
2%
BLM inside
12%
BLM outside
The localization results of the beam loss
w/ Catcher
300kW-eq.
17%
15%
S. Kato
Successful to localize the beam losses
(Dose rate of BPM @ 220kW operation : 6.2mSv/h → ~0.7mSv/h)

## Slide 41: Contents of this talk
Introduction and operational history of J-PARC 3GeV RCS
Simulation model for beam commissioning
Ring optics tuning and lattice imperfection measurement
Injection tuning, painting injection study and foil scattering
Extraction kicker field ringing compensation
High intensity beam study
Summary

## Slide 42: RCS kicker configuration (1)
Schematic diagram of kicker system
Kicker Magnet |  | 
Numbers |  | 8 (S:3, M:2, L3)
Configuration |  | Twin-C distributed magnet
Dimension | Vertical | 960mm
 | Horizontal | 776mm
 | Length | 638mm
Aperture size | Vertical | 186mm (S), 206mm (M), 232mm (L)
 | Horizontal | 360mm
 | Length | 638mm
Magnet core |  | Ferrite [PE14, TDK ltd]
Unit number |  | 20units/magnet
Characteristic impedance |  | 10W

## Slide 43: RCS kicker configuration (2)
Configuration of the one unit of kicker magnet

## Slide 44: Field measurement and Ringing
A
B
D
Field calculation of kicker magnet
magnetic field [A.U]
magnetic field [A.U]
D
time [sec]
Measured field of kicker magnet

## Slide 45
Extraction beam quality
Different beam positions between 1st and 2nd bunches by the field ringing
  Non-flatness of beam profile @ Neutron targets with octupole field
  Emittance growth by injection error @ MR injection points
Beam fluctuation in 1st bunch by the ringing
  Emittance growth
  Beam instability source
x[mm]@target
x[mm]@target
w/o offset at oct.
w/ offset of 2mm at oct.
simulation results
Kicker field
800nsec
400nsec
600nsec
2
1
2
800nsec
400nsec
2
1
2
kicker(1,3,5,7)
Dt = -120 nsec
kicker(2,4,6,8)
Dt = 0 nsec
For ringing cancellation

## Slide 46
Measured Dx[mm]
Dt [nsec]
Beam displacement measurement
caused by kicker field ringing
Beam condition : shorter single bunched beam (~150nsec→~30nsec)
Monitor : Beam Position Monitor (BPM) @ extraction beam transport line
Knob : Fire timing (Dt) of all kickers
Kicker field
+3.3mm
-5.5mm
Beam center positions of both 1st and 2nd bunches are ~0mm.
Beam fluctuation of 1st bunch is from -5.5 (-1.6%) to +3.3 mm(+0.75%).
Time structure of the ringing is not simple!

## Slide 47: Timing scan kicker-by-kicker
KM1
KM2
KM3
KM4
KM5
KM6
KM7
KM8
Dt [nsec]
Timing scan kicker-by-kicker were performed for understanding each ringing.
After that, we tried to optimize each kicker timing based on scan data for the ringing compensation.

## Slide 48: Comparison between all and each kicker timing scan
KM1
KM2
KM3
KM4
KM5
KM6
KM7
KM8
ID
0nsec
0nsec
0nsec
0nsec
0nsec
0nsec
0nsec
0nsec
① ΔT
② ΔT
timing ΔT [nsec]
①
②
Summed scan position for each KMs ( ) is a good agreement with measured position for all KM timing ( ).
⇒ We can discuss with kicker ringing compensation by using each scan data.
: Summed positions for each scan
: Measured position for all scan
10nsec
0nsec
0nsec
35nsec
0nsec
0nsec
10nsec
-10nsec
Measured Dx[mm]
Measured Dx[mm]

## Slide 49: Timing optimization for ringing compensation
①
③
: Sum positions for each scan
: Measured position for all scan
KM1
KM2
KM3
KM4
KM5
KM6
KM7
KM8
ID
0ns
0ns
0ns
0ns
0ns
0ns
0ns
0ns
① ΔT
60ns
-20ns
50ns
30ns
200ns
-30ns
50ns
-40ns
③ ΔT
Measured Dx[mm]
Measured Dx[mm]
timing ΔT [nsec]
Search of optimized timing were performed by using each scan data.

## Slide 50
Max ： Δ= 3.2mm (＋0.75%)
Min ： Δ= -5.5mm (－1.38%)
Max ： Δ= 0.6mm (＋0.15%)
Min ： Δ= -1.1mm (－0.28%)
Max ： Δ= 10.mm (＋2.33%)
Min ： Δ= -14.mm (－3.26%)
w/o compensation
w/ old compensation until 2013
w/ new compensation on 2014
: Sum positions for each scan
timing ΔT [nsec]

## Slide 51: Online monitor and drift correction system for kicker timing
There is a gradual change in Thyratron condition and Thyratron output timing has a drift over a period of minutes.
KM01
KM02
KM03
KM04
KM05
KM06
KM07
KM08
Online monitor of Thyratron output
Thyratron outputs of kickers are monitored online.
If difference from reference is more than 10nsec, kicker timing is corrected automatically.
Extraction beam stability is kept by this system.

## Slide 52: Contents of this talk
Introduction and operational history of J-PARC 3GeV RCS
Simulation model for beam commissioning
Ring optics tuning and lattice imperfection measurement
Injection tuning, painting injection study and foil scattering
Extraction kicker field ringing compensation
High intensity beam study
Summary

## Slide 53
No longitudinal
painting
V2/V1=80%
f2=-100 to 0 deg
Dp/p= 0.0%
V2/V1=80%
f2=-100 to 0 deg
Dp/p=-0.1%
V2/V1=80%
f2=-100 to 0 deg
Dp/p=-0.2%
Measurements (WCM)
Numerical simulations
Longitudinal beam distribution just after beam injection (at 0.5 ms)
Bf ~0.15
Bf >0.40
Dp/p (%)
f (degrees)
Density (Arb.)
f (degrees)
Dp/p (%)
f (degrees)
Density (Arb.)
f (degrees)
Dp/p (%)
f (degrees)
Density (Arb.)
f (degrees)
Dp/p (%)
f (degrees)
Density (Arb.)
f (degrees)
from H. Hotchi et. al., PRST-AB 15, 040402 (2011).
9/23
Longitudinal injection painting

## Slide 54
Measurement vs Simulation (Inj. Energy = 181MeV) :
bunching factor from injection to extraction
Time (ms)
Bunching factor
Time (ms)
539 kW (500 ms)
433 kW (400 ms)
326 kW (300 ms)
217 kW (200 ms)
104 kW (100 ms)
― Simulations
Time structure of measured bunching factor for each intense is in good agreement with simulated results.
Feed Forward of RF cavities is worked well up to 600 kW.
F. Tamura
H. Hotchi

## Slide 55
Measurement vs Simulation (Inj. Energy = 181MeV) :
extraction beam profile at 3 GeV
― Simulations
MWPM @ extraction beam line
539 kW (500 ms)
433 kW (400 ms)
326 kW (300 ms)
217 kW (200 ms)
104 kW (100 ms)
Charge density (Arb.)
Position (mm)
Li pulse length (ms)
RMS width (mm)
Vertical
Horizontal
● Measurements
○ Simulations
Horizontal
Vertical
Intensity dependence of RMS beam width
Our numerical simulation well globally reproduced
the experimental results up to 540 kW intensity beam.
H. Hotchi
H. Hotchi

## Slide 56
Expanded view
Beam survival rate
Painting parameter ID
○ Einj=181 MeV, 539 kW-eq. intensity (Nov. 2012)
○ Einj=400 MeV, 553 kW-eq. intensity (Apr. 2014)
By adding 100p
transverse painting
No painting
Painting parameter dependence of beam survival rate for 550 kW-eq. intensity
This experimental data clearly show
  the big gain from the injection energy upgrade
  the excellent ability of “painting injection”.
Further space-charge mitigation
by higher injection energy
Beam intensity (x1013)
Einj=181 MeV
Einj=400 MeV
Beam loss :
~30% ⇒ <1%
Time (ms)
DCCT data
By longitudinal
painting
H. Hotchi

## Slide 57
Beam Loss up to 570 kW-eq. intensity (400MeV)
Run#56 (Jun., 2014) with 400MeV injection
25.5 mA, 0.5 ms, 489 ns, 2 bunches,
Thinning 6/32~32/32 : 107~573 kW-eq.
“Twiss mismatch tuning”
“ (6.38, 6.42) ”
Loss power (W)
Intensity (x 1013)
BLM signal (arb.)
Beam losses occurred only around injection energy and are mostly localized at the collimator section.
Integrated beam losses increase linearly with beam intensity
Beam loss up to 570 kW-eq. intensity is well minimized, only from foil scattering.
Loss : ~< 0.1%
Time (ms)
― 4.775 x 1013 : 573 kW-eq
― 3.579 x 1013 : 429 kW-eq
― 2.681 x 1013 : 322 kW-eq
― 1.787 x 1013 : 214 kW-eq
― 0.889 x 1013 : 107 kW-eq
Foil scattering loss only
Scintillation type BLM @ Collimator
H. Hotchi

## Slide 58
Time (ms)
Particles /pulse (x 1013)
Circulating beam intensity over the 20 ms
from injection to extraction measured by CT
Injection
Extraction
8.41 x 1013 ppp : 1010 kW-eq.
6.87 x 1013 ppp : 825 kW-eq.
4.73 x 1013 ppp : 568 kW-eq.
7.86 x 1013 ppp : 944 kW-eq.
5.80 x 1013 ppp : 696 kW-eq.
In January 10, 2015
we successfully achieved
the 1-MW beam acceleration.
The beam losses observed for the 944-kW (blue) and 1010 kW (red) beams can be interpreted as longitudinal beam loss.
For this issue, we plan to upgrade the anode power supply using this summer maintenance period.
Achievement of 1MW-eq. intensity beam acceleration
H. Hotchi
Time (ms)
BLM signals (a.u.)
BLM @ collimator section
BLM @ high dispersion area in the arc section
8.41 x 1013 ppp : 1010 kW-eq.
6.87 x 1013 ppp : 825 kW-eq.
4.73 x 1013 ppp : 568 kW-eq.
7.86 x 1013 ppp : 944 kW-eq.
5.80 x 1013 ppp : 696 kW-eq.
Mainly from foil scattering during injection
H. Hotchi

## Slide 59: Summary
The RCS was beam-commissioned in October 2007.
The output beam power has been steadily increasing progressions in the beam tuning, hardware improvements and realistic simulations.
After completing output energy and peak current upgrade of the LINAC, the RCS started the 1-MW beam tuning from October 2014.
The 1-MW beam acceleration was successfully demonstrated on January 2015.
Now we are gradually increasing the routine output beam power by a 100-kW step every one month. If this beam power ramp-up scenario is going well, the 1-MW routine beam operation is to start up from the next spring via the summer maintenance period.

## Slide 60: Thank you for your attention.

## Slide 61: Backup of slides

## Slide 62: RCS beam commissioning system
Operation Interface
Operation Interface based on
Beam simulation
Control server of devices
and monitors (EPICS)
IOC
IOC
Real accelerator
IOC
Control server of
simulation parameters
(EPICS)
Virtual accelerator
Accelerator Model
(code:SAD)
File

## Slide 63: High intensity beam and space charge effect
Dn =
Increasing beam intensity
Defocusing force by space charge
Different betatron tune particle-by-particle (tune spread)
Emittance growth and beam losses
νx
νy
(6.40, 6.42)
Tune footprint in tune diagram (Simulation)
νy = 6
νx = 6
4x=27
x=7
x=6.5
x=6
x=5.5
x=7.5
y=7
y=7.5
4y=27
y=6.5
y=6
y=5.5
x+y=13
2x+2y=27
X-2y=-6
2x+2y=24
x+2y=21
x+2y=18
Bare tune
Horizontal tune, nx
Vertical tune, ny
181 MeV inj.
(for 550 kW)
400 MeV inj.
(for 1 MW)
Dn =
Dn =
Notes: ５０π→２×10^15 [particle/m^3], 216π→4.5×10^14 [particle/m^3]

## Slide 64
Transverse injection painting
x’(rad)
x (m)
y’(rad)
y (m)
Horizontal painting
process by PBH1-4
Vertical painting
process by PBV1-2
Field forms of the injection bump magnets for 100p-mm-mrad painting
Design
painting process
Measured
painting process
Design
painting process
Measured
painting process
100p
100p
PBH1
PBH2
PBH3
PBH4
PBV1
PBV2
SB
etp=100p mm mrad
The flattop of SB was restored!!
Well adjusted.

## Slide 65
Injection beam tuning : DB2
Dp/p : ~0.082% (sigma)
Dp/p : ~0.182% (sigma)
DB2 off
DB2 -1865
M. Yoshimoto
Momentum spread of the injection beam
estimated by the longitudinal tomography for turn-by-turn WCM data

## Slide 66
s (m)
Beam size, sigma (mm)
Horizontal
Vertical
Ip=25.5 mA
Ip=45.9 mA
Ip=25.5 mA
Ip=45.9 mA
Injection beam tuning : Twiss parameter @ RCS injection point
Ip=45.9 mA
(Run#57)
Ip=25.5 mA
(Run#56)
Position (mm)
Hor.
(U)
Ver.
(V)
Hor.
(U)
Ver.
(V)
Beam profile @ RCS injection point
Multi-wire profile monitors 1-4
RCS injection point
Beam envelop along the L3BT
T. Maruta & K. Okabe
We adjusted the Twiss parameter of the injection beam so that the injection
beam ellipse fits the design painting area of 100p mm mrad as possible.
“DB2 -1865”

## Slide 67
Emittance & Twiss parameter of the injection beam
 | DESIGN | DB2 OFF Run#56 Ip=25.5 mA | DB2 OFF Run#57 Ip=45.9 mA | DB2 -1865 Run#57 Ip=45.9 mA
ax | -1.252 | -1.038 | -0.812 | -0.934
ay | -1.822 | -1.618 | -1.714 | -1.644
bx (m) | 10.226 | 10.436 | 6.552 | 6.106
by (m) | 8.995 | 11.147 | 9.485 | 9.717
ex (p mm mrad, rms, un-norm) | 0.25 | 0.600 | 0.889 | 0.957
ey (p mm mrad, rms, un-norm) | 0.25 | 0.537 | 0.587 | 0.564
Momentum spread (%) | 0.2 (full) | 0.066 (sigma) | 0.082 (sigma) | 0.182 (sigma)

## Slide 68
(x, x’)
(y, y’)
Design painting area
(Circulating beam ellipse after painting)
Painting area estimated
for the case of Ip=25.5 mA (Run#56)
Painting area estimated
for the case of Ip=45.9 mA (Run#57)
x’ (rad)
x (m)
y’ (rad)
y (m)
100p
145p (Ip=25.5 mA)
180p (Ip=45.9 mA)
100p
Design injection beam ellipse
Injection beam ellipse
for the case of Ip=25.5 mA (Run#56)
Injection beam ellipse
for the case of Ip=45.9 mA (Run#57)
Transverse injection painting area
estimated for the 46.0-mA injection beam (DB2 -1865)
110p (Ip=25.5 mA)
115p (Ip=45.9 mA)
Circulating
beam ellipse
Injection
beam ellipse
Painting
process
Painting
process
Injection
beam ellipse
Circulating
beam ellipse

## Slide 69
6.44 x 1013 (Thinning 24/32) : 773 kW-eq
5.33 x 1013 (Thinning 20/32) : 639 kW-eq
4.25 x 1013 (Thinning 16/32) : 510 kW-eq
3.19 x 1013 (Thinning 12/32) : 383 kW-eq
2.10 x 1013 (Thinning 8/32) : 252 kW-eq
6.87 x 1013 : 825 kW-eq
5.84 x 1013 (Thinning 22/32) : 701 kW-eq
4.79 x 1013 (Thinning 18/32) : 574 kW-eq
3.73 x 1013 (Thinning 14/32) : 447 kW-eq
2.65 x 1013 (Thinning 10/32) : 318 kW-eq
Time (ms)
Result of the first 1-MW trial
Particles /pulse (x 1013)
W/ multi-harmonics (h=2,4,6)
feed-forward for
beam loading compensation
Anode current measured as
a function of the beam power
Cavity#12
Interlock 110 A
Trip
M. Yamamoto
252-kW-eq
773-kW-eq
RF trip
1-MW-eq
Circulating beam intensity over the 20 ms
from injection to extraction measured by DCCT
The beam intensity was smoothly increased up to 770 kW with no significant beam loss, but when the beam intensity got to over 800 kW, the accelerating RFs suddenly tripped;
the anode power supply of the RF system tripped
due to the over current.
In the present condition,
the required anode current
surpasses the interlock level
when the beam intensity
gets to over 800 kW.
Injection
Extraction
Anode current (A)
Beam power (kW)

## Slide 70
Possible measures against the RF trip & plan
Reduce the required anode current by
shifting the resonant frequency
of the RF cavity; 124 A to 109 A
Cavity#12
M. Yamamoto
110 A
115 A
Use a remaining margin
of the anode power supply;
110 A to 115 A
124 A
109 A
Re-try 1-MW beam acceleration
in Dec., 2014 & Jan., 2015
Increase the anode power supply itself to get sufficient margin
using the next summer shutdown period of 2015;
115 A (15 sets of inverter units) ⇒ 138 A (18 sets of inverter units)
By taking these possible measures,
the required anode current for
the 1-MW beam acceleration will get to
be within the limit.
W/ multi-harmonics (h=2,4,6)
feed-forward
for beam loading compensation
Anode current measured as a function of the beam power
Start up the 1-MW user operation from Oct. 2015 as originally planned
Anode current (A)
Beam power (kW)
Load map to 1 MW newly made after the beam test

## Slide 71
4.78 x 1013 (Thinning 32/32) : 573 kW-eq
2.68 x 1013 (Thinning 18/32) : 322 kW-eq
0.89 x 1013 (Thinning 6/32) : 107 kW-eq
3.58 x 1013 (Thinning 24/32) : 429 kW-eq
1.79 x 1013 (Thinning 12/32) : 214 kW-eq
6.44 x 1013 (Thinning 24/32) : 773 kW-eq
5.33 x 1013 (Thinning 20/32) : 639 kW-eq
4.25 x 1013 (Thinning 16/32) : 510 kW-eq
3.19 x 1013 (Thinning 12/32) : 383 kW-eq
2.10x 1013 (Thinning 8/32) : 252 kW-eq
5.84 x 1013 (Thinning 22/32) : 701 kW-eq
4.79 x 1013 (Thinning 18/32) : 574 kW-eq
3.73 x 1013 (Thinning 14/32) : 447 kW-eq
2.65 x 1013 (Thinning 10/32) : 318 kW-eq
Beam loss monitor signal (arb.)
Time (ms)
Time (ms)
Beam intensity (x1013)
Loss power (W)
Run# 56 (Ip=25.5 mA)
107 kW ~ 573 kW-eq
Run# 57 (Ip=45.9 mA)
252 kW ~ 773 kW-eq
○ ・・・ Run#56
● ・・・ Run#57
773kW-eq
107kW-eq
Intensity dependence of beam loss (DB2 -1865)
BLM signal @ collimator over the first 5 ms in the low energy region
The beam loss appears mainly for the first 1 ms
of the beam injection.
The beam loss amount almost has
a linear response for the beam intensity.
The beam loss of up to 773-kW intensity beam
is nearly minimized, and its remaining beam loss
is mainly from foil scattering during injection.
Beam loss estimated for 773 kW intensity beam;
<0.2% (160 W << 4-kW collimator limit).
Mainly from foil scattering
Injection bump OFF
Injection

## Slide 72
Beam loss : measurements vs calculations (Run#56)
Loss power (W)
Intensity (x 1013)
BLM signal (arb.)
― 4.775 x 1013 (Thinning 32/32) : 573 kW-eq
― 3.579 x 1013 (Thinning 24/32) : 429 kW-eq
― 2.681 x 1013 (Thinning 18/32) : 322 kW-eq
― 1.787 x 1013 (Thinning 12/32) : 214 kW-eq
― 0.889 x 1013 (Thinning 6/32) : 107 kW-eq
Loss △:
Time (ms)
Number of
lost particles/turn
Loss power (W)
BLM signals @ collimator
Calculations
Intensity (x 1013)
0.11%
0.09%
0.08%
0.07%
0.07%
The numerical simulation well reproduced the experimental beam loss data.
Run# 56 (Ip=25.5 mA)

## Slide 73
Beam loss at the collimator
BLM signals (a.u.)
Time (ms)
Time (ms)
Number of lost
particles per turn
Measurements : BLM signals at the collimator over the first 6 ms
Calculations
8.41 x 1013 ppp : 1010 kW-eq.
6.87 x 1013 ppp : 825 kW-eq.
4.73 x 1013 ppp : 568 kW-eq.
7.86 x 1013 ppp : 944 kW-eq.
5.80 x 1013 ppp : 696 kW-eq.
The beam loss at the collimator section appears
for the first 1-ms region.
The remaining beam loss mainly arises
from foil scattering during injection.
The other beam loss, such as space-charge
induced beam loss, was well minimized
by injection painting even for the 1-MW beam.
The remaining beam loss for the 1-MW beam
was estimated to be 0.17% (240 W in power)
<< Collimator limit of 4 kW.
We expect the 1-MW routine beam operation
will be ready after this summer maintenance
period, namely by solving the remaining
longitudinal beam loss after completing
the RF anode power supply upgrade.
16/23

## Slide 74
Recent efforts for further beam loss mitigation
Most of the foil scattering beam loss is well localized at the collimators,
but some of them with large scattering angles cause un-localized beam loss,
making relatively high machine activations near the charge-exchange foil;
~15 mSv/h @ chamber surface for the 400-kW routine beam operation.
The machine activation is expected to be within the permissible level
even if assuming the 1-MW routine beam operation, but we tried further
beam loss mitigation to keep the machine activation as low as possible.
Next issue : further mitigation of the foil scattering beam loss
Present : etp=100 p mm mrad
etp=150 p mm mrad
Average number
of foil-hits/particle:
~42
~27
The foil scattering beam loss
can be reduced by larger
transverse painting, especially
on the horizontal plane.
But such a large transverse painting had not been realized
until recently due to
beta function beating
caused by the edge focus
of the injection bump magnets.
H. Hotchi et al, NIM, Sect. A 778, 102 (2015).
x 0.6
17/23

## Slide 75
Edge focuses are generated
at the entrance and exit of the injection bump magnets.
Beam injection is performed with a time dependent
horizontal local bump orbit by using 8 sets of
rectangular pulse dipoles magnets (SB1-4 & PBH1-4 ).
Beta functions (m)
s (m)
Horizontal (Bump on)
Vertical (Bump on)
Beta function beating caused by the injection bump magnets
Horizontal (Bump off)
Vertical (Bump off)
There is no beta function beating on the horizontal plane,
because the horizontal edge focus effects are
canceled out by another focusing property
intrinsic on the bending plane.
The vertical edge focus affect the beam as is,
making 30% beta function beating
on the vertical plane at maximum
during injection period.
Beta function beating caused by the edge
focus of the injection bump magnets
Beta function beating makes a distortion of the lattice super-periodicity and
additionally excites various random betatron resonances.
1st super-period
2nd super-period
3rd super-period
18/23

## Slide 76
Random betatron resonances
excited through a distortion of the super-periodicity
Horizontal tune nx
Vertical tune ny
Present
operating point
(6.45,6.42)
Horizontal tune nx
Vertical tune ny
nx+2ny=19
Random resonances
that can be additionally excited through a distortion of the super-periodicity
on the vertical plane caused by the edge focus of the injection bump magnets
Systematic resonances
These random resonances cause an additional shrinkage of
the dynamic aperture during the injection period, and leads to
extra beam loss when applying large transverse painting.
Especially, the random 3rd order sum resonance (nx+2ny=19)
strongly affects the beam in the present operational condition.
19/23
Plotted up to
4th order resonances

## Slide 77
Correction of beta function beating
We have recently installed 6 sets of pulse type quadrupole correctors (QDTs),
to compensate beta function beating, and to minimize the effect of the random resonances
through the recovery of the super-periodic condition.
QDT
Beta functions (m)
s (m)
Beta functions (m)
s (m)
Beta function beating correction by the quadrupole correctors.
Vertical beta function
beating was successfully
corrected by QDTs,
while keeping the super-
periodic condition
on the horizontal plane.
1st super-period
2nd super-period
3rd super-period
Before correction
After correction
20/23

## Slide 78
Now we are conducting the 500-kW routine
beam operation with this large transverse
painting using QDTs.
By this large transverse painting, and also by re-optimizing the foil position,
the residual radiation level near the charge exchange foil was well reduced as expected.
Beam loss reduction by QDTs (Run#62)
Time (ms)
BLM signal (arb.)
BLM signals @ collimator
Date : Apr. 3-8, 2015 (Run#62)
Injection beam condition
Injection energy : 400 MeV
Peak current : 29.8 mA
@ the entrance of RCS
Pulse length : 0.5 ms
Chopper beam-on duty factor : 60%
⇒ 5.58 x 1013 particles/pulse,
corresponding to 670 kW at 3 GeV
Operating point;
(6.45, 6.42)
Experimental condition
Transverse painting area:
100p mm mrad (Horizontal)
100p mm mrad (Vertical)
150p mm mrad (Horizontal)
100p mm mrad (Vertical)
150p mm mrad (Horizontal)
100p mm mrad (Vertical)
+ QDTs
When expanding the horizontal
painting area to 150p mm mrad,
significant extra beam loss appeared.
But this beam loss was well mitigated
as expected by introducing QDTs.
21/23

## Slide 79
Number of foil-hits
Parameter ID
44.7
30.9
18.1
x 0.69
x 0.59
Reduction rate in total ; x 0.4
Average number of foil-hits per particle
(Calculation)
By re-optimizing the foil position;
100p (Hor.)-100p (Ver.) mm mrad, Dx=9mm
By expanding horizontal painting area;
150p (Hor.)-100p (Ver.) mm mrad, Dx=9mm
Residual dose level at the charge exchange foil
Dx=13mm
30 mm
30 mm
Dx=9mm
Charge-exchange foil (330-mg/cm2-thick HBC)
The foil was pulled
out by 4 mm following
the improvement of
the injection beam
quality.
Injection
beam
By these attempts, the foil scattering beam loss was reduced, and as a result,
the residual dose level near the charge exchange foil was well reduced as expected;
~15 mSv/h @ chamber surface (2-hour after the 400-kW beam operation).
~8 mSv/h @ chamber surface (2-hour after the 500-kW beam operation).
Expectation ; (15 mSv/h) x 0.4 x (500 kW/400 kW) = 7.5 mSv/h
22/23
RCS beam tuning is in progress well towards realizing 1-MW routine beam operation.