## Slide 1: SNS beam loss and control
By M. Plum
ICFA mini-workshop on beam commissioning for high intensity accelerators, Dongguan June 8-10, 2015

## Slide 2: Motivation
In high power accelerators, e.g. neutron spallation sources and neutrino production sources, beam loss is one of the biggest issues
Beam loss should be minimized to allow hands on maintenance and to minimize worker dose
Radiation damage to equipment is also a concern
Beam loss minimization is a major driver for the design of high power accelerators
As accelerators become more powerful the allowed fractional beam loss becomes smaller (e.g. 10-6/m fractional loss of 1 GeV 1 MW proton beam creates ~ 1 mSv dose rate at 30 cm after 4 hours of cool down)
A large fraction of the accelerator physics effort at SNS is dedicated to understanding and reducing the beam loss

## Slide 3: H− vs H+ beam loss mechanisms
  Residual gas stripping
  Intra-beam stripping
  H+ capture and acceleration
  Field stripping
  Black body radiation stripping
  Beam halo/tails (resonances, collective effects, mismatch, etc.)
  RF and/or ion source turn on/off transients
  Dark current from ion source
H− only

## Slide 4: How we measure beam loss
Argon filled ionization chamber detectors (~307)
Scintillation detectors with photomultiplier tubes (~55)
  Neutron detectors - especially useful below ~100 MeV (e.g. DTL)
  Fast loss detectors
Photo of ionization chamber BLM
Typical BLM display

## Slide 5: Typical activation levels for 1 MW operations
CCL 5 – 20
DTL 1 – 6
SCL 10 – 50
All numbers are mrem/h at 30 cm from beam line after 1 MW operations followed by ~48 hours of low-power studies
(divide by 100 to get mSv/h)
95
Ring injection 5 – 300
Ring collimation 5 – 60
Ring extraction
<5
RTBT
<5 – 15
HEBT 5 – 20
90
500
40
150
90
50 at CM2
50 at CCL4
180 LEDP
Causes of beam loss, in approx. order
Stripper foil
Aperture limitation
Residual gas stripping
Extraction inefficiency
Lattice transition
Collimation inefficiency
Intra-beam stripping
Notes: Surveys for 8/May/2012

## Slide 6: Beam loss control and mitigation
Scraping – best done at low beam energies
Increase beam size in superconducting linac, to reduce intrabeam stripping
Adjust quadrupole magnet and RF phase setpoints to empirically reduce losses

## Slide 7: 1: Beam loss reduction by scraping
RTBT
HEBT
Injection
Extraction
RF
Collimators
In MEBT:
Left-right scrapers
Top-bottom added 2013
In HEBT:
Two pairs of left-right scrapers
Two pairs of top-bottom scrapers
Two collimators
In HEBT:
Left-right (high and low momentum) scrapers
Followed by beam dump
In Ring:
Four scrapers (0, 45, 90, 135 deg.)
Three collimators
Most effective
Occasionally used
Almost never used
Rarely used

## Slide 8: 1: MEBT Scraping
Standard part of production
Reduces linac and injection dump losses by up to ~60%
Effectiveness in loss reduction varies from source to source
MEBT Emittance without scraping
MEBT Emittance with scraping
No scraping
scraping
Gaussian fit
DTL profile, log scale
HEBT profile
Courtesy A. Aleksandrov
x [mm]
x’ [mrad]
x’ [mrad]
x [mm]

## Slide 9: 1: Scraping at low beam energy (2.5 MeV)
Beam Charge (typically scrape ~3-4% of the beam)
time
Warm linac beam loss (~55% lower loss at this location)
Ring Injection Dump beam loss (~57% lower loss at this location)
Scrapers in
The effectiveness of the MEBT scrapers varies with the ion source and the machine lattice
Courtesy J. Galambos
Scrapers out

## Slide 10: 2: Beam loss reduction by increasing the beam size in the SCL
Most of the beam loss in the SCL is due to intra-beam stripping (H− + H−  H− + H0 + e)
IBSt reaction rate is proportional to (particle density)2
Quad gradient reduction leads to beam loss reduction
~40%
~50%

## Slide 11: 3: Beam loss reduction by empirically adjusting magnets and RF phase
Best beam loss is obtained by empirical adjustments to quadrupole gradients and RF cavity phases
  The quadrupole changes sometimes result in beam that is transversely mismatched at lattice transitions (e.g. CCL to SCL, SCL to HEBT)
  The biggest deviations in RF phase are at the entrance to the SCL
  One degree phase changes can approx. double the beam loss at some places
  Typical phase changes are 1 to 10 deg

## Slide 12: 3: Mis-match in the linac and transport line
Low-loss tune is mis-matched at beginning of SCL
Low loss tune is mis-matched at beginning of HEBT
These are FODO lattices
The low-loss tune is mis-matched in the SCL and HEBT
Vert. size
Horiz. size
Vert. size
Horiz. size

## Slide 13: 3: Linac RF phases design vs production (2012)
MEBT
DTL
SCL
CCL
Some RF phases must be empirically adjusted to achieve the low-loss tune

## Slide 14: 3: Linac RF phases design vs production (2015)
MEBT
DTL
SCL
CCL
Improvements in automated warm linac phase and amplitude determination have reduced phase changes needed to achieve the low loss tune
Typical RF phase changes (design – production)
Beam energy adjustment

## Slide 15: Stability of low loss tune
The low loss tune is very stable
All magnets and RF cavities can be turned off and the beam loss will still be low when they are turned back on
  Power supply stability: 10-4 for ring dipoles, 10-3 for quadrupoles, 10-2 for dipole correctors
  Good setpoint reproducibility
  Hysteresis cycling is important for the large magnets. Cycling parameters determined empirically.
  Klystron gallery temperature stability is important due to sensitivity of LLRF system
Magnet cycling app

## Slide 16: Stability of low loss tune (cont.)
Biggest cause of changes during operation:
  Stripper foil degradation – foil curls and wrinkles
  Extraction kicker timing drifts (upgrade is in progress)
Photo of used SNS stripper foil
Photo by C. Luck

## Slide 17: Superconducting Linac beam loss trends
Big drop in losses with focusing strength reduction in early 2009
Modest benefit since
BLMs along the SCL

## Slide 18: Ring beam loss trends
Ring injection is the primary beam loss area
Estimated total fraction beam loss in ring is 1.9x10-4

## Slide 19: Occasional beam loss (errant beams)
A large amount of beam loss can occasionally occur due to:
  RF trips off due to an interlock
  Fluctuations in the ion source
  Drifts in the RF system (e.g. due to temperature in klystron gallery)
  Pulsed magnets miss a pulse or provide only a partial pulse
The integrated beam power lost may be small compared to the continuous beam loss, but the consequences can be large…

## Slide 20: Why occasional beam losses are important
Example: damage to superconducting linac (SCL) cavity
  Beam hitting RF cavity surface desorbs gas or particulates creating an environment for arcing or low-level discharge
  RF cavity performance degrades over time
  At SNS, some cavity fields have been lowered, some cavities have been turned off. Lower fields = lower beam energy.
  SCL cavities do not trip off with every errant beam pulse, but the probability for a trip increases with time. These trips cause downtime.
  At SNS, SCL cavity performance degradation from errant beam can usually be restored
    Requires cavity warm up during a long shutdown and then RF conditioning before resuming beam operation

## Slide 21: Beam loss due to warm linac RF
Abnormal RF pulse with beam
Normal RF pulse with beam
Normal RF pulse with no beam
LLRF output
558 useconds in
CCL
546 useconds in HEBT
Field
Time (usec)
12 useconds lost in the SCL
(Courtesy C. Peters)

## Slide 22: Beam loss due to ion source
Abrupt beam loss caused by sudden changes in the ion source
Fast beam current monitor in MEBT

## Slide 23: At SNS, the majority of trips originate in the warm linac
> 90% of BLM trips were due to Warm Linac RF faults
  RF faults occur at different times during the pulse
    Faults during the RF fill had reproducible times
    Faults during the RF flattop were random
  Focused on improving warm linac operation
< 10% of BLM trips were due to the Ion source/LEBT
  Most ion source induced BLM trips occur during the first week of a new source installation
    High voltage arcing

## Slide 24: Plans for further improvements
Our goal is to improve our understanding of the accelerator beam dynamics, and our model of the machine, so that the model will accurately determine the low loss tune
  Determine if our empirically-determined low loss tune is actually a local minimum – there may be further improvements to be found
  Maximize beam size in linac to reduce intra-beam stripping – make best use of available aperture
Consider adding additional scraping between warm and cold linac sections
  Minimize and control beam halo formation

## Slide 25: Summary
During first years of operation beam losses were improved by empirical tuning, adding scrapers, modifications to ring injection / injection dump
Today losses are stable and reproducible
SNS beam power is not limited by beam losses
The ring injection area has the highest levels of activation, due to the stripper foil
Most beam loss in SCL is caused by intra-beam stripping
  Linac losses are linear with beam pulse length
  Linac losses are approx. quadratic with beam current (IBSt)

## Slide 26: Summary (cont.)
The low-loss tune is not the same as the design tune, can only be found by empirical tuning
Occasional beam loss (errant beams) is mainly due to warm linac RF cavities. We are now working to correct this.
Unexpected results from commissioning:
  scraping in MEBT is surprisingly effective
  beam loss due to intra-beam stripping
  occasional beam loss (errant beams) degrades SC cavities

## Slide 27
Thank you for your attention!

## Slide 28
Back up slides

## Slide 29: 3: SNS Linac Transverse Lattice: Design vs. Operation
Warm linac CCL quads are equal to design
SCL quads operated much lower than design
HEBT quads operated close to design
CCL quad fields
SCL quad fields
HEBT quad fields

## Slide 30: 3: Example: beam tails are created in DTL
Mismatched production tune
Better matched beam
Horizontal
Vertical
Semi-log scale
Start of DTL (7.5 MeV)
End of DTL
(86 MeV)
Beam tails improved but still present
Courtesy C. Allen
Gaussian fits
Notes: 3/Jul/2012 data w/ & w/o matching to DTL

## Slide 31: SC Linac Activation vs time (Courtesy C. Peters)
Fairly steady activation level since 2010

## Slide 32: Ring Injection Activation (Peak) (Courtesy C. Peters)
No obvious jump in activation downstream from the foil

## Slide 33: Residual Activation Decay (Zhukov, Assadi, Popova)
SCL decays quite fast – model comparisons are underway
Possibly useful information for diagnosing nature of the beam loss
Real time measurement of residual activation after shutdown

## Slide 34: Capturing the occasional beam loss events in the SNS linac
Differential Beam Current Monitor (BCM) systems
  Use BCMs in the MEBT, CCL, and HEBT to see how much beam is lost in the SCL
BLM systems
  76 ion chamber detectors along the SCL
Automated report system
  SCL BLM trip occurs, or BCM system detects abnormal signal
    Record BCM waveforms, BLM waveforms, BLM signal level
    Send data to a webserver for immediate viewing

## Slide 35: How much beam is lost
Differential BCMs showed different types of faults
  Average 15-20 usec of beam lost in the SCL
680 useconds in
CCL
664 useconds in
HEBT
16 useconds lost in the SCL
16 useconds
End of DTL = 30 J
End of CCL = 66 J
End of SCL = 350 J

## Slide 36: Beam loss due to ion source/LEBT
Normal
Abnormal
Low current pulse causes beam loss in SCL
Normal ion source pulse
~ 33 mA