## Slide 1: CSNS Accelerator Control and Beam Instrumentation JIN Dapeng, XU Taoguang … June 9, 2015
jindp@ihep.ac.cn
xutg@ihep.ac.cn

## Slide 2: Outline
2
Overall design and progress of the CSNS accelerator control and beam instrumentation systems
Next to do
Summary

## Slide 3: Architecture of control system
3
FPS
Timing
MPS
LAN

## Slide 4: Overall design and progress
4
Architecture layers.
Global control software : EPICS based.

## Slide 5: Overall design and progress
5
Tasks of the control system.
Network based global control backbone.
Timing system.
Machine protection system.
Global data archiving, alarms, and consultation.
Some equipment level controls : front end, vacuum, power supplies remote, LINAC RF remote, injection and extraction, collimators and stripping foils remote …

## Slide 6: Overall design and progress
6
Progress of control system
Temporary network for LINAC control and commissioning built and used.
Temporary data archiver settled.
Part of timing system built and used.
Control of front end completed and used.
Vacuum control of front end completed and used.

## Slide 7: Overall design and progress
7
Progress of control system
Part of PS remote control built and used.
LLRF remote control built and used.
Part of MPS/FPS (Fast Protection System) built and under test.
Other work goes on smoothly according to the progress of the different equipment.

## Slide 8: Overall design and progress
8
Overall network topology.

## Slide 9: Overall design and progress
9
Network for LINAC control and commissioning.

## Slide 10: Overall design and progress
10
Timing system : structure.
Event based.

## Slide 11: Overall design and progress
11
Timing system : LINAC.

## Slide 12: Overall design and progress
12
Photo of temporary main timing station.
Home made
324MHz Power Amplifier
R&S
Signal Generator
To RF Ref. Line
VME FOUT Module
MRF EVG-230 Module

## Slide 13: Overall design and progress
13
Timing system : OPIs.

## Slide 14: Overall design and progress
14
Front end control : structure.

## Slide 15: Overall design and progress
15
Photos of front end control in use. Ion source hall.

## Slide 16: Overall design and progress
16
Machine protection system.
Requirements for drift tubes, bunchers and de-buncher.
17s
5s due to Bragg Peak
Un-chopped beam, 15mA
Beam size : 0.2cm * 0.2cm RMS
Hitting the components directly
10s if chopped
Critical most cases

## Slide 17: Overall design and progress
17
Machine protection system : architecture.

## Slide 18: Overall design and progress
18
Distribution of MPS part (PLC based).

## Slide 19: Overall design and progress
19
Distribution of FPS part (FPGA and high speed serial link based).

## Slide 20: Overall design and progress
20
FPS : How to stop the beam and recover
FPS
IS Extraction
Timing
IS HV Control
Below 10kV?
RFQ Power
LLRF Beam
Gate
Interlock
Reset
Feedback

## Slide 21: Overall design and progress
21
Main Board
VME
IS Mother Board
MPS Mother Board
Timing Mother Board
LLRF Mother Board
LLRF Mother Board
BLM Mother Board
OPI
Opt. adaptor
Opt. transceiver
FPS Central Station :
Field photo

## Slide 22: Overall design and progress
22
FPS : Illustration of connections
Mother board
Main board
Daughter card
Main board

## Slide 23: Overall design and progress
23
Heart-beat functions for real-time safety
Heart-beat signal generation in the CPLD on the daughter card of front end
Heart-beat signal check and counting in the FPGA on the main board at central station

## Slide 24: Overall design and progress
24
Power supplies remote control.
PS cabinets
OPI

## Slide 25: Overall design and progress
25
LINAC RF remote control. Codes embedded in LINAC LLRF local control with C#.

## Slide 26: Overall design and progress
26
LINAC RF remote control : OPI.

## Slide 27: Overall design and progress
27
Distribution of beam monitoring and measurement devices.

## Slide 28: Overall design and progress
28
Distribution of beam loss monitors.

## Slide 29: Overall design and progress
29
Number of beam instrumentation devices along the beam.
 | BCT | BPM | BLM | FBLM | FCT | WS | EM | Foil | MWPM | WCM
LEBT | 2 |  |  |  |  |  | 1 |  |  | 
MEBT | 2 | 7 | 3 |  | 5 | 4 | 1 |  |  | 
DTL | 2 | 1 | 12 | 1 | 3 |  |  |  |  | 
DTL temp. | 1 | 1 | 1 |  | 2 | 1 | 1 |  |  | 
LRBT | 4 | 20 | 28 | 3 | 5 | 8 |  | 1 | 5 | 3
 | BCT | BPM | BLM | FBLM | FCT | WS | MWPM | WCM | tune exciter | 
RCS | 3 | 38 | 72 | 9 | 3 |  |  | 2 | 2 | 
RTBT | 4 | 33 | 50 | 2 |  | 8 | 2 |  |  | 

## Slide 30: Overall design and progress
30
Acquisition and electronics system of beam instrumentation.
Mostly NI PXI-express based with windows and LabView. IOCs in PXI-express controller.
VME/Linux based for BPMs in RCS, IOC in upper server with Windows/Linux + LabView.
Common data will be stored in global Archiver, large size data will be stored in files via NFS for further analysis. Waveform and average value readout for frond end devices with Max 1MHz.

## Slide 31: Overall design and progress
31
Till now, the devices for front end (Ion source, LEBT, RFQ, MEBT) have been installed. A Faraday cup is installed for temporary beam dump.
BPM, beam emittance and beam current data have been got. Wire scanner have been put into use.

## Slide 32: Overall design and progress
32
Beam instrumentation devices installed in the Ion Source hall.

## Slide 33: Overall design and progress
33
Results from the wire scanner.
Wire horizontal
Wire 45-degree
Wire vertical

## Slide 34: Overall design and progress
34
Results of emittance measurement.

## Slide 35: Next to do
35
Installation and commissioning of devices and equipment after MEBT.
Further debug of the beam instrumentation devices installed to improve performance.
Installation in the Central Control Room will start around this September.

## Slide 36: Summary
36
Design and progress of the control and beam instrumentation systems are briefly introduced.
Equipment for the front end have been installed and put into use. All parts run steadily till now.
Much work needs to be done next.
Thanks a lot!