## Slide 1: DA Study for the CEPC Partial Double Ring Scheme
Yiwei Wang, Feng Su, Dou Wang, Yuan Zhang, Huiping Geng, Jie Gao
8 April 2016, CEPC workshop

## Slide 2: Outline
CEPC parameters
Lattice design
  arc, interaction region, partial double ring
Dynamic aperture study
Summary

## Slide 3: CEPC primary parameter （wangdou20160325）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.09

## Slide 4: ARC lattice
60  /60 FODO cell
  n=6
  All 3rd RDT due to sextupoles cancelled
  All 4th RDT except 2Qx-2Qy due to sextupoles cancelled
90  /60  FODO cell
  n=12
  All 3rd RDT due to sextupoles cancelled
  All 4th RDT except 4Qx due to sextupoles cancelled
90  /90  FODO cell
  n=4
  All 3rd RDT due to sextupoles cancelled
  4th RDT except 4Qx, 2Qx+2Qy, 4Qy, 2Qx-2Qy due to sextupoles cancelled
  Should be non-interleaved sextupole scheme

## Slide 5: ARC lattice
60/60 degree FODO cell
  156=26*6 cells in each section to make resonance driving terms cancellation
Length of ARC: 55km

## Slide 6: RDT in ARC
Resonance driving terms (RDT) of ARC lattice
With 2 families of sextupoles in 6 cells
  All 3rd RDT due to sextupoles cancelled
  All 4th RDT except 2Qx-2Qy due to sextupoles cancelled
  Amplitude-dependent tune shift dQx/dJx, dQy/dJy, dQx/dJy accumulated in FODO cells which can be further optimized
3rd RDT
4th RDT
dQx/dJx, dQy/dJy, dQx/dJy
2Qx-2Qy

## Slide 7: Tune shift
tune vs. dP/P
  Second order chromaticity arise due to stronger focusing
2 families in ARC

## Slide 8: IR lattice
  IR lattice design with local chromaticity correction
Additional sextupole for 3rd order chromaticity
IP
FT
CCY
CCX
MT
L*= 1.5m
x*= 0.22mm
y*= 1mm
GQD0= -200T/m
GQF1= 200T/m
LQD0=1.69m
LQF1=0.90m

## Slide 9: Chromaticity correction
3rd order vertical chromaticity
3rd order vertical and horizontal chromaticity
Preliminary result
to be further optimized with whole ring

## Slide 10: Check chromaticity with ARC+IR
4 families in IR
2 families in ARC
Preliminary result
to be further optimized with whole ring
ARC 6.28nm
3rd order vertical chromaticity
ARC 2.9nm
3rd order vertical and horizontal chromaticity

## Slide 11: Partial double ring
Separator: 12*62.5 urad=0.75 mrad
Septum: 4.25 mrad
Exit of septum X=0.028875m

## Slide 12: Whole ring
Circumference=61km, Emittance 3.19nm
High order chromaticity correction with whole ring is under going.
To get a ring around 54km, the PDR should be included into the ARC

## Slide 13: Dynamic aperture
W/O error of the magnets
Synchrotron motion and radiation damping included
Tracking with 240 turns
Coupling factor =0.003 for y
Preliminary result of dynamic aperture for on momentum: (13x, 90 y)
  High order chromaticity correction and other aberration analysis is under going

## Slide 14: Summary
A preliminary lattice designed for CEPC partial double ring scheme
  ARC: 60/60 degree FODO cell
  IR: L*=1.5m, y*= 1mm, c=15mrad
  PDR: 3km
Local chromaticity correction for IR
Preliminary result of dynamic aperture
  on momentum
  High order chromaticity correction and other aberration analysis with whole ring is under going

## Slide 15: PDR lattice
The bending angle in PDR is small compare with its length
  If scale bending angle with (6km/54km)*2/4=175 mrad
  Actually: Left PDR 0.75mrad+14.25mrad-15mrad-15mrad
  Actually: Right PDR +15mrad +15mrad-14.25mrad-0.75mrad
Present PDR almost doesn’t contribute to the emittance
The PDR should be included into the ARC, otherwise
the total length will be 55km+6km