## Slide 1: CEPC SRF System Heat Load
2015-11-18

## Slide 2: CEPC Top-level Parameters related to SRF System (1)
Parameter | Unit | Main Ring | Booster Injection | Booster Extraction
Beam energy | GeV | 120 | 6 | 120
Circumference | km | 54.752 | 54.752 | 54.752
Luminosity / IP | cm-2s-1 | 2.04E+34 | - | -
Energy loss / turn | GeV | 3.11 | 17.6 keV | 2.81
SR power | MW | 103.42 | 16.2 W | 2.46
Revolution period | s | 1.83E-04 | 1.83E-04 | 1.83E-04
Revolution frequency | kHz | 5.4755 | 5.4755 | 5.4755
Bunch charge | nC | 60.56 | 3.35 | 3.2
Bunch number | - | 100 | 50 | 50
Beam current (total) | mA | 33.2 | 0.92 | 0.87
Bunch spacing | μs | 1.825 | 3.65 | 3.65
Beam spectrum spacing | MHz | 0.55 | 0.274 | 0.274

## Slide 3: CEPC Top-level Parameters related to SRF System (2)
Parameter | Unit | Main Ring | Booster Injection | Booster Extraction
Momentum compaction | - | 3.36E-05 | 7.69E-05 | 7.69E-05
Energy spread | % | 0.1629 | 0.1 (linac) | 0.127
Bunch length | mm | 2.65 | 1.5 (linac) | 2.66
RF voltage | GV | 6.87 | 0.213867 | 5.12
RF frequency | GHz | 0.65 | 1.3 | 1.3
Harmonic number | - | 118800 | 237423 | 237423
Synchrotron tune | - | 0.180 | 0.32076 | 0.32076
Energy acceptance (RF) | % | 5.99 | 17.307 | 2.091
Transverse damping time | turns | 77.05 | 682122 (125 s) | 85.2 (15.56 ms)
Longitudinal damping time | turns | 38.52 | 341219 (62 s) | 42.7 (7.789 ms)
Lifetime Bhabha | min | 51.77 | - | -
Lifetime BS (sim.) | min | 47 | - | -

## Slide 4: CEPC SRF System Layout
Total RF module length: 1.4 km
Total RF voltage: 12 GeV
Beam power: 104.5 MW
HOM power: 2 MW
Installed RF power: ~ 160 MW
Installed cryogenics: ~ 100 kW @ 4.5 K
 | Collider | Booster
Modules per section | 12 | 4
Module length | 10 | 12
Cavities per module | 4 | 8
No. of modules | 96 | 32
No. of cavities | 384 | 256
Pretzel Scheme
Two symmetric half sections in each of the eight RF sections.

## Slide 5
scaled from 1.3 GHz cryomodule
Euro-XFEL/ILC/LCLS-II type
Cryomodule Layout
X
X
Enlarge two- phase pipe and chimney.
Omit 5K shield while keep 5K intercept for power coupler.

## Slide 6
CEPC Collider RF Section Configuration
IPs & Pn (n: six parasitic crossing points)
Main Ring module (10 m)
Four 650 MHz 5-cell cavities inside
IP or Pn
FFS (350 m)
or 2 FODO cells (95 m)
One FODO cell (47.2 m)
Half FODO cell (23.6 m)
\\
Pretzel scheme Half RF Section (6 modules, 70 m), 3 module pairs (valve boxes)
DIS
SEP
SEP (Pn)
5λ/2
3λ/2 [(2n+1)λ/2, 2 cav. with one klystron]
λ = 0.461 m
RF length of one module = 29 λ/2 = 6.7 m
For counter-rotating beams, all 5-cell cavity centers must be at nλ/2 from Pn.
Beam time structure various in cavities, modules, RF sections and diff. schemes.

## Slide 7
Pretzel Scheme
48 bunches / beam, 96 parasitic collision points (~ 500 m spacing)
Horizontal separation, no off-center orbit in RF section
One pair of electrostatic separators for each arc (green)
One pair of electrostatic separators for P2, P3, P4, P6, P7, P8
H.P. Geng

## Slide 8: Local Double Ring Scheme
One bunch train per beam
No pretzel
Crab waist possible
Cost less than whole double-ring
More bunches for high luminosity Z, W
J. Gao, M. Xiao, M. Koratzinos
Parameters | Value | Unit
Circumference | 54374 | m
Length of one FODO cell | 47.2 | m
Harmonic number | 118800 | 
One bucket length in the ring | 0.46 | m
Bucket number in double beam pipe | 6156 | 
Local double section 10% of the whole ring
120 FODO cells length
1.416km on each side of IP
e-
e+
~3 km (10 μs) macro-bunch
RF

## Slide 10
2 K static: CEPC has no current leads, but input and HOM coupler static load may be larger.
2 K dynamic: Booster cavity + (input coupler scaled from ILC); MR cavity
Booster input coupler dynamic: scaled from ILC, duty factor 0.364 % (only beam time, w/o filling and decaying time, ~ x 1.5) to 20 %, power 300 kW (190 kW ?) to 20 kW; 2 K: 5 W
Input coupler
ILC TDR, XFEL measurement
HOM cable, absorber, bellow

## Slide 11: Booster RF Transients
4s ramp beam phase change（off-crest）
89.99°
56.7°
/s
6 GeV
120 GeV
Booster magnet field cycle
extraction to main ring
injection from linac
4s ramp cavity voltage (red)
νs constant
/s
/ MV
4s ramp RF power
Qe=1E7
Red: df=25Hz
Blue: df=50Hz (w/o beam inductance)
Duty factor for continuous injection and without cavity para-phase：Cavity wall loss: 21.2 % (~ 20 %) （Q0 const.）; HOM heat load: 50 %; Power Source：22.4 %
For normal operation with 90 s injection cycle, all duty factors reduce to 22 % of the continuous inj.

## Slide 12: HOM Power
 |  | CEPC main ring | CEPC booster | ILC beam
Bunch length | mm | 2.65 | 1.5 - 2.66 | 0.3
HOM loss factor per cavity | V/pC | 1.8 | 4 | 12
Bunch charge | nC | 59.4 | 3.1 | 3.2
Bunch spacing | ns | 1810 | 3627 | 554
Beam current | mA | 33.2 (two beam) | 0.85 | 5.8
CW HOM power per cavity | W | 3509 | 10.7 | 221.8
HOM duty factor | - | 100% | 50% | 50%
HOM power per cavity with DF | W | 3509 | 5.3 | 110.9

## Slide 13: ILC TDR
6 W HOM power per module for 8 cavities (5.2 mA, 9 mA?)

## Slide 14
Level | Measured | Calculated | XRB | Factor | XRC
40/80 K | 100-120 | 100-120 | 83 | 1.5 | 125
5/8 K | 6-11 | 6-12 | 13 | 1.5 | 20
2 K | 6 | 2.1 | 4.8 | 1.3 | 6
Static heat load summary of PXEFL modules
Conclusions
40/80 K: 100-120 W depending on the performance of MLI.
5/8 K: 6-12 W depending on the outer shield temperatures.
2 K: 3.5-6 W depending on the installation skills of current leads.
Measured and calculated values have a good agreements at 5/8 K and 40/80 K.
Big deviation at 2 K caused by underestimation of cabling heat load and the installation skills of current leads.
Specified refrigerator capacity still could cover the heat load at 2 K and 40/80 K (Even come to limit) and have enough margin at 5/8 K.
XRB: XFEL refrigerator budget, XRC: XFEL refrigerator capacity

## Slide 15: ILC Input Coupler
0.02 W
0.22
2.06
0.05
0.38
5.22

## Slide 17: CEPC MR Input Coupler
Static heat load
  2 K: 0.06 W
  5 K: 0.6 W
  80 K: 6 W
Dynamic heat load
  2 K: 1 W
  5 K: 10 W
  80 K: 50 W

## Slide 18: Power Coupler
Main ring 650 MHz 300 kW coupler:
Booster 1.3 GHz 4 kW coupler:
KEK STF1-type coupler developed by IHEP (test to 800 kW with DF 0.75 % = 6 kW) or TTFIII coupler can be used.
very high power handling capacity
two windows for vacuum safety and cavity clean assembly, effective cooling
very small heat load, simple structure for cost saving, high yield and reliability
Tristan (70 kW) / KEKB (380 kW) / BEPCII (120 kW) type as baseline. KEK cERL injector coupler (one window) as reference.

## Slide 19: HOM Heat Load Budget
 | Main Ring | Booster
HOM power / cavity | 3.5 kW | 5.3 W
HOM power / module | 21 kW | 56 W
HOM 2 K heat load / module | 13 W (0.6 %) | 5.9 W (10%)
HOM 5 K heat load / module | 39 W (1.8 %) | 3 W
HOM 80 K heat load / module | 390 W (18 %) | 43.8 W
Percent of total cryogenic load | 22 % | 11 %
Main Ring heat load: design upper limit (estimated to have enough margin)
Booster heat load: scaled from ILC TDR (DF 50 % for continuous injection)

## Slide 20: LCLS-II

## Slide 21: LCLS-II HOM Power

## Slide 22: LCLS-II Untrapped HOM Power to 2K

## Slide 23: HOM Heat Load Estimation
Assume 10 kW HOM power propagating through the beam tubes and bellows (thin copper film RRR=30, in abnormal skin effect regime), power dissipation < 2 W/m @ 2K.
  Even RRR=1 for copper plating (normal skin effect regime), power dissipation < 10 W/m
HOM power loss in cavity at 2 K less than 0.3 W (all modes Qext < 106)
Heat load at 5 K and 80 K dominated by HOM cable heating. Assume 0.1 dB/m power dissipation of the LEP/LHC-type rigid coaxial line (copper plated stainless steel) and 1 m length, total heat load is 10 W for the resonant excitation of TM011 mode.
Further study: HOM propagating, heat load calculation, statistical approach to study heat load at 2 K (LCLS-II), trap mode …