## Slide 1: Robinson Instability Analysis for CEPC Main Ring
Hongjuan Zheng, Jiyuan Zhai, Haipeng Wang, Jie Gao
2012.12.25

## Slide 2: Outline
Robinson instability limits
Loaded generator-cavity-beam system
Beam parameters
Robinson instability of CEPC

## Slide 3: Different Definitions of Synchronous Phase
Below transition
Above transition
SY Lee, etc
SY Lee, etc
Wiedemann, Robinson, etc
P. B.Wilson Merminga, etc
Synchrotron auto focusing
[1] Haipeng Wang. Beam-Cavity Interaction Related SRF System Design Principles and Simulation Techniques (I), IHEP Seminar, Dec.1, 2015, Beijing

## Slide 4: Synchronous phase is used in several physical relations
Acceleration
SR equilibrium bunch length
Synchrotron tune
Beam loading optimization
Detuning angle Robinson Instability
[1] Haipeng Wang. Beam-Cavity Interaction Related SRF System Design Principles and Simulation Techniques (I), IHEP Seminar, Dec.1, 2015, Beijing

## Slide 5: Stability of the system
The 1st Robinson condition states that the beam is stable at positive h if the lower synchrotron sideband samples a larger cavity resistive impedance with respect to the upper synchrotron sideband (the opposite for negative h).
h >0 => unstable
h <0 => stable
w + ws
w - ws
w + ws
w - ws
h >0 => stable
h <0 => unstable
The Robinson 2nd limit can be also derived from the bunched beam coherent instabilities theory. The coherent frequency of the barycentre motion of the bunches wsc is given by:
and the Robinson 2nd limit is reached when wsc gets to zero.
The damping constant aR is given by:
[1] Alessandro Gallo. Beam Loading and Low-level RF Control in Storage Rings.

## Slide 6: Loaded Generator-Cavity-Beam System
Both generator and beam are considered as current source,
generator feed energy in to cavity;
beam extracts energy from cavity.
When above transition, particles with higher energy have larger revolution time. Beam current needs to lags cavity voltage to satisfy the phase stability criteria, which means the beam effective impedance is inductive.
So, for the generator to see a resistive impedance, the cavity needs to be capacitive-detuned, it means yT < 0 and w0 < wRF, and voltage lags beam current by the phase |yT|, because then cavity impedance looks capacitive.

## Slide 7: Beam Loading and Phasor Diagram
yT: Tuning angle of impedance
yT < 0 for above transition
loaded impedance:
;
yS: Synchronous phase angle
yL: Loading angle
angle between the generator current and the cavity voltage ;
IB: fundamental harmonic component of beam current
IB = 2 I0, where I0 is the average beam current;
w0: cavity resonance frequency,
wRF: generator RF frequency, Synchronous beam revolution frequency
times harmonic number
real
image

## Slide 8: P.B. Wilson Phasor Diagram Using Cos(s)
L+=
=s
[1] Haipeng Wang. Beam-Cavity Interaction Related SRF System Design Principles and Simulation Techniques (I), IHEP Seminar, Dec.1, 2015, Beijing

## Slide 9: Beam Parameters
Parameter | Unit | Value | Parameter | Unit | Value
Beam energy | GeV | 120 | Circumference | m | 54752
Number of IP |  | 2 | SR loss/turn | GeV | 3.11
Bunch number/beam |  | 50 | Bunch population |  | 3.79E+11
Synchrotron radiation (SR) power/beam | MW | 51.7 | Beam current | mA | 16.6
Bending radius | m | 6094 | Momentum compaction factor |  | 3.36E-5
Revolution period | s | 1.83E-4 | Revolution frequency | Hz | 5475.46
Emittance (x/y) | nm | 6.12/0.018 | βIP (x/y) | mm | 800/1.2
Transverse size (x/y) | μm | 69.97/0.15 | ξx,y/IP |  | 0.118/0.083
Bunch length SR | mm | 2.14 | Bunch length total | mm | 2.65
Lifetime due to Beamstrahlung | min | 47 | Lifetime due to radiation Bhabha scattering | min | 51
RF voltage | GV | 6.87 | RF frequency | MHz | 650
Harmonic number |  | 118800 | Synchrotron oscillation tune |  | 0.18
Energy acceptance RF | % | 5.99 | Damping partition number |  | 2
Energy spread SR | % | 0.132 | Energy spread BS | % | 0.096
Energy spread total | % | 0.163 | During the collision |  | 0.23
Transverse damping time | turns | 78 | Longitudinal damping time | turns | 39
Hourglass factor | Fh | 0.68 | Luminosity/IP | cm-2s-1 | 2.04E+34

## Slide 10
Robinson 1st stability requires that f < frf
Tuning angle for main RF cavities

## Slide 11: Robinson working point without loop gain
Loop gain=0, Pf=272.9kW, ΨL=0, Qext=2.282×106，Q0=4×1010

## Slide 12: Robinson working point without loop gain
Loop gain=0, Pf=300kW, ΨL=-10°, Qext=2.282×106 ，Q0=4×1010

## Slide 13: Robinson working point without loop gain
Loop gain=0, Pf=280kW, ΨL=0°, Qext=2×106 ，Q0=4×1010

## Slide 14: Robinson working point with loop gain
Loop gain=0.1, Pf=280kW, ΨL=0°, Qext=2.282×106 ，Q0=4×1010

## Slide 15: Conclusion
Robinson instability is not a serious problem for Higgs.
More work need to be done for Z factory and bunch train scheme……

## Slide 16
Thank you for your attention!