## Slide 1: Interaction region design for the partial double ring scheme
Yiwei Wang, Xiaohao Cui, Dou Wang, Feng Su,
Sha Bai, Huiping Geng, Yuan Zhang, Jie Gao
CEPC AP meeting, 19 Feb 2016

## Slide 2: Introduction
Main parameters
Interaction region lattice
  Final doublet
  Chromaticity correction section
  Matching section
  Nonlinear chromaticity correction
  Break down of –I (geometric-chromatic aberration)
ARC lattice consideration

## Slide 3: Main Parameters of PDR
 | Pre-CDR | H-high lumi. |  | H-low power |  | Z
Number of IPs | 2 | 2 |  | 2 |  | 2
Energy (GeV) | 120 | 120 |  | 120 |  | 45.5
Circumference (km) | 54 | 54 |  | 54 |  | 54
SR loss/turn (GeV) | 3.1 | 2.96 |  | 2.96 |  | 0.062
Half crossing angle (mrad) | 0 | 14.5 | 8.9 | 11.5 | 8.7 | 16.5
Piwinski angle | 0 | 2 | 3.1 | 2 | 2 | 2.6
Ne/bunch (1011) | 3.79 | 3.79 | 1.32 | 2.81 | 2.0 | 0.37
Bunch number | 50 | 50 | 144 | 40 | 57 | 1100
Beam current (mA) | 16.6 | 16.9 | 16.9 | 10.1 | 10.1 | 36.2
SR power /beam (MW) | 51.7 | 50 | 50 | 30 | 30 | 2.2
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.1
Momentum compaction (10-5) | 3.4 | 3.0 | 2.3 | 2.6 | 2.5 | 5.4
IP x/y (m) | 0.8/0.0012 | 0.306/0.0012 | 0.058/0.0016 | 0.22/0.001 | 0.115/0.001 | 0.3/0.001
Emittance x/y (nm) | 6.12/0.018 | 3.34/0.01 | 2.32/0.0058 | 2.67/0.008 | 2.56/0.0078 | 1.18/0.0069
Transverse IP (um) | 69.97/0.15 | 32/0.11 | 11.6/0.097 | 24.3/0.09 | 17.6/0.088 | 18.8/0.083
x/IP | 0.118 | 0.04 | 0.01 | 0.04 | 0.028 | 0.02
y/IP | 0.083 | 0.11 | 0.11 | 0.11 | 0.11 | 0.042
VRF (GV) | 6.87 | 3.7 | 3.6 | 3.6 | 3.7 | 0.28
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.3 | 3.0 | 3.2 | 3.0 | 3.0
Total z (mm) | 2.65 | 4.4 | 4.0 | 4.2 | 4.0 | 3.0
HOM power/cavity (kw) | 3.6 | 3.3 | 1.0 | 1.5 | 0.95 | 0.73
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13 | 0.13 | 0.05
Energy acceptance (%) | 2 | 2 | 2 | 2 | 2 | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.2 | 2.2 | 2.4 | 2.0
n | 0.23 | 0.49 | 0.46 | 0.47 | 0.46 | 0.08
Life time due to beamstrahlung_cal (minute) | 47 | 53 | 32 | 41 | 32 | 
F (hour glass) | 0.68 | 0.73 | 0.89 | 0.69 | 0.7 | 0.83
Lmax/IP (1034cm-2s-1) | 2.04 | 2.97 | 2.75 | 2.03 | 2.07 | 1.25
D. Wang, Jan 2016, HK

## Slide 4: Final doublet
constraint R22=0, R44=0 at the exit of QF1
  point to pararell image on both x and y planes
  get numerical solution with MAD as it’s not easy to get a analytical solution of even with thin-lens model
L*
d
l1
l2
QD0
QF1
  L*, d, G1, G2
  y, x, R, B1, B2,
  y*, x*
  l1, l2

## Slide 5: Final doublet
Acceptance can be further reduced with thinner septum magnet or smaller acceptance

## Slide 6: Final doublet
LD1 LD2 G1 G2 LQ1 LQ2 KSIY KSIX B1 B2
1.5 0.5 -200 200 1.68924427 0.8975406954 -190.6883514 -6.165431938 -4.762983257 4.762983257
R x
0.025 0.0225*2
RQ1 could be smaller than RQ2 to avoid conflict of Q1,e+ and Q1,e-
R should be re-optimized

## Slide 7: Final doublet
total length = 4.586785 dmux = -0.009271 dmuy = -0.000283
betax(max) = 299.406832 betay(max) = 4169.298422
Dx(max) = 0.000000 Dy(max) = 0.000000
Dx(r.m.s.) = 0.000000 Dy(r.m.s.) = 0.000000

## Slide 8: Chromaticity correction section

## Slide 9: Final transformer

## Slide 10: Matching section

## Slide 11: Final focus

## Slide 12
Yunhai CAI, 2016, HK

## Slide 13
Yunhai CAI, 2016, HK

## Slide 14: Odd dispersion

## Slide 15: Crab sextupole
Dedicated section (for local correction)
Oide’s scheme (for global correction)

## Slide 16: ARC
60/60 degree
  All the 3rd and 4th order driving term except 2vx-2vy are cancelled in 6 cells
  Amplitude-dependent detuning terms need to be corrected
90/90 degree
  All the 3rd and 4th order driving term can be cancelled
  Global chromaticity correction is complicate
60/90 degree
  Check with driving terms along beamline

## Slide 17: Summary
For Higgs low-power parameters, a linear lattice has been designed including final doublet optimization, odd dispersion scheme for geometric-chromatic aberration correction.
Nonlinearity correction is going on.
A dedicated section for crab sextupole need to be designed.
ARC optimization is also going on.