## Slide 1: Beam-Beam Simulation (draft for 04-08 workgroup meeting)
ZHANG, Yuan
Apr 1st, 2016

## Slide 2: Primary parameter for CEPC double ring （wangdou20160325）
 | Pre-CDR | H-high lumi. | H-low power | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 8.5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.08/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.002 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7/0.046 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.005 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.084 (Fl=3) | 0.073 (Fl=2.6)
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.27 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.61 | 3.09

## Slide 3: Case: H-high lum
Lifetime: 118 min
IBB: Strong-Strong Beam-Beam Code
with Beamstrahlung effect
Developed by Y. Zhang@IHEP

## Slide 4: Case: H-low power
Lifetime: 97 min
IBB: Strong-Strong Beam-Beam Code
with Beamstrahlung effect
Developed by Y. Zhang@IHEP

## Slide 5: Case Z-1
IBB: Strong-Strong Beam-Beam Code
with Beamstrahlung effect
Developed by Y. Zhang@IHEP

## Slide 6: Case Z-2
IBB: Strong-Strong Beam-Beam Code
with Beamstrahlung effect
Developed by Y. Zhang@IHEP