## Slide 1: Fast Radiation Simulation and Visualized Data Processing Method
GHMT R&D Center
Accelerator Physics Department
Jinlong Wang
2016-9-23

## Slide 2: Abstract
Typical FLUKA simulation time for a primary number 106 is 1~2 hours on a standalone computer, in order to get a better statistics, the general way is to increase the primary, for a complicated shielding case the primary number is up to 109. Thus a fast radiation simulation method is introduced which is called Multicore FLUKA. Flair and SimpGEO are good additional tools for FLUKA, they are helpful to geometry model, compile an input file and visualize the standard FLUKA output. What more, Gun plot is powerful to merge multi data to figures. Full beam line radiation is also discussed.

## Slide 3: Contents
Introduction
Fast Radiation Simulation
Complicated Model
Visualized Data Processing
Data Merge Method
Full Beam Line Simulation
Summary

## Slide 4
1.Introduction

## Slide 5: Purpose
Purpose 1:
Reduce the simulation time for high primary number (up to 108~9).
Purpose 2:
Make the modeling and input file compiling faster and easier.
Multicore FLUKA
Flair
Purpose 4:
Merge multi data to figures.
Gun plot
Purpose 3:
Visualize the FLUKA output data.
SimpleGEO+DaVis3D
Purpose 5:
Increase the accuracy.
Full Beam Line Simulation

## Slide 6
2. Fast Radiation Simulation

## Slide 7: Work flow of Multicore FLUKA
T_Multicore = T0/(4*Node number)

## Slide 8: Coding
Python+shell scripts
**.inp: input file
FlukaMulticoreRun.py: The main program
rtfluka.sh: shell scrip, change the random number
CopyFiles.py DeleteAll.py: Auxiliary functions deal with files

## Slide 9: Specification of FlukaMulticoreRun.py
Variables in rectangle should be changed to your settings
Coding

## Slide 10: Verification
Multicore FLUKA is proved to be powerful in the radiation work of Sun Yat-Sen Proton Hospital. Dose distribution is smooth and clear. The primary number is 9×10^8 for every source simulation. However, we only spent 1~2 months in total.

## Slide 11
3. Complicated model

## Slide 12: 3D SimpleGEO geometry of proton therapy facility
GEO modeling directly by FLUKA is difficult, and the 3D model from CAD software such as NX, Solid works, etc. is different format from FLUKA.
SimpleGEO Advantages:
Like CAD
Easy to create bodies and can rotated to any angle easily
SimpleGEO Disadvantages:
Low accuracy
Directly import complicated SimpleGEO model always cause errors and difficult to figure out the reason.
SimpleGEO model is always used for data visualize

## Slide 13: FLAIR geometry of proton therapy facility
FLAIR Advantages:
Higher accuracy
Easy debug
Directly used for FLUKA
SimpleGEO Disadvantages:
More like program
Difficult to create complicated model
Few bodies to choose
Edit FLUKA simulation input file

## Slide 14: The Degrader Model
Simple GEO
Fast but almost can not work in fluka
Easy to rotate
Less parameters
FLAIR
Slow but accurate
Many parameters

## Slide 15
4. Visualized Data Processing

## Slide 16: The video display of DaVis3D
DaVis3D is one plugin tools of SimpleGEO, it’s a novel post processing tool for FLUKA output data.

## Slide 17: Profiles
Thus the primary should be increased.
Obviously, the shielding wall stop particles
Statistics outside the wall is not as good as inside.

## Slide 18: Degrader & collimator and beam shape
Beam size will increase in graphite degrader and decrease after tantalum collimator, increase in target again.

## Slide 19: Degrader & collimator and beam shape
DThic=18.8cm
DThic=5.3cm
Energy≈195MeV Efficiency(T2T3) ≈18.26%
Energy≈75MeV Efficiency(T2T3) ≈7.08%
BPM1
BPM2

## Slide 20: Efficiency
Etr(MeV) | Thick(cm) | T2-MCNPX(%) | T2-FLUKA(%)
230 | 0 | 100.00 | 100.00
215 | 2.3 | 99.28 | 99.56
195 | 5.3 | 96.44 | 97.50
175 | 8.2 | 92.65 | 93.20
155 | 10.8 | 88.60 | 90.00
135 | 13.2 | 83.93 | 84.90
115 | 15.3 | 79.26 | 80.90
95 | 17.15 | 75.00 | 76.20
75 | 18.8 | 71.19 | 72.80
70 | 19 | - | 71.50
T2 simulated by Fluka can consists with MCNP data.

## Slide 21: Simple GEO + DaVis3D

## Slide 22
5. Data Merge

## Slide 23: Fix beam treatment room
Energy(MeV | Weight
230 | 0.176
210 | 0.140
180 | 0.123
160 | 0.313
130 | 0.248
Total | 1.000
Flair can merge data directly from the output for one simulation. But for different sources we need flexible merge tool which can set the weight of source, set color palette, and contour plot. Thus Gun plot is a good choice.

## Slide 24
set palette defined ( 1 "grey",2 "magenta", 3 "blue",4 "green",5 "yellow", 6 "red", 7 "cyan")

## Slide 25
set palette defined ( 1 "red",2 "green", 3 "dark-blue",4 "blue",5 "honeydew", 6 "dark-pink", 7 "cyan")

## Slide 26
There are 16 sources in this work and every source have 5 energy point.

## Slide 27
6. Full Beam Line Simulation

## Slide 28
(a) Dose Distribution, (b) Proton Flux Beam Line
The most ideal simulation is to have a full beam line with magnet field in dipole and quadruple, and all the slits are adjusted to the correct efficiency. This method can get an accurate dose distribution

## Slide 29
7. Summary

## Slide 30
Full beam line is an ideal method which can present the most accurate radiation distribution, but need more investigation in the future.
Multicore FLUKA, Flair, SimpleGEO and full beam line are important tool or method for radiation shielding.
Multicore FLUKA can save simulation time and liberate the researcher to focus on physics, it is flexible and can satisfy the user requirement.
Flair and SimpleGEO are used for modeling and visualized data processing.