## Slide 1: Radiation Protection Aspects for LCLS-II High Power Electron Accelerator
James C. Liu, Ph.D. and CHP
Deputy Department Head,
Radiation Protection Department
SLAC National Accelerator Laboratory
Menlo Park, CA, USA 94025
Sept. 22-23, 2016 at CSNS, China

## Slide 2: Outline
  Introduction to LCLS-II Layout and Beam Parameters
  U.S. Regulations and SLAC Requirements
  LCLS-II Safety Aspects (Use EBDs as an Example):
        Prompt Radiation
        Residual Dose Rates
        Groundwater
        Radioactive Air (Concentration and Effluent)
        LCW Heat Exchanger System
  Protection from SCRF Cavity
  Conclusions
2
  EBD: Electron Beam Dump LCW: Low Conductivity Water

## Slide 3
Linac Coherent Light Source (LCLS)
Injector at 2-km point
Existing Linac (1 km)
(with modifications)
First Hard FEL Machine April 2009
e– Transfer Line (340 m)
X-ray Transport Line (200 m)
UCLA
Undulator (130 m)
Near Experiment Hall
Far Experiment Hall
3
Notes:   Since October 2009 LCLS has provided x-rays to users
  Electron source is the original SLAC linac
  One fixed gap undulator
  X-ray energy, pulse length, is set by electron beam
  Six experimental stations
  One or two experiments scheduled at a time

## Slide 4
LCLS 2009
LCLS-II 2020
New Injector and
New Superconducting Linac
Existing Bypass Line
New Transport Line
Two New Undulators
Replacing the Existing One
Repurpose Existing Experimental Stations
New Cryo Plant
4
Linac Coherent Light Source
Near Experiment Hall
Far Experiment Hall

## Slide 5: LCLS-II Layout and Beam Parameters
HXU
SXU
Sec. 21-30
Sec. 11-20
0.2-1.3 keV (1 MHz)
L3
1-5 keV (1 MHz)
LCLS-I Linac
3-15 GeV
1 kW
proposed
FACET-II
LCLS-II Injector &
3 SCRF Sections
0.25 GeV
1.6 GeV
4.0 GeV
1 MW, 1 MHz
L2
BSY
(Beam Switch Yard)
Kickers
Septums
BEAM DIRECTION
Beam Split by Kickers and Septums
4 Beamlines
LCLS Cu Linac
LCLS-II Hard
LCLS-II Soft
LCLS-II Dump
5
250 kW Dump
0.1-20 keV* (120 Hz)
1-25 keV (120 Hz)

## Slide 6: LCLS-II Layout: EBD, FEE and NEH
FEE
EBD
FEE HALLWAY AND FEE MAZE
NEH HUTCH 1
SXR
HXR
2 Electron Beam Dumps
(2 EBDs, 2x120 kW)
FEL Stopper Sets
FEE
NEH
6
undulators

## Slide 7: LCLS-II Main Radiation Source Terms
250-kW BSY Dump inside Muon Shield
Halo Collimators & SCRF along Linac
BYD
Two 120-kW EBDs
Aboveground BTH
7

## Slide 8: LCLS-II Electron Normal Beam Losses
Area | Linac-BSY | BSY | BTH | Dump Lines | 
Beamline Component | Halo Collimators R1 estimate* | Dump | Two 225-m-long beam lines | BYD (0.1% of EBDs | Two EBDs
Maximum Power for worker dose impacts | 310 W (32 max.) | 250 kW | 450 W (1 W/m) | 2x120 W | 2x120 kW
Average Power (5000 h/y with use factor) for public/environmental impacts | 70 W (13 max.) | 90 kW | 450 W (1 W/m) | 75 W | 27 kW + 48 kW
LCLS-II-2.7-PR-0079-R1 by J. Welch; RSC16-02 June 2016
* R0 estimates: average power 3000 W along ~30 halo collimators of SC Linac
LCLS-II 1 MW versus LCLS-I 1 kW
LCLS-II radiation protection for public, environment and workers is more challenging, considering now that there are less safety margin and the constraints of building LCLS-II on existing LCLS-I configuration (Monte Carlo calculations and optimization are very important)
8

## Slide 9
 | Prompt Radiation | Residual Dose Rates | Radioactive Air Concentration | Ozone
Federal Limit | Department of Energy (DOE) 10 CFR 835 DOE Order 420.2c Radiation Worker (RWT): 50 mSv/y General Employee (GERT): 1 mSv/y ALARA |  |  | OSHA 29 CFR 1910.1000 PEL = 0.1 ppm
SLAC Design Limit | Shielding Design RWT ≤ 5 µSv/h GERT ≤ 0.5 µSy/h | Non-Radiation Area ≤ 50 µSv/h | Air Immersion ≤ 1 DAC (25 µSv/h) | PEL 0.1 ppm
 | 1) ES&H Manual, Chapter 9 “Radiological Safety” 2) Radiation Protection Program Manual and Procedures 3) Radiation Safety Systems: Technical Basis Documents |  |  | 
Radiological Requirements for Worker Protection
For 11C, 13N and 15O, DOE Immersion 1 DAC = 0.22 MBq/m3
For 41Ar, DOE Immersion 1 DAC = 0.11 MBq/m3
9
Notes: 1DAC-h= 2.5 mrem
2 DAC-h- RA limit

## Slide 10
 | General Program | Direct Radiation | Radioactive Air Effluent | Ground Water | Waste Water
Federal |  |  | 40 CFR 61H (NESHAPs) | 40 CFR 141 (NPDWR) | 10 CFR 20K
State & Local |  |  | BAAQMD | RWQCB Order | CCR17, SBSA Permit
DOE Order 458.1 Limit | 1 mSv/y to MEI ALARA |  | 0.1 mSv/y to MEI (Maximum Exposed Individual of the Public) | MCL for 3H: 740 Bq/L | 3H: 185 GBq/y All other radionuclides: 37 GBq/y to sewer
SLAC Design Limit |  | 50 µSv/y to MEI | 1 µSv/y MEI for each air release point so that no continuous monitoring is needed | EPA Detection Limit of 37 Bq/L 3H | LCW discharge
 | 1) ES&H Manual, Chapter 9 “Radiological Safety” 2) Radiological Environmental Protection Program Manuals and Procedures 3) Radiation Safety Systems: Technical Basis Documents |  |  |  | 
Radiological Requirements for Public/Environment Protection
10

## Slide 11: LCLS-II Safety Aspects: Example of 2 EBDs
Bend Magnets
(BYDs)
East End of Undulator Hall
FEE & NEH
Extensive Dump Shielding (dictated by GW, which also address other hazards)
2 EBDs
Prompt Radiation in NEH
11
FLUKA used for this complex geometry
Residual Dose Rate
Radioactive Air IN/OUT
Groundwater
LCW for EBDs

## Slide 12: Prompt Radiation to FEE and NEH
2 x 240 kW at 8 GeV
Dump shielding for groundwater protection helps reduce prompt
FLUKA-calculated prompt radiation in NEH within the limit of 0.5 µSv/h (1 mSv/y) for users
  FEE is not occupiable
Muon radiation dominant in 8 GeV upgrade case
12
2 x 120 kW at 4 GeV
FEE
NEH
Very high radiation level around dump creates material damage issue

## Slide 13: Radiation Damage to Materials near EBDs
1-MeV Equivalent Neutron Fluence
13
Absorbed Dose
Electronics are of concern:
Limit: 1E13 n/cm2
Limit: 100 Gy

## Slide 14: EBD Shielding for Residual Dose Rate
Changes required to dump pit design (3D view and elevation view)
  Reduce residual dose rate from 500 μSv/h to 50 μSv/h (Non-Radiation Area) by Inserting a 20 cm concrete shell around the dump to absorb neutrons in the core lowering activation of the concrete tunnel
Residual dose rates above one dump for Ti=30 days, Tc=1h, 5kW
Before Changes
After Changes
[μSv/h]
50
14
  Service of dumps that are highly activated!

## Slide 15: Groundwater Protection: Tritium Production in Soil around EBD Enclosure
4 GeV baseline: saturation activity of 40 Bq/dm3 of 3H in soil
8 GeV upgrade:
  4 times higher H-3 production in soil in forward direction
  2 times higher H-3 production in soil on side of the dumps
15
75 kW at 4 GeV
113 kW at 8 GeV

## Slide 16: Groundwater Protection for 2 EBDs
  3H is the main concern due to high leachability from soil to water
10 m
membrane
  3H in ground water is expected to be below EPA detection limit of 37 Bq/L.
  Geomembrane will reduce rainwater flux
Groundwater table 10 m below dump enclosure
Minimal direct activation
16
  For 43 kW over a year, most irradiated 1 m3 rainwater path, worst drift speed, no diffusion and no dilution  44 Bq/L of 3H (EPA MCL = 740 Bq/L)
Notes: Activation from direct path is negligible

## Slide 17: Groundwater Protection for 2 EBDs and BSY Dump
  BSY Dump with 1.7 m iron and 1.8 m concrete floor (52 kW)
Saturation Activity 3H (Bq/L) | BSY Dump | 2 EBDs
Direct Activation in GW | 4 | 0
Indirect Rain Path to GW | 22 | 44
Geomembrane | Recommended | Required
  2 EBDs (43 kW)
17
Groundwater table below dump enclosure
Small direct activation

## Slide 18
LCLS-II Radioactive Air and Ozone Concentrations
Calculated with FLUKA (dominated by air gaps between dump and shielding)
1-day irradiation and no decay | Linac Halo Collimators | BSY Dump | BYD Magnets | Two EBDs | half-life (min)
Beam Power (kW) | 0.001 (reference) | 240 | 0.24 | 2x120 | 
Local Shielding | No | Yes | No | Yes | 
11C (Bq/m3) | 1.28E+02 | 6.94E+05 | 4.08E+03 | 3.40E+04 | 20.4
13N (Bq/m3) | 2.24E+02 | 1.53E+06 | 5.52E+03 | 1.02E+05 | 10.0
15O (Bq/m3) | 2.40E+02 | 1.00E+06 | 5.90E+03 | 4.53E+04 | 2.0
41Ar (Bq/m3) | 1.03E+02 | 1.65E+06 | 1.21E+04 | 6.07E+03 | 109.3
Sum (Bq/m3) | 6.94E+02 | 4.88E+06 | 2.76E+04 | 1.88E+05 | 
Ozone (ppm) | 0.0007 | 0.38 | 0.046 | 0.0005 | 34.7
18
For 11C, 13N and 15O, DOE Immersion 1 DAC = 0.22 MBq/m3
Ozone G value = 10, OSHA ozone PEL = 0.1 ppm

## Slide 19
Dose to Public MEI from Radioactive Air Effluent
 | Linac Halo Collimators | BSY Dump | BYD | 2 EBDs
Average Power (kW) | 0.001 (reference case) | 90 with shielding | 0.075 | 75 with shielding
Air Exchange per Day | 1 | 8 | 1 | 1
MEI Location | MEI #02 (Sand Hill Rd.) | MEI #16 (SLAC Guest House) | MEI #08 (East End close to SLC) | MEI #08 (East End close to SLC)
Distance to MEI | 790 m North West from S4 | 420 m North East | 550 m East | 550 m East
11C (µSv/y) | 9.3E-6 | 6.4E-2 | 1.0E-4 | 5.7E-4
13N (µSv/y) | 1.3E-5 | 1.1E-1 | 1.1E-4 | 1.4E-3
15O (µSv/y) | 3.9E-6 | 2.2E-2 | 5.4E-5 | 2.7E-4
41Ar (µSv/y) | 1.4E-5 | 1.9E-1 | 5.2E-4 | 1.7E-4
Total (µSv/y) | 3.9E-5 | 3.9E-1 | 7.9E-4 | 2.4E-3
Calculated with EPA-approved CAP88 code (annual NESHAPs report):
DOE/EPA dose limit: 100 µSv/y to public MEI
1 µSv/y to public MEI from each air release point so that no continuous air monitoring is required
19

## Slide 20: Deployment of AMS, RDM and Interlocked Detector in Linac
Eberline AMS-4 field-tested in Linac
AMS-4 detection limit is 0.02 DAC for 13N
Equivalent to MEI dose of 0.07 µSv/y for BSY dump (the worst case)
20
AMS
RDM
BSOIC

## Slide 21: LCW Heat Exchanger System for High Power Dumps
  Radiological Hazards:
        15O (2-min half-life) and 11C (20-min half-life) in LCW; decay after beam off
        3H (12.3-yr half-life, beta emitter) remained in LCW
LCLS-II-1.2-PR-0211-R0
by J. Liu
21
        Erosion/corrosion products (22Na, 54Mn, 60Co, 65Zn, etc.) and 7Be in resin/filters
        Potential leakage of radioactive LCW
        Explosion from H2 build-up in surge tank and release of radionuclides
Notes: There are over 150 site –wide separate LCW systems cooling various components: magnets, halo and protection collimators, dumps (80-100)
BAS-II, BSY Collimators (HX1), SL10, SL30 (HX2), BDE, NFF, SFF systems
Historically, during high power operations (A-line, SLC), ~35 systems have been radioactive
Require RP coverage –
All resin bottles, filters need to be monitored
Plans are to use HX2 for LCW for a new high power BSY dump and the two EBD
LCLS-I operations,
Historically

## Slide 22: LCW HX2 System for BSY Dump and 2 EBDs
22

## Slide 23
Induced Activity and Impact on LCW System Design for Three Types of Dumps | BSY Dump (volume-cooled) | 2 EBD Dumps (surface-cooled) | 3 CEBAF Dumps (internally-cooled)
3H saturation activity (185 GBq/y discharge limit to sewer) | 510 GBq @ 90 kW average power | 3,3 GBq @ 76 kW average power | EBDs: 11 GBq @76kW BSY: 18.5 GBq @90kW
7Be saturation activity @ average power | 74 GBq @ 90 kW | 0.44 GBq @ 76 kW | EBDs: 1,5 GBq @76kW BSY: 2.4 GBq @90kW
15O, 11C, 13N saturation activity @ 240 or 250 kW maximum power; 1 TVL = 17 cm concrete | 2850 GBq 15O, 703 GBq 11C & 0.56 Sv/h at 1 m | 18.5 GBq 15O, 3.7 GBq 11C & 3.5 mSv/h at 1 m | 222 GBq 15O, 48 GBq 11C & 42 mSv/h at 1 m
22Na, 54Mn, 60Co, 65Zn Maximum activities estimated from historical data 1 TVL = 23 cm concrete | 5 mSv/h at 1 m from two 400-L resin tanks (= 15 GBq 60Co) | 0.05 mSv/h at 1 m from two 400-L resin tanks (= 0.15 GBq 60Co) | 0.4 mSv/h at 1 m from two 400-L resin tanks (= 1.2 GBq 60Co)
Induced Activity in LCW for LCLS-II Dumps
23

## Slide 24
42 mSv/h @ 1 m 15O/11C in
surge tanks
0.4 mSv/h
@ 1 m resin tanks
Shielding Limit: 5 µSvh
  Radiological Controls:
      Concrete housing and shielding for underground piping
      Access controls to housing with interlocked detectors
      High capacity resin tanks with efficient exchange and disposal features
      Hydrogen recombiner to eliminate H2 explosion
      Containment of LCW leakage and management of LCW discharge with 3H
Radiological Controls of HX2 LCW for Dumps
Concrete (cm) |  | 3 CEBAF Dumps
15O/11C In LCW | Wall | 48
 | Ceiling | 60
Resin Activity | Wall | 50
 | Ceiling | 50
24

## Slide 25
Radiation from Superconducting RF Cavities (SCRF)
3D Rendering of FLUKA input model
8 Cavities with nine cells each
Quadrupole between 2 Cryomodules (16 MV/m)
M. Santana et Al. "Studies of Radiation Fields from LCLS-II Super Conducting RF Cavities”, Int. J. of Modern Physics, TBP 2015
25
SCRF Cavity

## Slide 26: Studies of Radiation from SCRF
  Radiation from field emission including capture current effects have been simulated via ‘soft’ coupling Track3P (X. Chen, L. Ge, Z. Li) and FLUKA (Nuclear Data Sheets 120, 211-214, 2014) using extensive customized code and a detailed geometry of up to 9 cryomodules.
  Results are normalized to the captured field emission, which (at 16 MV/m) should be limited to: < 10 nA/cryomodule
Longitudinal [cm]
Vertical [cm]
Longitudinal [cm]
  Tracking of field emission showers allows studies for MP/RP purposes:
  Radiation fields inside the tunnel and streaming through linac penetrations
  Radiation damage of cryomodule components, wiring, instrumentation, electronics, …
  Activation of Helium, cryomodule, tunnel
  Activation of air (equivalent to electron losses in collimators)
26

## Slide 27: Residual Dose Rate near Cryomodules
Maps of residual dose rate [mrem/h] in L2 after very long operation and 4 cool-down times
  Less than RA in general area after 1 h
10 nA field emission and 16 MV/m gradient
27

## Slide 28
Evaluated the hazards and developed mitigation/controls and monitoring to protect workers, public and environment for LCLS-II (MW, MHz, SCRF accelerator):
  Prompt radiation and radiation from SCRF field emission
  Activation of dumps, collimators, shielding, components, cooling water, cables
  Environmental impact to air, soil, groundwater,
  Monte Carlo codes such as FLUKA need to be used for activation and shielding calculations and optimization
  Subjects not covered, but important:
      Forward-peaked bremsstrahlung from BYD-EBD to FEE and NEH
      Radiation damage to undulators, devices and components
      Containment of electron beam: no passively-safe MW dump (rely on adequate cooling, distribute power in several lines, interlocks with fast response time, etc.)
      Containment of FEL:
        High energy density per pulse (eV/atom) can ablate any solid!
        High average power density (up to 600 watts at MHz)
Conclusions
28

## Slide 29: LCLS-II RP Team
  Core team members: Mario Santana (Lead), J. Bauer, Jan Blaha, James Liu, Ludovic Nicolas, Stan Mao, Shanjie Xiao
  RPD team members: Olga Ligeti, Ryan Ford
  Team profile: RP staff has experience in design and operation of large-scale of similar projects including LCLS, SSRL/SPEAR3, LCLS-II (prev. version), FACET or LHC, as well as WFO consulting
  The team gathers proficiency in the most important radiation transport simulation codes,
  RP-LCLS2 org chart
Project Leader
Mario Santana
BCS / PPS
Stan Mao
J. Bauer
Injector
Jan Blaha
XTOD – NEH,
FEL Beamlines
Shanjie Xiao
James Liu
Dumps
Mario Santana Ludovic Nicolas
Simulations
Mario Santana
Ludovic Nicolas
Shanjie Xiao
Other Areas
Mario Santana
Ludovic Nicolas
Environmental
James Liu
Jan Blaha
Areas
Functions
RSO
Sayed Rokni
BSY / BTH / UH
Mario Santana
Ludovic Nicolas
Magnet damage
Stan Mao
James Liu
Maranda Cimeno
Mario Santana
LINAC
Mario Santana
Jan Blaha
29

## Slide 30
Thank You

## Slide 31: SLAC Radiation Safety Systems
Access Control System
(keep people away from radiation)
Beam Containment System
(keep radiation away from people)
Shielding
Dump
Collimator
Radiation Safety System
Beam
Shut-Off Ion Chambers
(BSOIC)
Outside Shielding
Beam Parameter Monitors
Beam Loss Monitors
31
Protection of Safety Devices

## Slide 32: Radiation Fields within Undulators
SXR components & optics implemented in FLUKA per MAD files
High detail level near beam path, based on CAD drawings
32

## Slide 33: Radiation Fields within Undulators
Normal loss ~ line source @ 1 mradian/2π
Mis-steering 1 mradian up magnet #1
Fluence [cm2/e-]
Fluence maps used to decide detector type, settings, placement and also for calibration
33

## Slide 34: LINAC \ Gun & Injector
Courtersy H. Alvarez
Elevation view of the dose rate [mrem/h]
  Additional shielding on the maze has been designed according to preliminary dark current (P~1 W, <E>~20 MeV) average energy. Source models + other terms are being refined and shielding will be reviewed accordingly
  Penetrations to Klystron Gallery are OK
  Mitigation needed for penetration above maze

## Slide 35: Penetrations to Klystron Gallery
There are over 450 penetrations from the Linac to the upper accessible Klystron Gallery!!
170 penetrations have Line-of-sight
Penetrations for waveguides/cables are 60% open
Penetration for helium supply/return or helium release are 100% open
Multiple configurations source/penetration were studied
35

## Slide 36: Radiation Streaming Through Penetrations
There is a line-of-sight for north penetrations.
Shielding and/or exclusion area is required.
250 mSv/h
2 MW loss @ 4 GeV
South
North

## Slide 37: Solution to the Penetration Issue

## Slide 38: Direct Radiation (Skyshine) to Public
Dominated by skyshine from high-energy neutrons penetrating 4’-6’ concrete roofs of Head House and BTH
4 GeV, 48 W (limited by 7 LION pairs)
Estimated with SKYSHINE code
0.4 mrem/y at 500 m (site boundary) & 1.7 mrem/y at 350 m (guest house) from 24 h/d and 250 d/y operation
  SLAC RSS: 5 mrem/y per facility, 10 mrem/year for all facilities
If without LIONs, 1 W/m ×225 m ×2 = 450 W, 15.7 mrem/y at 350 m
ESB
Head House
BTH
RP-RPG-131105-MEM-01 by S. Mao
LCLS-II-2.7-PR-0079-R0 by J. Welch
Notes:   -Baseline design does not allow access to BTH and downstream areas during LCLS-II beam Operations
  -damping ring enclosures at Sector 1 (SC LINAC L1 beamline) are personnel exclusion zones (not shown)

## Slide 39: PMS for Direct/Skyshine Radiation Monitoring
    New PMS Neutron Detector
    Thermo WENDI2 (2 bar 3He)
    0.1 µrem/h to 10 rem/h of 252Cf
    $17K M&S
    New PMS Photon Detector
    Canberra EgoGamma GM
    1 µR/h – 1000 R/h
    $6K M&S
  Shielding design goal: 5 mrem/y to public MEI
  0.4 mrem/y at site boundary & 1.7 mrem/y at guest house from 24 h/d and 250 d/y operation and 48 W loss at BTH limited by BCS-LIONs
  8 upgraded PMS near site boundary
  One prototype purchased and to be tested in FY17
  All to be purchased in FY18 and installed in FY19
Existing PMS at SLAC
39

## Slide 40: Protection and Monitoring for Groundwater
EPA/DOE requirements: no impacts to groundwater
Design goal: shielding for BSY dump, 2 EBDs, and some halo collimators to be < EPA detection limit of 1000 pCi/L of 3H and ALARA (e.g., geomembrane)
4 new wells next to high loss points:
  South of S4
  South of S10
  In MSY, south of BSY dump
  South of 2 EBDs
Periodic sampling (part of the existing 100 wells on site)
To be installed by FY18 for pre-operation monitoring
$25K each well
Dump Lines
LCLS-II-1.2-PR-0160-R0 by J. Liu
40

## Slide 41: AMS, RDM and PMS Locations
8 PMS Locations (1 movable)
6 AMS Locations (1 movable, 13 additional sampling heads)
8 RDM Locations (2 movable)
41

## Slide 42: LCW Systems for LCLS-II Dumps and Spreader Line
HX2 and HX1 including piping to BSY are all SS316L
BSY dump LCW to HX2 West Surge Tank (SL10)
EBD LCW to HX2 East Surge Tank (SL30) after disconnect all Cu lines and de-Cu cleaning
D2 (Cu) and spreader line septa and collimators (Cu) to HX1
BSY Dump (Al)
HX2
(upgrades needed)
2 EBDs
(Al dump and SS piping)
SC-Linac Spreader Line
(Cu)
HX1
(no upgrades for RP)
SL10
SL30
Cu-LinacD2
(Cu)
42

## Slide 43: Benchmark of LCW System with JLAB
three 100-gallon resin tanks
Vented surge tank with hydrogen recombiner with H sensor (T shape on top)
3 resin tanks, 2 filter tanks, drip pan (left), sealed concrete floor for contamination control
Hall C dump LCW housing with gate alarm interlocked to beam
43

## Slide 44
 | Linac Halo Collimators | BSY Dump | BTH | BYD and 2 EBDs
Groundwater (no impact: < EPA detection limit of 1000 pCi/L 3H) | Shielding for Some collimators 2 Wells | Dump shielding 1 Well |  | Dump shielding geomembrane 1 Well
Direct Radiation (5 mrem/y, 8 PMS site-boundary) | >20’ earth | >20’ earth | 4’-6’ concrete roof | >20’ earth
Radioactive Air (10 mrem/y & 0.1 mrem/y to MEI, 1-DAC to worker) | Cryo FE monitoring 3 AMS | Dump shielding Vent for access 1 AMS | 1 AMS | Dump shielding 1 AMS
Residual Dose Rate (5 mrem/h non-RA, 1-h delay access) | Shielding for some collimators 2 RDM | Dump shielding 2 RDM | 1 RDM | Dump shielding 2 RDM
LCW System (housing, resin tanks, filter tanks, leak controls, Locked door interlocked to detector, H2 recombiner) | 4 new LCW systems for S0-S10 & HX1 | HX2 upgrades |  | HX2 upgrades
Design Criteria, Mitigation, Controls and Monitoring
44

## Slide 45: Dump Activation - Serviceability
The dump is being designed for no service, and removal at end of life
At least one spare dump will be available
Extraction of the dump would not occur before 1 week cool-down
The dump should be extracted into a ‘fresh’ shielding container
  Residual dose rate [mSv/h] for the extracted main dump stopper at 30 cm from its cylindrical surface
45

## Slide 46: Radiation Sources to XTES
Dump Shielding
BYD Magnets
e-
FEL
Spontaneous
Bremsstrahlung
Main Dump
Undulator & Dump Hall
NEH
FEE
Mirror
Mirror
FEL
Spontaneous
Secondaries from e- loss
e-
e- loss at BYD
    Gas bremsstrahlung is negligible
    No insertion device is allowed at high rep-rate (via interlock) to limit bremsstrahlung
    Spontaneous Synchrotron
    SXR: mostly cut by mirrors due to the low cut-off energy
    HXR: higher cut-off, hutch shielding needs be revisited (off-project)
Collimator
Collimator
  FEL
    SXR (0.2-1.25 keV): can be contained by beampipes and chambers
    HXR (1-25 keV): hutch shielding needs be revisited (off-project)
Main radiation source is from e- losses on BYD magnets (4 GeV, 120 W on each of SXR and HXR)
Collimator

## Slide 47: Main radiation sources in LCLS
X-Rays
Electrons
Beam Transport Hall (BTH)
Near Experimental Hall (NEH)
Front End Enclosure
(FEE)
Undulator Hall (UH)
X ray tunnel
(XRT)
Far experimental Hall
(FEH)
Single Beam Dumper
(TDKIK)
Tune-up Dump
(TDUND)
Main Dump
(MDUMP)
Collimators & other
Bremsstrahlung
3 beam dumps
Collimators & other losses
Failure modes. Configuration controls…
MULTIPLE RADIATION SOURCES

## Slide 48
Injector
50 W PIC, 1 pair
100 W LION, 2 pair
30 kW PIC, 1 pair, fast, protect stopper
375 W - 50 kW MCB
6 kW at max Allowed Beam Bower (ABP)
Linac
S1-S27
1 kW LION, 2 pair (along bypass)
100 W LION, 5 pair
5% ACM comparator to protect personnel in gallery
50 kW - 2 MW MCB
250 kW max ABP
S28-BSY
No BCS to limit losses
2 MW MCB
250 kW max ABP Dump line
120 kW max ABP per undulator line
BTHW
BTH
100 W PICs, 9x, fast, protect S BTMs
100 W PICs, 9x, fast, protect H BTMs
35 W LIONs, 7 pair
2 MW MCB
120 kW max ABP per beam
Undulator
20 W LION, 5 pair
20 W PIC, 2x, fast protect BTM
2 MW MCB, 120 kW max ABP per beam
Dump
5% ACM Comparator 2x, purpose?
100 W LION, 3 pair
100 W PICs, 10x, fast, protect coll. and safety dump
2 MW MCB, 120 kW max ABP per beam
MUON WALL
FCDG0DU
100 MeV
SC
BEGGUNB
0.75 MeV
SPEC1
135 MeV
GSPEC1
6 MeV
Cu
GUN1
6 MeV
DIAG0
BX01
BXSP1H
BXG
ENDDMPH
4 or 15 GeV
(DUMPH)
XPP
CXI
XCS
MEC
ENDDMPS
4 GeV
(DUMPS)
SXR
D2B, 4 GeV
L0
L1
L2
L3
L0
L1
D2, 4 or 15 GeV
FCG1
6 MeV
L3
BC2
5 GeV
TD11
250 MeV
L2
D10
DUMPBSY 4 GeV
SXR
HXR
(TDKICKC)
15 GeV
(BYKIKC)
TDUND15 GeV
TDUNDB
4 GeV
TDKIK
IMBCSDOG
IMBP28
IMSP1D
IMSP1H
IMSP1S
IMBCSC0
BYKIK
IMDUMP
IMUNDOB
STSP6HA*
STSP6HB
STSP6HC
STSP6HD
STSP5S
ST60
ST61
STBP34A
STBP34BSTBP34C
Comparator
IM01
IM11B
IM21B
IMSP0S
IMBCS4B
IMSP0H
IM31
IMBCS1
IMBCS2
IM36
IMUNDI
IMUNDO
IMBCS3
IMBCS4
IMBSY34
IMBSY3
IMBSY2
IMBSY1
IMSP0D
IMSP2D
BCS ACM
Calibration ICT
KEY
Xray Stopper
e- Stopper
e- Dump
Comparator
Comparator
STC0
LCLS toroid
BCS Requirements

## Slide 49: Estimated Beam Loss by Area (J. Welch)
See PRD: LCLSII-2.7-PR-0079