## Slide 1: Booster 误差效应及轨道校正的初步研究
魏源源
2016年4月22日

## Slide 2: Magnet Field errors
The earth field outside the magnet: Bx=0.550.026Gs, By=0.450.027Gs, Bz=0.250.03 Gs  B= 0.80.04Gs
Inside the magnet, By=7.00.05Gs is dominated by residual field, Bx=0.40.04Gs reduced due to the shielding while Bz=0.250.03 Gs.
The 24h field stability (sB) for 30 Gs-150 Gs is about (1-2)10-3;
The magnet ramps smoothly around the low fields with accuracy better than 110-3;
The field error DBy/By  10-4 for x(-60, 60) mm and By(30-150) Gs
Dipole magnets 〈ΔB/B〉 < 2×10-3 Quadrupole magnets 〈ΔK/K〉 < 5×10-4
Booster Magnet Field errors

## Slide 3
Component | 〈y〉 (mm) | 〈x〉 (mm) | 〈tilt〉 (mrad)
Dipole magnets | ±0.2 | ±0.3 | ±0.1
Quadrupole magnets | ±0.1 | ±0.1 | ±0.1
Alignment parameters

## Slide 4: Orbit Distortion with Field Errors and Alignment
60◦、70m cell lattice
(130.47,130,45), 6GeV
Simulate with AT

## Slide 5
BB
BPM
BPM
HCOR
VCOR
BPM：784，H&V
HCOR: 392
VCOR: 392
Orbit Correction System

## Slide 6: Correction result with 2 sets of errors

## Slide 7: To do list
Optimize the distribution of correction components
Consider the effect of earth field ?
Consider the field components of the magnets.