## Slide 1: CEPC parameter choice and partial double ring design
Dou Wang, Jie Gao, Feng Su, Yuan Zhang, Jiyuan Zhai, Yiwei Wang, Bai Sha, Huiping Geng, Tianjian Bian, Na Wang, Xiaohao Cui, Zhe Duan, Yuanyuan Guo

## Slide 2
bypass (pp)
bypass (pp)
Advantage:
Avoid pretzel orbit
Accommodate more bunches at Z/W energy
Increase luminosity and reduce beam power with crab waist collision

## Slide 3: Machine constraints / given parameters
Energy E0
Circumference C0
NIP
Beam power P0
y*
Emittance coupling factor 
Bending radius 
Piwinski angle 
y enhancement by crab waist Fl ~1.5 (2.6)
Energy acceptance (DA)
Phase advance per cell (FODO)

## Slide 4: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 5: Parameter choice – step 1
Fl: y enhancement by crab waist, ~ 1.5.
Beam-beam limit:

## Slide 6: Parameter choice – step 2

## Slide 7: Parameter choice – step 3
-- phase advance/cell, -- bending angle/cell.
Estimate :
BS life time: 30 min
y:

## Slide 8: Parameter choice – step 4

## Slide 9: Parameter choice – step 5
Hour glass effect:
Effective bunch length: overlap area of colliding bunches

## Slide 10: Parameter choice – step 6
Energy acceptance from RF:
Vrf , s

## Slide 11: Parameter choice – step 7
Beam lifetime due to radiative Bhabha scattering
Beam lifetime due to Beamstrahlung
*V.I. Telnov, "Issues with current designs for e+e- and gammagamma colliders“, PoS Photon2013 (2013) 070. https://inspirehep.net/record/1298149/files/Photon%202013_070.pdf
HOM power per cavity
HOM loss factor:

## Slide 12: parameter for CEPC partial double ring （wangdou20160420）
 | Pre-CDR | H-high lumi. | H-low power | H-20MW | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 2.6 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 2.66 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 29 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 6.8 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 20 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.267/0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 2.06/0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 23.4/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.032 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.84 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 1.29 | 3.09 | 3.09

## Slide 13: CEPC Higgs Luminosity vs beam power

## Slide 14: CEPC single ring parameter-54km
 | H |  | Z | 
 | Pre-CDR | Low-HOM |  | 
Number of IPs | 2 | 2 | 2 | 
Energy (GeV) | 120 | 120 | 45.5 | 
Circumference (km) | 54 | 54 | 54 | 
SR loss/turn (GeV) | 3.1 | 3.1 | 0.062 | 
Ne/bunch (1011) | 3.79 | 1.0 | 0.13 | 
Bunch number | 50 | 187 | 4800 | 100
Beam current (mA) | 16.6 | 16.6 | 55.5 | 1.1
SR power /beam (MW) | 51.7 | 50 | 3.45 | 0.072
Bending radius (km) | 6.1 | 6.1 | 6.1 | 
Momentum compaction (10-5) | 3.4 | 3.4 | 3.4 | 
IP x/y (m) | 0.8/0.0012 | 0.06/0.001 | 0.4/0.0012 | 
Emittance x/y (nm) | 6.12/0.018 | 6.13/0.018 | 0.9/0.018 | 
Transverse IP (um) | 69.97/0.15 | 19.2/0.13 | 18.9/0.15 | 
x/IP | 0.118 | 0.031 | 0.072 | 
y/IP | 0.083 | 0.074 | 0.028 | 
VRF (GV) | 6.87 | 6.87 | 0.68 | 
f RF (MHz) | 650 | 650 | 650 | 
Nature z (mm) | 2.14 | 2.13 | 1.5 | 
Total z (mm) | 2.65 | 2.4 | 1.5 | 
HOM power/cavity (kw) | 3.6 | 1.0 | 0.55 | 0.01
Energy spread (%) | 0.13 | 0.13 | 0.05 | 
Energy acceptance (%) | 2 | 1.5 |  | 
Energy acceptance by RF (%) | 6 | 6.1 | 4.5 | 
n | 0.23 | 0.21 | 0.028 | 
Life time due to beamstrahlung_cal (minute) | 47 | 46 |  | 
F (hour glass) | 0.68 | 0.66 | 0.82 | 
Lmax/IP (1034cm-2s-1) | 2.04 | 2.1 | 1.04 | 0.022

## Slide 15: parameter for CEPC PDR-88km （wangdou20160329）
 | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 80 | 45.5
Circumference (km) | 88 | 88 | 88 | 88
SR loss/turn (GeV) | 2.0 | 2.0 | 0.4 | 0.04
Half crossing angle (mrad) | 15 | 15 | 15 | 15
Piwinski angle | 2.0 | 2.6 | 6.3 | 12.1
Ne/bunch (1011) | 1.75 | 1.53 | 0.565 | 0.24
Bunch number | 257 | 176 | 1150 | 6600
Beam current (mA) | 24.5 | 14.7 | 35.5 | 86.5
SR power /beam (MW) | 50 | 30 | 14.3 | 3.6
Bending radius (km) | 9.0 | 9.0 | 9.0 | 9.0
Momentum compaction (10-5) | 1.9 | 1.5 | 1.9 | 1.9
IP x/y (m) | 0.36/0.0011 | 0.36/0.0011 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 1.63/0.005 | 1.15 /0.0035 | 0.76/0.0023 | 0.24/0.0011
Transverse IP (um) | 24.4/0.074 | 20.5/0.062 | 8.7/0.048 | 4.9/0.033
x/IP | 0.04 | 0.033 | 0.0053 | 0.0033
y/IP | 0.091 | 0.091 | 0.061 | 0.06
VRF (GV) | 3.1 | 2.57 | 0.57 | 0.074
f RF (MHz) | 650 | 650 | 650 | 650
Nature z (mm) | 2.7 | 2.94 | 3.55 | 3.93
Total z (mm) | 3.25 | 3.53 | 3.65 | 4.0
HOM power/cavity (kw) | 2.2 | 1.1 | 0.99 | 0.97
Energy spread (%) | 0.1 | 0.1 | 0.07 | 0.04
Energy acceptance (%) | 1.5 | 1.4 |  | 
Energy acceptance by RF (%) | 3 | 2.1 | 1.4 | 0.9
n | 0.29 | 0.31 | 0.27 | 0.2
Life time due to beamstrahlung_cal (minute) | 32 | 40 |  | 
F (hour glass) | 0.78 | 0.82 | 0.94 | 0.97
Lmax/IP (1034cm-2s-1) | 4.18 | 2.63 | 3.52 | 5.02

## Slide 16: parameter for CEPC PDR-100km （wangdou20160329）
 | H-high lumi. | H-low power | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 
Energy (GeV) | 120 | 120 | 80 | 45.5 | 
Circumference (km) | 100 | 100 | 100 | 100 | 
SR loss/turn (GeV) | 1.7 | 1.7 | 0.33 | 0.034 | 
Half crossing angle (mrad) | 15 | 15 | 15 | 15 | 
Piwinski angle | 2.0 | 2.83 | 8.65 | 15.8 | 
Ne/bunch (1011) | 1.43 | 1.22 | 0.42 | 0.165 | 
Bunch number | 436 | 307 | 2400 | 15800 | 182260
Beam current (mA) | 30 | 18 | 48.7 | 125.3 | 1449.7
SR power /beam (MW) | 50 | 30 | 16.0 | 4.3 | 50
Bending radius (km) | 11 | 11 | 11 | 11 | 
Momentum compaction (10-5) | 1.8 | 1.4 | 1.4 | 1.3 | 
IP x/y (m) | 0.297/0.0011 | 0.3/0.0011 | 0.1/0.001 | 0.1/0.001 | 
Emittance x/y (nm) | 1.63/0.0049 | 1.03/0.003 | 0.46/0.0014 | 0.14/0.00065 | 
Transverse IP (um) | 22/0.074 | 17.6/0.59 | 6.8/0.037 | 3.8/0.026 | 
x/IP | 0.033 | 0.025 | 0.003 | 0.002 | 
y/IP | 0.083 | 0.083 | 0.055 | 0.054 | 
VRF (GV) | 3.1 | 2.25 | 0.41 | 0.053 | 
f RF (MHz) | 650 | 650 | 650 | 650 | 
Nature z (mm) | 2.45 | 2.77 | 3.8 | 3.94 | 
Total z (mm) | 2.94 | 3.33 | 3.9 | 4.0 | 
HOM power/cavity (kw) | 2.3 | 1.1 | 0.98 | 0.97 | 11.3
Energy spread (%) | 0.1 | 0.1 | 0.065 | 0.037 | 
Energy acceptance (%) | 1.46 | 1.4 |  |  | 
Energy acceptance by RF (%) | 3.5 | 2.2 | 0.9 | 0.7 | 
n | 0.27 | 0.28 | 0.26 | 0.18 | 
Life time due to beamstrahlung_cal (minute) | 40 | 49 |  |  | 
F (hour glass) | 0.8 | 0.85 | 0.96 | 0.985 | 
Lmax/IP (1034cm-2s-1) | 4.75 | 3.01 | 4.46 | 6.59 | 76.4

## Slide 17: CEPC PDR Luminosity vs circumference
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 18: 100km CEPC PDR vs Fcc-ee
PHOM,CEPC=11.3 kw
The large difference of Z is due to the constraint for RF HOM power.
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 19: CEPC PDR y vs circumference (Higgs)

## Slide 20: CEPC PDR bunch number vs circumference
Higgs

## Slide 21: CEPC PDR bunch charge vs circumference

## Slide 22: CEPC PDR energy acceptance vs circumference (Higgs)

## Slide 23: CEPC PDR SR loss vs circumference

## Slide 24
CEPC Partial Double Ring Lattice

## Slide 25: Arc redesign-lower emittance
Length of FODO cell: 47.2m
Phase advance of FODO cells: 60/60 degrees
Emittance: 7.9nm, p=5.38E-5
Bunch length: 2.3mm
Length of FODO cell: 37.5m
Phase advance of FODO cells: 60/60 degrees
Emittance: 4.3nm , p=2.25E-5
Bunch length: 3.3mm

## Slide 26: Low emittance arc – 90/60
Length of FODO cell: 37.5m
Phase advance of FODO cells: 90/60 degrees
Emittance: 2.3nm, p=1.07E-5
Bunch length: 3.1mm
BDIS1
BDIS2
Dispersion supressor:
Angle(BDIS1)=3.583724E-3
Angle(BDIS2)=-8.598108E-4
Angle(B0)=2.723923E-3
B0
B0

## Slide 27: Low emittance arc – 90/90
Length of FODO cell: 37.5m
Phase advance of FODO cells: 90/90 degrees
Emittance: 2.3nm, p=1.02E-5
Bunch length: 3.1mm
BDIS1
BDIS2
Dispersion supressor:
Angle(BDIS1)=3.50284406482E-3 Angle(BDIS2)=-7.78931580723E-4 Angle(B0)=2.723923E-3
B0
B0

## Slide 28: Non-interleave sextupoles in arc (90/90 FODO)

## Slide 29: Partial double ring FFS design with crab sextupoles
Crab sextupole
Critical energy: Ec=190 keV
Dipole strength: B=0.019 T
Betax=0.25m
Betay=0.00136m
K2hs=26.8 m-3
K2vs=32.2 m-3
IP
The second FFS sextupoles of the CCS-Y section work as the crab sextupoles.

## Slide 30: Final doublet
L*=1.5m
L(QD0)=1.46m, G(QD0)=-200T/m
L(QF1)=1.29m, G(QF1)=97T/m
L0=1.5m
IP

## Slide 31: Crab sextupole strength
The crab sextupole should be placed on both sides of the IP in phase with the IP in the horizontal plane and at π/2 in the vertical one.
x=2, y=2.5
13% strength of main sextupoles

## Slide 32: Combine with partial double ring lattice
30 mrad
10 m

## Slide 33: DA of the whole ring (arc+PDR+bypass+FFS)
Arc sextupole: 2 groups
Su Feng 2016.03.30
Crab sextupoles - off

## Slide 34: Chromaticity correction in FFS
Fine tuning the phase of main sextupoles.
Weak sextupoles are -10% of main sextupoles to correct the sextupoles’ length effect*
K2hs=-6.99 m-3
K2vs=32.16 m-3
*A. Bogomyagkov, S. Glukhov, E. Levichev and P. Piminov, “effect of the sextupole finite length on dynamic aperture in the collider final focus”, arXiv:0909.4872v1 [physics.acc-ph]

## Slide 35: DA after chromaticity correction
Arc sextupole: 2 groups
DA (on-momentum): 27x  57y
DA (0.5%): 2x  2y
Crab sextupoles - off

## Slide 36: Higher order chromaticity correction in FFS
Quadrupole pair, sextupole pair, octupole pair.

## Slide 37: summary
A consistent calculation method for CEPC parameter choice with carb waist scheme has been created. Larger ring has the potential to reach higher luminosity.
Based on partial double ring scheme, we can get higher luminosity (50%) keeping Pre-CDR beam power or to reduce the beam power (30 MW) keeping same luminosity.
For “H-high lumi” mode, the HOM power per cavity can not be reduced under 1kw. The minimum value is about 2 kw.
Based on partial double ring scheme, we get a set of Z parameter with 3.1*1034cm-2s-1 luminosity using 1100 bunches.
CEPC single ring scheme is neither easy to reduce cavity HOM power for Higgs nor to accommodate more bunches for Z.
FFS with crab sextupoles and lower emittance arc has been designed. On-momentum DA of whole ring is good enough and the optimization of DA bandwidth is ongoing.

## Slide 38
Thanks！