## Slide 1: ATLAS phase II strip tracker upgrade
Zhijun Liang
IHEP, CAS
Tsinghua University

## Slide 2: Outline
Introduction to ATLAS tracker phase II upgrade
ALTAS tracker phase II upgrade activity in China
  Silicon strip detector module R & D
  CMOS sensor R & D
Summary

## Slide 3: High luminosity LHC
In ten year, CERN will upgrade Large
Hadron collier (LHC) to high luminosity LHC
Higgs precision measurements
new physics search
HL-LHC
LHC
LHC
High luminosity LHC

## Slide 4: ATLAS tracker phase-II upgrade
ATLAS need to build a new full-silicon tracking detector (ITK) to handle high luminosity LHC (HL-LHC) upgrade
Radiation hardness requirement
In ATLAS phase II upgrade
（ Equivalent neutron flux ）
2×1015 Neq/cm2
Present ATLAS strip detector is designed only up to 2×1014 Neq/cm2

## Slide 5: Timeline of ATLAS strip detector upgrade
End of 2016 , technical design report（TDR）
2018-2019 pre-production
2020-2023 production

## Slide 6: Research grant for ATLAS ITK phase II upgrade
ATLAS China group got the research grant supported by Ministry of Science and Technology of China (MOST): 13 million Yuan
This grant covers the following R & D and small scale production: Front-end electronic readout ASIC design for ATLAS strip detector
Silicon strip detector module prototyping and production
CMOS-based silicon strip detector performance study

## Slide 7: Silicon Strip Detector Module Production
China is going to build 1000 strip modules in phase 2 upgrade
  Contribute 5% of ATLAS phase 2 strip detector
  covers large area of detector : 10m2
ATLAS Strip detector Phase 2 upgrade | total | ATLAS China group expected contribution
Area | 190 m2 | 10 m2
Modules | 20,000 | 1000

## Slide 8: Stave/Petal concept
Stave/Petal concept

## Slide 9: Silicon detector module
Basic unit of strip detector: module
  Silicon sensor
  PCB hybrid controller (readout ASIC + controller electronic)
  Power board

## Slide 10: Frontend electronic
China contribute to the readout ASIC prototyping
  L0 trigger has higher requirement on trigger rate
  Redesign the digital part of readout ASIC
  Collaborate with CERN electronics group and University of Pennsylvania
  More details in Weiguo’s talk
HCC
Hybird controler
ABC
ABC
ABC
ABC
ABC
ABC
ABC
ABC
ABC
ABC
Readout chip
HCC*
Hybird controler
ABC*
ABC*
ABC*
ABC*
ABC*
ABC*
ABC*
ABC*
ABC*
ABC*
Readout chip
STAR
analogue
Digital
Power control
prototype of readout ASIC:
ABCN130 chip

## Slide 11: Beam test for ATLAS upgrade
contribute to beam test DAQ framework development (EU-DAQ)
Active in beam test study : measure S-curve of module and hit efficiency
beam test result from ATLAS China included in ATLAS upgrade TDR.
Before irradiation
After irradiation
S-surve of strip module before/after irradiation
S/N after irradiation is estimated to be about 20

## Slide 12: Silicon strip detector module prototyping and production
contribute to module R & D
Manufacturing module building tool
Readout chip
Hybrid PCB
Hybrid controller
Detector Module
sensor
Power board
Detector module
ASIC Pickup tool

## Slide 13
Made by
Liverpool
Made by
IHEP
Prototype module made by China group
Silicon strip detector module prototyping
participate in module tooling R & D
  The planarity tool made in China is within 20 μm
  Meet the design requirement
Contribute to module prototyping.

## Slide 14: Export control
Key Radiation hard chip, embargo against China
  Frontend readout chip ABC130
  hybrid control chip HCC,
  monitoring chip AMAC,
  DC-DC chip FESAT
Embargo exemption：
  CERN hires layers to apply for embargo exemption for many countries.
  Prof Joao Costa is contact for about embargo exemption application for China
International Collaboration：
  Make use of facility aboard from our collaborators to train our people.
  Learn the key technology

## Slide 15: International Collaboration
collaborate with Rutherford Appleton Lab(RAL) in module R & D
ATLAS China group visit RAL in 19 Sep,2016
  Discuss the collaboration in ATLAS upgrade project

## Slide 16: Laboratory
State key lab has a 150 m2 Thousand grade clean room
With probe station, wire bonder for detector R & D
BJ 820
Flash CNC 300

## Slide 17: CMOS silicon strip sensor R & D
China contribute to new detector technology R & D: CMOS strip sensor
  CMOS technology has been widely used in digital camera, cell phone
  The advantage of CMOS sensor:
  Lower material budget, Monolithic, has potential to reduce the cost
CMOS sensor is the alternative solution for ATLAS strip upgrade
  First time using CMOS technology in Strip tracker
母板
子板
FPGA

## Slide 18
AMS 350 technology
  Pixel size: 40X800 μm
  Digital readout
  Frontend electronic (Amplifier) intergated on sensor
2016-12-17
18
CMOS silicon strip sensor R & D
EPJC 70 (2010) 723

## Slide 19
2016-12-17
19
Nuclear Instruments and Methods in Physics Research A 831 (2016) 156–160
Contribute to testing CMOS sensor
  First measurement on CMOS amplifier performance after irradiation.
  ATLAS china group member is the first author and corresponding author
CMOS silicon strip sensor R & D

## Slide 20: CMOS silicon strip sensor R & D
CMOS testing in local lab
Laser induced Scanning Transient Current Technique (Laser TCT)
Testing CMOS strip sensor with laser TCT in Laboratory
Electronic and DAQ system
Laser TCT system
IHEP Laboratory
Mother Board
FPGA
Laser

## Slide 21: ABCN’ readout chip and prototype module for CMOS sensor
Prototyping a CMOS strip detector module in next two year.
Need a new readout chip ABCN’
  Mainly to handle buffering of data
3 interested parties: Oxford, IHEP, UBC

## Slide 22: ABCN’ FPGA emulator 1/2
ABCN’ readout chip R & D, Before CMOS sensor is ready
  We need to emulator to emulate the CMOS sensor output
  IHEP and USTC team make FPGA emulator : Two versions
    Fixed pattern: put out the same pattern of hits every 25ns
    Pseudo-random pattern: generate random hit pattern

## Slide 23: ABCN’ frontend readout chip
China contribute to ABCN’ chip development
  Buffering the digital data from CMOS sensor
  Full Digital readout chip
  Back-end readout : Nexys Video FPGA
power
Nexys Video
FPGA
ITSDAQ control and readout
ABCN’
DAQ s/w
SCTDAQ s/w with adaptations
Array 1, 128 strips
Test structures
Array 2, 128 strips
Array 3, 128 strips
CHESS-2
logical blocks within FPGA
Digital daughterboard
Adaptor board
A
B
B is FMC
A is an edge connector

## Slide 24: Summary
ATLAS tracker upgrade activity in China
  R & D for key technology
    High spatial resolution
    Large area detector
    Radiation hardness
  Plan to make significant contribution in ATLAS upgrade project

## Slide 25: Backup
IHEP activity in ATLAS tracker upgrade
Front-end electronic readout ASIC design for ATLAS strip detector
Silicon strip detector module prototyping and production
CMOS-based silicon strip detector performance study

## Slide 26: Silicon detector module
Basic unit of strip detector: module
  Silicon sensor
  PCB hybrid controller (readout ASIC + controller electronic)
  Power board
Readout ASIC
Module controller
Power board
Silicon sensor

## Slide 27: Digital electronic design in readout ASIC
IHEP contribute to redesign of digital part of readout ASIC chip
setup verification system to verify the ASIC design (based on SystemVerilog )
IEEE RT2016 poster（Libo Cheng）
TWEPP2016 talk（Weiguo Lu）
Next steps :
1.finalizing the digital part of ASIC design and simulation
2.Plan to test the performance of readout ASIC next year

## Slide 28: 芯片禁运问题
目前硅微条探测器模块芯片，包括读出芯片ABC、控制芯片HCC、电流监控芯片AMAC、DC-DC芯片FESAT以及高压转换芯片因为抗辐照原因，均对中国禁运。
积极申请禁运豁免：ATLAS和CMS合作组内多个国家面临相同问题，CERN专门聘用律师统一协调针对技术（GF/IBM CMOS工艺）申请禁运豁免（出口许可）。高能所为ATLAS合作组代表单位，高能所Joao Costa教授被任命为ATLAS方联络人。
国际合作：在禁运问题完全解决之前，积极利用国际合作，借用国外合作单位先进设施开展预研工作。充分锻炼人才队伍，为后期回到国内开展建造任务奠定扎实基础。

## Slide 29: 硅微条探测器模块
硅微条径迹探测器最基本机械单元，由硅微条传感器、复合PCB控制板（读出电子学ASIC芯片+控制芯片）、电源板等构成，使用银胶或紫外凝胶粘合，通过打线实现电气连接。
前端读出电子学ASIC芯片
模块控制芯片
高、低压电源控制板
硅微条探测器模块及主要组件
硅微条传感器