## Slide 1: CEPC parameter choice and partial double ring design
Dou Wang, Jie Gao, Feng Su, Yuan Zhang, Jiyuan Zhai, Yiwei Wang, Bai Sha, Huiping Geng, Tianjian Bian, Na Wang, Xiaohao Cui
CEPC AP meeting, 2016.04.29

## Slide 2: Machine constraints / given parameters
Energy E0
Circumference C0
NIP
Beam power P0
y*
Emittance coupling factor 
Bending radius 
Piwinski angle 
y enhancement by crab waist Fl ~1.5 (2.6)
Energy acceptance (DA)
Phase advance per cell (FODO)

## Slide 3: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 4: parameter for CEPC partial double ring （wangdou20160420）
 | Pre-CDR | H-high lumi. | H-low power | H-20MW | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 2.6 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 2.66 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 29 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 6.8 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 20 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.267/0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 2.06/0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 23.4/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.032 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.84 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 1.29 | 3.09 | 3.09

## Slide 5: parameter for CEPC partial double ring （wangdou20160428）
 | Pre-CDR | H-30 mrad | H-40 mrad | H-50 mrad | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 20 | 25 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.15 | 3.0 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.88 | 3.83 | 0.74 | 0.46
Bunch number | 50 | 67 | 66 | 50 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 16.9 | 16.9 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 50 | 50 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.45/0.00136 | 0.54/0.00164 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.1 /0.0064 | 2.1/0.0064 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 30.7/0.093 | 33.7/0.1 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.046 | 0.035 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 4.01 | 3.55 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 2.6 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 3.3 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 2.5 | 3.0 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 3.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.38 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 34 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.84 | 0.89 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 3.01 | 2.66 | 3.09 | 3.09

## Slide 6: CEPC Higgs Luminosity vs crossing angle-50MW

## Slide 7: CEPC Higgs Luminosity vs beam power

## Slide 8: CEPC PDR Luminosity vs circumference
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 9: Partial double ring FFS design with crab sextupoles
Crab sextupole
Critical energy: Ec=190 keV
Dipole strength: B=0.019 T
Betax=0.25m
Betay=0.00136m
K2hs=26.8 m-3
K2vs=32.2 m-3
IP
The second FFS sextupoles of the CCS-Y section work as the crab sextupoles.

## Slide 11: Higher order chromaticity correction in FFS
Quadrupole pair, sextupole pair, octupole pair.

## Slide 12
Thanks！