## Slide 1: CEPC Booster 误差效应及轨道校正的初步研究
魏源源 张闯 崔小昊 边天剑
2016年4月29日

## Slide 2: Magnet Field errors
The earth field outside the magnet: Bx=0.550.026Gs, By=0.450.027Gs, Bz=0.250.03 Gs  B= 0.80.04Gs
Inside the magnet, By=7.00.05Gs is dominated by residual field, Bx=0.40.04Gs reduced due to the shielding while Bz=0.250.03 Gs.
The 24h field stability (sB) for 30 Gs-150 Gs is about (1-2)10-3;
The magnet ramps smoothly around the low fields with accuracy better than 110-3;
The field error DBy/By  10-4 for x(-60, 60) mm and By(30-150) Gs
Dipole magnets 〈ΔB/B〉 < 2×10-3 Quadrupole magnets 〈ΔK/K〉 < 5×10-4
Booster Magnet Field errors

## Slide 3
Component | 〈y〉 (mm) | 〈x〉 (mm) | 〈tilt〉 (mrad)
Dipole magnets | ±0.2 | ±0.3 | ±0.1
Quadrupole magnets | ±0.1 | ±0.1 | ±0.1
Alignment parameters

## Slide 4: Orbit Distortion with Field Errors and Alignment
60◦、70m cell lattice
(130.47,130,43), 6GeV
Simulate with AT

## Slide 5
BB
BPM
BPM
HCOR
VCOR
BPM：782，H&V
HCOR:
VCOR:
Orbit Correction System

## Slide 6: Correction results
校正前水平轨道
校正前垂直轨道
校正后水平轨道
校正后垂直轨道

## Slide 7: Earth field effect
Earth field will cause the change of beam energy
Consider the earth field of drift -> Δp/p~0.442%
Earth field of drift
Earth field of drift & errors

## Slide 8: Earth field effect
Consider the earth field all along the ring -> Δp/p~2%
Earth field along the ring
Earth field of drift+errors

## Slide 9: To do list
Consider the effect of earth field including Bx and Bz
Consider the field components of the magnets.