## Slide 1: TPCs for neutron
Yulan Li
Tsinghua University
TPC tracker detector technology mini-workshop
2016-9-1
IHEP, Beijing, China

## Slide 2
nTPC: TPC as a fast neutron spectrometer
  Working principle
  Performance simulation
  System design
  Neutron beam test results
nimTPC: TPC as a fast neutron imaging detector
  Working principle
  Simulation
Outline

## Slide 3
  Energy of recoil proton (): total charge of all the pads other options: track length, dE/dx …
  Slope of proton track : track fitting
nTPC Working Principle: Elastic Scattering with H

## Slide 4
Performance Simulation (1)
fitting
Energy deposited in TPC
Proton’s recoil angle
Initial energy of proton
vs.
Neutron’s energy spectrum
=5MeV
Ar-C2H6(50-50)
distribution

## Slide 5
Performance Simulation (2)
Simulation result of energy resolution and efficiency
Huang Meng, Li Yulan, Deng Zhi, et al. A fast neutron spectrometer based on GEM-TPC. 2012 IEEE NSS-MIC Conference Records, 146-148.
Huang Meng, Li Yulan, Deng Zhi, et al. The characteristics of signals from nTPC and its application in background suppression. 2013 IEEE NSS-MIC Conference Records, 1-3.
Niu Libo, Li Yulan, Huang Meng, et al. Track reconstruction based on Hough-transform for nTPC. Chinese Physics C, 2014, 38 (12): 126201.
Niu Libo, Li Yulan, Huang Meng, et al. Adaptive multitrack reconstruction for particle trajectories based on fuzzy c-regression models. Chinese Physics C, 2015, 39 (3): 38-44.

## Slide 6
System Design
Gain of 3GEM(P30)
Pad
TU-TPC
Gas and drift field optimizing
Detector | Size | Φ30cm×50cm (TU-TPC)
 | Gas | Ar-CH4(70-30) or Ar-C2H6(50-50)
 | Drift field | ~200V/cm
 | Readout detector | 3GEM
 | pad | ring, 5mm×2mm
ASIC | Shaping time | 80ns
 | Gain | 2mV/fC
DAQ | Sampling parameters | 12bit，25MHz
 | Triggering Mode | Single trigger
Data processing | Platform | Labview
 | Mode | Online
nTPC design parameters
Based on: TU-TPC
Huang Meng, Li Yulan, Niu Libo, et al. Design of a neutron-TPC prototype and its performance evaluation based on an alpha-particle test. Chinese Physics C, 2015, 39 (8): 086003.

## Slide 7
Neutron Beam Test - Setup
@ Key Laboratory of Nuclear Data Measurement and Evaluation Technology, China Institute of Atomic Energy

## Slide 8
Discrimination of Background Events (1)
edge protons:
only part energy deposition collected
Discrimination method:
Starting position of track
Associated γ：
12C and 40Ar
Protons produced by the scattered neutrons
 | Source | Discrimination method
1H | Collision of scattering neutrons with working gas | Starting position
12C 40Ar | Collision of incident neutrons with working gas | 
e- | Interaction of gamma with working gas | 
1H | Edge protons | 
 | Source | Discrimination method
1H | Collision of scattering neutrons with working gas | Starting position
12C 40Ar | Collision of incident neutrons with working gas | 
e- | Interaction of gamma with working gas | 
1H | Edge protons | 

## Slide 9
Discrimination of Background Events (2)
Track length(mm) vs. deposited energy(pC)
Deposited energy(pC) vs. recoil angle(Degree)

## Slide 10
Reconstruction of Neutron Spectrum
Deposited energy vs.
recoil angle θ
Reconstructed
neutron spectrum
Charge response vs. neutron energy
1.2MeV
1.81MeV
2.5MeV
Peak=22.8pC
Peak=39.7pC
Peak=30.3pC

## Slide 11
Energy Resolution vs Detection Efficiency (1)
=2.5MeV
Cutting angle
Track fitting length (relative）
=2.5MeV
Starting position
Cutting in starting position:
Energy resolution from 11.7% to 9.1% (FWHM)
Huang Meng, Li Yulan, Niu Libo, et al. Analysis and optimization of energy resolution of neutron-TPC. NUCLEAR SCIENCE AND TECHNIQUES, 2015, 26 (040602).

## Slide 12
Energy Resolution vs Detection Efficiency
Optimized results of the neutron energy resolution
Due to that the effective readout pads only covers about 45°angle range, the detection efficiency of the neutron-TPC could be improved further by add more channel.
Neutron energy | recoil angle cutting | Track fitting part (ratio) | Starting position | Energy resolution(FWHM) |  | Detection efficiency
 |  |  |  | Simulation | Experiment | 
1.2 MeV | 30° | 0-1 | rst<10mm | 15.7% | 14.6% | 3.6×10-4
1.81 MeV | 30° | 0.1-0.6 | rst<5mm | 10.3% | 8.3% | 6.4×10-4
2.5 MeV | 25° | 0.1-0.4 | rst<5mm | 7.0% | 6.3% | 1.4×10-5

## Slide 13
nTPC: TPC as a fast neutron spectrometer
  Working principle
  Simulation
  System design
  Neutron beam experiment results
nimTPC: TPC as a fast neutron imaging detector
  Working principle
  Simulation
Outline

## Slide 14
①line-line mode
p'
n0
p
n
GEM
Outer-ring neutron convertors
α
n’
Energy, direction of both p and p’ measured:
Both energy and direction of n0 can be determined.
Energy, direction of p, and start position of p’ measured:
Direction of n0 limited to <90°in a plane.
②line-point mode
TPC for Fast Neutron Imaging: Working Principle
p'
n0
p
n
GEM
α
n’
Outer-ring neutron convertors
Event reconstruction:
Time windows:
p⊥n
p: direction of track
n: vector between positions of 2 events

## Slide 15
Φ30cm×50cm TPC filled with Ar-C2H6(50-50), no outer-ring neutron converters.
2MeV neutrons incidented from the axial direction.
①line-line
FWHM~8.0%
@2.5MeV
①line-line
FWHM~4.8°
@2.5MeV
②line-point
FWHM~8.9°@2.5MeV
Efficiency: 1.38×10-5
Efficiency: 3.31×10-6
TPC for Fast Neutron Imaging: Simulation

## Slide 16
Conclusion
nTPC is developed as a fast neutron spectrometer;
High energy resolution with relatively high efficiency;
Energy resolution reach 7.0%(FWHM) @ 2.5 MeV;
Detection efficiency > 10-5 @2.5MeV;
nimTPC for fast neutron imaging is under developed;
Angle resolution ~4.8°(FWHM) @2.5MeV in simulation;
Total detection efficiency~1.7×10-5@2.5MeV in simulation.

## Slide 17: Thanks a Lot!!