## Slide 1: Micromegas module for ILC-TPC
A decade of R&D
Paul COLAS, CEA Saclay
Early tests
Magnetic field
charge spreading
Ion Back Flow
Single-module tests
Micromegas development
Seven-module test
Integration issues : electronics, cooling
TPC Tracker Detector Technology Mini Workshop, Beijing, September 1, 2016

## Slide 2: Introduction
TPCs have good records in e+e- physics (ALEPH and DELPHI at LEP), and showed adaptability to dense high-rate environment (STAR, ALICE)
MPGDs yield a promise for improvement : smaller structures lead to smaller ExB effects, ion feedback can be naturally suppressed, light construction of large area is possible.

## Slide 3: Micromegas
S1
S2
S2/S1 = Edrift/Eamplif ~ 200/60000= 1/300
Charged tracks cross a medium with a low (drift) field : 200 V/cm.
Ionization electrons drift to a mesh maintained ~100 µ above sensitive pads : the very high field (O(60kV/cm)) multiplies the electrons.
Very small gap : very fast detector
Funnel effect: avalanche spread by diffusion of electrons, ions follow back field lines, most of them closing on the mesh.

## Slide 4: Charge spreading
Continuous RC network spreading evenly the charge over several pads
pads
mesh
E
B
~100m Amplification gap:
resistive foil: ~75m
insulator: ~100m

## Slide 5: Early tests
2001-2002 : Check that Micromegas works in a magnetic field. Requires non-magnetic mesh.
Study the ion back flow natural suppression
Select gas candidates
2000-2005 : development of the charge-spreading method (M. Dixit et al.). Tested in a 5T field: 30 µm resolution with 2mm pads

## Slide 7: EUDET/AIDA Test facility at DESY
GEMs
Micromegas
March 2015

## Slide 8
Module size: 22 cm × 17 cm
Readout: 1726 Pads
24 rows
Pad size: ~ 3 mm × 7 mm
Micromegas module
Bulk process for MM manufacture
Carbon-loaded kapton or Diamond-like carbon as resistive coating
Chips on board (wire bonding) – The resistive foil suffices to protect against sparks – 0.25 X° thick

## Slide 9: Gating
Necessary to fully suppress the space charge produced by ion back flow from the amplification gap
Practical solutions under study, e.g. gating GEM (see Akira Sugiyama’s talk)
Not possible at CEPC (see Huirong’s talk)

## Slide 10: Perfomance : resolution
Resolution 70 µm in rf and 200 µm in z at zero drift distance for 3mm-wide pads
Drift dependence follows expectation from diffusion

## Slide 11
Comparison of distortion between experiment and simulation
For the Micromegas modules on the LPTPC endplate.
For the simulated Micromegas modules
Distribution of the residuals as obtained
in Experiment after alignment correction.
Distribution of the residuals as
obtained in Simulation
B=0T
B=0T

## Slide 12
For the Micromegas modules on the LPTPC endplate.
For the simulated Micromegas modules
Distribution of the residuals as obtained
in Experiment without alignment correction.
Distribution of the residuals as
obtained in Simulation
B=1T
B=1T
Comparison of distortion between experiment and simulation

## Slide 13: 2-phase CO2 cooling
Can operate at room temperature (requires high pressure, no problem in O(1mm) pipes. Allows more uniform gas temperature and no worry with dripping condensed water.
No consequence of leaks : CO2 vaporizes
Excellent heat removal (high heat capacity and high latent heat)
Very little matter budget

## Slide 14: Thermal simulation of the gas volume and of the endplate modules
Thermal inhomogeneities cause changes in drift properties in the gas, hence distortions. Needs simulations.
D.S. Bhattacharya

## Slide 15: Warming up and cooling down of a module. Good agreement with data

## Slide 16: Summary
Basic demonstration that a TPC can operate at ILC with required performance is made
More work needed to demonstrate that it can work at a CC (time structure, ion back flow)
A lot of progress was made in a decade towards an engineered detector