## Slide 1: A SOI pixel sensor for vertex detector with highly compact digital pixel
Yang ZHOU, Yunpeng LU, Jing DONG, Ouyang QUN /SOI mini Workshop /2016.7.14/ BeiJing
Outline:
  Vertex detector specifications
  SOI/CMOS technology
  *CPV1 design & preliminary test results
  CPV2 design & simulation results
  Conclusion and outlooks
*CPV: Compact Pixel for Vertex

## Slide 2
Vertex detector specifications
Vertex detector:
  Inner most detector:
    - high flux density;
  Reconstruct the charm & bottom particle decay vertex:
    - Precise spatial & time resolution; - Thin (minimize scattering effect);
    - Low power consumption (simplify cooling system).

## Slide 3
General requirements of vertex detector：
    High granularity, fast readout, thin pixel sensors with low power consumption
Promising technologies: CMOS Pixel Sensor / SOI pixel sensor
  - 100% fill-factor
  - Miniaturized: sensor and signal processing integrated in the same silicon wafer
  - Low cost: standard commercial technology
  - Low power dissipation: monolithic sensor
  - Almost dead time free: very short reset time
  - Sensitive: signal collected by the sensing diode as low as 200
  - High granularity: pixel pitch on the scale of several tens of μm
High granularity is beneficial for both high flux and precise special resolution
Vertex detector specifications

## Slide 4
SOI/CMOS technology: concerning granularity
SOI pixel technology potential advantages:
  Thicker sensitive layer: simplify the electronic design
    - 2-3 times signal charges for Minimum Ionizing Particles (MIP) even after the sensor back thinning down to ≈ 50μm
  More compact layout: shrink the pixel size
    - PMOS & NMOS transistor could be closer (no NWELL PWELL used for transistors in SOI)
SOI
CMOS
Potentially high granularity
zhouyang@ihep.ac.cn
Sensitive layer: 10-20 μm thick
Sensitive layer: hundreds μm, could be back thinned to 50 μm

## Slide 5
 | ASTRAL | ALPIDE | CPV*
Process technology | 0.18 μm CMOS |  | 0.2 μm SOI
Readout strategy | Rolling shutter | asynchronous | Rolling shutter
Readout time | 20 μs | <2 μs | 
Power | 85 mW/cm2 | 39 mW/cm2 | 
Pixel size | 22 33 μm2 | 28 28 μm2 | 16 16 μm2
Spacial resolution | ≈ 5μm |  | < 3μm
Total signal for MIP | ≈1600 e- (≈20μm epi-layer) |  | ≈4000 e- (back thinning to 50μm, fully depleted)
 | ASTRAL | ALPIDE | CPV*
Process technology | 0.18 μm CMOS |  | 0.2 μm SOI
Readout strategy | Rolling shutter | asynchronous | Rolling shutter
Readout time | 20 μs | <2 μs | 
Power | 85 mW/cm2 | 39 mW/cm2 | 
Pixel size |  |  | 
Spacial resolution | ≈ 5μm |  | < 3μm
Total signal for MIP | ≈1600 e- (≈20μm epi-layer) |  | ≈4000 e- (back thinning to 50μm, fully depleted)
CPV compare with cutting edge sensors for Vertex detector: all with in-pixel discrimination process
Goal: take advantages of higher signal compared to CMOS technology, design a simple digital pixel structure to shrink the pixel size.
*Compact Pixel for Vertex
>65%
16
28
Pixel size
SOI/CMOS technology: *CPV prototype target

## Slide 6
CPV1: 1st SOI prototype
  - Designed in line with the technology roadmap
  - 16*16 μm2 with in-pixel-discrimination
  - Based on the measurement of full depletion*
  - Pixel array: 64*32 (digital) + 64*32 (analog)
  - Submitted June, 2015
  * Y. LIU, Y. LU, X. JU, Q. OUYANG, Chinese Physics C, Vol.40, No. 1 (2016)
64row*32col. digital pixel
64row*32col. analog pixel
Digital
Analog
16μm
16μm
CPV1 chip Layout
CPV1 digital pixel layout
  CPV1:design & preliminary test results

## Slide 7
Test set up:
  Chip delivered in Feb. 2016
  Mounted in a Pin Grid Array package (176 pins)
  Sub-board PCB prepared
  Fit in the SEABAS DAQ system
  FPGA firmware and PC software partly ready, modified from the existing system for other chips
Bare chip
Chip & Package
Sub-board
FPGA
Ethernet
  CPV1:design & preliminary test results

## Slide 8
Very preliminary results obtained by far:
  Gain of amplifier measured on analog pixels
    - Measured 10.2 agrees with the design value 10
  Transfer curve measured on digital pixels
    - Transition region ~5mV, equivalent to 120e- , temporal noise ~ 17e- (Fix Pattern Noise not included yet)
Chart: 
| 0.85 | 0.86 | 0.87 | 0.88 | 0.89 | 0.9 | 0.91 | 0.92 | 0.93 | 0.94 | 0.95 | 0.96 | 0.97 | 0.98 | 0.99 | 1
Pixel(16,32) | 1.64 | 1.63 | 1.61 | 1.58 | 1.52 | 1.44 | 1.33 | 1.25 | 1.14 | 1.05 | 1.02 | 0.92 | 0.86 | 0.83 | 0.73 | 0.73
Pixel(16,0) | 1.67 | 1.66 | 1.66 | 1.64 | 1.64 | 1.63 | 1.59 | 1.53 | 1.44 | 1.34 | 1.23 | 1.14 | 1.02 | 0.92 | 0.89 | 0.88
Chart: 
| 0.94699999999999995 | 0.94799999999999995 | 0.94899999999999995 | 0.95 | 0.95099999999999996 | 0.95199999999999996 | 0.95299999999999996 | 0.95399999999999996 | 0.95499999999999996 | 0.95599999999999996 | 0.95699999999999996 | 0.95799999999999996 | 0.95899999999999996 | 0.96 | 0.96099999999999997 | 0.96199999999999997 | 0.96299999999999997 | 0.96399999999999997
 | 11.65 | 11.65 | 11.63 | 11.56 | 11.52 | 11.32 | 10.67 | 9.28 | 6.04 | 1.5 | 3.9e-05 | 0.000258 | 0.000188 | 0.000166 | 0.000166 | 0.000165 | 0.000164 | 0.000161
Analog output (V)
Test input (V)
5mV
Test input (V)
Digital output
(a.u.)
preliminary
  CPV1:design & preliminary test results

## Slide 9
Very preliminary results with 55Fe: mostly 5.9 keV x-ray
  The sensor is working
  Statistical results is still in progress
  CPV1:design & preliminary test results
One frame result without hits
One frame result with 1 hit in the matrix
Pixel amounts
Pixel amounts
Pixel analogue output (ADC unit)
Pixel analogue output (ADC unit)

## Slide 10
  CPV2:design
10
CPV2*: 3 3 mm2
CPV2: 2nd SOI prototype:
  Constrains same with CPV1
  Several optimization on pixels offset, timing;
  - Submitted June, 2016

## Slide 11
  CPV2:design
CPV2 pixel schematic
Pre_amp
Inpixel_CDS
INV
Sensing node
Protection diode
In-pixel CDS stage: one capacitor + one switch with a clamping voltage
  Pre_amp offsets are stored on the capacitor, and cancelled with appropriate operation timing
  Clamping voltage is used to provide an appropriate DC voltage for INV and also used for threshold adjustment;

## Slide 12
Sensing diode | Sensing_node | CS_out | Gain_before_inv
4 fF + parasitic | 35 μV/e- | 357 μV/e- | 300 μV /e-
CS amplifier
Simulation results, real results will be slightly less, due to layout generated parasitic capacitances
DC operation point (511 mV) with RST
operation point various from pixel to pixel due to channel charge injection effect of RST transistor
DC response
Gain
INV
Ideal value for V_clamp = 865 mV, 35 mV input increasment (110 e- on the sensing node) could make the inverter overturn completely. Threshold could be set by adjusting V_clamp
A small input variation leads to a large output variation
  CPV2: simulation results

## Slide 13
50 ns to read one row: frame time depends on matrix size
100 ns to reset: the larger matrix size, the smaller dead time proportion
Row select switch_on
CS power_on (Low active)
Clamp
RST 20 ns is enough
Row select switch_on
Readout
At least 100 ns in this design
Sensor read out speed depends on this duration, it require at least around 50 ns
  CPV2: simulation results
CPV2 Pixel timing

## Slide 14
Signal | Sensing_node | CS_out | Inv_in | Inv overturn required
500 e- | ≈17.5 mV | 178.7 mV | 149.9 mV | 35 mV
Example of 1 hit operation
1 hit during last frame: 500 e-
timing
Pixel_out
INV_out
INV_in
CS_out
Long recover time
  CPV2: simulation results

## Slide 15
Pixel out
Signal_in: 500 e-
An example: 4 hits in 8 frames, output low means pixel fired
  CPV2: simulation results

## Slide 16
Conclusion:
  - Single pixel discriminate a hit require ≈110 e-, while a MIP generates ≈4000 e- in a SOI prototype thinned to 50 μm
  - The Inverter only sense the signal absolute value with the help of Offset cancellation stage;
  RST noise of Clamp transistor could not be cancelled, a larger value coupling capacitance could help to reduce it;
  The coupling capacitance value was chosen as 37.5 fF due to the layout limitation;
  It takes 50 ns to read one row in CPV2;
  CPV2 dead time proportion = 100 ns/frame time.
CPV2 Pixel schematic
Pixel Layout: 16 16 μm2
  CPV2: design

## Slide 17
  - R&D of the SOI pixel sensor used for future high energy particle Colliders is in progress in IHEP;
  - Two prototypes CPV1/CPV2 has been design and submitted in 0.2 μm SOI technology;
  Exciting preliminary test results have been obtained from CPV1;
  More test will be done to validate the concept of highly compact digital pixel with SOI technology used for vertex detector.
Conclusion and outlooks

## Slide 18
Thanks for your attention!