## Slide 1: CEPC partial double ring FFS design
Dou Wang, Jie Gao, Feng Su, Yuan Zhang, Yiwei Wang, Bai Sha, Huiping Geng, Tianjian Bian, Na Wang, Xiaohao Cui, Yuanyuan Wei
CEPC AP meeting, 2016.06.17

## Slide 2: CEPC vs. LEP2
parameter | CEPC |  |  | LEP2 | 
Physics working point | H |  | Z |  | 
energy/beam [GeV] | 120 |  | 45.5 | 105 | 45.6
Circumference [km] | 54 |  | 54 | 27 | 
Single ring/double ring | Partial double |  |  | Single | 
Pretzel scheme | No |  |  | Yes | 
bunches/beam | 67 | 44 | 1100 | 4 | 12
bunch population [1011] | 2.85 | 2.67 | 0.46 | 4.2 | 1.96
beam current [mA] | 16.9 | 10.5 | 45.4 | 3 | 4.2
luminosity/IP x 1034cm-2s-1 | 2.9 | 2.0 | 3.1 | 0.0012 | 0.0034
energy loss/turn [GeV] | 2.96 |  | 0.062 | 3.34 | 0.12
synchrotron power [MW] | 50 | 31 | 2.8 | 22 | 1.1
RF voltage [GV] | 3.6 | 3.5 | 0.12 | 3.5 | 
fRF [MHz] | 650 |  |  | 352 | 352

## Slide 3: CEPC vs. ILC
parameter | CEPC |  | ILC | 
Physics working point | H | Z |  | 
energy/beam [GeV] | 120 | 45.5 | 125 | 250
Linear/circular | circular |  | linear | 
bunches/beam | 67/44 | 1100 | 1312 | 1312
bunch population [1011] | 2.85/2.67 | 0.46 | 0.2 | 0.2
Normalized vertical emittance [nm] | 1738/1456 | 249 | 35 | 35
IP vertical betay [mm] | 1.36/1.24 | 1.0 | 0.41 | 0.48
IP RMS veritcal beam size [nm] | 100/88 | 53 | 7.7 | 5.9
beam current [mA] | 16.9/10.5 | 45.4 | 5.8 | 5.8
luminosity/IP x 1034cm-2s-1 | 2.9/2.0 | 3.1 | 0.97 | 2.05
energy loss/turn [GeV] | 2.96 | 0.062 | No | 
fRF [MHz] | 650 | 650 | 1300 | 1300
Average number of photons / particle n | 0.47 | 0.24 | 1.16 | 1.72

## Slide 4: CDR验收目标
充分考虑物理目标需求、机器亮度目标、加速器物理、探测器及重要硬件的可实现性、机器运行稳定性和可调节性，给出CEPC的合理优化加速器物理设计
考核指标：
  亮度：Higgs达到 21034cm-2s-1, Z达到 11034cm-2s-1
  动力学孔径：含error和beam-beam，on-momentum达到20x  40y，2%达到5x  10y

## Slide 5: Betax*= 0.25m,Betay*=1.36mm
K2HS := 11.96m-3
K2VS := 32.74 m-3
Critical energy= 190kev
Crab sex
dmux = -14.464497
dmuy = -200.084478

## Slide 6: DA of the whole ring (arc+PDR+bypass+FFS)
Arc sextupole: 2 groups
DA (on-momentum): 27x  57y
DA (0.5%): 2x  2y
Crab sextupoles - off

## Slide 7: Bandwith optimization

## Slide 8: parameter for CEPC partial double ring （wangdou20160325）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.09

## Slide 9: parameter for CEPC partial double ring （wangdou20160525）
 | Pre-CDR | H-high lumi. | H-low power
Number of IPs | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120
Circumference (km) | 54 | 60 | 60
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96
Half crossing angle (mrad) | 0 | 15 | 15
Piwinski angle | 0 | 4.0 | 4.0
Ne/bunch (1011) | 3.79 | 1.56 | 1.56
Bunch number | 50 | 135 | 81
Beam current (mA) | 16.6 | 16.9 | 10.1
SR power /beam (MW) | 51.7 | 50 | 30
Bending radius (km) | 6.1 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 2.2 | 2.2
IP x/y (m) | 0.8/0.0012 | 0.104/0.003 | 0.104/0.003
Emittance x/y (nm) | 6.12/0.018 | 2.03/0.0061 | 2.03/0.0061
Transverse IP (um) | 69.97/0.15 | 14.5/0.14 | 14.5/0.14
x/IP | 0.118 | 0.0086 | 0.0086
y/IP | 0.083 | 0.11 | 0.11
VRF (GV) | 6.87 | 3.72 | 3.72
f RF (MHz) | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.0 | 3.0
Total z (mm) | 2.65 | 3.9 | 3.9
HOM power/cavity (kw) | 3.6 | 1.3 | 0.76
Energy spread (%) | 0.13 | 0.13 | 0.13
Energy acceptance (%) | 2 | 2 | 2
Energy acceptance by RF (%) | 6 | 2.5 | 2.5
n | 0.23 | 0.44 | 0.44
Life time due to beamstrahlung_cal (minute) | 47 | 43 | 43
F (hour glass) | 0.68 | 0.97 | 0.97
Lmax/IP (1034cm-2s-1) | 2.04 | 1.60 | 0.96

## Slide 10
Change the circumference of booster?

## Slide 11
Thanks！