## Slide 1: CEPC APDR and PDR scheme
Dou Wang, Jie Gao, Zhenchao Liu, Yiwei Wang, Feng Su, Yuan Zhang, Bai Sha, Huiping Geng, Tianjian Bian, Na Wang, Xiaohao Cui
CEPC AP meeting, 2016.07.22

## Slide 3
CEPC Advanced Partial Double Ring Layout I
SU Feng
2016.5.23
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 1132.8m
4 ARC1, 124*FODO, 5852.8m
4 ARC2, 24*FODO, 1132.8m
4 ARC3, 79*FODO, 3728.8m
2 ARC4, 24*FODO, 1132.8m
C=62967.86m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
ARC1
ARC3
ARC2
ARC3
ARC2
ARC4
ARC1
APDR
APDR
APDR
APDR

## Slide 4
ARC
CEPC Advanced Partial Double Ring Layout II
SU Feng
2016.6.2
IP1_ee
IP3_ee
3Km
1/2RF
1/2RF
1/2RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 94.4m
12 Long Straights, 566.4m
4 Long ARC, 124*FODO, 5852.8m
4 Medium ARC, 104*FODO, 4908.8m
4 Short ARC, 14*FODO, 660.8m
C=65640.2m
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
APDR
APDR
APDR
APDR
APDR
APDR

## Slide 5: CEPC APDR SRF considerations
The 8-double ring and 6-double ring seem available when using the same parameter as PDR(VRF=3.62GV) for HL. The 8-double ring has a lower phase variation than the 6-double ring .
The phase region is from 35.2-33 degree for bunches in a bunch train for the 8-double ring HL mode. The phase region is from 35.2-32.3 degree for the 6-double ring HL mode.
The bunch energy gain in each cavity is constant.
The RF to beam efficiency is ~100%.

## Slide 6: parameter for CEPC partial double ring （wangdou20160325）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.09

## Slide 7
Bunch No. | Pre CDR (CW, Pg=Pavg) |  | PDR (CW, Pg=Ppulse, very low RF efficiency) |  | APDR 6 ring (H-low power, CW, Pg=Pavg) |  | APDR 8 ring (H-low power, CW, Pg=Pavg) | 
 | Vrf | Phase shift | Vrf | Phase shift | Vrf | Phase shift | Vrf | Phase shift
1 | 1 | 0 | 1 | 0 | 1 | 0.00 | 1 | 0.00
2 | 1 | 0 | 1 | 0 | 0.9984 | -0.16 | 0.9984 | -0.14
3 | 1 | 0 | 1 | 0 | 0.9968 | -0.31 | 0.9968 | -0.28
4 | 1 | 0 | 1 | 0 | 0.9952 | -0.47 | 0.9952 | -0.42
5 | 1 | 0 | 1 | 0 | 0.9936 | -0.63 | 0.9936 | -0.56
6 | 1 | 0 | 1 | 0 | 0.992 | -0.79 | 0.992 | -0.70
7 | 1 | 0 | 1 | 0 | 0.9904 | -0.94 | 0.9904 | -0.84
8 | 1 | 0 | 1 | 0 | 0.9888 | -1.10 | 0.9888 | -0.98
9 | 1 | 0 | 1 | 0 | 0.9872 | -1.26 | 0.9872 | -1.12
10 | 1 | 0 | 1 | 0 | 0.9856 | -1.41 | 0.9856 | -1.26
11 | 1 | 0 | 1 | 0 | 0.984 | -1.57 | 0.984 | -1.40
15 | 1 | 0 | 1 | 0 | 0.9776 | -2.20 |  | 
50 | 1 | 0 | 1 | 0 |  |  |  | 
67 |  |  | 1 | 0 |  |  |  | 
Assume Vrf is constant at the first bunch of bunch trains and the change of Vb is negligible.
By Zhenchao Liu

## Slide 8: Bunch length error with RF phase adjustment
Error of bunch length: ~4% (6 ring), ~3% (8 ring)

## Slide 9: Piwinski error with RF phase adjustment
Error of Piwinski angle: ~4% (6 ring), ~3% (8 ring)

## Slide 10: RF voltage error with RF phase adjustment
Error of VRF: ~ -2.4% (6 ring), ~ -1.6% (8 ring)

## Slide 11: Luminosity error with RF phase adjustment
Error of luminosity: ~ -3.5% (6 ring), ~-2.4% (8 ring)

## Slide 12: RF acceptance error with RF phase adjustment
Error of RF acceptance: ~ -10% (6 ring), ~ -7% (8 ring)

## Slide 13: HOM power with RF phase adjustment
Error of HOM power: ~ -2% (6 ring), ~ -1% (8 ring)

## Slide 14: BS life time with RF phase adjustment
Error of BS life time: ~68% (6 ring), ~39% (8 ring)

## Slide 15: Betax*= 0.25m,Betay*=1.36mm
K2HS := 11.96m-3
K2VS := 32.74 m-3
Critical energy= 190kev
Crab sex
dmux = -14.464497
dmuy = -200.084478

## Slide 16: DA of the whole ring (arc+PDR+bypass+FFS)
Arc sextupole: 2 groups
DA (on-momentum): 27x  57y
DA (0.5%): 2x  2y
Crab sextupoles - off

## Slide 17: Off-momentum DA optimization

## Slide 18: More sextupole families in IR
Arc sextupole: 2 groups

## Slide 19: More sextupole families in ARC
Arc sextupole: 192 groups
IR sextupole: 4 groups

## Slide 20
Thanks！