## Slide 1: Integration of Data Acquisition Systems of Belle II Outer-detectors for Cosmic Ray Test
S. Yamada(KEK), R. Itoh(KEK), K. Tomoyuki(KEK), Z. Liu(IHEP),
M. Nakao(KEK), S. Y. Suzuki(KEK), J. Zhao(IHEP)

## Slide 2
ECL
(Electromagnetic CaLorimeter)
PXD
(PiXel Detector)
SVD
(Silicon Vertex Detector)
CDC
(Central Drift Chamber)
ARICH
(Aerogel Ring Imaging Cherenkov Detector )
TOP
(Time Of Propagation)
KLM
(KL and Muon detector)
Schedule of the Belle-II experiment :
2016 : phase I run ( accelerator commissioning and beam background study )
2018 Jan. : phase II run ( with the Belle II outer sub-detectors )
2018 Dec. : phase III run ( with the full Belle II detector )
Belle II detector
It consists of 7 sub-detectors.
CDC, TOP, ECL and KLM were already installed.
Aerogel radiator
resistive plate chamber
+scintillator
quartz radiator
CsI(Tl) crystal blocks
Tracking
→ CDC
Particle ID
→ TOP, ARICH
EM calorimeter
→ ECL
Muon, Klong
→ KLM
Outer sub-detectors
Inner sub-detectors
Vertex determination:
→ PXD, SVD

## Slide 3: Schematic view of Belle II Data Acquisition System
X40
Readout
PCs
X210
readout
boards
x10 High Level Trigger+storage unit
HLT: ( 20nodes x 16cores )/ unit
1GbE/10GbE
switch
～ 3GB/s
～ 30GB/s
1- 2GB/s
(analysis info. Is added)
～1GB/s
2-3GB/s
Trigger rate
x1/3-1/5
Level1 trigger ～ 30kHz (max. value for DAQ development )
Inner sub-detectors
Outer sub-detectors
Common interface with FEEs of all sub-detectors except for the pixel detector
PXD event size is reduced online by Region of Interest obtained by track information.
  Trigger and
  Timing distribution
  Common readout-system
  for sub-detectors
  Event-building w/o PXD
  event-reduction
  Combine with PXD data
  and record
  PXD Data-reduction by Region of Interest
ROI

## Slide 4
Minimum DAQ setup (called as “Pocket DAQ”), which includes only COPPER readout boards and readout-PCs for the development of FEE firmware of each sub-detector
- Once readout of FEE at pocket DAQ becomes is achieved, in principle there should be no problem in the integration of the sub-detector DAQ to the Belle II DAQ system.
Belle II DAQ at KEK experimental hall
“Pocket DAQ” for each sub-detector
FEE development
After detector
installation
COPPER
Readout
Board
Readout PC
FTSW
FEE
Readout PC
FTSW
network
FEE
trg/clk
trg/clk
High Level Trigger/
Storage
How to integrate each FEE system with the Belle II DAQ system
COPPER
Readout
Board

## Slide 5
FPGA on
Front-end electronics board
Backend-DAQ
(DAQ gr.)
Two interfaces between FEE and DAQ for readout
  FEE and Trigger/Timing distribution network :
  FEE and backend DAQ :
Common FPGA core (“belle2link core”) is implemented in FEE’s FPGA for the interface
FIFO
HSLB(High-speed serial link board)
data
belle2link core
Common for all sub-detectors
Trigger/clock
Backend DAQ
Trigger/clock
Register access
Interface between FEE and backendDAQ : FEE side
Optical fiber
FEE board
COPPER
data

## Slide 6
Belle2Link : (D. Sun et. all, hysics Procedia Volume 37, 2012, pp. 1933-1939 )
Unified high speed link which connects Front-End Electronics (FEE) and DAQ system for signal with data transmission based on Rocket I/O
FEE side : Functions for I/F with FEE and Trigger Timing Distribution on FPGA
DAQ side : High Speed Link Board(HSLB) as a data receiver
- Attached on COPPER readout board
- FPGA : Xilinx Virtex 5
input/output SFP : x 1 or 2
Line rate : 3.125Gbps
HSLB
(Virtex5)
COPPER I/F
data
GTP link
COPPER : data readout board
A/D
conversion
Developed by IHEP
FEE
FEE I/F
data
FPGA
data
Belle2Link
HSLB
HSLB
HSLB
configutaion
by register access
HSLB board
Data transmission from FEE to backend DAQ

## Slide 7: Interface between FEE and backend DAQ : backend side
Common readout-boards for sub-detectors (except for PXD)
CPU board on COPPER(COmmon Pipeline Platforms for Electronics Readout ) :
  event-building of data from 4 HSLB boards, data-formatting and sening the data to readout PCs
Readout PC :
  event-building from around 10 COPPERs, Data-corruption check and send the events to high level trigger PC farm
Front-end
Electronics
A/D
conversion
HSLB
CPU card
TTRX
HSLB
HSLB
HSLB
Readout PC
(partial) Event-builder
DeSerializer
basf2
Serializer
DeSerializer
basf2
Serializer
DeSerializer
basf2
Serializer
DeSerializer
basf2
Serializer
DeSerializer
basf2
Serializer
To event builder, HLT PC farm
data
Read-out board (COPPER)
data
Rocket I/O
based protocol
Gigabit Ethenet
Belle2link

## Slide 8
High-rate test for TTD network and readout subsystem
Setup : barrel part of ECL and readout subsystem
Dummy triggers to 36 ECL FEE boards ->
The FEE sends event data to the back-end DAQ [18 COPPERs -> 7 readout PCs -> event builder on HLT input server ], where the data are discarded.
ECL FEE
ECL FEE
Barrel ECL detector
Des_ser_ROPC
…
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
HSLB
HSLB
HSLB
HSLB
COPPER
FTSW
PrPMC
ROPC
Des_ser_ROPC
Data handler
Partial Event builder
FTSW
Readout PC 7
…
Des_ser_ROPC
…
ROPC
Des_ser_ROPC
Data handler
Partial Event builder
Readout PC 1
…
FTSW
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
dumhslb
dumhslb
dumhslb
dumhslb
COPPER
HSLB
HSLB
HSLB
HSLB
COPPER
PrPMC
…
HLT
input server
eb0
/dev/null
ECL FEE
ECL FEE
ECL FEE
ECL FEE
ECL FEE
ECL FEE
ECL FEE
ECL FEE
Dummy
Trigger
Inputs

## Slide 9
Constant 30kHz trigger rate
Pseudo-Poisson 30kHz trigger rate
Efficiency = 99.2%
Efficiency = 98.4%
9
Throughput : about 33MB/s/COPPER ( the expected event size from MC )
  Event size was adjusted by HIT threshold of ECL FEE
  Total throughput for Barrel ECL : 600 MB/s
Constant 30kHz trigger -> efficiency = 99.2%
Pseudo-Poisson 30kH trigger -> efficiency = 98.2 %
  The deadtime comes from trigger limitation (5trigger in 26us due to SVD FEE ).
-> High efficiency(nearly 100%) was achieved !
Results of the high-rate test (cont’d)
CPU usage on
a COPPER board

## Slide 10: Belle II cosmic-ray test
Purpose : Detector and DAQ commissioning
Two types of data acquisition schemes
  local run : each sub-detector’s data are taken independently
  combined run : Combined data-taking with online event building
→ This local/global switching should be done in not only the commissioning period but actual Belle II experimental period. (daily calibration work etc. )
→ Should be smoothly switched w/o large modification of the setup
 | Feb 2017 | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan 2018
KLM |  |  |  |  |  |  |  |  |  |  |  | 
CDC |  |  |  |  |  |  |  |  |  |  |  | 
TOP |  |  |  |  |  |  |  |  |  |  |  | 
ECL |  |  |  |  |  |  |  |  |  |  |  | 
ARICH |  |  |  |  |  |  |  |  |  |  |  | 
Global
Cosmic ray test
Detector roll-in
Phase II run (beam collision)
install
Assembly work and readout test
Cosmic ray test
Cosmic ray test
Cosmic ray test
Cosmic ray test
Magnet ON
Schedule
TIPP2017
Detector roll-in last month
Combined CRT

## Slide 11
Combined data-taking with some of the sub-detectors
Belle II master FTSW can distribute common trigger over multiple sub-detectors.
Local data-taking at the same time
Each sub-detector TTD network has an input for local trigger source.
Since each sub-detector TTD network is separated with others, no need to modify cabling to switch local/combined data-taking
Trigger/Timing distribution(TTD) for Local/combined data-taking
FTSW modules
Master
FTSW
…
SVD
FTSW
CDC
FTSW
TOP
FTSW
KLM
FTSW
Combined
Trigger
Source
Local
Trigger
Source
FEE
FEE
FEE
SVD
FEE
FEE
FEE
FEE
CDC
FEE
FEE
FEE
FEE
TOP
FEE
FEE
FEE
FEE
KLM
FEE
…

## Slide 12
Sub-detectors
Readout subsystem
PC farms
HLT
HLT
Event
builder
FEE
FEE
FEE
FEE
FEE
FEE
COPPER
COPPER
COPPER
COPPER
COPPER
ROPC
ROPC
ROPC
belle2link
recording
recording
Data Quality
Monitor
FEE
FEE
FEE
FEE
FEE
FEE
COPPER
COPPER
COPPER
COPPER
COPPER
ROPC
ROPC
ROPC
Sub-detector1
Back-end DAQ system for for Local/combined data-taking :
Disk
Front-end electronics and readout subsystem(COPPER + readout PC)
  They can be running independently for each sub-detector
event builder, High level trigger :
  hardware is not independent for each sub-detector
-> Virtually independent system running on the same hardware
-> Controlled by slow control system
Data Quality
Monitor
Event
builder
belle2link
Sub-detector2

## Slide 13
Screenshot of data-taking for ECL and CDC
ECL run controller
ECL Data Quality Monitor
CDC run controller
CDC Data Quality Monitor
Run-control system for Local data-taking in parallel :
UI_CDC
UI_ECL
Shifter’s PC
Slow control daemon
COPPER
Slow control daemon
PC farm
Slow control daemon
COPPER
Slow control daemon
PC farm
Two sub-detector data-taking (CDC and ECL) was performed in parallel
  Each run control master manages each of the combined systems
  Separate control/monitoring for each system
Slow control
master
Slow control
master

## Slide 14
A CDC cosmic ray event from event-display
After the sub-detector installation, Data-taking from the full scale of CDC was performed.
  75 x COPPER boards (link x 299)
Trigger source : scintillator and CDC’s TSF(Track Segment Finder) system
Cosmic ray data-taking with sub-detectors
Installation of CDC
Shower event
Event rate
CDC (Central Drift Chamber)

## Slide 15
ECL cosmic ray test :
Event rate is about 110Hz.
Time from run-start [s]
Event rate [Hz]
TOP (Time Of Propagation) counter
direct
reflection
Hit timing distribution of cosmic ray events
Preliminary
Stable cosmic ray run was
achieved.
Cosmic ray event in Barrel blocks
Cosmic ray data-taking with sub-detectors (Cont’d)
Event rate
Quartz bar and ray of Cherenkov light
Cross section of ECL
Each sub-detector’s DAQ was successfully integrated and start collecting cosmic ray events.
ECL (Electromagnetic Calorimeter)

## Slide 16: Summary
In the Belle II experiment, we started to take cosmic ray events with the installed sub-detectors for detector and DAQ commissioning.
DAQ integration for the cosmic ray test
  Common interface between backend-DAQ and FEE for several sub-detectors
    High rate test w/ dummy trigger was performed for barrel ECL with trigger rate of 30kHz
  Partitioned DAQ components : (Trigger timing distribution, backend data-stream )
    Local/combined data-taking can be easily switched.
  Start taking cosmic ray evens w/ CDC, ECL, TOP, CDC+ECL+TOP combined