## Slide 1: CEPC Damping Ring Design
Dou Wang, Cai Meng, Jie Gao
CEPC AP meeting, 2016.08.26

## Slide 2: CEPC damping ring requirement
Energy: 1.1GeV
Storage time: 20ms
Injected emittance (normalized): 3500 mm-mrad, injected energy spread ~ 0.25%
Extracted energy spread <1×10-3
No strong requirement for the extracted emittance (<0.5inj)!

## Slide 3: SLC damping ring
E=1.2GeV
C0=35m
0=17ms
B0=2T

## Slide 4: CEPC DR consideration
 | Case I | Case II
Energy (GeV) | 1.1 | 
circumference | 35 | 70
Bending radius (m) | 1.57 | 4.57
B0 (T) | 2.34 | 0.8
U0 (keV) | 82.5 | 28.4
Damping time x/y (ms) | 3.1 | 18.1
Damping time z (ms) | 1.55 | 9.05
0 (%) | 0.075 | 0.044
inj (mm.mrad) | 3500 | 3500
inj (%) | 0.25 (1) | 0.25 (1)
ext (%) | 0.075 (0.075) | 0.047 (0.056)

## Slide 5: Discussion with IHEPmagnet people

## Slide 6: Overall Parameter estimation
 | Case III
Energy (GeV) | 1.1
circumference | 60
Bending radius (m) | 9.5
B0 (T) | 0.99
U0 (keV) | 28.4
Damping time x/y (ms) | 12.6
Damping time z (ms) | 6.3
0 (%) | 0.0489
inj (mm.mrad) | 3500
inj (%) | 0.25 (1)
ext (%) | 0.0493 (0.0506)

## Slide 7: Optics design consideration
L=1.22m
= 219 mm.mrad

## Slide 8: RF consideration
Chose fRF=650MHz, bunch length < 3mm (10ms)
We get Vrf = 4.2*107 z =1.47mm hRF=4.9%

## Slide 9: FODO cell in arc

## Slide 10: Dispersion supressor

## Slide 11: Whole ring
Circumference = 58.5m

## Slide 12: Layout of CEPC DR

## Slide 13: Lattice design result

## Slide 14: Beam parameter from real lattice
=302 mm.mrad
ex=einj*ã-2*t/tx+302.1*(1-ã-2*t/tx)=434 mm.mrad
ey=einj*ã-2*t/tx=145 mm.mrad