## Slide 1: CEPC Partial Double Ring Lattice Design and DA Study
SU Feng GAO Jie WANG Dou WANG Yiwei Li Yongjun BAI Sha
BIAN Tianjian GENG Huiping ZHANG Yuan
Institute of High Energy Physics
高能环形正负电子对撞机相关的物理和关键技术预研究”项目启动会，2016.9.27

## Slide 2: Outline
  CEPC PDR Lattice Design Progress:
    CEPC PDR Parameter and Lattice Layout
    CEPC PDR ARC Length Consideration and Redesign
    CEPC PDR DA Study ( NSGAII & DA Optimization)
    CEPC APDR Scheme
    CEPC Double Ring Scheme
    Summary
  CDR Report & CDR & Plan & Next to do

## Slide 3
CEPC PDR Parameter and Lattice Layout
Outline

## Slide 4
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 5.2 | 6.4
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.16 | 0.78
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 36.5 | 67.6
SR power /beam (MW) | 51.7 | 50 | 32.5 | 21.3 | 4.1
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.44 | 2.9
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.0078 | 0.88/0.008
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 9.7/0.088 | 9.4/0.089
x/IP | 0.118 | 0.041 | 0.042 | 0.013 | 0.01
y/IP | 0.083 | 0.11 | 0.11 | 0.073 | 0.072
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.74 | 0.11
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.95 | 3.78
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.88 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.7 | 1.2
n | 0.23 | 0.35 | 0.34 | 0.49 | 0.34
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.92 | 0.93
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 4.3 | 4.48
Parameter for CEPC partial double ring （wangdou20160918）

## Slide 5
CEPC Partial Double Ring Layout
SU Feng
2016.9.15
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3.7Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 3.7Km
IP2_pp/IP4_pp, 1132.8m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 944m
2 Short ARC, 24*FODO, 1132.8m
4 Medium ARC, 112*FODO, 5286.4m
4 Long ARC, 124*FODO, 5852.8m
C=60830.4m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
Bypass
about 42m

## Slide 6
For CEPC 120GeV beam:
Max. deflection per separator is 66μrad.
CEPC Partial Double Ring Layout
B1
B2
B3
B4
15mrad
Full crossing angle 30mrad
Separator
Version 1.0
sufeng
2016.9.15
1851.733m
12
62.5urad
4.5m
IP
507.1m
614.4m
307.2m
7.852m
65m
357.5m

## Slide 7
Chart: 
CEPC PDR1.0.3 noFFS

## Slide 8: Outline
2. CEPC PDR ARC Length Consideration and Redesign

## Slide 9
The circumference should be also considered of SPPC requirement…
ARC+Straight (>= 53 Km)
ARC+Straight+PDR
ARC+Straight+PDR+FFS
CEPC PDR ARC Length Consideration
Notes: One possible Option

## Slide 10
CEPC & SPPC Layout

## Slide 11: 准直段Lattice 设计 （From Jianquan 2016.8.12）
3537.8m

## Slide 12
Theory：
In Practice：
CEPC ARC Length According to SPPC

## Slide 13: SPPC Parameter Choice and Optimize
Version 201503

## Slide 14: SPPC Parameter Choice and Optimize
Version 201607

## Slide 16
Emittance Increase (2.06nm->2.1668nm)
Notes: Integration radius

## Slide 17
CEPC PDR1.0.3 noFFS

## Slide 18
Parameters of Separators sufeng201605 |  |  |  | 
Separator length | 4.5 | m |  | 
Electrode length | 4 | m |  | 
Maximum operating field strength | 1.875 | MV/m | 上限2MV/m | 
Beam energy | 120 | GeV |  | 
Maximum deflection per separator at 120GeV | 62.5 | urad | 微弧度 | 
Number of separators per collision point | 12*2=24 |  |  | 
Total number of separators (PDR) | 24*2=48 |  |  | 
Total number of separators (APDR6) | 24*6=144 |  |  | 
Total number of separators (APDR8) | 24*8=192 |  |  | 
Notes: Maximum operating field strength

## Slide 19
According to CEPC Pre-CDR Magnet Parameter
Dipole magnets | 
Quantity | 1984
Maximum field strength(T) | 0.07
Magnetic gap (mm) | 80
Bending angle (mrad) | 3.17
Magnetic Length (m) | 18
Bending radius (m) | 6094
Good field region (mm) | 100
Core cross section (W*H) (mm) | 450*400
CEPC MQ | 
Quantity | 2304
Bore diameter (mm) | 100
Field Gradient (T/m) | 10
Magnetic Length (m) | 2.0
Core width and height (mm) | 700*700
Core length (mm) | 1960
Super Conducting Q in CEPC IR | QF | QD
Field Gradient (T/m) | 304 | 309
Magnetic Length (m) | 1.25 | 0.72
Peak field in coil (T) | 7.2 | 7.1
Coil inner diameter (mm) | 40 | 40
Coil out diameter (mm) | 74 | 74
Cryostat diameter (mm) | 400 | 400
Coil mechanical length (mm) | 1500 | 950
CEPC MS | SD | SF
Quantity | 992 | 992
Aperture diameter (mm) | 120 | 120
Good field region (mm) | 100 | 100
Strength of sextupole field (T/m^2) | 180 | 180
Magnetic Length (m) | 700 | 400
Core width and height (mm) | 520 | 520
Length of iron core (mm) | 670 | 370

## Slide 20
Dipole Strength PDR1.0.3 without FFS
 | Angle(mrad) | L(m) | Rho(m) | Brho(E0/c)(T/m) | B(T) | Ek(KeV) | KeV/m
B0 | 3.205 | 19.6 | 6115.44 | 400 | 0.06541 | 626.349 | 31.956
BSepL | -0.0625 | 4.5 | -72000 | 400 | -0.00556 | 53.2 | 11.822
BMatch1L | -8.344 | 19.6 | -2348.99 | 400 | -0.1702 | 1630.66 | 83.1967
BMatch2L | 1.997 | 19.6 | 9814.72 | 400 | 0.0407 | 390.271 | 19.9118
BMatch3L | -7.653 | 19.6 | -2561.09 | 400 | -0.1562 | 1495.61 | 76.3069
B2 | 2.1428 | 19.6 | 9146.91 | 400 | 0.04373 | 418.764 | 21.3655
B3 | -2.1428 | 19.6 | -9146.91 | 400 | -0.04373 | 418.764 | 21.3655
BMatch3R | 7.653 | 19.6 | 2561.09 | 400 | 0.1562 | 1495.61 | 76.3069
BMatch2R | -1.997 | 19.6 | -9814.72 | 400 | -0.0407 | 390.271 | 19.9118
BMatch1R | 8.344 | 19.6 | 2348.99 | 400 | 0.1702 | 1630.66 | 83.1967
BSepR | 0.0625 | 4.5 | 72000 | 400 | 0.00556 | 53.2 | 11.822

## Slide 21
CEPC PDR1.0.3 with FFS (Yiwei20160817)
Chart: 

## Slide 22
CEPC ARC+PDR_FFS

## Slide 23
Emittance Increase (2.06nm->2.147368nm)
Notes: Integration radius

## Slide 24: Outline
3. CEPC PDR DA Study ( NSGAII & DA Optimization)

## Slide 25
SF1.K2
SF2.K2
SF3.K2
SF4.K2
SF5.K2
SF6.K2
SD1.K2
SD2.K2
SD3.K2
SD4.K2
SD5.K2
SD6.K2
'npop': 500,
'ngen': 100,
'nobj': 30,
'nvar': 12,
Objective
Variable
200CPU
T1=40min
T2=70h
cepc_ndr_0099.txt
NSGA-II & DA Optimization
Notes: algorithm

## Slide 26
Nonlinear Driving Term (ARC)
Betx：80.992367
bety：14.172123
2nm
Sizmax：402.47um
Sigmay：9.22um
X：60 Sigma
Y：813 Sigma
2 groups

## Slide 28
Nonlinear Driving Term (ARC)

## Slide 29
Nonlinear Driving Term (ARC_PDR_20160630)
Betx：80.992367
bety：14.172123
2nm
Sizmax：402.47um
Sigmay：9.22um
X：45 Sigma
Y：780 Sigma
2 groups

## Slide 30
Nonlinear Driving Term (ARC_PDR_FFS_2016.08.29)
Betx：0.219915m
bety：0.001m
2.147368nm
Sizmax：21.731um
Sigmay：0.08026um
2 groups
X：46 Sigma
Y：37 Sigma

## Slide 31: Outline
4. CEPC APDR Scheme

## Slide 32
New idea：Advanced PDR （APDR）
To solve the big problem of RF system

## Slide 33
CEPC Advanced Partial Double Ring Option I
SU Feng
2016.5.23
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 1132.8m
4 ARC1, 124*FODO, 5852.8m
4 ARC2, 24*FODO, 1132.8m
4 ARC3, 79*FODO, 3728.8m
2 ARC4, 24*FODO, 1132.8m
C=62967.86m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
ARC1
ARC3
ARC2
ARC3
ARC2
ARC4
ARC1
APDR
APDR
APDR
APDR
C=65km

## Slide 34
CEPC Advanced Partial Double Ring Optics I
PDR1
PDR3
APDR
APDR
APDR
APDR
Bypass2
Bypass4

## Slide 35
ARC
CEPC Advanced Partial Double Ring Option II
SU Feng
2016.8.15
IP1_ee
IP3_ee
3.7Km
RF
RF
RF
RF
IP1_ee/IP3_ee, 3703.46m
IP2_pp/IP4_pp, 1132.8m
APDR, 1426m
Short Straights, 94.4m
RF Station, 188.8m
ARC, 3020.8m
C=65640.2m
RF
RF
RF
RF
APDR
APDR
APDR
APDR
APDR
APDR
C=67km

## Slide 36
PDR1
APDR
APDR
APDR
APDR
APDR
PDR3
APDR
CEPC Advanced Partial Double Ring Optics II

## Slide 38: Outline
5. CEPC Double Ring Scheme

## Slide 39
RF station
RF station
C=61km
?

## Slide 40
e-ring
IP3
IP1
IP4
Bypass
42m
IP2
Bypass
42m
Double Ring Scheme

## Slide 41: Outline
6. Summary
The first version of CEPC Partial Double Ring Lattice was designed (Version 1.0). The whole length of CEPC PDR is 3781.27m, full crossing angle is 30mrad, maximum distance between two ring is 14.913m.
The Dynamic Aperture need to be optimized. Now the DA of CEPC with PDR and Bypass(at IP2/4) and without FFS is better than before, but the DA with FFS is not good enough.
The linear lattice of PDR may also be optimized.

## Slide 42: Outline
  CDR Report & CDR & Plan & Next to do

## Slide 43
  CDR Report & CDR & Plan & Next to do
CDR Report (by the end of 2016)
  LSS2/4/6/8(inj/extr、RF)：optics的考虑，根据各功能段，重新设计，不再是和弧区相同FODO代替，接入实际optics。
  PDR：优化设计，孔径进展，争取达标。
  APDR8：线性Lattice搭建好，孔径优化初步结果。
  Double Ring：Lattice搭建好，带对撞区，孔径优化初步结果。
CDR (by the end of 2017)
  针对于选定的某一方案，各指标达标。

## Slide 44
CDR Report (by the end of 2016) ------SPPC
  参数优化且完备，包含纵向动力学参数。
  LSS2/4/6/8(inj/extr、RF)：optics的考虑，根据各功能段，重新设计，不再是和弧区相同FODO代替，接入实际optics。
  Lattice优化设计好,动力学孔径优化结果好
  比较好的version 1 的SPPC Lattice。
  CDR Report & CDR & Plan & Next to do

## Slide 45
  CEPC_ARC_PDR_IR_96fam_damp
0.8mm
5um
21.731um
0.08026um
37 SigmaX
63 SigmaY

## Slide 46: DA result
Dynamic aperture result
  W/O error of the magnets
  Synchrotron motion included, w/ damping
  Tracking with 100 turns
  Coupling factor =0.003 for y
  Working point (0.08, 0.22)
DAx
DAy

## Slide 47
Thank You !

## Slide 48: Acknowledge
The authors would thank Frank Schmidt very much for the help in SixTrack and Dynamic Aperture Study.
Thanks for Gang Xu, Qing Qin, Yuan Zhang, Yuemei Peng, Qingjin Xu, Xiaohao Cui, Zhe Duan and Yudong Liu’s kind help and beneficial discussion!

## Slide 49: Reference
1. F. Zimmermann, “HE-LHC & VHE-LHC accelerator overview (injector chain and main parameter choices)”, Report of the Joint Snowmass-EuCARD/AccNet-HiLumi LHC meeting, Switzerland, 2013.
2. F. Zimmermann et al., “FCC-ee overview”, in Proc. HF2014, Beijing, China, Sep. 2014, p.6-15.
3. Layout and Performance, in LHC Design Report Volume 1, European Organization for Nuclear Research, 2004, p21-22.
4. The Science of the CEPC and the SPPC, in CEPC-SPPC: Pre-CDR, Volume II - accelerator, The CEPC-SPPC Study Group, Mar. 2015, p.28-35.
5. J. Gao, “Review of some important beam physics issues in electron positron collider designs”, Modern Physics Letters A, Vol. 30, No. 11, p. 1530006, 2015.
6. F. Su et al., “Method study of parameter choice for a circular proton-proton collider”, Chinese Physics C, Vol. 40, No. 1, p. 017001, 2016.
7. D. Wang et al., “Optimization Parameter Design of a Circular e+e- Higgs Factory”, Chinese Physics C, Vol. 37, No. 9, p. 97003-0970, 2013.
8. M. Xiao et al., “Study on CEPC performances with different collision energies and geometric layouts”, Chinese Physics C, Vol. 40, No. 8, 2016.
9. F. Su, J. Gao et al, “SPPC Parameter Choice and Lattice Design”, TUPMW001, Proceedings of IPAC2016.
10. F. Su, J. Gao et al, “CEPC Partial Double Ring Lattice Design”, THPOR009, Proceedings of IPAC2016.
11. F. Su, J. Gao, etc., “CEPC partial double ring lattice design and SPPC lattice design”, IAS White Paper, submitted for publication, Apr. 2016.
12. F. Schmidt, “Dynamic Aperture in large Proton Accelerators”, ”A Talk on DA study in IHEP”, May 2016.
13. Oide, FCC-ee_150917.
14. P. Raimondi, Status on SuperB effort, La Thuile, March 11, 2006.
15. Kalbreier, et al, “Layout, design and construction of the electrostatic separation system of the LEP e+e- collider”, CERN, Geneva, Switzerland. 16. R. Martin, et al, “Status of the FCC-ee interaction region design”, HF2014 Workshop, Beijing, China, 9-12 October, 2014.