## Slide 1: Simulation check of main parameters (wd-160918)
ZHANG, Yuan
2016-09-29

## Slide 2: parameter for CEPC partial double ring （wangdou20160918）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 5.2 | 6.4
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.16 | 0.78
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 36.5 | 67.6
SR power /beam (MW) | 51.7 | 50 | 32.5 | 21.3 | 4.1
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.44 | 2.9
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.0078 | 0.88/0.008
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 9.7/0.088 | 9.4/0.089
x/IP | 0.118 | 0.041 | 0.042 | 0.013 | 0.01
y/IP | 0.083 | 0.11 | 0.11 | 0.073 | 0.072
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.74 | 0.11
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.95 | 3.78
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.88 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.7 | 1.2
n | 0.23 | 0.35 | 0.34 | 0.49 | 0.34
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.92 | 0.93
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 4.3 | 4.48

## Slide 3: H-low power
Track marco particels: 2*106
Collision: 104
Particles Lost: 127 => Beamstrahlung Liftime: 260min

## Slide 4: W
100 slice, 106/bunch
Bunch lengthing so strong?!
Need more check:
For example, RAD by beamstrahlung off.

## Slide 5: Z
100 slice, 106/bunch
Bunch lengthing so strong?!
Need more check:
For example, RAD by beamstrahlung off.

## Slide 6
Large Piwinski Angle (shifted region between source charge and field)
Spectrum of Beamstrahlung radiation
Other?

## Slide 7: Backup slides

## Slide 8
16-01-HK