## Slide 1: ICFA Higgs Factory Workshop: eeFACT2016
Weiren Chou
International Creative Team Meeting
November 18, 2016, IHEP, Beijing, China

## Slide 2
History of the Higgs Factory Workshop Series
2012-07-04: CERN announced the discovery of Higgs boson.
2012-07-08: Four days later, ICFA approved a special workshop on Higgs Factory (HF2012), with a subtitle “Linear vs Circular,” which included 4 types of Higgs factories: linear (ILC, CLIC, SLC-type), circular (TLEP/FCC, CEPC, SuperTristan, Fermilab site filler), muon collider and γγ collider. It took place in November 2012 at Fermilab. A summary report was published and well received.
2014-10-9/12: HF2014 in Beijing, organized by IHEP, with a focus on CEPC and FCC-ee. Formal proceedings was published via JACoW.
2016-10-24/27: Upon ICFA’s request, the name was changed to “eeFACT2016.” In addition to FCC-ee and CEPC, it also covered SuperKEKB, BEPC II, VEPP-2000, DAFNE, etc. It took place in Daresbury, UK and was jointly organized by CERN, KEK and IHEP.
The next one will be 2018 – hopefully back to North America, but uncertain due to lack of interest in circular e+e- colliders in the US. We will try SLAC first; if unsuccessful, we will consider Hong Kong.

## Slide 3
eeFACT2016 Group Photo

## Slide 4
-- LHC was in the plans since 1983…
e+e- 1989-2000
p p 2009-203x

## Slide 5
Tunnel Cross Section – SPPC + CEPC Magnets
Drill/Blast Method
6 m
SPPC
CEPC
Booster
2015

## Slide 6
LHC Tunnel – Magnet Section
3.6 m

## Slide 10: Talk 2 - Higgs Factory Concept, F. Zimmermann (CERN)
Key points:
  FCC-ee & CEPC exploit lessons & recipes from past & present e+e- and pp colliders: combining successful ingredients of recent colliders → extremely high luminosity at high energies – up to and beyond 1036 cm-2s-1
  Crab waist successfully implemented in design. Low emittance “easy” for large rings.
  Limitations are being carefully studied: Beamstrahlung, energy sawtooth, luminosity lifetime, SR fans in interaction region, the “Talman barrier”, energy consumption, emittance growth from beamstrahlung, ...
  Mitigations and innovative schemes are being implemented: more RF sections, double ring, partial double ring, magnet tapering, top-up injection, weak bends, asymmetric IR optics, improved klystron efficiency, 2-in-1 arc magnets, ...
Discussion:
  It was asked when FCC-ee could start operation. The answer was not before ~2035-2037 given the present schedule of the HL-LHC.
  The technical readiness for a large e+e- collider like FCC-ee or CEPC was discussed. It was concluded that the required technologies exist, feasibility is guaranteed and performance estimates are realistic. R&D will improve the power efficiency.

## Slide 11
FCC-ee injector

## Slide 12: New designs are coming…
400MHz,
1 cell, Nb/Cu
CERN 400/800 MHz, multi-cells, Nb/Cu
O. Brunner, FCC Week 2016, Rome
Jlab cavities with coax and on-cell dampers
952.6 MHz

## Slide 13: New materials and processes
Advanced N2 doping 1.3 GHz at FNAL
Peng Sha
650 MHz cavities for PIP-II at FNAL
Nitrogen doping for high Qo, adopted by LCLS-II
N2 doping

## Slide 14: Nb3Sn: State of the Art and Repeatability
M. Liepe eeFACT2016 October 26, 2016 Slide 14
Single-cell 1.3 GHz cavity at 4.2K
4.2 K performance
Q0 > 1x1010 at 4.2K
Current quench field ~17 MV/m
Residual resistance Rres = 11nΩ at max field
Matthias Liepe
- 50%
- 75%
SRF operation at ~4K instead of 2K!
Greatly simplified cryo-system
Greatly reduced cryo AC power
Nb3Sn

## Slide 15: Beyond Niobium: Next Generation Nb3Sn SRF Cavities
 | Niobium | Nb3Sn
Critical Temperature Tc | 9 K | 18 K
Q0 at 4.2 K | 6 x 108 | 6 x 1010
Q0 at 2.0 K | 2.5 x 1010 | >1011
Max. gradient Eacc (theory) | 50 MV/m | 100 MV/m
Approximate Eacc and Q0 given for 1.3 GHz TESLA cavities with Rres small
η4.2 K / η2.0 K ≈ 3.6,
simpler cryoplant
Halve # of cavities to reach energy?
4 x 1010
Increase in Q0 via N-doping
M. Liepe eeFACT2016 October 26, 2016 Slide 15
Nb3Sn

## Slide 16: HOM Damping Schemes: Three Main Types
M. Liepe eeFACT2016 October 26, 2016 Slide 16
Antenna / loop HOM couplers
Beamline HOM loads
Waveguide HOM dampers
RF absorbing materials
Matthias Liepe

## Slide 17: Example: 2x100 mA Cornell ERL Main Linac SRF
M. Liepe eeFACT2016 October 26, 2016 Slide 17
HGRP support post
Beamline HOM absorber
Helium Gas Return Pipe
~40K thermal shield
SC magnet
~10 m
7-cell cavity

## Slide 18: Cornell ERL Test Module Beam Test
M. Liepe eeFACT2016 October 26, 2016 Slide 18
HTC-2: No HOM Absorbers
HTC-3: With HOM Absorbers
Beam operation:
  High CW currents >40 mA
  No significant heating from HOMs
  No sign of beam instability or weakly damped modes

## Slide 19: Example: JLAB 1A ERL SRF R&D
M. Liepe eeFACT2016 October 26, 2016 Slide 19
Two 1.5 GHz, one 750 MHz prototypes built and tested
Design for >20 kW HOM power per cavity
BBU simulations for 1.5 GHz ERL
1.5 GHz ERL cavities
1.5 GHz ERL cavity
750 MHz ERL cavity
Module concept
HOM load concept

## Slide 20
HOM heating due to small gaps at PEP-II
damaged spoiler, RF shield, BPMs,…
A. Novokhatski

## Slide 22
SuperKEKB IR

## Slide 23
SuperKEKB IR

## Slide 24
FCC-ee IR

## Slide 25: The IR region - baseline
FCC-ee IR

## Slide 26: Some eRHIC IR Design Conventions and Terminology
Detector 4.5m Clear Space
IP
Hadron Beam
Electron Beam
Hadron Rear Side
Hadron Forward Side
Crab Cavities
Crab Cavities
Crab Crossing Scheme (With No Dipoles Inside Detector*)
*Except possibly a shielded dipole on forward side to increase experimental acceptance.
1m
20m
Note Distorted Scale
eRHIC IR

## Slide 27: Talk 1 - Crab Waist Concept, P. Raimondi (ESRF)
Key points:
  Crab waist scheme overcomes limitations from hourglass and beam-beam. Allows lower beta*; gains luminosity with large Piwinski angle
  Key feature: crab waist compensation – a new idea from 2006. Positive and useful experience from Dafne
  Price to pay: challenges in final focus system design/construction – but feasible
  Now a key concept for the next generation of high lumi colliders
Discussion:
  It was discussed whether there is a good case for turning Dafne into a test facility for studies on the large Piwinski angle and the crab waist scheme. While this would be useful, it was not entirely clear what would be added beyond the SuperKEKB experience and whether this would not interfere with Dafne physics. Also, the resource needs and their benefits would need to be analyzed.
  It was asked what the limit on beta* is in the crab waist scheme and whether this limit is consistent with the FCC-ee design. The discussion showed that other limits in the final focus design (dynamic aperture) must also be considered.

## Slide 30
Polarization

## Slide 31
New method for beam polarization and energy measurement

## Slide 32: Measurements vs Calculations
Daresbury, UK 24-27 Oct 2016
eeFACT
2016

## Slide 33: Tuning knobs for luminosity at KEKB
A method of parameter search based on downhill simplex method was developed in 2007, which can search 12 parameters simultaneously. The speed of the luminosity tuning became faster. However, with this method the achievable luminosity was not improved.
chromaticity of x-y coupling at IP
L and sy at the SRM
~3days
Machine tuning

## Slide 34
CEPC Power Consumption (ref. Pre-CDR)
Efficiency
(AC to beam) = 20%
For a 500 MW collider in China:
Assuming 1.5 “Snowmass unit” a year for operation:
500 MW x 4000 hours = 2 x 109 kW-hr
Electricity price in China: RMB 0.5 yuan per kW-hr
Yearly cost: RMB 1B (US$ 150M)
(50 Chinese cents per kWh)

## Slide 35
Chart: 
| Linac & transport lines | Booster | Magnet | SRF | Cryogenics | Regular electricity | Utilities | Detectors
 | 10 | 43 | 75 | 220 | 25 | 30 | 45 | 15
CEPC Relative Power Consumption (Pre-CDR)
9%
16%
5%
10%
6%
48%
2%
3%

## Slide 36
48 kV
34 kV
40 kV
38 kV
36 kV
34 kV
42 kV
Dotted lines – only changing P drive
Solid lines – changing P drive and Voltage
Power, MW
Efficiency, %
HEKCW
comparing simulated performances of MBIOT and HEKCW MBK
after 80 years a breakthrough in klystron efficiency!
I. Syratchev
A 40-beam prototype “BAC” klystron has been built and successfully tested at VDBT, Moscow, this year!
h=90%!

## Slide 37
Constable

## Slide 38: How to apply CPD method to klystron
*An insulator needs to insert between the body and the collector to isolate the collector from body.
Conventional
Schematic diagram of one for CPD
Isolate a collector from body to apply high-voltage for energy recovery.
Body is a ground.
High-voltage applies to Collector-body
Collector
Vk
RF out
Ground
Insulator and gap
Vk
Vc
Without insulator
Watanabe
Notes: クライストロン電源は既存の構成を出来るだけ保持する方式を考える。下図はVkとVcを直列にする「Power=(Vk+Vc)*Ib」が、
後述する並列「Power=Vk*(Ik+Ic)」または、6.6kV交流へ変換し既存電源の入力とする方式を考えている(詳細検討未だ)。

## Slide 39: Example of the Power balance of klystron within without CPD
3Φ AC 6.6 kV, ~ 270 A
KPS, DC power supply
(90 kV, Max 20 A)
90 kV, 8 A -> 720kW supply
UHF 508.9 MHz
RF out: 300 kW (CW)
RF in: ~ 2W (CW)
Collector loss
Without CPD -> 420 kW
With CPD -> 184 kW
(recovery: 236 kW )
Example of
: Toshiba E37703, CPD
In case of 300 kW RF output (η = 42%) power,
* Without CPD (Vk = 90 kV、Ib = 8 A)
Required DC power is 720 kW
-> RF out 300 kW,
Dissipate power in Collector 420 kW
* With CPD (Vk = 90 kV、Ib = 8A、Vc = 30 kV)
η = 42 -> 62%
-> RF out 300 kW
Dissipate power in Collector 184 kW
Recovery power 236 kW <- Pick-up by cable from collector, then reuse to drive a klystron
After driving CPD, the required DC power is shifted to about 500 kW using by recovery power from the collector.
Power picks by cable
Watanabe

## Slide 40
The proposed layout for the main dipoles features a twin aperture yoke and busbars to provide the Ampere-turns
450 mm
320 mm
120 mm
90 mm
210 mm
I = 3570 A, B = 50 mT
0
0.5 T
1.0 T
60×80 mm
Zimmermann

## Slide 41
Also for the quadrupoles a twin design with a 50% power saving is possible, with an F/D polarity constraint
0
0.75 T
1.5 T
NI = 13500 A
(287 A × 47 turns) B’ = 8.71 T/m
320 mm
640 mm
520 mm
88 mm dia
Zimmermann

## Slide 42
The resistive power for the quadrupoles is about of factor of two lower if the combined function lattice is used
Cu conductor
cable losses to be added, for quadrupoles likely only a few %
if twins are not used, then the power goes up to 43 MW for the pure dipole lattice, and 20 MW for the combined function one
at 175 GeV | current density [A/mm2] | total power, 2 apertures [MW]
(modified) pure dipole lattice | 2.3 | 21.5
(modified) combined function lattice | 2.0 | 12.4 (7.8 twins + 4.6 single)
Zimmermann

## Slide 43
Summary
CEPC is becoming a major player in the world e+e- collider community.
But “the grass is always greener on the other side of the fence.” I just feel we are still so much behind our neighbors (CERN, KEK) in almost all the fields.
Our hope is that we have a young army, and soldiers will become commanders when CEPC takes off.
Several fields need special attention:
  SRF
  HOM damper
  IR
  MDI
  Polarization and energy calibration
  “Green CEPC” (power reduction)