## Slide 1: Status of ECAL Optimization Study
Ji-feng Hu, Jing Li,
Prof. Hai-jun Yang, Liang Li
INPAC, SJTU

## Slide 2: Outline
Why ECAL optimization matters?
How to make optimizations
Preliminary results
  Basic performance
  Physics benchmarks
To do list

## Slide 3: Why ECAL optimization matters?
Both physics goals and budgets require geometry optimization.
ECAL and HCAL are two essential components for gamma/lepton/jets reconstruction and identification.

## Slide 4: Software Version and Samples
Software versions,
  Simulation: Mokka-08-03 revised
  Reconstruction: Arbor_KD_3.3 plus track-related processors
  Digitization : G2CDArbor
Samples,
  single particle, energy@5,10,20,50,100 GeV
  @, 1000 Events
  @, 1E5 Events
Geometry: cepc_v1 using SiW in ECAL,
  Cell size @ 1X1, 5X5, 10X10, 20X20 mm
  Number of layers @ 16, 20, 26, 30
  fixed total material.
  other sub-detectors taken by default.

## Slide 5: ECAL and HCAL Simulation Chains
Mokka-08-03
(SimCalorimeterHit)
CEPC_v1
Digitization in G2CDArbor
(CalorimeterHit)
Energy threshold 50 keV, to be checked
Reconstruction in Arbor_KD_v3.3 (LICH)
(lepton Identification)
Some new parameters for Arbor thresholds at different geometry setups.
Linear response only now.
Simple digitization, re-calibration coefficients for non-default geometry.
Emulated digitization models are under development.
New plugin for recording energy deposit in non-sensitive region.
Analysis
Z, best combination of two leptons.
H, two most energetic neutral particles.
Default tracking and clustering

## Slide 6: ECAL Setup
Parts | Thickness (mm) | Absorber (mm) | Dimension (mm) | Cell size (mm^2)
Barrel | 5.25 (L0-19) 7.35 (L20-29) | 2.1 4.2 | R, 1843 -2028 Z, 0.00-2350 | 5.08x5.08
Endcap | 5.25 (L0-19) 7.35 (L20-29) | 2.1 4.2 | R, 226.8-2088 Z, 2450-2635 | 5.08x5.08
ECAL
One tower
(side view)
One Tower
(sectional view)

## Slide 7: Zoom in Side View (ROOT Geo)
10.5mm
PCB
Si plate(orange）
Side shadow(grey and blue)
W plate (2.1 mm)
W plate (4.2 mm)
(white grey, dark grey)
14.7mm
Illustration:
2 thin layers
4 thick layers.
name | Radiation length (cm)
Si plate | 9.349
PCB board | 2.817
W plate | 0.350
GroundorHVMix | 2.732

## Slide 8: Energy Density Function
Energy deposit fraction in ECAL
(1) 99% energy of incident photon will be deposited in ECAL.
(2) the turn point is due to thick layers.
(3) W plates absorb ~82% energy of photons.
Energy fractions in materials
(1)
(2)
(3)

## Slide 9: Relative Energy Resolution
More layers, better energy resolution
Energy resolution almost is independent of cell size.
30 Layers
16 Layers
Cell 5x5 mm^2
20 Layers
26 Layers
Cell 20x20 mm^2

## Slide 10: Test of Higgs->γγ
Z reconstructed by two charged leptons
Higgs by the most energetic two neutral particles.
Background not yet investigated.
Higgs invariant mass fitted with a Gaussian
Energy re-calibration at different geometry.
Some new parameters values for Arbor.

## Slide 11: Analysis Logic of HiggsWW
1. LcfiplusProcessor weights
/lcfiweights/d0prob_zpole.root
/lcfiweights/z0prob_zpole.root
2. LICH weights
/new_1pfo/
ArborPFOs
[FSR correction]
ArborPFOs
Z Tag
[the least mass difference]
PFOs of Z candidates
Isolated lepton Tag
[no any charged found within a cone angle]
Isolated leptons
Vertex, JetClustering and FlavorTag
The other PFOs
The other PFOs
FsrArborPFOs
Refined Jets
Revising some over counting in loops.
Revising some MC truth matching.
Switch to PFOs exported by LICH.
Package provided by Libo liao

## Slide 12: HiggsWWlvqq
(Left), Z mass, (red) line indicates the nominal mass.
(Right), the recoiling mass, , lepton 1 and lepton 2 are coming from Z.
100000 events
M(Z) in (60, 120) GeV
M(Z) in (60, 120),
recoiling M(H) in (120,160) GeV

## Slide 13: Background Suppression
Cut A, M(Z) in (68.98, 113.38) GeV, approximately within 3 sigma region of Z pole mass. Recoiling M(H) within (120, 160) GeV, Angle of two jets >0;
Cut B, cut A plus number of isolated lepton >=1, its energy >5 GeV (energy threshold needs be discussed).
Other backgrounds are under investigation.
MC Truth

## Slide 14: Summary
SiW ECAL optimization was preliminarily studied.
  4 X 4 combinations of geometry were tested.
  Physics channels of Higgsγγ, WW are being thoroughly investigated
  Conclusions will be made after fine digitization development.
To do list,
  Jet Energy Resolution in HCAL
  Benchmark of H->WW with background analysis.

## Slide 15: Acknowledge
Thanks to Man-qi Ruan, Gang Li, Li-bo Liao, Dan Yu, Shi Chen, Bing Liu, Chen-dong Fu etc. for their helpful discussions and supports.

## Slide 16: ECAL Geometry (16 Layers)
Si fixed,
Thicker W plate (7.98mm)

## Slide 17: Di-jets Mass
(Left) Solid angle between two jets.
(Right) Invariant mass of di-jets. (red) line indicates W nominal mass, (blue) line the Higgs nominal mass. The Higgs peak is contributed by the leading lepton of virtual W decays mixing in jets reconstruction. Higgs and real W peak mass are a little larger than their nominal mass, which tells not well fined calibration.
M(Z) in (60, 120) GeV,
recoiling M(H) in (120,160) GeV and
Solid angle > 0

## Slide 18: Zoom in Side View (ROOT Geo)
10.5mm
14.7mm
PCB
Si plate(orange）
Side shadow(grey and blue)
W plate (2.1 mm, white grey, dark grey)
Air gap(white)
W plate (4.2 mm)