## Slide 1: Hough Based Tracking For Low Pt In MDC

## Slide 2: outline
Motivation
Implementation of Hough transform based tracking
  Tracking performance of Ψ(2s)-> π+π-J/Ψ , J/Ψ ->l+l-
  MC
  DATA
Time occupancy
Summary and outlook

## Slide 3: Motivation

## Slide 4
Hough transform : a mathematical transformation
Transform a point in real space to a line or a curve in parameter space
Points rest on a line in real space ← → lines or curves focus in Hough space
ρ=xcos(θ)+ysin(θ) hits becomes sinusoidal curves
Review of Hough transform method

## Slide 5: HOUGH Implemented in MDC
Hough
track finding
Rungekutta
Kalman fitting
PATTSF
MDC Digi
compare and
Reserve good tracks
Now cut condition of HOUGH is for low pt tracks ( event )
Track (pt>120MeV) lost by PATTSF may also found by HOUGH
Low Pt track by TSF&HOUGH will compare and reserve*
Mdc hit
Hough map
2D fitting
3D fitting
3D hit finding
Peak finding
  *Compare tracks
  If pt and center position satisfy certain condition , we consider them same track ,
  reserve one track with more hits , or better (dr,dz) , decided by different physics channel

## Slide 6
Peak finding in HoughMap
  Conformal transform is used to convert hits in a circle track to hits in a line
  Use Hough transform to convert points in a line to curves in parameter space
  Vote lines in histogram
  Peak finding method to determine tracks
HOUGH Implemented in MDC
2D fitting
3D track finding
3D fitting
Cut condition on HoughMap :
………

## Slide 7
  (MC) Ψ(2s)-> π+π-J/Ψ , J/Ψ ->l+l-
    tracking efficiency
    track matching with MC truth
    ghost track rate
    efficiency varies with dip angle
  (DATA) Ψ(2s)-> π+π-J/Ψ , J/Ψ ->l+l-
    tracking efficiency
    signal of j/psi recoil mass
Tracking Performance

## Slide 8
Tracking performance check with
Ψ(2s) ->J/ Ψ p + p - , J/ Ψ ->l+ l-
Track level
  |vz| < 10 cm and |vr| < 1 cm
  P < 2.2GeV/c
  |cosθ| < 0.93
Event level
  chisqvt(l) <10 & chisq(J/Ψ)<10
  3.0GeV/ < M(J/Ψ) < 3.2GeV/
  1.4GeV/c < p(l)< 1.7GeV/c, 0.05GeV/c < p(p) < 0.5GeV/c
  Emcene>2.7GeV/
n4 : find 4 good tracks , pass selection
npion: find 3,4,5 good tracks , pass selection
efficiency：n4/npion

## Slide 9
Tracking performance check with
  Ψ(2s)-> π+π-J/Ψ , J/Ψ ->l+l-
From signal MC 500k events
mix noise in reconstruction
Tracking efficiency increased ~4.5% for 50<MeVpt<100MeV , relative increased ~6.5%
14% tracks inside pt(0.05~0.12)GeV
π tracks vs pt
(GeV)

## Slide 10: Track Matching with MC truth
We can see tracks found by HOUGH are most real tracks in MC
when set cutRate = 0.5
if >50% hits of the reconstructed track come from one track in MC -> match in MC
Matching efficiency vs cutRate
tracks reconstructed by HOUGH from the MC ppjs events
Set cutRate to 0.5, 0.6, 0.7,0.8,0.9
Matching efficiency all higher than 80%

## Slide 11: Ghost Track Rate
 | N=3,4,5 | N=4 | N=5 | N5/N(3,4,5)
PATTSF+HOUGH | 209257 | 193428 | 290 | 1.38%
PATTSF | 207338 | 189847 | 240 | 1.16%
find 5 tracks passed physics selection : a ghost track in this event
HOUGH won’t get much ghost tracks
Most ghost track from multi turn tracks

## Slide 12: Tracking efficiency vs cosθ
|cosθ|<0.2 6% tracks , increase 10%
|cosθ|>0.83 54% tracks , increase 2%
pt(0.05~0.12GeV)
π tracks distribution vs cos
Big dip angle tracks take the most part , so we can’t see clearly tracking efficiency increase in this channer

## Slide 13: Curved tracks salvaged by HOUGH (compare curfinder)
Hough transform can easily determine a circle track on HoughMap
Show 2D histogram

## Slide 14
In some cases , 2nd turn track close to the 1st
We collect hits but can’t tell from which turn
Bad track parameter , need some fitting method
Multi turn tracks retrieve by HOUGH

## Slide 15: Difficulties With Large Dip Angle Tracks
Layer max vs cos
Big dip angle tracks has few hits , hard to reconstruct

## Slide 16
Hits covered by other tracks
Stereo hits influenced by inner chamber noise

## Slide 17: Salvage Tracks (pt>0.12GeV)
HOUGH can get back lost track more than 120MeV
Noise hit nearby the track cause bad influence in PATTSF
PATTSF
PATTSF+HOUGH

## Slide 18
Salvage Tracks (pt>0.12GeV)
PATTSF
PATTSF+HOUGH
track lost because two track too close in PATTSF

## Slide 19
Data take from 8093~8195 , Boss version 6.6.5
Signal MC
Increase of tracking efficiency can be proved in data
Tracking efficiency check with
Ψ(2s) ->J/ Ψ p + p - , J/ Ψ ->l+ l-

## Slide 20: J/psi recoil mass increased after HOUGH
PATTSF+HOUGH
PATTSF
signal add 1.7% with HOUGH , signal/noise ratio don’t get worse
PATTSF+HOUGH : 96836 sig/sqrt(sig+noise)= 297
PATTSF: 95215 sig/sqrt(sig+noise)= 295

## Slide 21: Good J/psi event Found with HOUGH
Show some data events from besvis

## Slide 22: Time Occupancy
version | Time (ms)
PAT | 3.99e+08
TSF | 1.61e+09
Hough | 3.06e+08
version | Time (ms)
Reconstruction time(No HOUGH) | 1.85e+10
Reconstruction time(Add HOUGH) | 1.93e+10
Cpu : Intel(R) Xeon(R) CPU E5-2650 v2
@ 2.60GHz
Cpu cores :8
64 bit system
Three track finding algorithm
Time of one Reconstruction Job
Hough tracking package won’t cost too much time for the current reconstruction
Time cost increase 4.3%

## Slide 23: summary

## Slide 24: outlook

## Slide 25
e efficiency:
N4/(N3+N4)
PATTSF+HOUGH: 24279/46160= 52.6%
PATTSF :20864/41738=50%
N==4 increase 4422 , 10.6%