## Slide 1: HOM coupler design
Hongjuan Zheng，Fanbo Meng
2016-11-08

## Slide 2: Reduced model & 3D model with cavity-v.1
f=1349.71 MHz
TM01-TEM

## Slide 3: Qe with HOM couplers & Qe threshold-v.1
Beam parameters (wangdou20160918)
Qe (CST) is the result with HOM couplers
The other 3 Qe values are stand for the threshold for different design.
For Z design, the Qe for the TM011 mode can not meet the requirement.
Monopole mode results
For H design, the Qe for the TE111 mode can not meet the requirement. This mainly caused by the small frequency difference between this mode and the fundamental mode.
More work need to be done.
Dipole mode results

## Slide 4: Transmission line equivalent circuit results-v.2
l1
l2
l3
l4
Values for the transmission line equivalent circuit：
l1=4.83cm, l2=10.027cm, l3=2.0cm, l4=1.0cm, Ln=13.52nH, Cn=4.43pF, M23=8.29nH, C3=1.57pF, Zt=96.6 Ω, Z=50 Ω
Outer diameter of the coupling tube is 80 mm. Inner diameter of the coupling tube is 16 mm.

## Slide 5: Mutual inductance & notch filter inductance
decide the geometry and size
Using transmission line models to determine the mutual inductance and notch filter inductance.
Design requirement: M23=6.79 nH
a=30 mm, b=12 mm M23=6.78 nH
Design requirement: M12=8.29 nH
r=4.7 mm M12=11.925 nH
mutual inductance
notch filter inductance
a
b
r
Difference between v.2 and v.1:
Inner conductor radius increase.
The damping bandwidth change from 700-1400MHz to 780-1400MHz.
M23 change from sector to cuboid.
M12 change from sector to rod.

## Slide 6: 3D simulations-v.2
Reduced model
Coaxial line model
TM01-TEM
TEM-TEM
The 3D model is built with the TML results.
Compare the reduced model with coaxial line model, the notch frequency is different.
There are several stop bands with coaxial model.

## Slide 7: Reduced model vs TML model-v.2
TM01-TEM
after tune fundamental mode f

## Slide 8: Reduced model--different parameters-v.2

## Slide 9: Broadband coupler for SPL
对高次模阻尼在-10dB左右

## Slide 10: Increase the area of the probe end-v.2
增加探针头部和场接触面积（初步结果）
对TE111阻尼效果改善不大？
宽带阻尼效果变差，需要重新优化其他几个几何参量
基模阻尼效果不好
TE11-TEM
TM01-TEM

## Slide 11: HOM coupler tube length
Face1
HOM coupler r=40mm
d=100mm
h
h=70mm, power dissipated on face1 is
P1=0.157mW(Eacc)
When Q0=2E+10
Pc=12.5W
l1=48mm
l2=100mm
2r=10mm
a=36mm
h’=48-10+36/2=57 mm
h’

## Slide 12: HOM coupler tube length
Face1
Face2
model 1
1.3 GHz IHEP02 cavity end group
Face1_integral_e=15.1,
Face2_integral_e=3.1e+5
Face1
Face2
main coupler r=30mm
height=46mm
d=65mm
HOM coupler r=40mm
d=100mm
h
model 2
650 MHz cavity end group
h | F1_int._e | F2_int._e
75 | 9.2 | 4.7e+5
70 | 12.8 | 4.7e+5
65 | 17.5 | 4.7e+5
60 | 23.1 | 4.7e+5

## Slide 13: Qe with different depth of penetration
TE111-PI/2
TE111-PI/2
TE111-PI
TE111-PI
10mm
10mm
10mm
10mm
15mm
15mm
15mm
15mm
TE111-PI/2
TE111-PI/2
TE111-PI
TE111-PI
10mm
10mm
10mm
10mm
15mm
15mm
15mm
15mm
TM110-PI
TM110-PI
TM110-PI/2
TM110-PI/2
TM110-PI
TM110-PI
TM110-PI/2
TM110-PI/2
The polarization direction for the dipole is different.
The longer the depth of penetration, the better.
TE111
TM110

## Slide 14: Qe with different angles between HOM couplers
120deg
110deg
100deg
90deg
TE111-PI/2
TE111-PI/2
TE111-PI
TE111-PI
TE111-PI/2
TE111-PI/2
TE111-PI
TE111-PI
TE111-PI/2
TE111-PI/2
TE111-PI
TE111-PI
TE111-PI/2
TE111-PI/2
TE111-PI
TE111-PI
120deg
110deg
100deg
90deg
120deg
110deg
100deg
90deg
TM110-PI-1
TM110-PI-2
TE111
TM110

## Slide 15: 存在的问题&下一步
存在问题
对TE111的阻尼如何解决？（离基模太近，保证基模的阻尼足够则不能保证TE111的阻尼）
下一步
继续探索增加内导体端部与场的接触面积的可能性
窄带耦合器设计（loop型），与宽带耦合器结果对比