## Slide 1: UIUC mRPC R&D o Introduction & Physics Motivation o RPC design & assembly o Cosmic Ray Muon Test o Beam Test
with BNL (lead), Howard University, CCNY, IHEP and ACU, Matthias Grosse Perdekamp, UIUC

## Slide 2: Previous RPC Work at UIUC: 2 Gap Bakelite RPCs for Triggering – Adapting CMS Design for PHENIX at RHIC
o RPC system (1.2ns timing resolution) for the PHENIX W-trigger.
UIUC (lead), RBRC, UC Boulder, ISU, CIAE, Columbia, GSU, UCR,
Korea University, ACU, Muhlenberg, Hanyang University
o R&D 2002 to 2008, construction 2008 to 2011, data taking 2011-2013,
final results released at Spin 2014 at PKU in Beijing
Two 10 m diameter RPC-3 stations
Two 3 m diameter RPC-1 stations

## Slide 3: ePHENIX: SIDIS with TOF for PID
Carried out initial event generator simulation for a mRPC TOF wall added to the endcap of a future ePHENIX detector at a possible EIC.
Choose one channel (of many possible in SIDIS with PID) to demonstrate utility of a TOF based PID: measurement of AUT resulting from non zero strange quark distributions.
Assumed very high timing resolution: 10 ps for the simulation!
psTOF significantly increases statistical significance !
Previous event generator level simulation: Difference ΔAUT in AUT for δsI(x) and δsII(x)
ΔAUT
RICH only
TOF only
TOF & RICH
π
K
p
psTOF Wall
TOF response with propaga-
ted errors in momentum and
timing resolution in v vs p
for π, K and p

## Slide 4: TOF PID: Particle Separation vs σt
Momentum range of TOF PID reaches interesting levels if one can achieve ~ 10-20 ps
Timing resolution | Distance | Pion-Kaon Separation | Kaon-Proton Separation
σtot=100 ps | 1m |  | 
σtot=10 ps | 1m |  | 
σtot=10 ps | 3m |  | 

## Slide 5: Two TOF Options Considered for ePHENIX
mRPC technology likely will be cheaper and available earlier, but not perform as well compared to the MCP-PMT based TOF
psTOF Walls
MCP-PMT TOF
mRPC TOF

## Slide 6: mRPC Design Derived from ALICE/Williams mRPC
 | MRPC ( C. Williams et al. ) | MRPC ( UIUC & BNL)
Gas Gap Width | 160um (fishing line) | 105um (fishing line, and 165, 125, 75um)
# of Gas Gaps | 4 stack x 6 layers = 24 | 4 stack x 9 layers = 36
# of thin glass layers | 4 stacks x 5 layers = 20 (250um thick glass) | 4 stack x 8 layers = 32 (210um thick glass)
Preamplifier | Differential type, NINO chip | TI LMH6554 2.8-GHz + Evaluation Board
TDC and DAQ | Oscilloscope (10Gs) | DRS4-V5(5Gs) + PC
Time resolution | 20 ps published (16 ps private comm) | 18 ps with cosmic rays, 25 ps at 80 Hz/cm2
Gas gap width : 160um
(16ps timing resolution)
Gas gap width : 105um
ALICE/CERN, Crispin Williams
BNL&UIUC Prototype
4 x
4 x
PCB
glass
Gas gap

## Slide 7: BNL/UIUC PCBs for Electrode and Signal Pickup
PCBs (3 layers)
- One board flavor – interchangeable
- HV connection integrated on board
- Rounded readout strips
- Outer dimension : 196mm x 70mm x 1.5mm
- Readout strip : 4 strips, 170mm x 10mm
- The strips are placed in the middle layer
PCB Design
HV feed pad
Post for spacers
+ fishing line
12 PCBs
ch1
ch2
ch3
ch4

## Slide 8: UIUC Electrodes on the PCB Surface
Carbon coating with carbon spray
Polished the surface with soft paper
Measured the resistivity
( 0.5 ~ 1.5 M Ohm/Square)
Preparing carbon painting
Silicon (RTV 159)
Thick glass plate (550um) for a insulation
HV connection pad
Carbon electrode
Double sided Kapton tape

## Slide 9: UIUC Electrode PCBs
Electrode coating ✔
Electricity Insulation ✔
Cable connection ✔
10 PCBs for two MRPCs(4 stacks)
Silicon (RTV 159)

## Slide 10: Wiring of Fishing Line for Gas Gap
105um diameter of fishing line
Stacking glass plates and fishing lines
4 stacks

## Slide 11: MRPC Prototypes Assembled at UIUC
Two MRPCs assembled
Close view of glass plates

## Slide 12: MRPCs
MRPC1
MRPC2
Differential Preamp.
TI, LMH 6554
2.8GHz bandwidth
Waveform
Analyzer
(DRS4-V5)
5GHz sampling
speed
Gas chamber in the cosmic ray test stand at UIUC
Gas Input & Output
HV : eg. 20kV ( +11kV, -11kV)

## Slide 13: Time Resolution Measurement at UIUC
MRPC-A
MRPC-B
DRS4-V5
(Wave form digitizer)
PC
(DAQ)
DC0,1,2
SC1
SC4
preamp
preamp
Gas Cylinder
USB
50 Ohm cable (<1m)
ch2
ch2
Muon trigger
Gas Mixture : “Freon” (R134a) 90% : Iso 5% : SF6 5%
SC2
SC3
DC3,4
Pb Block

## Slide 14: Raw Cosmic Ray Events: Scope Traces
w/o preamp ,+-9kV(18kV)
Top MRPC
Bottom MRPC
[mv] vs [ns]

## Slide 15: Efficiency and Time Resolution
25.4ps / √2
~ 18ps
Cosmic rays
22kV
C. Williams
CERN, 2010
[ns]
MRPC1- MRPC2
Cosmic rays
22kV
Efficiency
Preamp : NINO
10 GHz, Oscilloscope

## Slide 16: Beam (Halo) Test at COMPASS, CERN
MRPCs
Beam
Halo
Obsorber
π-
Parasitic to COMPASS Drell-Yan Run 2015
- Fixed target experiment – transversely polarized targets
- 190 GeV π- beam, Intensity of 4x108 /s
Setup the MRPCs at the downstream of the COMPASS detectors
Varied flux rate by moving the MRPC up and down position
Maximum flux rate measured ~80Hz/cm2
Two MRPCs in the same gas chamber
COMPASS Spectrometers
For the MRPC rate capability test, Oct 15th ~ Nov 15th 2015

## Slide 17: Efficiency and Time Resolution
36ps / √2
= 25.4ps
COMPASS
19kV
[ns]
Obtained 25.4ps with flux rate of 80Hz/cm2
Overall efficiency results are lower than cosmic ray
-> Background issue? (no tracking system included)
Efficiency results on 5Hz/cm2 lower than on the 80Hz/cm2
-> possibly related to gas issue.
Need more tests.
Time resolution [ps]
MRPC1 – MRPC2 [ps]
25ps
Blue : 5Hz/cm2
Black : 80Hz/cm2

## Slide 18
SLA (Stereo Lithography Apparatus)
Build size : 250x250x250mm
Vertical resolution : 0.0025mm
Position repeatability : 0.0076mm
Typical velocity : 5mm/sec
Two resins
  WaterClear Ultra 10122
  (Dielectric constant : 3.0 ~ 4.0)
  ProtoGen O-XT 18420
  (Dielectric constant : 3.1 ~ 3.6)
0.3 mm gas gap width
5 gas gaps every column
(I) Experimenting with 3D Printed Gas Gaps for mRPCs

## Slide 19
2 stacks, 10 gas gaps, 0.3mm gas gap width
easy assembly!
Cosmic ray signal @ 14kV.
97% Freon R134a, 3% SF6.
First (noisy) Signals from 3D Printed Gas Gaps in a mRPC at UIUC

## Slide 20
12 layers of 25um thick Mylar
13 gas gaps with 125um gas gap width
Used 125um thick Mylar for the spacers.
(II) Experimenting with Mylar mRPCs
Side view of 12 Mylar layers
25um Mylar film
125um Mylar
Spacers

## Slide 21: Summary
UIUC has been working with BNL, Howard, ACU, CCNY and IHEP Protvino on 20ps timing resolution mRPCs.
Reached resolution of 18 ps with cosmic rays and 25 ps with 80 Hz. Possibly additional test beam for
systematic studies.
Use of float glass limits rate capabilities.
Consider different resistive plate materials.
Funding situation uncertain. Focus currently on R&D
for RPC and mRPC use in port scanners.

## Slide 22: Issues on the size of signals
Did not operate correctly pressure regulation at COMPASS limited by access during
beam operation ….
Height of signal changed significantly at the COMPASS experimental hall
Pressure ~ 1bar
(Top) Pressure > 1bar
(Bottom) Pressure >> 1bar
Gas flow : Input flow (Yellow arrow), output flow (Red arrow)
Beam
[mV]
[ns]

## Slide 23: Time Correlations
Ch1
Beam direction
Ch2
Ch3
Ch4
MRPC1
MRPC2
HV 19kV
R134a 98% : SF6 2%
80Hz/cm2
MRPC1 ch1
MRPC2 ch2
Blue : MRPC1, ch1 – ch3
Red : MRPC2, ch2 – ch4
[ns]
[ns]
MRPC1 – MRPC2
MRPC1 – MRPC2
Ch1 Signal slope [mV/ns]
(ch1 – ch3) – (ch2- ch4)