## Slide 1: TOF readout for high resolution timing for SoLID
Alexandre Camsonne
Jefferson Laboratory
Hadron China 2017
TOF miniworkshop
July 28 2017

## Slide 2: Outline
SoLID SIDIS
SoLID requirements for TOF
Readout options : discriminator TDC vs sampling
A/D chips
TDC options
Sampling chips
DRS5 option from PSI
Kansas University Amplifier
SoLID SIDIS background studies
SoLID TOF chip specs wish list
Conclusion

## Slide 3: SoLID SIDIS setup

## Slide 4: Pion Kaon Separation by TOF

## Slide 5: SoLID requirements
TOF for SIDIS experiment for Kaon ID
Baseline 80 ps , ideally 20 ps
Trigger rate 100 KHz min, ideal 200 KHz
FADC based trigger with up 8 us latency
GEM readout 4 us latency
Need 4 us latency for TOF ideally 8 us

## Slide 6: Two options
Depends on detector performance : Usual method : discriminator + TDC
    Amplifier discriminator
    TDC : ASIC or new FPGA technique
  Waveform sampling
    No discriminator
    Full bandwidth
    Better timing resolution up to 1 ps
    Need algorithm to extract time on board
    Or readout full waveform ( very large amount of data)

## Slide 7: Readout options
Amplifier Discriminators front end
  NINO (CERN) (8 channels – 32 channels version )
  GSI Padiwa (16 channels) 150 $ for 16 channels
  MAROC ( Omega IN2P3)
  VMM3 (BNL)
  Need to check timing performance of discrimination and amplification, bandwidth, timewalk corrections

## Slide 8: TDCs
HPTDC 25 ps
  V1290 (32 channels about 10 K$ )
  CAEN planning to develop better TDC
FPGA TDCs
  TRB3 11 ps ( 192 channels / 2300 euros )
  VETROC JLAB 20 ps ( need development ) 128 channels about 6 K$ ( 5 board ordered for Compton, can test TDC )

## Slide 9: Sampling chip
Chip | Sampling Frequency (GHz) | Bandwidth GHz | Number of samples | Number of channels | Readout frequency (MHz) | Resolution (ps)
PSEC4 | 4 to 15 | 1.5 | 256 | 6 | 40 to 60 | 9
SAMPIC | 3 to 8.2 | 1.6 | 64 | 16 – 8 (at 10 GHz) | 80 | 5
DRS4 | 0.7 to 5 GHZ | 0.950 | 1024 | 9 | 33 | 1
DRS5 | 10 | 3 | 4096 | 32 | 300? | 5?
PSEC5 | 5 to 15 | 1.5 to 2 | 32768 | 4 | 500 | 5?
Latest generation with multilevel analog buffer : dead time less up to a few MHz and allow for L2 ( DRS5 )

## Slide 10: Plans for DRS5
Increase analog bandwidth ~5 GHz
  Smaller input capacitance
Increase sampling speed ~10 GS/s
  Switch to 110 nm technology
Deeper sampling depth
  8 x 4096 / chip
Minimize readout time (“dead time free”) for muSR & ToF-PET
  (minor) reduction in analog readout speed (30 ns  20 ns)
  Implement FIFO technology
J. Milnes, J. Howoth, Photek
~MHz event rate
CTA
mSR

## Slide 11: Next Generation SCA
Low parasitic input capacitance  High bandwidth
Large area  low resistance bus, low resistance analog switches  high bandwidth
Short sampling depth
Digitize long waveforms
Accommodate long trigger delay
Faster sampling speed for a given trigger latency
Deep sampling depth
How to combine
best of both worlds?

## Slide 12: Cascaded Switched Capacitor Arrays
shift register
input
fast sampling stage
secondary sampling stage
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
32 fast sampling cells (10 GSPS/110nm CMOS)
100 ps sample time, 3.1 ns hold time
Hold time long enough to transfer voltage to secondary sampling stage with moderately fast buffer (300 MHz)
Shift register gets clocked by inverter chain from fast sampling stage

## Slide 13: How noise affects timing
voltage noise
band of signal
timing jitter arising
from voltage noise
timing jitter is much smaller
for faster
rise-time
voltage noise Du
timing uncertainty Dt
signal height U
rise time tr
number of samples on slope

## Slide 14: TDC vs. Waveform Digitizing
Q-sensitive
Preamplifier
PMT/APD
Wire
Shaper
TDC
Constant
Fraction
Discriminator
CFD and TDC on same board  crosstalk
CFD depends on noise on single point, while waveform digitizing can average over several points
Inverter chain is same both in TDCs and SCAs
Can we replace TDCs by SCAs?  yes if the readout rate is sufficient

## Slide 15: Typical Waveform
Only short segments of waveform need high speed readout

## Slide 16: Dead-time free acquisition
Self-trigger writing of short 32-bin segments
Simultaneous reading of segments
Quasi dead time-free
Data driven readout
    Ext. ADC runs continuously
    ASIC tells FPGA when there is new data
Coarse timing from 300 MHz counter
Fine timing by waveform digitizing and analysis in FPGA
20 * 20 ns = 0.4 ms readout time  2 MHz sustained event rate
Attractive replacement for CFD+TDC
DRS5

## Slide 17: WaveDAQ System
Crate Management Board
Power supply 24V / 300W
Fan / Temp. control
Power cycle each slot
FPGA Firmware upload
Local control via buttons
Ethernet remote control
Data Concentrator Board (DCB)
Trigger Concentrator Board (TCB)

## Slide 18: PSI WaveDAQ
WaveDAQ system has been designed to fulfill needs of MEG II experiment
System has huge potential for many others (costs: ~150 US$ / channel incl. crate, power, HV)
Status: Crate fully working, trigger board and WaveDREAM board successfully tested, beam test 2015, DCB under design
4 crate system end of 2016, full system (35 crates) in 2017
DRS5 chip (no dead-time) planned for 2018+

## Slide 19: PSEC

## Slide 20
Eric Oberla
http://annie.uchicago.edu/lib/exe/fetch.php?media=2014_3_1_annie_electronics.pdf

## Slide 21: SoLID MRPC High resolution TOF
A MRPC prototype for SOLID-TOF in JLab
Y. Wang, X. Fan DOI: 10.1088/1748-0221/8/03/P03003 JINST 8 (2013) P03003
Test in beam at JLAB in 2011 during g2p experiment
Better
than 95 %
efficiency
Timing resolution
~ 85 ps

## Slide 22: Test run signals
40 ns
~ 1 us
Signal after long cables
4ns samples
1 tick = 10 samples = 40 ns
500 ns

## Slide 23: In time signal
Good signals

## Slide 24: Effect of background
Data was taken at 50 nA
scale by 240 to have an idea of 12 uA
baseline
widens
Accidental pulses

## Slide 25: Amplifier Kansas University
SiGe amplifier developped to TOTEM Ultra Fast silicon detector by Kansas University
less than 10 ns width with diamond detector

## Slide 26: Amplifier laser signal silicon
Silicon pulsed at 10 MHz with KU amplifier

## Slide 27: SoLID background

## Slide 28: Single rate
Beam on target
Average rate/channel:
  total induced charge > 0.0 pC: 1.2 MHz
  total induced charge > 0.5 pC: 893.2 kHz
total induced charge cut (pC) | Average rate / channel (MHz)
0.0 | 1.20
0.1 | 1.11
0.2 | 1.06
0.3 | 1.00
0.5 | 0.95
0.6 | 0.84
0.7 | 0.80
0.8 | 0.76
0.9 | 0.72
1.0 | 0.69
1.1 | 0.65
total induced charge > 0 pC
Study by Sanghwa Park ( Stony Brook )

## Slide 29: Total incident particle rate - cut scan
Charge cut scan: scan range (0.2 - 0.9) pC
Study by Sanghwa Park ( Stony Brook )

## Slide 30: Total incident particle rate - cut scan
Charge cut scan: scan range (0.2 - 0.9) pC
Charge > 0.2 pC
~ 95% reduced
(#total incident particles)
Study by Sanghwa Park ( Stony Brook )

## Slide 31: SoLID background
Single channel rate at about 1 MHz level
Assume 30 ns timing window, about 3% probability to have a hit
Preliminary rate show pile-up should be ok
TDC option should work
Sampling option still desired option for better timing resolution and pile-up events

## Slide 32: Pile-up

## Slide 33: Pile-up example calorimeter DVCS

## Slide 34: Ideal features for SoLID TOF
5 to 10 GHz sampling rate
20 ps or better timing resolution
1 GHz or more analog bandwidth
Waveform readout
On chip Zero suppression
Discriminator for fast trigger
External trigger ( single channel trigger rate is about 1 MHz )
can handle up to 200 KHz of trigger rates
Data transfer capability
  on chip suppression required
  assume 3300 channels 10 ns at 10 GHz 12 bit at 200 KHz and occupancy 1 % : 900 MB/s (1.6 MB/s per chip 6 channel per chip : 10 Mbit/s link ok, 100 Mbit/s link desired)
8 us buffer latency ( 4 us minimum)

## Slide 35: Conclusion
SoLID SIDIS experiment requires 80 ps
20 ps timing resolution extend K/pi separation at high momentum up to 5.5 GeV
Preliminary background studies about 1 MHz per channel but need more studies
TDC and A/D option should work
New generation chips available in 2018
Sampling option desired for SoLID DRS5 or AARDVARC good candidates