## Slide 1: Optics design for CEPC collider ring
Yiwei Wang, Yuanyuan Wei, Yuan Zhang, Sha Bai, Dou Wang,
Huiping Geng, Chenghui Yu, Jie Gao
IHEP, Beijing
CEPC-SPPC workshop, IHEP, 6-8 NOV 2017

## Slide 2
Outline
Introduction
Optics of Collider ring (linear optics, nonlinearity correction)
  Interaction region
  Arc region
  RF region
  Straight section region
  Whole ring
Summary

## Slide 3
Introduction
Circumference=100 km
  2 interaction regions, 2 RF regions, 4 straight sections, 8 arc regions
In the RF region, the RF cavities are shared by two rings for H mode.
Twin-aperture of dipoles and quadrupoles is adopt in the arc region to reduce the their power. The distance between two beams is 0.35m.
Compatible optics for H, W and Z modes
  For the W and Z mode, the optics except RF region is got by scaling down the magnet strength with energy.
  For H mode, all the cavities will be used and bunches will be filled in half ring.
  For W & Z modes, half number of cavities will be used and bunches can be filled in full ring.
Notes: 2 fold symmetry

## Slide 4
Parameters of CEPC collider ring
 | Higgs | W | Z
Number of IPs | 2 |  | 
Energy (GeV) | 120 | 80 | 45.5
Circumference (km) | 100 |  | 
SR loss/turn (GeV) | 1.68 | 0.33 | 0.035
Half crossing angle (mrad) | 16.5 |  | 
Piwinski angle | 2.75 | 4.39 | 10.8
Ne/bunch (1010) | 12.9 | 3.6 | 1.6
Bunch number | 286 | 5220 | 10900
Beam current (mA) | 17.7 | 90.3 | 83.8
SR power /beam (MW) | 30 | 30 | 2.9
Bending radius (km) | 10.9 |  | 
Momentum compaction (10-5) | 1.14 |  | 
IP x/y (m) | 0.36/0.002 |  | 
Emittance x/y (nm) | 1.21/0.0036 | 0.54/0.0018 | 0.17/0.0029
Transverse IP (um) | 20.9/0.086 | 13.9/0.060 | 7.91/0.076
x/y/IP | 0.024/0.094 | 0.009/0.055 | 0.005/0.0165
RF Phase (degree) | 128 | 134.4 | 138.6
VRF (GV) | 2.14 | 0.465 | 0.053
f RF (MHz) (harmonic) | 650 |  | 
Nature bunch length z (mm) | 2.72 | 2.98 | 3.67
Bunch length z (mm) | 3.48 | 3.7 | 5.18
HOM power/cavity (kw) | 0.46 (2cell) | 0.32(2cell) | 0.11(2cell)
Energy spread (%) | 0.098 | 0.066 | 0.037
Energy acceptance requirement (%) | 1.21 |  | 
Energy acceptance by RF (%) | 2.06 | 1.48 | 0.75
Photon number due to beamstrahlung | 0.25 | 0.11 | 0.08
Lifetime due to beamstrahlung (hour) | 1.0 |  | 
F (hour glass) | 0.93 | 0.96 | 0.986
Lmax/IP (1034cm-2s-1) | 2.0 | 4.1 | 1.0

## Slide 5
Linear optics of Interaction region
Provide local chromaticity correction of both plane
L*=2.2m, c=33mrad, GQD0=151T/m, GQF1=102T/m
IP upstream of IR: Ec < 100 keV within 400m, last bend Ec = 47 keV
IP downstream of IR: Ec < 300 keV within 250m, last bend Ec = 95 keV
The vertical emittance growth due to solenoid coupling is less than 4%.
Relaxed optics for injection can be re-matched easily as the modular design.
L*= 2.2m
x*= 0.36mm
y*= 2mm
GQD0-151T/m
GQF1102T/m
LQD0=1.73m
LQF1=1.48m
FT
CCY
CCX
CW
max deviation between two beamlines 9.7m
Notes: New IR bends

## Slide 6: Nonlinearity correction of Interaction region
  Local chromaticity correction with sextupoles pairs separated by –I transportation
  up to 3rd order chromaticity corrected with main sextupoles, phase tuning and additional sextupole pair 2,3)
Ref: 2) Brinkmann 3) Y. Cai

## Slide 7: Nonlinearity correction of Interaction region
  Local chromaticity correction with sextupoles pairs separated by –I transportation
  all 3rd and 4th RDT due to sextupoles almost cancelled 1)
  tune shift dQ(Jx, Jy) due to finite length of main sextupoles corrected with additional weak sextupoles 3,4)
  Break down of -I due to energy deviation corrected with ARC sextupoles
    could be further optimized with odd dispersion scheme 5),
    Brinkmann sextupoles 2) or pair of decapoles 3)
Ref:
1) K. Brown
2) Brinkmann
3) Y. Cai
4) Anton
5) K. Oide
6) J. Bengttson’s

## Slide 8: Optics choice of ARC region
 | Interleave sextupoles | Non-interleaved sextupoles
60  /60 | n=6 All 3rd RDT due to sextupoles cancelled All 4th RDT except 2Qx-2Qy due to sextupoles cancelled dQ(Jx,Jy): accumalte to be large dQ(): small even with 2 families DA on momentum: limited by tune shift dQ(Jx,Jy) DA off momentum: easy to optim. | -
90  /60  | n=12 All 3rd RDT due to sextupoles cancelled All 4th RDT except 4Qx due to sextupoles cancelled dQ(Jx,Jy): accumalte to be large dQ(): small even with 2 families DA on momentum: limited by tune shift dQ(Jx,Jy) DA off momentum: easy to optim. | -
90  /90  | n=4 All 3rd RDT due to sextupoles cancelled 4th RDT except 4Qx, 2Qx+2Qy, 4Qy, 2Qx-2Qy due to sextupoles cancelled dQ(Jx,Jy): accumalte to be large dQ(): small even with 2 families DA on momentum: limited by tune shift dQ(Jx,Jy) DA off momentum: easy to optim. | n=5 All 3rd RDT due to sextupoles cancelled 4th RDT except small 4Qx, 2Qx+2Qy, 4Qy, 2Qx-2Qy due to sextupoles cancelled dQ(Jx,Jy): small dQ(): correct with many families DA on momentum: large as small tune shift dQ(Jx,Jy) DA off momentum: with many families to correct dQ() and –I break down
For the Arc region, the FODO cell structure is chosen to provide a large filling factor.

## Slide 9: Linear optics design of ARC region
-I
-I
  FODO cell, 90/90, non-interleaved sextupole scheme, period =5cells
Twin-aperture of dipoles and quadrupoles is adopt in the arc region to reduce the their power. The distance between two beams is 0.35m.
SD
SD
SF
SF
Notes: Should be 5 cells

## Slide 10: Nonlinearity correction of ARC region
  FODO cell, 90/90, non-interleaved sextupole scheme, period =5 cells
  tune shift dQ(Jx, Jy) is very small
    DA on momentum: large
  Chromaticity dQ() need to be corrected with many families
    DA off momentum: with many families to correct dQ()
  With 2 families of sextupoles in each 4 periods i.e. 20 cells
    all 3rd and 4th resonance driving terms (RDT) due to sextupoles cancelled, except small 4Qx, 2Qx+2Qy, 4Qy, 2Qx-2Qy
    break down of -I due to energy deviation cancelled
    thus cells numbers equal to 20*N in each ARC region
Notes: Should be 5 cells

## Slide 11: FODO cell for cryo-module
336 / 6 / 2RF stations / 2 sections / 2= 7 cells in each section
get a smallest average beta function to reduce the multi-bunch instability caused by RF cavities
  90/90 degree phase advance
  as short as possible distance between quadrupoles, but should be larger than a module length (12m)
90/90 deg
Half cell: 14m+2m
max: 53.8 m
min: 9.5 m
cryo-module
quadrupole

## Slide 12: Optics design of RF region
Common RF cavities for e- and e+ ring (Higgs)
An electrostatic separator combined with a dipole magnet to avoid bending of incoming beam(ref: K. Oide, ICHEP16)
RF region divided into two sections for bypassing half numbers of cavities in Z mode
common RF cavities
combined magnet
Esep=1.8 MV/m
Lsep=50m
Ldrift=75m
x=10cm at entrance of quad
Phase tuning
Phase tuning

## Slide 13: Optics design of Straight section region
The function of the straight section is phase advance tuning and injection.
  Independent magnets for two rings
  0.3m between two quadrupoles of two rings allows a larger size of quadrupoles
Phase tuning
Phase tuning
Injection

## Slide 14
Linear optics of the collider ring
  An optics fulfilling requirements of the parameters list, geometry, photon background and key hardware.

## Slide 15
Sawtooth orbit correction
With only two RF stations, the sawtooth orbit in CEPC collider ring around 1mm for H and becomes 1um after tapering the magnet strength with beam energy.

## Slide 16
LQF=LQD=2.0 m
LQD0=1.73 m, LQF1=1.48m
LQF=LQD=2.0 m
LQD0=1.73 m  2.0, LQF1=1.48m
Synchrotron radiation of quadrupole
large
contribution of QD0 dominant
small
contribution of QF1 and ARC
quadrupole comparative
Radiation power due to quadrupoles:

## Slide 17
Synchrotron radiation of quadrupole (cont.)
x
y
With 10 families of IR sextupoles and 4 families of ARC sextupoles
Hard line: w/ damping only
Dashed line: w/ damping and fluctuation (20 samples, maximum)
Dot-dashed line: w/ damping and fluctuation (20 samples, minimum)
LQF=LQD=2.0 m
LQD0=1.73 m, LQF1=1.48m
LQF=LQD=2.0 m
LQD0=1.73 m  2.0, LQF1=1.48m
25y
35y
The length of QD0 will be optimized to trade off synchrotron radiation and chromaticity.
Further optimization with longer QD0 by MODE is undergoing.

## Slide 18: Summary
  Linear optics of the CEPC collider ring designed fulfilling requirements of the parameters list, geometry, photon background and key hardware.
Nonlinearity correction made to give a good start point of dynamic aperture optimization.
Reducing the synchrotron radiation from QD0 significantly increase the vertical dynamic aperture for on-momentum particle.
Study with errors and correction is undergoing.

## Slide 19
Performance with errors
2968 BPMs, 1502 horizontal and 1460 vertical correctors are used for the orbit correction.
If IR is included, the optics will be very sensitive to the errors. We haven’t find a good solution of optics correction with sextupoles for the whole ring till now.
RMSCOD  24 um (x) and  38 um (y) along the ring after orbit correction