## Slide 1: MPGD Overview
CEPC2017 workshop
Atsuhiko Ochi, Kobe University

## Slide 2: Contents
Introduction to MPGDs
MPGD in High Energy Physics
RD51: international MPGD collaboration
Recent topics of MPGD R&D

## Slide 3: Introduction to MPGD: (Micro Pattern Gaseous Detector)
Using PCB (Printed Circuit Board) technology, we can make fine electrodes for 10μm order.
MSGC (Micro Strip Gaseous Counter) 1988
  A. Oed (France)
  Fine position resol.(～30μm)、 High rate capability （107 /mm2/s）
  However, stability is not sufficient

## Slide 5: Properties of MPGDs
Gas multiplication and/or read out are performed by “micro pattern” instead of conventional wire chambers
Fine patterning realized …
  Fine position resolution ( < 100 micron )
  Fine timing resolution ( < 10nsec )
  High operational capacity for intense irradiation ( > 107 counts/mm )
  ….

## Slide 6: MPGDs: Probably one of the most versatile technology
Single Stage
Multi Stage
Thin Drift
Large Drift
Charge readout
Light readout
Conversion in gas
Conversion outside the gas
Hybrids (different MPGD)
In the extreme case.. Without gas
Flushed
Sealed
Mixture
Pure Noble Gas
Pure Quencher
High Pressure
Ambient Pressure
Low Pressure
Charged Particles
Photons
Neutrons
Tracking
Calorimeter
TPC
Small
Large
Planar
Semi-Cylindrical
Cylindrical
Spherical
Low Gain
Very High Gain
High Granularity
Fast
High Rate
Low Rate
Low Material Budget
Radio-Pure
Thin Windows
Low Fields
High Fields
Pads
Strips
Self Triggering
No Gain

## Slide 7: MPGD in High Energy Physics

## Slide 8
TOTEM (GEM)
LHCb (GEM, mRWELL)
NA48 (micromegas)
DIRAC (MSGC-GEM)
COMPASS(2TGEM+mm, micromegas, GEM)
ATLAS(micromegas)
ALICE(GEM)
GLACIER(LEM)
CAST(micromegas,InGrid)
CMS(GEM, mRWELL)
RED = LHC
Some of them running,
Some of them approved for upgrades
Some of them under evaluation
Fresh Installation
MPGDs and CERN
E. Oliveri, MPGD2017

## Slide 9
GEM / Micromegas : ATLAS and CMS upgrades
Development and optimization of large-area MPGDs for tracking and triggering
MM for the ATLAS Muon System Upgrade:
Standard Bulk MM suffers from limited efficiency at
high rates due to discharges induced dead time
Solution: Resistive Micromegas tecgnology:
2.4 x 1m2
MM resistive chamber constructed and characterized at CERN RD51 lab
GEMs for the CMS Muon System Upgrade:
Single-mask GEM technology (instead of double-mask)
Reduces cost /allows production of large-area GEM
R&D: 6 generations of triple-GEM detectors
Assembly optimization: self-stretching technique: assembly time reduction from 3 days  2 hours
 Add a layer of resistive strips above the readout strips
Spark neutralization/
suppression (sparks still occur, but become inoffensive)

## Slide 10: Further upgrade of ATLAS (2023~)
For large eta muon detector
  Very high rate ~ 107Hz/cm2
Pixelalated Micromegas
Drift plane
Anode
Resistive cathode (-HV)
Pickup electrode
Thin
substrate
(35 μm)
400 μm
Thick substrate
50 μm
Resistive μ-PIC
DLC cathodes
Spark rates in Neutron
Micro-Resistive WELL
Fast timing Micromegas
Use of pico second timing resolution

## Slide 11
ALICE Time Projection Chamber Endplate Upgrade with GEMs
Ion Back Flow in a GEM system reduced from > 5 % (3 GEM) to < 1% (4 GEM)
discovered enhanced ion trapping
at high rates
IROC
OROC1
OROC2
OROC3
Preproduction:
Single-mask GEM allows for production
of ~1 m foils
ALICE TPC Upgrade  replace MWPC with 4-GEM
(to limit space charge effects)
Continuous TPC readout for 50 kHz Pb-Pb readout
Maintain physics requirements:
IBF < 1%, energy; s(E)E < 12% achieved
C. Garabatos

## Slide 12
TOTEM GEM Tracker @ LHC
Sensitive
area
Δϕ=192o
Δϕ=192o
Open
Closed
Stable operation at very high rates up to 12 MHz/cm2
Achieved spatial (time) resolution: 135 mm (7 ns) at high intensity 2* 108 s-1
E. Oliveri
total, inelastic and elastic cross-section measurement
TOTEM Readout Plane

## Slide 13
Experiment/ timescale | Application domain | MPGD technology | Total detector size (single module size) | Operation characteristics/ performance | Special requirements/ remarks
ILC Time Projection Chamber (pad and pixel readout) for ILD: Start > 2030 | High Energy Physics (tracking) | Micromegas GEM | Total area: ~ 20 m2 Single unit detect: - pad readout: ~ 400 cm2 - pixel readout: ~ 130 cm² | Max. rate: < 1 kHz Spatial res.: <150µm Time res.: ~ 15 ns dE/dx: 5 % (Fe55) Rad. Hard.: no | Si + TPC Momentum resolution : dp/p < 9*10-5 1/GeV
ILC Particle Flow Hadronic (DHCAL) Calorimetry for ILC/SiD Start > 2030 | High Energy Physics (calorimetry) | GEM, THGEM RPWELL, Micromegas | Total area: ~ 4000 m2 Single unit detect: 0.5 - 1 m2 | Max.rate:1 kHz/cm2 Spatial res.: 1cm2 cells Time res.: ~ 300 ns dE/dx: 12 % (Fe55) Rad. Hard.: no | Jet Energy resolution: 3-4 %
MPGD Technologies for the International Linear Collider
Particle Flow Calorimetry (ILD/SiD):
ILD
Concept:
SiD
Concept:

## Slide 14
ILC Time Projection Chamber (TPC): MPGD-Based Readout
MPGDs are foreseen as TPC readout for ILC (endcap size~10 m2):
Standard “pad readout” (1x 6 mm2): 8 rows of det. modules (17×23 cm2); 240 modules per endcap
Wet-etched triple GEMs
Laser-etched double-GEMs 100µm thick (“Asian”)
Resistive MM with dispersive anode
“Pixel readout” (55x 55mm2): ~100-120 chips per module → 25000-30000 per endcap
GEM + pixel readout
InGrid (integrated Micromegas grid with pixel readout)
Resistive MM /
InGrid :
InGrid:
Laser- etched GEMs /
Wet-etched triple GEM:
Primary ions create distortions in the
electric field  O(10μm) track distortions
● Machine-induced bkg. and ions from gas
amplification  track distortions 60 μm
=> Gating is needed
● Wire gate is an option
● Alternatively: GEM-gate
J. Kaminski

## Slide 15
ILC DHCAL Particle Flow Calorimetry: Resistive Micromegas
PCB with
pads
& resistive
pattern
Use at future LC or the HL-LHC:
  Operation at high rates
  Suppress discharges, preserve linearity
  High granularity for PF calorimetry,
  Small pads ~1x1 cm2,
  Large dynamic range (1 – 100s of MIPs)
Tests with X-rays, Cu 8 keV, at high rates:
(intermediate RC, Gain=4000):
Excellent linearity up to 1 MHz/mm2
25% lower Gain at 10 MHz/mm2
M. Chefdeville, T. Geralis

## Slide 16: RD51

## Slide 17: RD51
International collaboration for MPGD (Micro Pattern Gaseous Detectors) research and development
  Since 2007
The name of “RD51” means, 51st R&D projects in CERN. However, this collaboration is not only dedicated to CERN projects.
Activities:
  Collaboration meeting is held on twice a year (one is at CERN)
  Additional workshop is held on 1-2 times a year (at CERN)
  Facility of large area MPGD production
  Common beam test facility in SPPS beamline
  Common readout system development: Scalable Readout System (SRS)
  Simulation software (Garfield++)
  Common project: Matching fund for R&D
  Common use of R&D laboratory in CERN
More than 80 institutes (>400 people) are joined.
  Spokes person: Leszek Ropelewski (CERN), Silvia Dall Torre (Trieste)
  Chair of Collaboration Board: Joao Veloso (Portugal)
  Deputy Chair CB: Atsuhiko Ochi (Kobe)

## Slide 18
RD51
Large Area Detectors
Assembly Optimization
RD51 Common Projects
Generic R&D, QA
Long Term Stability
Software Tools and
Simulations
MPGD Electronics
CERN MPGD
Workshop,
Quality Control
and Industrialization
RD51 Common
Test Beam and Lab Facilities
WG5:
WG4:
WG1:
WG2:
WG7:
WG6:
Conferences / Schools
Academia-Industry
Matching Events
RD51 Collaboration Organization
WG3/NEW WG:

## Slide 19
A fundamental boost is offered by RD51: from isolate MPGD developers to a world-wide net
A combined map of organizations working
with MPGDs built with collaboration-spotting
software developed at CERN
 huge growth in interest in the MPGD
technologies
Collaboration Spotting Software:
http://collspotting.web.cern.ch/)
RD51 and the Rise of Micro-Pattern Gas Detectors
J.-M. Le Goff

## Slide 20: Scalable Readout System
Once upon a time
  Complete non experiment-specific read-out systems; for example:
    RMH, MWPC read-out developed at CERN; PCOS III by Le Croy
Then, experiment dedicated systems
Still, up-to-date read-out systems available off-the-shelf needed
  A must for detector developers, wider use according to needs
Scalable Readout System (SRS) for MPGDs (developed with RD51)
A variety of FE chips: APV25, VFAT, Beetle, VMMx, Timepix
Common acquisition hardware & software
Scalable readout architecture: ~100 ch.s  ~100 k ch. (ATLAS MAMMA project)
So successful, to be used outside MPGDs (SiPM, ALICE Ecal, …)
Cheap!
~ 2 € / ch + FE

## Slide 21
Total cost （128ch board X 4 + modules + Crate, etc.) ~ 5000CHF

## Slide 22
Focus on providing techniques for calculating electron transport in small-scale structures
The main difference with traditional gas-based detectors is that the electrode scale
(~ 10 mm) is comparable to the collision mean free path
Development and Maintenance of Garfield++: Garfield++ is a collection of classes for the detailed simulation of small-scale detectors.
Garfield++ contains: - electron and photon transport using cross sections provided by Magboltz - ionisation processes in gases, provided by Heed and MIP - ionisation and electron transport in semi-conductors - field calculations from finite elements, boundary elements, analytic methods Simulation Improvements:
 Transport:
- ion mobility and diffusion, measurement and modelling
- Magboltz cross sections (Ar, Xe, He, Ne; GeH4, SiH4, C2H2F4 ) are frequently
updated in collaboration with LXCAT (http://www.lxcat.laplace.univ-tlse.fr)
- e-ion recombination process in Xe
- thermal motion
 Photons:
- update in UV emission
- inclusion of IR production
- photon trapping and resulting excitation transport
- photon absorption in the gas (gas feedback)
- photon absorption in and electron emission from walls (feedback)
- photo cathodes
Development of MPGD Simulation Tools

## Slide 23: Recent topic for MPGD
Resistive electrodes for MPGDs

## Slide 25: Resistive-strip protection concept for ATLAS upgrade
We can divide the production process of resistive strip from that of readout board.
Note:
Resistance values
and
Strip pitches and sizes are only for illustration
+HV
Mesh
(GND)
Resistive strip is formed by large size screen printing

## Slide 26
The µ-RWELL architecture
The µ-RWELL_PCB is realized by coupling:
a “suitable WELL patterned kapton foil as “amplification stage”
a “resistive stage” for the discharge suppression & current evacuation:
  “Low particle rate” (LR) << 100 kHz/cm2: single resistive layer  surface resistivity ~100 M/ (CMS-phase2 upgrade - SHIP)
  “High particle rate” (HR) >> 100 kHz/cm2: more sophisticated resistive scheme must be implemented (MPDG_NEXT- LNF & LHCb-muon upgrade)
a standard readout PCB
Drift/cathode PCB
Copper top layer (5µm)
DLC layer (0.1-0.2 µm)
R ̴50 -100 MΩ/□
Rigid PCB readout electrode
Well pitch: 140 µm
Well diameter: 70-50 µm
Kapton thickness: 50 µm
1
2
3
µ-RWELL PCB
G. Bencivenni et al., 2015_JINST_10_P02008
The µ-RWELL detector is composed by two elements:
the cathode and the µ-RWELL_PCB .

## Slide 27
gluing the DLCed foils on the readout -PCBs @ MDT
Coupling the DLCed Kapton with r/o-PCBs

## Slide 28: Resistive μ-PIC
Resistive cathode + capacitive readout
  Cathode : DLC
  Pick-up electrodes are embedded in substrate
  Two dimensional readout
  Gain ~ 5×104 (Ar 70% + C2H6 30%)
  Spark reduction  10-4 (@gain=10000)
Cathode (pickup)
Anode
300mV
従来型μ-PICの放電率
高抵抗陰極型μ-PICの放電率
Gain Curve

## Slide 29
Well-defined PSF of ETCC: Evolution of MeV gamma-imaging beyond Compton Camera
Kyoto Univ.
30cm-cubic Gaseous Time Projection Chamber
--- tracking of recoil electron ---
SPD ->a Point Spread Function(PSF)
Tanimori et al., ApJ (2015), 810, 28
PSF ~ 40˚
PSF ~ 1˚
Cosmic γ-ray detector
Significance maps and contours of three 137Cs sources with different intensities at a distance of 2 m.
Without tracking information.
Using the arcs with SPD resolution of 200˚ before improving
SPD resolution of 100˚
Combination of SPD resolutions of 90˚ and 45˚
Fine 3D-electron tracking gives ϕ, and well-defined PSF (1-2˚)
Environmental γ-ray camera
(for nuclear plant disaster)
Micro TPC + PSA
Power Supply
Battery (25V, 100Ah)
137Cs Imaging on ground
1-5μSv/h : Not decontaminated
<1Sv/h : Decontaminated
Preliminary
γ-ray from air
From ground
(Low dose)
From ground
(High dose)
Small system
for field measurements.
Weight: 100kg (with batt.)
One day operation available
with once charging

## Slide 30: Very fast timing (Pico second order)
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
preamplification
Charged particle
Semitransparent mode
~80 photons/cm

## Slide 31: Localizing the e- creation point
Limit the direct gas ionization
use a radiator / photocathode electron emitter:
Cherenkov light produced by charged particles crossing a MgF2 crystal
Photoelectrons extracted from a photocathode (CsI)
  Simultaneous & well localized ionization of the gas (time jitter for the Cherenkov light ~10 ps)
  Well defined, small drift gap with strong electric field (~10kV/cm), or no drift
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
preamplification
Charged particle
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
Charged particle
Reflective mode
Semitransparent mode
~80 photons/cm
~80 photons/cm

## Slide 32: Summary
There is many type of MPGDs with versatile.
For current and future HEP experiments, there are many projects for large are, high rate capability, precise resolution, fast timing, low IBF …
The RD51 is international MPGD collaboration with exchange ideas, share the facilities and developing common readout system and simulation tools.
Thank you !

## Slide 33: Backup

## Slide 34: MPGD@High Energy Physics
Experiment/ timescale | Application Domain / | MPGD technology | Total detector size / single module size | Operation characteristics/ performance | Special requirements
ATLAS Muon System Upgrade Start: 2018-2019 Operation > 15years | High Energy Physics (Tracking/ Triggering) | Micromegas | Total area: 1200 m2 Single unit detect: (2.2x1.4m2 ) ~ 2-3 m2 | Max. rate:15 kHz/cm2 Spatial res.: <100µm Time res.: ~ 10 ns Rad. Hard.: 1 C/cm2 | Redundant tracking and triggering. Robustness against ageing Challenging constraints in mechanical precision:
ATLAS Muon Tagger Upgrade: start > 2023 | High Energy Physics (Tracking/triggering) | μ-PIC | Total area: ~2m2 | Max.rate:100kHz/cm2 Spatial res.: <100µm | 
CMS Muon System Upgrade: start > 2020 | High Energy Physics (Tracking/ Triggering) | GEM | Total area: ~ 143 m2 Single unit detect: 0.3-0.4m2 | Max. rate:10 kHz/cm2 Spatial res.: ~100µm Time res.: ~ 5-7 ns Rad. Hard.: 10 LHC y | Redundant tracking and triggering Robustness against ageing
ALICE Time Projection Chamber: start > 2020 | Heavy-Ion Physics (Tracking + dE/dx) | GEM with TPC | Total area: ~ 32 m2 Single unit detect: up to 0.3m2 | Max.rate:100 kHz/cm2 Spatial res.: ~300µm Time res.: ~ 100 ns dE/dx: 12 % (Fe55) Rad. Hard.: 50 mC/cm2 | 50 kHz Pb-Pb int. Rate; continues TPC readout Low IBF and good energy resolution
TOTEM Tracking: Start 2009-now | High Energy/ Forward Physics (5.3≤¦eta¦ ≤ 6.5) | GEM (semicircular shape) | Total area: ~ 4 m2 Single unit detect: up to 0.03m2 | Max.rate:20 kHz/cm2 Spatial res.: ~120µm Time res.: ~ 12 ns Rad. Hard.: ~ mC/cm2 | Operation in pp, pA and AA collisions.
LHCb Muon System Start: 2010 - now | High Energy / B-flavor physics (muon triggering) | GEM | Total area: ~ 0.6 m2 Single unit detect: 20-24 cm2 | Max.rate:500 kHz/cm2 Spatial res.: ~ cm Time res.: ~ 3 ns Rad. Hard.: ~ C/cm2 | Redundant triggering Robustness against ageing
FCC Collider Start > 2035 | High Energy Physics (Tracking/Triggering/ Calorimetry/ Muon detect./) | GEM/MM/ THGEM/ InGrid | Total area: 10.000 m2 (for MPGDs around 1.000 m2 ) | Max.rate:100 kHz/cm2 Spatial res.: <100µm Time res.: ~ 1 ns | Maintenance free for decades