## Slide 1: Status of Semi-Digital Hadronic Calorimeter (SDHCAL)
Haijun Yang (SJTU)
(on behalf of the CALICE SDHCAL Group)
International Workshop on CEPC
IHEP, Beijing, November 6-8, 2017

## Slide 2: Outline
SDHCAL Technological Prototype
  Description
  Test Beam Results
  Hadronic Shower Studies
R&D for Large SDHCAL Modules
  Detectors
  Electronics
  DAQ
  New Challenges
Summary and Conclusion

## Slide 3: SDHCAL for ILD
The SDHCAL-GRPC is one of the two HCAL options based on PFA and proposed for ILD. Modules are made of 48 RPC chambers (6λI), equipped with semi-digital, power-pulsed electronics readout and placed in self-supporting mechanical structure (stainless steel) to serve as absorber.
Proposed structure for SDHCAL-ILD:
  Very compact with negligible dead zones
  Eliminates projective cracks
  Minimizes barrel and endcap separation
  SDHCAL prototype should be able to study hadronic showers and very close to ILD module
Challenges:
  Homogeneity for large surfaces
  Thickness of only a few mm
  Lateral segmentation of 1cm X 1cm
  Services from one side
  Embedded power-cycled electronics
  Self-supporting mechanical structure

## Slide 4: SDHCAL Prototype Construction
10500 64-ch ASICs were tested and calibrated using a dedicated ASICs layout ( 93% ).
310 PCBs were produced, cabled and tested, assembled by sets of six to make 1m2 ASUs
50 detectors were built and assembled with electronics into cassettes.
Self-supporting mechanical structure.
Full assembly took place at CERN.
170 DIF, 20 DCC were built and tested.
DAQ system using both USB and HTML protocol
was developed and used.
JINST 10 (2015) P10039

## Slide 5: SDHCAL Performance
The SDHCAL prototype was exposed to hadron, muon and electron beams
in 2012, 2015 and 2016 on PS, H2, H6 and H8-SPS lines.
Power-pulsing using the SPS spill structure was used to reduce the power consumption.
Self-triggering mode is used but external trigger mode is possible
The threshold information helps to improve on the energy reconstruction by better
accounting for the number of tracks crossing one pad
New data were taken in 2015, 2016 and 2017 with an
improved DAQ system
Noise Hits
Hit time spectrum
for 40 GeV pion

## Slide 6: Event Selection of Hadron Beams
No containment selection.
No Cerenkov detector
Triggerless mode
Power pulsed mode

## Slide 7: Energy Estimation
The thresholds weight evolution with the total number of hits obtained by minimizing a χ2 , Χ2 = (Ebeam-Erec)2/Ebeam
Erec = α (Ntot) N1 + β(Ntot) N2 + γ(Ntot) N3
N1,N2 and N3 : exclusive number of hits associated to first,
second and third threshold.
α, β, and γ : quadratic functions of total number of hits (Ntot)
- Events of H2 runs corresponding to energies :
5, 10, 30 , 60, 80 GeV were used to fit the 9 parameters.
- Then the energy of hadronic events in both
H2( only pions) and H6 (presence of protons)

## Slide 8: Energy Estimation
Comparison of semi-digital versus binary readout
Erec (binary) = C N tot + D N2 tot + F N3tot
Erec (semi-digital) = α (Ntot) N1 + β(Ntot) N2 + γ(Ntot) N3
 Substantial improvement for beam energy >  40 GeV
JINST 11 (2016) P04001

## Slide 9: Data vs MC
JINST 11 (2016) P06014
Hadronic shower is more compact in MC than in data

## Slide 10: Data vs MC
SDHCAL High-granularity impact
Hough Transform is an example to extract tracks
within hadronic showers and to use them to
control the calorimeter in situ
Excellent data/MC agreement for
efficiency and multiplicity obtained with
cosmic muons and test beam muons.
80 GeV hadron
40 GeV pion
40 GeV pion

## Slide 11: Separation of electron/hadron
The technique could be
extended to hadronic showers in magnetic field.
JINST 12 (2017) P05009
It improves on the energy reconstruction by dealing with the hits belonging
to the track segments independently of their threshold.
10 GeV
30 GeV
80 GeV
Energy Resolution

## Slide 12: Arbor PFA
CALICE note CAN054
SDHCAL high granularity is desirable
It helps to optimize the connection of hits belonging to the same shower
by using the topology and energy information
ArborPFA algorithm:
It connects hits and clusters using distance and orientation information, then correct tracker momentum information.
Efficiency
Purity

## Slide 13
Energy Resolution vs No. of Layers
SDHCAL has 48 layers which
aims for ILC Detector
6mm gRPC + 20mm absorber
Optimization no. of layers for CEPC at 240GeV
40-layer SDHCAL yields decent
energy resolution.

## Slide 14
pi
e-
muon
pi
BDT for pion/e, mu Identification

## Slide 15: Pion eff. vs Backgrounds eff.
For same Pion efficiency, we compare electron & muon efficiencies from “simple cut” and “BDT” methods.
BDT has modest improvement for electron suppression and significant improvement for muon suppression.
CALICE note CAN059

## Slide 16: SDHCAL for Future Experiements
Detectors as large as 3m X 1m need to be built
Electronic readout should be the most robust with
minimal intervention during operation.
DAQ system should be robust and efficient
Mechanical structure to be similar to the final one
Envisage new features such as timing, etc..
Goal: to build new prototype with few but large GRPC
and new components  ILD Module0
SDHCAL
ILD Module
GRPC
Glass Resistive Plate Chambers

## Slide 17: Detector Conception
2 m
1 m
inlet
outlet
Prototype circulation system
New circulation system
Construction and operation of large GRPC need some improvements with
respect to the present scenario. Gas distribution : new scheme is proposed
Cassette conception to ensure good contact between the detector and electronics is to be improved
Construction of a few large RPCs has started

## Slide 18: New Electronics
DIF #1
DIF #2
DIF #3
144 ASICs= 9216 channels/1m2
USB
HDMI
ASU1
3072 ch
ASU2
DIF
100 cm
33 cm
HADROC chip
(ASIC)
1m2 board  6 ASUs hosting 24 ASICs
Electronics readout for the 1m3 prototype
1 DIF (Detector InterFace) for 2 ASU (Active Sensor Unit.- PCB+ASICs)  3 DIFs for ONE 1m2 GRPC detector
Electronics readout for the final detector
Only 1 DIF per GRPC (any size) with small dimensions to fit in the small space available at the ILD detector
DIF dimensions

## Slide 19: DAQ System
Global system architecture
HR2, HR3, Petiroc..
For now, KC705
GBT
GLIB
Front-End control and data collection
Clocking and main FSM
PC
gEth
gEth
GBT
PC
GLIB
DIF
Roc based ASU
Clk
Sync cdes
SLC
Async cdes
Veto, trg
data
Implementation of a GBT-based communication system for ROC chips. This aims to reach higher performance using robust and well maintained system in the future

## Slide 20: Mechanical Structure
Improvement on the present system is being made by using Electron Beam Welding rather than bolts to reduce the deformation and the spacers thickness.
Industrial production of flat large absorber plates (3 m X 1 m) by roller leveling process

## Slide 21: Next Step: Better Timing
Multi-gap RPC are excellent fast timing detectors
Several MRPC were designed and built . Excellent efficiency when tested with HARDROC ASICs.
Next step use PETIROC (< 20 ps time jitters) to single out neutron contributions.
Timing could be an important factor to separate showers and better reconstruct their energy

## Slide 22: Next Step: Cooling
108 chips
Rectangular section tubes : 2x1 mm
Copper plate over: 1.5 mm
PCB plate under: 1.4 mm
symmetry
symmetry
1.5 m
0.5 m
Flow in
Flow out
Simulation ¼ structure PCB + Chips
Water cooling :
h = 10000 W/m²/k
Thermal load :
80 mW/chip without power pulsing
27.147 (max) – 24.591 (min) =2.556 oC
Cooling becomes necessary if the power-pulsing scheme is not possible (CEPC project)

## Slide 23: Summary and Conclusion
SDHCAL (since 2011) is the first technological and still the unique complete prototype built for future experiments.
Results of beam tests validate the concept. Many results are obtained.
There is still a place for improvement by using genuine techniques (Hough Transform, MVA, …)
New prototype is on the rails and in principle could be achieved in 2018.
New features such as timing and cooling will play important role in future colliders R&D.
Many thanks for great efforts from CALICE SDHCAL working groups !

## Slide 24: Backup Slides

## Slide 25: Energy Reconstruction
Energy reconstruction formula:
are parameterized as functions of total number of hits(N1+N2+N3)
optimizer
fitted with a Gaussian
Function in a 1.5 range around the mean
20GeV
40GeV
.

## Slide 26: New Electronics: ASIC
HARDROCR3 main features:
Independent channels
Zero suppress
Extended dynamic range (up to 50 pC)
I2C link with triple voting for slow control parameters
packaging in QFP208, die size ~30 mm2
Consumption increase (internal PLL, I2C)
6,3 mm
4,7 mm
H3B TESTED : 786, Yield : 83.3 %
Up to 50 pC
FSB2

## Slide 27: ASU (Active Sensor Unit)
One important challenge is to build a PCB up to 1m length with good planarity to have a homogeneous contact of pads with RPCs in order to guarantee an uniform response along all the detector. After investigation in some companies,
1x0.33 m2 with 13 layer ASUs have been built.
ASU
The ASU-ASU (= ASU-DIF) connections also produced

## Slide 28: New Electronics: DIF
DIF sends DAQ commands (config, clock, trigger) to front-end and transfer their signal data to DAQ. It controls also the ASIC power pulsing
• Only one DIF per plane (instead of three)
• DIF handle up to 432 HR3 chips (vs 48 HR2 in previous DIF)
• HR3 slow control through I2C bus (12 IC2 buses).
Keeps also 2 of the old slow control buses as backup & redundancy.
• Data transmission to/from DAQ by Ethernet
• Clock and synchronization by TTC (already used in LHC)
• 93W Peak power supply with super-capacitors
(vs 8.6 W in previous DIF)
• Spare I/O connectors to the FPGA (i.e. for GBT links)
• Upgrade USB 1.1 to USB 2.0
FPGA XC7A35TFGG484
TEXAS TM4C1294U
POWER
POWER
POWER

## Slide 29
Assembling procedure
6mm(active area) + 5mm(steel) =
11 mm thickness
4.7 mm
4.3mm
ASICs : HARDROC2
64 channels
Trigger less mode
Memory depth : 127 events
3 thresholds
Range: 10 fC-15 pC
110fC, 5pC, 15pC
Gain correction  uniformity
Readout Electronics for RPC
Printed Circuit Boards (PCB) were designed to reduce the cross-talk with 8-layer structure and buried vias.
Tiny connectors were used to connect the PCB two by two so the 24X2 ASICs are daisy-chained. 11m2 has 6 PCBs and 9216 pads.
DAQ board (DIF) was developed to transmit fast commands and data to/from ASICs.
Imad Laktineh (IPNL)
Notes: 29

## Slide 30: PFA and Imaging Calorimeter
Simulation of W, Z reconstructed masses in hadronic mode.
60%/E
30%/E

## Slide 31: CALICE: Imaging Calorimeter
https://twiki.cern.ch/twiki/bin/view/CALICE/CalicePapers
Readout cell size:
144 - 9 cm2  4.5 cm2  1 cm2  0.25 cm2  0.13 cm2  2.5x10-5 cm2
Technology:
Scintillator +
SiPM/MPPC
Gas detectors
Silicon
Silicon
Silicon (MAPS)
Scintillator +
SiPM/MPPC
Silicon

## Slide 32
32
Assembling procedure
6mm(active area) + 5mm(steel) =
11 mm thickness
PCB support (polycarbonate)
PCB (1.2mm)+ASICs(1.7 mm)
Mylar layer (50μ)
Readout ASIC
(Hardroc2, 1.6mm)
PCB interconnect
Readout pads
(1cm x 1cm)
Mylar (175μ)
Glass fiber frame (≈1.2mm)
Cathode glass (1.1mm)
+ resistive coating
Anode glass (0.7mm)
+ resistive coating
Ceramic ball spacer (1.2mm)
Gas gap
Large area gRPC:
Negligible dead zone
(tiny ceramic spacers)
Large size: 1  1 m2
Cost effective
Efficient gas distribution system
Homogenous resistive coating
Schematic of RPC
Ran Han (BISEE)
Haijun Yang (SJTU)
Notes: 32

## Slide 33
DHCAL with RPC
80 GeV Pion
Prototypes of DHCAL based on RPC
ANL (J. Repond, L. Xia et.al.)
1m3, 1 threshold, TB at CERN/Fermilab
IPNL (I. Laktineh et.al.)
1m3, 3 thresholds, TB at CERN since 2012