## Slide 1: CEPC SRF System Study Jiyuan Zhai (IHEP) On behalf of CEPC SRF Team
International Workshop on High Energy Circular Electron Positron Collider
November 7, 2017 IHEP, Beijing

## Slide 2: Outline
SRF layout and parameters
RF transient and instability
Technology design and R&D
Summary

## Slide 3
CEPC SRF System Layout
 | H | W | Z
Collider Ring | 650 MHz 2-cell cavity |  | 
Lumi. / IP (1034 cm-2s-1) | 2 | 4 | 1
RF voltage (GV) | 2.14 | 0.465 | 0.053
Beam current (mA) | 17.7 x 2 | 90.2 | 83.7
Cavity number | 336 | 108 x 2 | 12 x 2
SR power (MW) | 30 | 30 | 2.9
2 K cavity wall loss (kW) | 6.4 | 1 | 0.1
Booster Ring (extraction) | 1.3 GHz 9-cell cavity |  | 
RF voltage (GV) | 1.83 | 0.7 | 0.36
Beam current (mA) | 0.53 | 0.53 | 0.51
Cavity number | 96 | 64 | 32
RF input power (MW) avg. | 0.1 | 0.02 | 0.01
2 K wall loss (kW) avg. | 0.2 | 0.1 | 0.03
# CRFA1 module:
H-14, W-9, Z-1
# BRFA module:
H-6, W-4, Z-2
Same cavities for H, W, Z and one-time full installation
Common collider cavities for H, independent for W & Z

## Slide 4
Michelangelo L. Mangano (CERN), CEPCWS17

## Slide 5
Michelangelo L. Mangano (CERN), CEPCWS17

## Slide 6: CEPC SRF System Layout
1.3 GHz SRF - TESLA / XFEL / ILC / LCLS-II / SCLF …
650 MHz SRF - ADANES (CADS) / PIP-II / eRHIC …

## Slide 7: CEPC Collider Ring SRF Parameters
 | H | W | Z
SR power / beam [MW] | 30 | 30 | 2.9
RF voltage [GV] | 2.14 | 0.465 | 0.053
Beam current / beam [mA] | 17.7 | 90.2 | 83.7
Bunch charge [nC] | 20.6 | 5.8 | 2.6
Bunch length [mm] | 3.5 | 3.7 | 5.2
Cavity number (650 MHz 2-cell) | 336 | 216 | 24
Gradient [MV/m] | 13.8 | 9.4 | 9.6
Input power / cavity [kW] | 179 | 278 | 242
Klystron power [kW] (2 cavities / klystron) | 800 | 800 | 800
HOM power / cavity [kW] | 0.48 | 0.33 | 0.11
Optimal QL | 1.1E6 | 3.1E5 | 3.8E5
Optimal detuning [kHz] | 0.24 | 1.0 | 1.0
Q0 @ 2 K at operating gradient (long term) | 1E10 | 1E10 | 1E10
Total cavity wall loss @ 4.5 K eq. [kW] | 22.7 | 6.7 | 0.8
Input coupler power limit 300 (500) kW, variable, low heat load, be short to reduce cryomodule diameter.
Cavity acceptance Q0 > 4E10 (N-doping), module horizontal test > 2E10 (clean assembly and magnetic hygiene)
Cavity number determined by coupler power capacity, less is better for W and Z to reduce the detuning. 2-cell is a balance of gradient, beam loading and HOM power and damping.
Optimized for the Higgs mode of 30 MW SR power per beam, with enough operating margin and flexibility.

## Slide 8: CEPC Luminosity Limitation from SRF
Average HOM power produced in each 650 MHz 2-cell cavity in a multi-cavity module: 2 kW
  Not a luminosity limit for H and W up to 30 MW beam
  Limit Z luminosity to ~ 2 x 1035 cm-2s-1
  Use KEKB/BEPCII type cryomodules (one single cell cavity per module) for even higher luminosity
Longitudinal coupled-bunch instabilities driven by fundamental impedance of the RF cavities
  Not a serious limit for W up to 30 MW / beam
  Z: cure with RF direct and comb feedback (current limit? variable coupling range? coupler power?)
  Less cavities and cell numbers are preferred to have high stored energy and low impedance. Again, KEKB / BEPCII type cavity, but high gradient and very high input coupler power.
Coupled-bunch instabilities driven by HOM impedance of the RF cavities
  Not a serious limit for W but limit Z luminosity to ~ 1034 cm-2s-1
  Move the idle cavities off-line, gain > 10 times more beam current.
  Improve the HOM coupler design for monopole mode
  KEKB / BEPCII type cavity with deep HOM damping

## Slide 9: Variable Coupling and Power Saving
Variable coupling (Qe: 1E5 ~ 2E6) of power coupler is necessary especially with “high efficiency klystron”:
Collider Ring: same mode, different beam current
  Not so significant, but 10 % is ~ 20 MW AC power (and lower efficiency for lower klystron operation power)
  Compensate Qext scattering
  Enable matching for higher current
Collider Ring: different modes at max design current
  46 % and 32 % more RF power for W and Z with fixed H coupling. Under coupling not good for stability
  Booster
  cavity BW change (easy control or power saving)

## Slide 10: CEPC Booster SRF Parameters
10 GeV injection | H | W | Z
Extraction beam energy [GeV] | 120 | 80 | 45.5
Bunch charge [nC] | 0.62 | 0.17 | 0.078
Beam current [mA] | 0.53 | 0.53 | 0.51
Extraction RF voltage [GV] | 1.83 | 0.7 | 0.36
Extraction bunch length [mm] | 2.9 | 2.0 | 1.1
Cavity number in use (1.3 GHz TESLA 9-cell) | 96 | 64 | 32
Gradient [MV/m] | 18.4 | 10.5 | 10.8
QL (over-coupled) | 1E7 | 1E7 | 1E7
Cavity bandwidth [Hz] | 130 | 130 | 130
Beam peak power / cavity [kW] | 8.8 | 2.6 | 0.5
Input peak power per cavity [kW] (with detuning) | 14.1 | 4.4 | 3.4
Input average power per cavity [kW] (with detuning) | 1 | 0.4 | 0.3
SSA peak power [kW] (one cavity per SSA) | 25 | 25 | 25
HOM average power per cavity [W] | 0.4 | 0.15 | 0.10
Q0 @ 2 K at operating gradient (long term) | 1E10 | 1E10 | 1E10
Total average cavity wall loss @ 4.5 K eq. [kW] | 0.8 | 0.3 | 0.1

## Slide 11: Booster Injection Time Structure
X. Cui

## Slide 12: Booster Voltage Ramp
Energy acceptance η / 0.2 %
Beam energy E0 / 10 GeV
Synchrotron tune νs / 0.01
Gradient Eacc / MV/m
Beam energy increase linearly with time.
RF voltage ramp with constant synchrotron tune to avoid synchrotron-betatron oscillation.
Equilibrium bunch length and quantum lifetime not too short.
Multipacting during voltage ramp?
Counter-phasing can also be used to ramp the effective RF voltage.
Very narrow bandwidth SRF cavity operation with microphonics and Lorentz detuning in a fast ramp synchrotron. Challenging but doable.

## Slide 13: Booster Voltage Ramp
I0 / 0.53 mA
φs / 90 deg
E0 / 120 GeV
ΔfOD / - 339 Hz
ΔfLFD / - 452 Hz
Pg / 14 kW
Vrf / 1.83 GV
Eacc / 18.4 MV/m
I0 / 0.53 mA
φs / 90 deg
E0 / 120 GeV
ΔfOD / - 339 Hz
ΔfLFD / - 452 Hz
Pg / 14 kW
Vrf / 1.83 GV
Eacc / 18.4 MV/m
Assume 10 % Lorentz force detuning (LFD) remains not compensated by piezo actuators, 40 Hz peak-to-peak microphonics (not hard, but need careful cryomodule design and quiet operation condition). LFD factor for TESLA 9-cell cavity with helium vessel and tuner: 1 Hz / (MV/m)2
Ensure the detuning not to cause Robison instability during injection and ramping.
With detuning, forward power 14 kW / cavity for + 20 Hz microphonics, 20 kW for - 20 Hz microphonics.

## Slide 14
CEPC Booster RF voltage linear ramp (Higgs mode)

## Slide 15: Outline
SRF layout and parameters
RF transient and instability
Technology design and R&D
Summary

## Slide 16: Beam Cavity Interaction
CEPC large ring features:
  Large circumference and small revolution frequency (dense beam spectrum)
  W and Z low energy and small radiation damping
  Low injection energy of Booster
Beam loading effects define RF system design and configuration of W and Z:
  Transient beam loading of beam gaps for beam abort, ion-clearing or in bunch trains
  Fundamental mode (FM) induced coupled bunch instabilities (CBI), due to large cavity detuning (low RF voltage and high current) and the parked cavities
  Higher-order-modes (HOM) induced coupled bunch instabilities
Less cavities and cells are preferred to have high stored energy and low impedance.

## Slide 17: Beam Gap Transient
Phase shift caused by beam gaps in DR or APDR
  results in less longitudinal focusing, smaller energy acceptance, lifetime and luminosity, and possible other dynamical problem. Small phase shift can be estimated by (K. Bane, etc., EPAC96):
Max phase variation proportional to number of bunches in a bunch train, or number of bunch trains (for fixed total bunch number) or the gap length.
CEPC Collider Ring | H | W | Z
Max relative voltage drop for 1 % beam gap of the baseline | 0.8 % | 3.0 % | 2.7 %
Max bunch train phase shift for 1 % beam gap of the baseline [deg] | 0.7 | 2.5 | 2.1
Max bunch train phase shift for 1 % beam gap of HL-Z [deg] | / | / | 14
Max bunch train phase shift for 1350 bunch trains of HL-Z [deg] | / | / | 0.5
Max relative voltage drop for 4+4 4 km APDR | 3 % | 26 % | 23 %
Max bunch train phase shift for 4+4 4 km APDR [deg] | 3.2 | 21.0 | 17.8
1 % gap (3.3 us) may be too long for the abort kicker and ion-clearing. 1 us or less is enough.

## Slide 18: Phase Shift Correction Methods
Increase cavity stored energy (less cell number, higher RF voltage, low RF freq)
More uniform distribution (increase bunch train number or length)
Pulsed power (power source hardware limit and low RF-to-beam efficiency)
Klystron phase modulation
Beat cavity (small frequency shift of part of RF sources and cavities, beating)
CEPC-SPPC Workshop, Apr. and Sept. 2016
http://indico.ihep.ac.cn/event/5277/session/9/contribution/45/material/slides/ http://indico.ihep.ac.cn/event/6149/session/2/contribution/55/material/slides/

## Slide 19: Pulsed Power Correction
Constant amplitude and phase of the cavity voltage.
To avoid complicated Lorentz force detuning correction in ring.

## Slide 20: Phase Compensation with Beat Cavity
Tune freq of some RF sources and cavities slightly different from the normal RF sources (650 MHz) and cavities (optimal detuning) – beating
Use linear part of beat wave to compensate voltage and phase variation due to beam loading (non-linearity increases with train length, max. half-fill of the ring)
Higher order beats are more effective but more non-linear
bunch train freq = train # x revolution freq = beat freq / m
K. Kubo etc. Compensation of bunch position shift using sub-RF cavity in a damping ring, PAC93
electron bunch train
positron
bunch train
Number of beat cavities:

## Slide 21: APDR Phase Correction with Beat Cavity
Machine Parameter： wangdou20160918/23（Circumference 61 km） | H Low Power | H High Lumi | W | Z | Z 1-cell
Bunch charge (nC) | 32 | 32 | 18.6 | 12.5 | 12.5
Bunch number (one beam) | 70 | 107 | 400 | 1100 | 1100
Bunch spacing (ns) [bunch train length < 3.2 km] | 152.3 | 98.5 | 26.2 | 9.2 | 9.2
Cavity voltage (MV) | 7.4 | 7.3 | 3.9 | 3.7 | 3.7
Synchrotron phase (deg) | 123 | 122 | 128 | 146 | 146
PDR 1+1 max voltage drop | 11 % | 18 % | 72 % | 140 % | 70 %
PDR 1+1 max phase shift (deg) | 12 | 19 | 67 | / | 49
PDR 3rd order beat cavity# (29 kHz) | 33 | 51 | 83 | 28 | 14
APDR 4+4 max voltage drop | 3 % | 4 % | 18 % | 35 % | 18 %
APDR 4+4 max phase shift (deg) | 3 | 4.8 | 16.7 | 24.2 | 12.1
APDR 2nd order beat cavity# (79 kHz) | 10 | 16 | 27 | 9 | 4

## Slide 22
Phase Shift of HL-Z Beam Gap
Simulation based on D. Teytelman’s MATLAB code
Transfer functions
(Pedersen Model)
1065 trains, 20 bunches each (Tg = 195.7 ns, Tb = 6.15 ns)
1% long gap
mitigate ion-trapping and fast beam ion instability (FBII)

## Slide 23: Comparison of Simulation and Formula
CEPC Z-baseline
CEPC Z-HL
K. Bane, etc., EPAC96
D. Teytelman’s code

## Slide 24: CEPC Z-HL Simulation (T. Kobayashi, KEK)

## Slide 25: CEPC H Simulation (T. Kobayashi, KEK)

## Slide 26: Second Robinson Stability (CEPC HL-Z)
Fast direct feedback (group delay 2 us, loop gain 22).
~ 10 % more power to have Robinson stable operation of high current Z-pole.
by Haipeng Wang’s Mathcad code

## Slide 27: Fundamental Mode Instability of W & Z
Mode number | Impedance / cavity (Ω) | Growth Time (ms) | Growth Time / Damping Time | Growth Rate/ Syn. Freq.
W / -1 | 5.59E+06 | 15.8 | 0.20 | 0.53
Z / -2 | 6.85E+05 | 315.5 | 0.73 | 0.03
Z / -1 | 5.68E+06 | 38.0 | 0.09 | 0.22
Direct (and comb) RF feedback loops to decrease the fundamental-mode impedance and the growth rates at least to the manageable level of the longitudinal bunch-by-bunch feedback system.
CEPC baseline Z FM-CBI (without parked cavities)
CEPC Z FM-CBI with beam current (without parked cavities)

## Slide 28: CEPC Z FM-CBI with beam current (without parked cavities)
P_FPC = 300 kW
Long. radiation damping time: 433 ms

## Slide 29: FM CBI and Power of Parked Cavities
-1 -2 -3 -4 -5 -6 -7 -8 -9 - 10 -11 -12
Beam excited FM power
Sync. oscillation period
Radiation damping time
CBI mode No.
Large detuning and narrow BW to reduce FM power excited by the beam (limit?), but fast-growing CBI modes. Alternating detuning (positive and negative detuned cavities cancel each other) will mitigate the instabilities.
Small input power is required to have the signal to detune the cavity (?). Circulators and loads should keep working for the excited FM power. Cavities should be kept at 2 K to extract HOM power.
Power increases with square of the beam current. Different fill pattern will change the exited power.
Better to move the large number of idle W and Z cavities off the beamline (in the empty place of the future SPPC magnets) or with multi-by-pass (but needs lattice change and longer straight section), rather than parking (detune) them. Similar for the Booster. This will also reduce the HOM impedance significantly. Affect RF section layout and configuration. Dependent on CEPC physics operation model (H, W, Z).
CEPC baseline Z mode FM CBI and beam excited power per cavity of the 156 parked cavities (reduce FM coupling to Qe = 2E6)

## Slide 30: Fill Pattern and Beam Power Spectrum
Normalized beam power spectrum in terms of the fill pattern parameters:
h (f [frequency], nt [number of bunch trains], nb [bucket number between bunch], Mb [number of bunches in one train])
Train repetition: nt f0
Fine structure repetition: f0
Bunch repetition: frf / nb
Fine structure repetition: frf / nb / Mb
Amplitude ~ 1 / (Mb nt)2
Bunch structure dominates when Mb >> nt
Train structure dominates when nt >> Mb
Red: h (1, 1, 10900)
Blue: h (10, 19, 1090)
Green: h (1, 19, 10900)
Pink: h (1090, 4, 10)
Detuned cavities are not always safe. Different fill pattern will move the beam spectrum peaks to generate large power. Slightly change the detune of each cavity to avoid resonance. Same attention should be paid to HOMs.
3.3 MHz
16.25 MHz
162.5 MHz
Frequency (MHz)
h
60 kHz

## Slide 31
HOM power-resonant case
31
Take TM011 mode for example
R/Q=65.2Ω, the most dangerous monopole mode
Qe=2.46E+5
Resonant case | H | W | Z
HOM power (kW) | 20.1 | 130.5 | 112.4
If the HOM frequency is 26 kHz away from the beam spectrum for Z running, the HOM power will be less than 1 kW, while only 11 kHz for H running.
Time average HOM spectrum for Z

## Slide 32: Collider HOM CBI Qext Threshold
Average beta_x,y in RF cavity ~ 30 m
Mode | f (MHz) | R/Q* (monopole Ω, dipole Ω/m) | Qe (H) | Qe (W) idle cavities on-line | Qe (W) idle cavities off-line | Qe (Z) idle cavities on-line | Qe (Z) idle cavities off-line
TM011 | 1165.574 | 65.2 | 1.2×105 | 1.2×104 | 1.9×104 | 6.1×102 | 8.5×103
TM020 | 1383.898 | 1.3 | 5.2×106 | 5.1×105 | 8.2×105 | 2.6×104 | 3.6×105
TM021 | 1717.475 | 19.9 | 2.7×105 | 2.7×104 | 4.3×104 | 1.4×103 | 2.0×104
TM012 | 1832.801 | 17.26 | 2.9×105 | 2.9×104 | 4.6×104 | 1.5×103 | 2.1×104
TE111 | 844.738 | 279.8 | 3.2×104 | 5.2×103 | 8.3×103 | 5.5×102 | 7.7×103
TM110 | 907.592 | 420.1 | 2.1×104 | 3.5×103 | 5.6×103 | 3.7×102 | 5.2×103
TE121 | 1475.553 | 125.8 | 7.1×104 | 1.2×104 | 1.9×104 | 1.2×103 | 1.7×104
TM120 | 1662.599 | 18.8 | 4.7×105 | 7.7×104 | 1.2×105 | 8.2×103 | 1.1×105
3 kHz beam spectrum lines, impossible to detune the HOMs (or just no damping? Q0_TM0mp = Q0_TM010* frf / fHOM)

## Slide 33: Collider HOM CBI with all Effective Qext = 1E4
 | H | W | Z
Cavity number in beam line | 336 | 168 | 168
Shortest growth time of the HOM modes with parked cavities on-line [ms] | 101 (TM110) | 56 (TM110) | 26 (TM011)
Shortest growth time of the HOM modes with parked cavities off-line [ms] | 101 (TM110) | 90 (TM110) | 364 (TM011)
Radiation damping time [ms] | 48 transverse | 162 transverse | 433 longitudinal
Beam feedback time [ms] | 3.3 | 3.3 | 18
Beam current threshold with beam feedback [mA] | 573 | 1528 | 129
Corresponding L / IP [1034 cm-2 s-1] | 61 | 65 | 1.5
L / IP limit from 50 MW SR power [1034 cm-2 s-1] | 3.1 | 6.4 | 15.8

## Slide 34: Booster HOM CBI and Feedback
All larger than beam transverse feedback time limit of 3.3 ms (10 turns) and longitudinal feedback time limit of 3 ms (synchrotron oscillation period)
If the parked booster cavities are moved off beamline, the growth time will be increased to 1.5 and 3 times for the W and Z respectively.
Cavity HOM frequency spread will have more margin
Average beta_x,y in RF cavity ~ 30 m
Modes | f (GHz) | R/Q (monopole Ω, dipole Ω/m) | Qe measured | CBI Growth Time (ms) |  | 
 |  |  |  | H-extraction | W-extraction | Z-extraction
TM011 | 2.45 | 156 | 5.9E4 | 2061.0 | 1314.9 | 788.5
TM012 | 3.845 | 44 | 2.4E5 | 1144.6 | 730.2 | 437.9
TE111 | 1.739 | 4283 | 3.4E3 | 6817.3 | 4465.1 | 2680.6
TM110 | 1.874 | 2293 | 5.0E4 | 865.9 | 567.1 | 340.5
TM111 | 2.577 | 4336 | 5.0E4 | 457.9 | 299.9 | 180.1
TE121 | 3.087 | 196 | 4.4E4 | 11511.5 | 7539.7 | 4526.4
 |  |  |  | H-injection | W-injection | Z-injection
TM011 | 2.45 | 156 | 5.9E4 | 187.2 | 176.3 | 185.2
TM012 | 3.845 | 44 | 2.4E5 | 104.0 | 97.9 | 102.9
TE111 | 1.739 | 4283 | 3.4E3 | 568.1 | 558.1 | 589.2
TM110 | 1.874 | 2293 | 5.0E4 | 72.2 | 70.9 | 74.8
TM111 | 2.577 | 4336 | 5.0E4 | 38.2 | 37.5 | 39.6
TE121 | 3.087 | 196 | 4.4E4 | 959.3 | 942.5 | 994.8

## Slide 35
Frequency Spread
Considering the whole RF system, there will be finite tolerances in the cavity construction.
To find the total effects of all the RF cavities, we need to take into account the spread in the resonance frequencies of different cavities.
For small frequency spread, this will result in an “effective” quality factor Q of the whole RF system.
fR=1.16554GHz, Q=1.10×105, δf=1MHz, 336 RF cavities
A. Hofmann and J. R. Maidment, LEP note 168, 28.6.79.
N. Wang et al. Impedance and collective effects of CEPC, 55th ICFA Advanced Beam Dynamics Workshop on High Luminosity Circular e+e- Colliders – Higgs Factory (HF2014)

## Slide 36: Outline
SRF layout and parameters
RF transient and instability
Technology design and R&D
Summary

## Slide 37: RF Design and Optimization of 650MHz 2-cell cavity
Parameter | Unit | Value
Cavity frequency | MHz | 650
Number of cells | - | 2
Cavity effective length | m | 0.46
Cavity iris diameter | mm | 156
Beam tube diameter | mm | 156
Cell-to-cell coupling | - | 3%
R/Q | Ω | 213
Geometry factor | Ω | 284
Epeak/Eacc | - | 2.4
Bpeak/Eacc | mT/(MV/m) | 4.2
 | P (W) (U = 1J) | Qe
Port 1 | 0.001867 | 2.19E12
Port 2 | 0.001352 | 3.02E12
Port 3 | 0.005441 | 7.51E11
Port 4 | 0.003435 | 1.19E12
Port 5 | 0.003320 | 1.23E12
The length of the cavity beam pipes and ports should be long enough to ensure negligible power dissipation on the gaskets and flanges surface, but cannot be too long to go beyond the critical temperature of Nb.
Special gapless gaskets will be considered to avoid the additional dissipation at different joints.
Cooling of cavity ports by extended helium vessel could be considered especially for the power coupler.
Copper plating is necessary for the bellows between cavities. RF shielded bellow might be needed.

## Slide 38: Cavity Mechanical Analysis
Without tuner and bellow
df/dp
  -68.7 Hz/mbar
  The stress under 2 bar (44.5 MPa)
Tuning
  Tuning sensitivity: 310 kHz/mm
  Stiffness: 16001 N/mm
LFD
  LFD coefficient= - 4.16 Hz/(MV/m)2
LFD @ 5MV/m
Tuning simulation
Stress @ 2 Bar

## Slide 39: Cavity Fabrication
Cavity with more cells (4 or 5-cell)
A must for higher energy operation, and low HOM power (due to low current)
Possible for H with shared cavity if the input coupler power capacity could be increased to 500 ~ 800 kW or use two couplers per cavity for same gradient. If same coupler power, the gradient will be too low and cost more, beam loading effect ... But 1.5 times more HOM power, HOM damping and trapping, cavity pretuning, handling and infrastructure...
Not suitable for high current W and Z
Three 2-cell cavities with coaxial HOM coupler, one 5-cell cavity with waveguide HOM coupler will complete fabrication at the end of 2017.

## Slide 40: 650 MHz Cavity Tuner
Parameters | Unit | Value
Cavity tuning sensitivity | kHz / mm | 310
Cavity spring constant | kN / mm | 16
Coarse (slow) tuner frequency range | kHz | 340
Coarse tuner frequency resolution | Hz | ＜ 20
Fine (fast) tuner frequency range | kHz | ＞ 1.5
Fine tuner frequency resolution | Hz | 3
Motor and piezo temperature | K | 5~10
Motor number |  | 1
Piezo number |  | 2
Operating pressure | Torr | ＜ 5E-5
Operating lifetime | year | 20
Must have high reliability, access port on the cryomodule
Installed at the end of cavity, piezo always compressed
The installation space is limited by HOM coupler

## Slide 41: 650 MHz Single-cell Cavity (before N-doping)
130um BCP + 3 h 750 C annealing + 30um BCP + 120 C bake 48 h
Shielded dewar, remnant magnetic field 20 mG. Additional magnetic shield around cavity.

## Slide 42: N-doped 650 MHz Single-cell Cavity
After N-doping of two 650 MHz single cell cavities (BCP treated), Q0 increased obviously at low field for both cavities, which is first observed in China.
650S1: Q0=7e10 @ Eacc=10 MV/m. But Q0 decreased quickly at high field (>10 MV/m).
650S2: Quench at Q0=6.9e10 @ Eacc=8.8 MV/m.
Flux gate and Helmholtz coil will be added soon for demagnetization.
EP facility will be ready to use in mid 2018.

## Slide 43: N-doped 650 MHz Single Cell Cavity
A. Rowe. LINAC2016
FNAL PIP-II

## Slide 44: Furnaces for N-doping/infusion
2) Furnace at OTIC
Cryo-pump
Successful N-doping
Tantalum heater (not molybdenum). N-infusion not allowed
1) Old Furnace at IHEP
Diffusion pump, not oil free
N-doping failed
not suitable for high Q
3) New Furnace at PAPS
Ordered and will deliver in mid 2018
for N-doping & N-infusion
Maximum operation temperature: 1200 ℃
Effective heating zone: Ф 600 mm x 1500 mm
Vacuum pressure at 900 ℃: < 1e-4 Pa
Oil-free pump system with two cryo-pumps (CTI OB400)
N2 injected with feedback controller
4) New Small Furnace at IHEP (just delivered)
For N-doping and infusion of Nb sample and 1.3 GHz single-cell cavity
Φ300 mm × 500 mm
Outside heating
Cryopump 2500 L/s for H2
MFC vent controlling
Ultimate vacuum
25℃ : 6E-7Pa, 850℃: 2.4E-5Pa

## Slide 45: SIMS Results of N-doping Samples
Doping with Furnace at IHEP
Doping with Furnace at OTIC
after ~5 um EP, N, NbN and CsN all disappear.

## Slide 46: IHEP EP Facility
In design and construction
Located at OTIC Ningxia
Commission in mid 2018
In collaboration with KEK
Flow chart of acid mixing and storage unit
Flow chart of circulation unit

## Slide 47: CEPC Input Coupler Challenges
Frequency (GHz) | 0.65
Power (kW) | 300
Coupling (Qext) | Variable: 1E5~2E6
Heat load spec (dynamic 300 kW, TW, CW) | Dynamic: 1 W / 6 W / 10 W @ 2 K / 5 K / 80 K Static: 0.3 W / 3 W / 6 W @ 2 K / 5 K / 80 K
  High power handling capability: CW, 300 kW ( > 400 kW, update).
  Wide-range variable coupler with low heat load to save power.
  Clean assembled with cavity in class 10 clean room
  Balance coupler vacuum part length (cryomodule diameter size) and heat load.

## Slide 48: CEPC Variable 650 MHz Input Coupler Design
RF design complete, thermal and mechanical design ongoing.
Thermal anchor or helium gas cooling of outer conductor. Water or gas cool of inner conductor.
Start fabrication in end 2017.

## Slide 49: Input Coupler Heat Load
Water cooling of the outer bellow is a must.
RF shielding of the gap between the coupler and cavity connecting flange is very important, since which made great contributions to the 2K heat load.
Try helium gas cooling for next step

## Slide 50: Coupling Adjusting Mechanism
Two bellows on outer or inner conductor.
Method other than changing the penetration depth of the antenna tip : RF short plunger on the doorknob waveguide (standing wave, frequency change, adjusting range …)

## Slide 51: ADS 650 MHz Input Coupler (fixed)
RF, mechanical and thermal design.
ADS 650 MHz input coupler tested up to 130 kW CW (limited by the power source).

## Slide 52
650 MHz Cavity HOM Spectrum and Power
Dangerous monopole: aroud 1200MHz
Dangerous dipole: 800 MHz ~ 900 MHz, 1200 MHz
HOM coupler: 800~1400 MHz
HOM absorber: operating frequency＞1.4 ~ 20 GHz

## Slide 53: 650 MHz Cavity HOM Coupler Design
Heat loss
Mechanical designs
RF design
Multipacting analysis
> 1 kW power
Five-pages report from the International Review Committee of the CEPC HOM Coupler Design chaired by Bob Rimmer (JLAB), July 18, 2017.

## Slide 54: RF Design
equivalent circuit (transmission line model)  optimize each part according to S21 curve
 change to 3D model  electromagnetic optimization
Port1
Port3
Port2
Modes | f (GHz) | R/Q (monopole Ω, dipole Ω/m) | Qe simulation
TM011 | 1165.574 | 65.2 | 2.46E+05
TM020 | 1383.898 | 1.3 | 1.55E+05
TE111 | 844.738 | 279.8 | 1.50E+04
TM110 | 907.592 | 420.1 | 4.58E+02

## Slide 55: TM011 Mode at 1.126 GHz
cut off:TE11 1126MHz
cut off: TM01 1471MHz
Double notch
Due to mode transition
Need to optimize the antenna structure for this mode

## Slide 56: HOM Damping Result
Monopole modes impedance per cavity (cavity impedance thresholds with feedback and parking cavities in beamline)
Without frequency spread
Dipole modes impedance per cavity (cavity impedance thresholds with feedback and parking cavities in beamline)
Without frequency spread

## Slide 57: Tolerance Analysis

## Slide 58: Thermal analysis - Procedure
Materials thermal conductivity change with temperature
Initial static temperature distribution
According to the temperature distribution T, calculate the surface resistance Rs
Power dissipation
(calculated based on Rs)
According to the dissipation power Ploss, load surface heat source
According to the surface heat source, recalculate the temperature distribution T
<convergence factor δ
No
Yes
Get the steady state temperature distribution
Preliminary calculation
Dynamic thermal analysis procedure
Static thermal analysis results
electric conductivity iterative procedure
Thermal conductivity iterative procedure

## Slide 59: Thermal Analysis and Mechanical Structure
Power dissipation caused by the fundamental mode and 1 kW HOM is in the mW range.
A helium tank outside the HOM coupler is needed.
No active cooling by liquid helium inside the loop.

## Slide 60
Coaxial transmission line with HOM coupler model used to measure the transmission properties of the coupler
symmetry cone & asymmetry cone (200-150-200)
Fabricate two 2-cell aluminum cavities
Measure damping performance of HOM couplers
Check the actual spread of the HOM spectrum due to mechanical tolerance
Low Power Test Bench and Model Cavities

## Slide 61: HOM Absorber
Water cooling pipe
SiC+AlN composite for broadband microwave absorbing
Brick structure to reduce the fabrication cost
Microwave absorbing material test system

## Slide 62: ε and μ Test Result for Ferrite
Chart: ε'
Chart: ε''
Chart: μ'
Chart: μ''

## Slide 63: HOM Damping for TM111
Integral simulation of “cavity + HOM absorber + taper”:
Cavity + HOM absorber + taper model
absorber
Simulate the real HOM absorbing situation
For example: TM111 mode, frequency=1.456GHz, system QL=56.7

## Slide 64: Broadband Absorbing Efficiency
64
50%
The broadband absorbing efficiency is larger than 50%.

## Slide 65: TE121
f (MHz) | R/Q (Ω/m) | Qe (4 ports) | Qe (6 ports)
1476.923 | 126 | 5441 | 19
1514.663 | 13 | 3.75e+6 | 2E+4
f=1476.923MHz
f=1514.663MHz
1
2
3
4
EB
EB
1
2
3
4
5
6
For TE121-2 mode, only a small amount of HOM power come out from HOM coupler.
A large amount of stored energy concentrate in the middle cell. The field values in the beam pipe is low. Even so it can meet the CBI requirement.

## Slide 66: TM012
f (MHz) | R/Q (Ω) | Qe (4 ports) | Qe (6 ports)
1814.447 | 0.07 | 3.07e+4 | 1095
1832.825 | 17 | 2.14e+7 | 2.8E+4
f=1814.447 MHz
f=1832.825 MHz
For TM012-2 mode, a large amount of stored energy concentrate in the middle cells.
Both end cells are distorted by the presence of the beam pipe on either end of the cavity.
Tuning the end cells for the "trapped modes" is one way to improve the field profile.
Compared with the symmetric end cell design, an asymmetric end cell design is better.
Modify the curve from equator to iris, the iris ellipsis to untrap the TE121 and TM012 mode, but still have the TM010 flat.
Even so it can meet the CBI requirement.

## Slide 67: TM012-2
Detuned cavity 1 and cavity 2 from cavity 3, keep the field flatness of the fundamental mode

## Slide 68
CEPC 650 MHz Cavity Cryomodule
Overall length (flange to flange, m) | 8.0
Diameter of vacuum vessel (m) | 1.3
Beamline height from floor (m) | 1.2
Cryo-system working temperature (K) | 2
Number of cavities and tuners | 6
Number of couplers | 6
Number of RT HOM absorbers | 2
Number of 200-POSTs | 6
Static heat loads at 2 K (W) | 5
Alignment x/y (cavities) (mm) | 0.5
Alignment z (mm) | 2
Structure based on ADS cryomodule. High Q requirement drives new design features (fast cool down and magnetic hygiene).
Fast cool down rate is supposed to be 10 K/min during 45 K to 4.5 K.
Ambient magnetic field at cavity surface should be less than 5 mG. Magnetic shielding and demagnetization of parts and the whole module should be implemented for the magnetic hygiene control.

## Slide 69: 1.3 GHz SRF Technology for CEPC Booster
TESLA cavity. Nitrogen-doped bulk niobium and operates at 2 K. Q0 > 3 × 1010 at 24 MV/m for the vertical acceptance test. Q0 > 1×1010 up to 20 MV/m for long term operation.
XFEL/ILC/LCLS-II or other type variable power coupler. Peak power 30 kW, average 4 kW, Qext 1E7-5E7, two windows.
XFEL/LCLS-II type end lever tuner. Reliability. Large stiffness. Piezos abundance, radiation, overheating. Access ports for easy maintenance.
XFEL and LCLS-II type cryomodule, without SCQ. Technology R&D in synergy with Shanghai XFEL (SCLF). No big challenge.

## Slide 70: SRF Industrialization
TESLA FG 9-cell cavity by HERT (new vendor). Processed and tested at KEK. Two more TESLA cavities in fabrication by HERT (material delivered). High gradient and N-doping / infusion study.
CEPC Industry Consortium

## Slide 71: CEPC SRF R&D Plan (2017-2022)
Two small Test Cryomodules (650 MHz 2 x 2-cell, 1.3 GHz 2 x 9-cell)
Two full scale Prototype Cryomodules (650 MHz 6 x 2-cell, 1.3 GHz 8 x 9-cell)
Schedule
  2017-2018 (key components, IHEP Campus)
    high Q 650 MHz and 1.3 GHz cavities, N-doping + EP
    650 MHz variable couplers (300 kW)，1.3 GHz variable couplers (10 kW)
    high power HOM coupler and damper, fast-cool-down and low magnetic module, reliable tuner
  2019-2020 (test modules integration, Huairou PAPS)
    Horizontal test 16 MV/m, Q0 > 2E10
    beam test 1~10 mA
  2021-2022 (prototype modules assembly and test, Huairou PAPS)

## Slide 72: Test Module with Beam
CW 10 mA
50 MeV
650 MHz test module
DC photo cathode gun
1.3 GHz test module

## Slide 73: IHEP New Large SRF Facility
4500 m2 SRF lab in the Platform of Advanced Photon Source Technology R&D (PAPS), Huairou Science Park, Beijing.
Mission: World-leading SRF Lab for Superconducting Accelerator Projects and SRF Frontier R&D.
Mass Production: 200 ~ 400 cavities (couplers) test per year, 20 cryomodules assembly and horizontal test per year.
Construction: 2017 - 2020

## Slide 74: PAPS Site

## Slide 75: SRF Lab and Cryogenics
2.5 kW @ 4.5 K

## Slide 76: International Review of PAPS SRF Facility
Seven-pages report from the International Review Committee chaired by Carlo Pagani (INFN), July 14, 2017.

## Slide 77: Summary
CEPC baseline SRF parameters and hardware specifications established. Challenges:
  Unprecedented cavity high Q0, large number of very high power variable input couplers, high HOM power in a multi-cavity cryomodule, fast SRF cavity voltage ramp with narrow bandwidth in a storage ring.
  RF transient and coupled bunch instabilities for W and Z operation due to large circumference, low energy and high current. Manageable for baseline. Higher current Z-pole needs more investigation.
SRF key components design and R&D launched, with support of PAPS SRF facility.
CEPC SRF industrialization synergy with SCLF, ADANES, HIAF, HEPS (~ 1000 cavities in next five years), FCC-ee and ILC.
Welcome more domestic and international collaboration.

## Slide 78: Acknowledgement
We thank Carlo Pagani (INFN-LASA and Milano University), Bob Rimmer (JLAB), Haipeng Wang (JLAB), Dmitry Teytelman (Dimtel), Tetsuya Kobayashi (KEK), Eiji Kako (KEK) and SRF Cavity Group of KEK, Hitoshi Hayano (KEK) etc. for their valuable suggestions and kindest help.